HERCGA - Simulate CGA Graphic mode on the Hercules MonoGraphic Card.




This memory-resident utility allows you to "fool" most software requiring
a Color Graphics Adapter into using your Hercules (or compatible) mono-
chrome adapter in the graphics mode.  Graphics images are reproduced
in normal aspect ratio, using as much of the available screen area as
is possible.

The trick used here is to take over the INT 10h (video routine) and
to re-program the video controller of the HGC whenever the CGA graphic
mode is ask.

HERCGA can also take over the INT 8 (timer interrupt) depending on the
options (Automatic, Force Best Screen Mode or Disable Best Screen).
The routine hooked into the hardware timer interrupt (int 8) copies
one line to the third displayed line to give a filled-out image (Best Screen).
CGA use 3 line and HERCGA used 4 when in the Best Screen Option.

The method used here works and results in some useful color gray-scaling,
but it does have a few minor drawbacks -

    1.	Since the copy operation occurs in real-time concurrent with the
	display, some "ghosting" on moving images is inevitable.

    2.	Since the image is expanded vertically by 1/2, small line details
	will be affected by the line doubling technique.  This is mostly
	an aesthetic annoyance.

    3.	Those utilities which "read" the CGA registers at 03d4 et seq.
	are going to find no registers to read.  This does not seem to
	affect many programs.

    4.	40x25 text mode is not supported - the hardware just isn't there.
	This mode is mapped into 80x25 and again, doesn't seem to bother
	many utilities.



Quite a few programs have been tested, including Flight Simulator, PC-CAD,
BASICA, KING QUEST I, II, III (a lot of game) with no hitches.








HERCGA can be use in two differents ways -- Batch mode and Interactive mode.



BATCH MODE.

      Syntax : HERCGA option1 option2

	      Option1 -- I : Install program in memory.
			 U : Uninstall program from memory.
			 B : Install program in the upper memory and Boot.
			     (This option is use for Bootable program. Mostly
			      game.)

	     Option2 --  A : Automatic Best Screen mode selection.(Default)
			     (This option leave to HERCGA the choice of
			       installing Best Screen option (int 8)).
			 N : Disable Best screen option.(preferable in fast
			      real time application).
			 F : Force Best Screen Option.(in this mode HERCGA
			      force whatever program to be hooked with the
			      timer interrupt routine of HERCGA.)

   If option2 is omitted Automatic mode take effect.

   If F option is use some bootable program can be very slow.

   The first time a program is use with HERCGA, the automatic option
   is desirable to see if force mode have to be use or if it can.

   If option1 and option2 are ommited, the iteractive mode take effect.

   N.B - Option2 can not be place first on the command line.








INTERACTIVE MODE.

   In this mode, a menu screen will be display with the following option,
    and a satus line.

	   F1 -- Install program in memory.
	   F2 -- Uninstall program from memory.
	   F3 -- A tri-state toggle key that permit to chose between
		 Automatic mode, Disable Best Screen or Force Best Screen.
	   F9 -- Install program in upper memory and boot.
	   ESC -- Exit to DOS.



  If you want to change the status of the best screen option of the program
  currently in memory, HERCGA have to be first uninstall.



  In best screen mode a problem can occur when scrooling text in the
   320x200 graphic mode. Part of caractere can be missing.



       -------------------------------------------------------------

The program set40.com on the diskette can be use to set the hercules card
in a 40x25 graphic/text mode (equivalent of the medium resolution graphic
mode on the CGA 320x200).

When a software prompt for the mode you normally use on your CGA, Composite
or RGB. Normally the best answer will be RGB mode.





IN CASE OF TROUBLE :

-  If the bootable option do not work with a software; In that case try
   to use a old version of DOS (1.25, 2.00 or 2.10) before installing
   HERCGA in memory, or be shure to have no resident programs in memory
   before calling HERCGA even *.sys device in the onfig.sys file (the best
   is to have no 'config.sys' at all)

- If your program seem to crash at one time. It is probably because of
  resident program that was load before HERCGA. Remove all residents programs
  from memory even the ones in the files 'config.sys' before loading HERCGA.
  (rename config.sys for config.old and reboot)

- Some weird hercules compatible card that can support CGA and Hercules
  (Dual frequency video Card) don't have the same memory mapping has
  the original Hercules card and HERCGA will not work propperly with them.
  Solutions : Get rid of them.

- If the program seem to be much to slow in updating the graphic screen
  try to re-install HERCGA with the option 'Disable Best Screen'.

- Some PC-XT BIOS make text disapear at the DOS prompt (only the cursor
  remain). At this time your computer is not crashed. You just have to work
  blind and type whatever you have to type to execute your program.



	Written in October 1987 by
	Norbert Desautels   Montreal  Quebec