H E R C S A V E   1 . 1
                                          
                     Hercules Graphics Card (tm) Screen Blanker
                                     Version 1.1
          
          
          
          
          
          
          
          
          
          
          
          
          
          
          
          
          
          
          
          
          
          
          
          
          (C) Copyright 1988 by Benjamin Diss
          
          Limited permission is granted to individual users for product
          evaluation and testing.  Continued use of this shareware program
          requires registration as described later in this document.
          
          All other rights are explicitly reserved by the author.












          
          - INTRODUCTION -
          
          Images that appear on a computer monitor for an extended period
          of time may burn the phosphors of the monitor.  This leaves a
          ghost image on the screen.  To help eliminate this problem a
          hoard of screen blanking utilities have been distributed.  These
          programs install themselves in memory and monitor keyboard
          activity and sometimes even video activity.  When there is no
          activity they blank the screen, assuming that the user has no
          immediate need for it.
          
          Unfortunately, none of these programs work properly with the
          Hercules Graphics Card (HGC) while in graphics mode.  When these
          programs restore the screen they assume the video card is IBM
          compatible and treat it as such.  This results in a screen full
          of "garbage" characters.
          
          HERCSAVE eliminates this problem by working within the
          limitations of the HGC.  It allows screen blanking in both text
          and graphics modes.
          












































          
          - USAGE AND INSTALLATION -
          
          HERCSAVE operates by turning the display off after a user
          specified period of keyboard inactivity and on when a key is
          pressed.  HERCSAVE does not monitor video activity as some other
          blankers do.
          
          HERCSAVE can be installed by typing the following at the command
          prompt:
          
               HERCSAVE [s][/o]
          
          S -  represents the number of seconds of keyboard inactivity
               before blank and is a mandatory entry.
          
          O -  causes the program to use the OFFICIAL HERCULES blanking
               routine.
          
          The time before blank may be changed after the program is
          installed by entering the command again with the new seconds.
          The blanking method cannot be changed once HERCSAVE is installed.
          
          There should be no need to use the optional blanking method.
          Install the program in your system and use it.  If you notice
          anything unusual after the screen restores in graphics mode you
          may want to try the optional method.  However, most users do not
          prefer to use this method.
          
          The program is intended to be run from the autoexec.bat file.
          HERCSAVE is a well behaved resident program so it can be loaded
          in any order with other resident programs.  Use your favorite
          text editor to place the appropriate entry into your autoexec.bat
          file.
          































          
          - TECHNICAL CONSIDERATIONS -
          
          The screen can be blanked and restored using two methods.  The
          default is to turn the vertical retrace off to blank and on to
          restore.  The optional method is the OFFICIAL HERCULES blanking
          routine.  It sets the vertical size to zero to blank and restores
          the vertical size register to restore the screen.
          
          The program installs only the required code.  Any routine not
          needed is not in resident memory after installation.
          
          The program copies the required blanking and restoring procedures
          to the resident code space.  It redirects only two interrupts and
          uses minimal memory by releasing the environment space before
          going resident.  Version 1.1 requires only 480 bytes of resident
          memory.
          
          HERCSAVE is optimized for the 80286 but doesn't include any
          specific instructions.  Interrupt routines are word aligned to
          assist the prefetch que in loading the first instruction.  Timing
          optimizations are based on 80286 cycle times.  The program runs
          well on 8088, 8086, and V20 based machines.  Full advantage is
          only found when run on an 80286 or an 80386.
          









































          
          - REGISTRATION AND DISTRIBUTION -
          
          The general public is encouraged to share and distribute copies
          of this program free of charge provided the archive file is kept
          intact, and all files are unaltered.  Users who find HERCSAVE
          useful and intend to use it should register their copy.
          Registration entitles the user to a current version of the
          program, technical support, and product upgrades.
          
          Support from users allows the author to develop additional
          features and future versions of the program.  Your payment of
          $20.00 would be greatly appreciated.  Send payments and other
          correspondence to:
          
               Benjamin Diss
               Micro Computer Consultant
               5800 Oakwood Dr.
               Suite 1B
               Lisle, IL  60532
               
          The author may also be reached on CompuServe and GEnie:
          
               CIS# 71270,341
               GEnie - BDISS
          
          The assembly language source code, site licenses, and custom
          versions are available from the author for a modest fee.
          
          Hercules, Hercules Graphics Card, and HGC are registered
          trademarks of Hercules Inc.
          
          IBM is a registered trademark of International Business Machines
          Inc.