H E R C S A V E   1 . 2
                                          
                     Hercules Graphics Card (tm) Screen Blanker
                                    Version 1.2
       
       
       
       
       
       
       
       
       
       
       
       
       
       
       
       
       
       
       
       
       
       
       
       
       (C) Copyright 1988,89 - Benjamin Diss
       
       Limited permission is granted to individual users for product
       evaluation and testing.  Continued use of this shareware program
       requires registration as described later in this document.
       
       All other rights are explicitly reserved by the author.
       











       - INTRODUCTION -
       
       Images that appear on a computer monitor for an extended period of
       time may burn the phosphors of the monitor.  This leaves a ghost image
       on the screen.  To help eliminate this problem a hoard of screen
       blanking utilities have been distributed.  These programs install
       themselves in memory and monitor keyboard activity and sometimes even
       video activity.  When there is no activity they blank the screen,
       assuming that the user has no immediate need for it.
       
       Unfortunately, none of these programs work properly with the Hercules
       Graphics Card (HGC) while in graphics mode.  When these programs
       restore the screen they assume the video card is IBM compatible and
       treat it as such.  This results in a screen full of "garbage"
       characters.
       
       HERCSAVE eliminates this problem by working within the limitations of
       the HGC.  It allows screen blanking in both text and graphics modes.
       








































                                         (1)






       - USAGE AND INSTALLATION -
       
       HERCSAVE operates by turning the display off after a user specified
       period of keyboard inactivity and on when a key is pressed.  HERCSAVE
       does not monitor video activity as some other blankers do.
       
       HERCSAVE can be installed by typing the following at the command
       prompt:
       
                 HERCSAVE s [/o]
       
       s -  represents the number of seconds of keyboard inactivity before
            blanking.  It is a mandatory entry.
       
       /o - causes the program to use the optional retrace blanking routine.
       
       The time before blank may be changed after the program is installed by
       entering the command again with the new seconds.  The blanking method
       cannot be changed once HERCSAVE is installed.
       
       HERCSAVE supports HOT-KEY blanking.  Once installed, pressing
       <ALT>-<LEFT SHIFT> will instantly blank the screen.
       
       There should be no need to use the optional blanking method.  Install
       the program in your system and use it.  If you notice anything unusual
       after the screen restores in graphics mode you may want to try the
       optional method.
       
       The program is intended to be run from the autoexec.bat file.
       HERCSAVE is a well behaved resident program so it can be loaded in any
       order with other resident programs.  Use your favorite text editor to
       place the appropriate entry into your autoexec.bat file.
       
       

























                                         (2)






       - TECHNICAL CONSIDERATIONS -
       
       The screen can be blanked and restored using two methods.  The default
       is to set the vertical size to zero to blank and restore the size to
       restore the screen.  The optional method turns the vertical retrace
       off to blank and on to restore the screen.
       
       The program installs only the required code.  Any routine not needed
       is not in resident memory after installation.
       
       The program copies the required blanking and restoring procedures to
       the resident code space.  It redirects only two interrupts and uses
       minimal memory by releasing the environment space before going
       resident.  Version 1.1 requires only 496 bytes of resident memory.
       
       HERCSAVE is optimized for the 80286 but doesn't include any specific
       instructions.  Interrupt routines are word aligned to assist the
       prefetch que in loading the first instruction.  Timing optimizations
       are based on 80286 cycle times.  The program runs well on 8088, 8086,
       and V20 based machines.  Full advantage of these optimizations is only
       found when run on an 80286 or an 80386.
       
       History:
       
       3-4-89  - fixed a bug in the hot key routine (thanks to John Lin)
       12-8-88 - 1.1a changed the default blanking method to 'verticle size'

































                                         (3)






       - REGISTRATION AND DISTRIBUTION -
       
       The general public is encouraged to share and distribute copies of
       this program free of charge provided the archive file is kept intact,
       and all files are unaltered.  Users who find HERCSAVE useful and
       intend to use it must register their copy.  Registration entitles the
       user to a current version of the program, technical support, and
       product upgrades.
       
       Support from users allows the author to develop additional features
       and future versions of the program.  Any comments, either good or bad,
       are welcome as user feedback stimulates the design process.  Your
       payment of $15.00 would be greatly appreciated.  Send payments and
       other correspondence to:
       
            Benjamin Diss
            The Smart Solutions Group
            5800 Oakwood Dr.
            Suite 1B
            Lisle, IL  60532
            
       The author may also be reached on CompuServe and GEnie:
       
            CIS# 71270,341
            GEnie - BDISS
       
       The assembly language source code, site licenses, and custom versions
       are available from the author for a modest fee.
       
       Hercules, Hercules Graphics Card, and HGC are registered trademarks of
       Hercules Inc.
       
       IBM is a registered trademark of International Business Machines Inc.


























                                         (4)