PEGAINT (Paradise EGA interrupt)
          Version 1.01
          Ron Gazaway
          
              
          Purpose
          ------- 
          
          This routine is intended to filter the BIOS servicing of INT 10
          service number 0.  Video I/O Set mode.  The translation table is
          specific to the Paradise Autoswitch 480 EGA video board.
           
          !!! This function will only work on 80286 machines. !!!
          
                   
          Usage
          ----- 
           
          This routine installs itself as a TSR utility on invocation.  It
          is not intelligent enough to detect multiple invocations (ie.,
          multiple invocations result in multiple copies being present in
          ram) nor does it have the ability to de-install itself.
           
          After installation the routine monitors BIOS INT 10 calls watching
          for service 0 (set mode) and service 0xF (get mode).  On detection
          of the set mode service call the routine converts the mode number
          which is being requested to another mode number based on a
          conversion table.
              The general effect is as follows:
           
                 requested mode                     actual mode
          --------------------------------      ----------------------------
          
            0 - 40x25 b/w text    CGA             3 - 80x25 color text
            1 - 40x25 color text  CGA          0x51 - 80x30 color text
            2 - 80x25 b/w text    CGA          0x51 - 80x30 color text
            3 - 80x25 color text  CGA          0x51 - 80x30 color text
            7 - 80x25 b/w text    MDA/MGA      0x51 - 80x30 color text
            8 - 160X200 16 color graphics Jr.  0x10 - 640x350 color graphics
            0x10 - 640x350 16 color graphics   0x50 - 640x480 color graphics
             ( any "undefined" mode )          0x50 - 640x480 color graphics
            248 - no function                 toggle PEGAINT active/inactive
           
          The mode number which was requested is saved for use in servicing
          the get mode interrupt (0xF).  On detection of the get mode
          service request the actual mode which the Paradise board is
          operating in will be replaced with the mode number which was last
          requested.
           
          When mode number 248 is requested PEGAINT will go into an inactive
          and perform no INT 10 filtering.  When mode 248 is requested again
          PEGAINT will return to active filtering of INT 10 call.  This is a
          toggle function.     
               
               
          Revision history
          ----------------
          
          PEGAINT:  rev 1.0   August 12, 1987   original
                    rev 1.01  October 29, 1987  added functional description
          
          
     
          Copyright/License/Warranty
          --------------------------
                
          This document and the program file DOTAB.EXE ("the software") are
          copyrighted by the author.  The copyright owner hereby licenses
          you to: use the software; make as many copies of the program and 
          documentation as you wish; give such copies to any one; and
          distribute the software and documentation via electronic means. 
          There is no charge for any of the above. However, you are
          specifically prohibited from charging, or requesting donations,
          for any such copies, however made; and from distributing the
          software and/or documentation with commercial products without
          prior permission.  An exception is granted to not-for-profit
          user's groups, which are authorized to charge a small fee (not to
          exceed $7) for materials, handling, postage, and general overhead. 
          NO FOR-PROFIT ORGANIZATION IS AUTHORIZED TO CHARGE ANY AMOUNT FOR
          DISTRIBUTION OF COPIES OF THE SOFTWARE OR DOCUMENTATION, OR TO
          INCLUDE COPIES OF THE SOFTWARE OR DOCUMENTATION WITH SALES OF
          THEIR OWN PRODUCTS.  THIS INCLUDES A SPECIFIC PROHIBITION AGAINST
          FOR-PROFIT ORGANIZATIONS DISTRIBUTING THE SOFTWARE, EITHER ALONE
          OR WITH OTHER SOFTWARE, AND CHARGING A "HANDLING" OR "MATERIALS"
          FEE OR ANY OTHER SUCH FEE FOR THE DISTRIBUTION.  NO FOR-PROFIT
          ORGANIZATION IS AUTHORIZED TO INCLUDE THE SOFTWARE ON ANY MEDIA
          FOR WHICH MONEY IS CHARGED.  PERIOD.  There is no restriction on
          the use of this software in commercial or institutional
          environments.  No copy of the software may be distributed or given
          away with out this document; and this notice must not be removed. 
          There is no warranty of any kind, and the copyright owner is not
          liable for damages of any kind.  By using this software, you agree
          to this.
               
               The software and documentation are:
               
               Copyright (c) 1987 by
               Ronald O. Gazaway 
               6-2 King Arthur's Way 
               Newington CT  06111