Screen Design Aid - V3.0 - BASIC Interface Revision.


        EINTERFACE TO COMPILED BASIC PROGRAMSF

             The  current  distribution  diskette  contains  an  enhanced 
        version  of  the  interface bridge for used with  compiled  BASIC 
        programs.   This  enhanced version permits inclusion of up to  10 
        screens in program memory at one time,  and elminates one of  the 
        modules required during Link.  It follows the interface described 
        in  the original documentation,  in that it expects to be  called 
        with  three  parameters  passed  by  the  call.   The  first  two 
        parameters  are  integer variables,  while the third is a  string 
        variable.  The functions supported, and the proper content of the 
        passed variables are:

             Display Menu - Parm 1 = 0, Parm 2 = Screen number (1 to 10),
                            Parm 3 = unused.

             Output String- Parm 1 = 1, Parm 2 = Field number, Parm 3 =
                            string to be displayed.

             Input String - Parm 1 = 2, Parm 2 = Field number, Parm 3 =
                            string variable to accept the input string.

             Out/In       - Not supported

             Field Clear  - Parm 1 = 4, Parm 2 = Field number, Parm 3 =
                            unused.

             Position     - Parm 1 = 5, Parm 2 = Field number, Parm 3 =
                            unused.

        As discussed in the original documentation, a string being output 
        will be t t uncated or extended by blanks to the field size defined 
        for  the screen.   Input strings will be similarily  extended  by 
        blanks  or  t  t ncated  to  fit the entry  length  of  the  string 
        parameter passed to this function.  

             To  use this facility,  prepare screens as described in  the 
        main  document.   Having  completed  the design  step,  form  one 
        assembly module, of the form:

             CODE SEGMENT   PARA PUBLIC    'CODE'
                  ASSUME    CS:CODE,DS:CODE
             ;
                  PUBLIC    BASMEN
             ;
             BASMEN    EQU  $
         
                  (Include the source form of the screens desired
                   in the sequence desired...note the sequence)

             ;
                  DW        -1                  ;Must be included!!!!!
             ;
             CODE ENDS
                  END


                                        1





        Screen Design Aid - V3.0 - BASIC Interface Revision.


             Be   particularily  careful  that  the  final  define   word 
        containing 0FFFFH (-1) is included.   Assemble this  module,  andby 
        then  when performing the "Link" of your Basic program,  use  the 
        following control string:

                  your-program+BASSCR+screen-module  (sequence critical)

        when prompted for the "object" code to be linked.  Obviously, the 
        obuse ct  form of the BASMEN you just produced and the  the  ect  form 
        of BASSCR must be available to the Link program.  

             BASSCR requires 3CEH memory, while the screen module size isby 
        a  function  of  the  number and content of  the  screens  to  be 
        displayed.   Execution ion inormal as for any other compiled Basic 
        program.   This  function  performs properly  whether  the  Basic 
        program  was  compiled  for "ststsalone" or "?n  time  library" 
        execution.








































                                        2