Inliner

    Version 1.00                                     File: INLINER.PAS
Last revised: 12 Apr 1985                          Author: Anthony M. Marcy

DESCRIPTION

   Inliner is an assembler which translates 8088 assembly language directly
into Turbo Pascal INLINE code.  It is written in, and generates code for,
Turbo Pascal 2.00 for the IBM PC.  This program is in the public domain.
   Inliner accepts a source language similar, but not identical, to that
of the IBM Macro Assembler (MASM).  It produces a single Turbo INLINE statement
ready to be merged into a Pascal program or used as an Include file.
   All 8088 instructions are supported.  MASM pseudo-ops are not, and there
are a few differences in syntax between Inliner and MASM, as detailed below.
   System requirements are those for running Turbo.  If you can compile
Inliner, you can run it.  (If you can't compile it, you don't need it.)
Maximum assembly program size is set by the size of memory.  Inliner can use
all available contiguous memory.
   The new version 3.00 of Turbo has changes to the INLINE statement which
make it not always compatible with code written for Turbo 2.00.  Inliner 1.00
is designed to work with Turbo 2.00.  In particular, assembly programs which
contain both labels and constant identifiers, and assembled by Inliner, may
not compile correctly under Turbo 3.00.

GETTING STARTED

   You will be prompted for a source file and a target file.  If no source
filename extension is given, .ASM is assumed.  The default target file is
your source filename with extension .PAS; a carriage return accepts the
default, or you may enter any legal filename.
   Quick trick: entering TRM: as the source file will allow you to type your
input directly into Inliner.  It will not be saved, however, and no editing
is available.  End your input with ctrl-z.  Entering NUL as the target file
will cause no output file to be generated, but you can still see the output
on the screen.  Handy if you just need a line or two, or for testing what
will "work".
   Inliner may also be started from the DOS command line, thus:
                A> inliner infile.asm outfile.pas
The second parameter may be omitted, in which case the default is assumed.


INSTRUCTION FORMAT

   An Inliner source line takes the general form:
               label: opcode operand, operand ;comment
Each of these components is optional.

   A LABEL can be anything that would be legal as a Turbo identifier, limited
in length to a maximum of twenty characters.  The colon is mandatory after
a label.

   OPCODEs are the standard Intel mnemonics.  LOCK and the various REP
prefixes are supported.  The segment override prefix can only be placed before
an operand, not before the opcode.

   OPERANDs can be of three general kinds: register, address, and immediate.
Register operands are the usual mnemonics - AX,BX, etc.
Address operands have the following form:
               prefix: (type) [base] [index] offset
Each component is optional.  The ordering is strict.
       prefix is a segment override -- DS, CS, SS, or ES
       type is a single letter --  N   Near
                                   F   Far
                                   S   Short
                                   W   Word
                                   B   Byte
       base is a base register -- BX or BP
       index is an index register -- SI or DI
       offset is either a literal constant or a Turbo identifier

Turbo identifiers are copied into the INLINE code.  Any identifier which does
not occur as a label is assumed to be a Turbo identifier. The compiler replaces
variable names with their offsets within their segments; it replaces constant
identifiers with their values.  The location counter, *, is also legal.  See
the Turbo manual for details.
     ADD AL,var1     ;var1 is a global variable in the data segment
     ADD AL,[BP]var2 ;var2 is a local variable in the stack segment
     ADD AL,CS:var3  ;var3 is a typed constant in the code segment

Immediate operands are distinguished by being prefixed with an equal sign.
They may be constants or Turbo variables.  Thus,
     MOV AX,=2 ;loads the value 2 into AX
     MOV AX,2  ;loads AX with the word at offset 2 in the data segment
     MOV AX,var1  ;loads AX with the contents of variable var1
     MOV AX,=var1 ;loads the offset of variable var1 into AX
The equal sign is optional in the INT, RET, IN, and OUT instructions, and
before character literals.

   CONSTANTs can be decimal integers (positive or negative), hex constants
in Turbo format (preceded by $), constant identifers, or character literals
enclosed in single quotes.  Examples:  2   -128   $FF   cons   'x'
   The type must be specified when it cannot otherwise be deduced:
     ADD AX,[BP]2  ;AX - must be a word operand
     INC (W)[BP]2  ;requires (W) or (B)
Immediate numeric constants default to (B)yte if in the range -128..255,
otherwise (W)ord.

   JMP requires special treatment.  A (F)ar jump to an absolute address may be
coded with two operands, both immediate constants, representing the segment
and the offset:
     JMP =$0060,=$0100   ;absolute address 0060:0100
A (N)ear jump to an offset in the CS requires a single immediate operand:
     JMP =$0100   ;address CS:0100
     JMP =*-1   ;this instruction jumps to itself
An indirect jump takes either a register or an address operand.  In the latter
case, the type must be specified:
     JMP AX     ;must be (N)ear
     JMP (F)[BP][SI]
     JMP (N)var1
Lastly, the jump target may be an Inliner label.  For forward references,
more efficient code can be generated if (S)hort is specified when possible:
     JMP lab1
     JMP (S)lab2

   CALL is similar to JMP, except that (S)hort cannot be used.

   The conditional jump instructions -- JE, JNE, etc. -- take a single
operand which may be either an immediate constant in the range -128..127
or an Inliner label.

   The string instructions vary slightly from MASM syntax.  REP, REPZ, etc.,
are considered prefixes which must be placed before a string opcode on the
same line.  The special no-operand forms of the string opcodes -- MOVSB,
MOVSW, etc. -- are not implemented.  Instead, use the basic opcode with
a type specifier.  The full two-operand forms may also be written.
     REP CMPS (B)
     REP MOVS (W)[SI],[DI]

   Other instructions resemble their counterparts in MASM.  Refer to the
Macro Assembler manual for their formats.  Inliner does not support any
pseudo-ops, such as PROC, END, DW, or ASSUME.  Nor does it support the
8087 mnemonics.
   Pascal declarations should be used to define data, in place of DB, DW,
EQU, etc.  But remember that your variables are Turbo variables -- Inliner
cannot see your declarations to check type or addressibility.  You must
provide segment overrides where needed.


EXAMPLES

   Here are some more examples of Inliner code:

     PUSH BP
 h2: CMP var1,=-1    ;byte variable assumed
     CMP var1,(W)=-1  ;unless overridden
     MOV var2,=var4  ;address is always two bytes
     JE (S)h5
     REPE SCAS(B) ;instead of SCASB
     shl ax,cl   ;lower case is OK
     ESC = 23 , [ DI ] var2 ;spaces are OK, too
     MOV ES:4,'&'
 h5: SUB (W)var3,=$40
     NOP
     CALL (N)xyz ;indirect through variable xyz
                 ;unless xyz is a label
     MOV [BX][DI],CS
     RET (N) 4   ;(N) or (F) required

     -----------------------------------------------------------------

   Inliner is supported on the RBBS-PC operated by
              James Miles
              "The Programmer's Toolbox"
              (301) 540-7230 (data)
              24 Hrs.
Comments, bug reports, and suggested improvements are encouraged.  Address
them to ANTHONY MARCY or to SYSOP.  If you make extensions or revisions
to this program, please upload so that all may share.

                             Enjoy!