INTRODUCTION
============

PIBASYNC.ARC is an archive file which contains a set of routines for
implementing fully-buffered asynchronous serial port I/O from Turbo Pascal
on the IBM PC and compatibles.  The routines have been extracted
from my PibTerm v4.0 program.

Features of PibAsync:

   -- Both input and output buffering for the serial port, resulting
      in improved performance especially under multitaskers
   -- Buffer sizes are user-definable up to 32K bytes each for
      the input and output ring buffers
   -- Speeds up to 19200
   -- Support for Com1: through Com4:
   -- The ability to re-define port addresses, base RS 232 addresses,
      and IRQ lines for non-standard ports
   -- Optional XON/XOFF handling at the interrupt level
   -- Optional CTS/DSR handling at the interrupt level
   -- Machine code (via INLINE) provides respectable speed for
      the basic functions

Limitations:

   -- Only one serial port is supported at a time.  It would be
      an interesting project for someone to provide multiple
      simultaneous port access.
   -- 38400 baud is not available.  If someone would like to add
      that, please feel free to do so and make it available for
      the rest of us.


ARCHIVE CONTENTS
================

The following 14 files should be present in PIBASYNC.ARC:

     ASCII.GLO     --- Some Ascii character set definitions
     ASYINT.ASM    --- ASM source for asynchronous handler
     ASYNCREC.ASM  --- ASM source for receive-a-character routine
     ASYNCSEN.ASM  --- ASM source for send-a-character routine
     DUMBTRM.PAS   --- Sample dumb terminal emulator
     FDELAY.ASM    --- ASM source for 1 ms delay calculation
     FIXBRACK.PAS  --- Routine for neatening .OBJ files produced
                       by the INLINE assembler.
     GLOBTYPE.GLO  --- Global declarations for non-async-related variables
                       needed by async code
     PIBASYN1.MOD  --- Asynchronous I/O routines, part 1
     PIBASYN2.MOD  --- Asynchronous I/O routines, part 2
     PIBASYN3.MOD  --- Asynchronous I/O routines, part 3
     PIBASYNC.GLO  --- Global declarations for async-related variables
     README.DOC    --- What you're reading now
     TIMEREC.ASM   --- ASM source for receiving character with delay

The .ASM files can be assembled with Dave Baldwin's program INLINE.COM,
which converts the assembler source to Turbo Pascal INLINE statements.
(You will need at least v2.11 of INLINE.COM to correctly assemble this code.)
The PIBASYN*.MOD files already contain the processed assembler source,
so you do not need to run INLINE on the .ASM files unless you want to alter
them.


COMPATIBILITY WITH PREVIOUS VERSIONS
====================================

The calling sequences of these revised routines are largely compatible
with those previously available as part of earlier versions of
PibTerm.  If you used those earlier routines, you should be able
to convert to these (with a resulting increase in efficiency) with
very little trouble.  The major important changes are that the
routines Async_Init and Async_Close now take arguments.


DOCUMENTATION
=============

See the documentation block headers for individual routines in PIBASYN*.MOD
for details on the calling sequences and usage of the routines.


SAMPLE PROGRAM
==============

The DUMBTRM.PAS routine demonstrates how to use the PibAsync routines to
build a dumb terminal emulation program.


USE OF THE ROUTINES
===================

You may use these routines for any NON-COMMERCIAL purpose whatsoever.
If you change these routines, you MUST make the revised source
available.  Many individuals used the code from previous versions
of PibTerm and incorporated interesting changes in the async routines,
but did NOT make the resulting changes available in source form
so that all of us could benefit.  I take a dim view of that;  I have
made this source code available so that others can learn from what
I have done (and correct my mistakes).  I expect you to provide
the same courtesy in return.


SUPPORT
=======

Please realize that these routines are not a commercial effort and that
I simply cannot afford the time or money to individually support users.
I WILL NOT return phone calls about these routines, and I WILL NOT
fix your code for you.

There are a number of commercial packages of asynchronous routines
available for Turbo Pascal.  If you need a package for commercial
development, you should consider one of them.

You may send messages to me as indicated below, if you wish.  I will not
necessarily answer all queries individually, however.


COMMENTS, ETC.
==============

You may send comments to me via one of the following means.
I may not answer all messages individually.  Also, I don't check for
mail in these systems every day, so don't expect that a message
will reach me in less than a couple of weeks (except via BITNET).


US Mail:

     Philip R. Burns
     Vogelback Computing Center
     Northwestern University
     2129 Sheridan Road
     Evanston, IL  60208

BITNET:     PIB@NUACC.BITNET

CompuServe: CIS ID  72437,62

BBSs:

     Gene Plantz's BBS   (subscription only)
     Ron Fox's BBS       (312) 940 6496  (open)
     Bob Blacher's BBS   (202) 547 2008  (open)

-- Thanks,
   Phil Burns   11/01/86


Correction for v4.1 of these routines:
=====================================

I corrected delay loops by avoiding the use of a Turbo run-time library
variable.  This 1-millesecond delay variable changed meaning at
v3.02 of Turbo, causing the various delay loops in PibAsync to
run incorrectly (for too short a time).  I now calculate and use
my own delay loop value, independent of Turbo's.

-- Phil Burns   12/27/86


Correction for v4.2 of these routines:
=====================================

A couple of routines incorrectly left a word on the stack that should
have been popped in cases when the circular buffers were full.  Those
problems have been fixed in this version.

-- Phil Burns   01/24/86

Correction for v4.3 of these routines:
=====================================

The send routine incorrectly tested for the wrong circular buffer pointer
when the output buffer was full.  This resulted in output buffer overruns
with lots of attendant nasty problems.

-- Phil Burns   03/25/87

Correction for v4.4 of these routines:
=====================================

The code to setup mark and space parity was incorrect.  This has been
corrected in this version.

-- Phil Burns   07/20/87