[74036,3110]
ARGLIB.DOC     16-Mar-85 6400         76

    Keywords: PORTABLE FILE ARGUMENTS CPM-80 CPM-86 MS-DOS TURBO
    PASCALMT+ BSD UNIX PASCAL

                                                                PAGE 1



           ArgLib - A Portable Pascal File Argument Library

                            15 March 1985

                           Willett Kempton




What ArgLib Does
----------------

     Arglib provides a portable means of reading file arguments from
the operating system command line into a Pascal program.  It also
allows assignment of a name to a file variable and detection of empty
files.  ArgLib became necessary because almost every company's version
of Pascal has implemented these functions in a different way.  By
calling ArgLib, rather than writing system-specific code in each
program, software can be more easily moved across compilers, operating
systems and computers.

ArgLib is currently available for:

  1. Turbo Pascal, CP/M-80, CP/M-86, MS-DOS
  2. Pascal/MT+, Pascal/MT+86
  3. Berkeley UNIX Pascal, pi, pc

Specifics on these implementations follow:

     1.  ArgLib.pas: Turbo pascal.  Tested with Turbo v 1 and v 2, on
         CP/M-80, CP/M-86, and MS-DOS on a DEC Rainbow.  Requires a
         minor modification (marked in the code) to switch among these
         operating systems.  Also, a bug in 8-bit Turbo (v1, v2)
         truncates any command line arguments past 31 characters.

     2.  ArgLibMT.pas: Pascal/MT+86 and Pascal/MT+.  Tested with MT+86
         V 3.1.  Note that in the MT+ version, "argcount" must be
         called prior to "argv".  This is the typical calling sequence
         anyway, but is REQUIRED under MT+ systems.

     3.  ArgLibUX.pas: Berkeley UNIX Pascal.  Tested on Pascal version
         3.0, using both the pi interpreter and the pc compiler on a
         VAX 11/750 running BSD 4.1.



Procedures avaliable
--------------------

     argcount: Argument count.  Function returning an integer count of
how many file arguments were given on the command line.

     argv(count,name): Argument Value.  Procedure setting the variable
"name" to argument number "count" from the command line.









ArgLib  -- Portable file argument library                       PAGE 2



     resetOK(file,name): Assign, reset, and check.  Assign the file
variable "file" to read from the external file or device named "name".
If the external file is nonexistant or empty, return false.  Otherwise
return true.

     For example, suppose that the user calls program "cp" with two
files:

    A>CP FILEA FILEB

     argcount     --> returns the value  2
     argv(1,name) --> sets "name" to 'FILEA           '
     argv(2,name) --> sets "name" to 'FILEB           '
     resetOK(f,name) --> resets f for reading from "name";
                         if nonempty, return TRUE

     Note that under UNIX, argv(0,name) would set "name" to 'CP', but
in the micro version it sets "name" to blank.

     Most pascal systems will require ArgLib to be included after the
last variable of the main program and before the first procedure.
After the include, the following symbols are available.

Symbols available to calling program

 const
   MaxArgStrLen = 16; (* max chars per argument; VARIES WITH OS! *)
 type
   ArgStrType = packed array [1..MaxArgStrLen] of char;

 procedure argv(argn : integer; var name : ArgStrType);

 function argcount : integer;

 function resetOK (var f: text; name: ArgStrType) : boolean;

     Design tradeoffs were as follows.  Execution speed was sacrificed
for compact code, since these routines will typically only be called
once.  Standard Pascal (ISO standard) was used whenever possible (no
'string', etc.).  (Berkeley UNIX Pascal provides no string type.)


Testing ArgLib
--------------

     A test program is provided with ArgLib.  It is called ArgTest.pas
and it includes ArgLib into its source.  The following is a session
using argtest on CP/M:


F>dir
F: SMALL       : EMPTY       : ARGTEST.CMD

F>type empty









ArgLib  -- Portable file argument library                       PAGE 3



F>type small
this is a small file

F>type nothing
NO FILE
F>argtest empty small nothing
file arguments=3
 0=               empty
 1= EMPTY         empty
 2= SMALL         exists
 3= NOTHING       empty

F>

Note that both the empty and the nonexistant files are detected.


Hints for Portable Code
-----------------------

     Some of the programs you write will only be used a few times, or
by their nature, will only be used on one system.  These need not be
portable.  Other programs will retain their value over a period of
years.  During those years, you are likely to use different computers,
and almost certain to use several different compilers.  To preserve
your software-writing investment, you want to be able to transfer your
programs without having to re-write them for each system.  Programs
which allow easy transfer are considered "portable".

     For those programs which you want to be portable, do not use the
compiler manufacturer's manual to guide your writing.  Use a manual on
"Standard Pascal", which is a subset of most commercial Pascals.  The
Standard is defined by ISO, the International Standards Organization,
and by ANSI, the American member of ISO.  The defining ISO document
(ISO dp7185, December 1980) is precise but difficult to read.  Two
readable descriptions of Standard Pascal are available.  One is
"Standard Pascal, User Reference Manual", by Doug Cooper, (1983, W.
W.  Norton & Company).  The other is the THIRD edition of "Pascal User
Manual and Report", by Jensen and Wirth (1984, Springer Verlag).
Either is preferable to the second edition of Jensen & Wirth (1974),
which is less readable and partially inconsistent with the final ISO
standard.

     Sometimes, system dependent features will be necessary, for
example in getting file names from the operating system command line.
When they are needed, they can be localized in a few routines which
can be called in a standard way.  Then to change all your software for
a new system, you need only change a few routines.  ArgLib is an
example of this strategy.








PORTABLE FILE ARGUMENTS CPM-80 CPM-86 MS-DOS TURBO PASCALMT+ BSD UNIX
These routines allow Pascal programs to get arguments (e.g. files,
options) from the command line.  Works in all Turbo systems, with
a one -line change (marked in comments).  Versions are also available
for Pascal/MT+ and BSD UNIX pascal (request upload).