Mite-Size 12-13-88 version
A Set of Merges to Minimize Code Size
for RBBS 17.1C

by Ken Goosens (data line 703-978-6360)

12-13 corects and enhances the 12-11 Lit release for 17.1C

                 What These Merges Do

These merges allow you select what functions to eliminate
from RBBS in order to reduce the size of the compiled program
and reduce the amount of memory needed.

WARNING!!!  These merges must be applied to the UNMODIFIED
source code to RBBS 17.1B.   The merges substitute code for
code in RBBS, and therefore may destroy other changes you
have made to RBBS.   If you have fixes, you may want first to
reduce the code, then add in the fixes.

                   History of Changes

12-13.  Two variables left out of 12-11 release of SETLIT.INC:
        DOORRTN, and ASMFREESP.  Added.

        Three LIT files added:  ASMANSI (omits ANSI.OBJ) by using only
           Basic screen writes.   CONFERENCE (no conferences).  And
           DOORS (no doors).
        
        Documentation (this file) corrected:  base should use is
           17.1B, and QB 4.5 added as possible compiler.


              Why Code Reduction May be Needed

In the absence of an overlay linker or optimizing compiler for
BASIC, RBBS has gotten steadily larger in code size as new functions
have been added, and will continue to do so rather than not add
new functions.  The increase in code size causes a problem on
systems that wish to run 2 nodes within 640K of memory, or
otherwise has only a restricted amount of memory to use.

These merges allow sysops with a supported BASIC compiler to
reduce code size.  This is achieved by eliminating the code
for unused functions, redundant code (typically doing the same
thing in both BASIC and assembler), and functions which the
sysop is willing to sacrifice.

RBBS can then continue to grow while still supporting sysops
with limited memory.


               How to Apply the Merges

1st, you need a copy of the unmodifed source code for 17.1B.
Put this in a separate subdirectory (e.g. 171B)

2nd, in the subdirectory where you normally recompile RBBS,
copy all the files in this application.  Be sure to have
a copy of RBBSSUB5.BAS, since this file will not be modified.

3rd, modify the file MAKELIT.BAT by putting in the drive/path
for the original code (the first parm to BLED).  The lines
you should modify all begin with "*$", which is the default
for a BLED metacommand.   The lines beginning with "* " are
BLED comments, which are ignored in a merge.

4th, get BLED version 2.0 or higher.  The latest is 2.1.
Earlier versions lack the necessary features.
Either put BLED in with the merges or in your
path.  The new BLED functions are documented in BLED.DOC.

5th, use your favorite text editor to modify the file
SETLIT.INC.   Directions are right in the file.   Here is where
you specify what options use are using and which you don't
want.   This is the fundamental "driver" used.   The typical
way you remove code is by setting a variable to the value
"OFF", e.g. BAUD450 to "OFF" to save code by not supporting
changing 300 baud to 450, or LIBRARY to "OFF" if not using the
Library section.

6th, execute the MAKELIT.BAT, which will generate the code
needed to support your application (a new RBBS-PC.BAS,
RBBSSUB2.BAS, and RBBSSUB3.BAS).  The version will say
"17.1A Mite-Sized".  You should get no BLED warnings.

7th, recompile.  Hint:  QB 3 produces the largest code.
QB 2.01 is smaller, and QB 1.02 is the smallest.   QB 4.5
works but produces the largest code of all.
Never use the /E option in linking.  You should
get no errors when recompiling.

8th, reconfigure RBBS for the reduced code, if needed.  For example,
disable the commands for functions you remove, such as taking out
the 'A' command if you turn questionnaires off.


                   What the Files Mean

SETLIT.INC - An file shared by all merges, which sets the
options the sysop wants and does not want.  Basically
defines BLED metavariables.

RBBSLIT.MRG, SUB1LIT.MRG,SUB2LIT.MRG, SUB3LIT.MRG, SUB4LIT.MRG,
SUB5LIT.MRG.

The fundamental BLED merges for rbbs-pc.bas, rbbssub1.bas,
rbbssub2.bas, rbbssub3.bas, and rbbssub4.bas,
respectively.  Each reads in (includes) SETLIT.INC to set
the metavariables, then uses the values to determines what
merges to process in the run.

*.LIT.  Files that reduce the code.


You are welcome to enhance these merges with further code reduction.
Please report any problems to Ken Goosens, data # 703-978-6360.
Realize that there is no way I can test the many different
environments or all the combinations of choices.