Documentation on New Modem Controls
by Ken Goosens, 22 Sept 89

RBBS 17.3 gives the sysop greater control over modem strings.
The modem strings can now have two special characters:

{  for an embedded carriage return
~  for a one second delay

E.g.  "~ATZ{" will wait one second, send "A", then "T", then "Z",
then carriage return, followed by a final carriage return (all modem
commands have a final carriage return added by RBBS).

The new control strings allow the sysop to finely tune the modem
controls.   Two new types of applications are possible:

o   Speed modem processing.

RBBS has a config parameter, time to delay between modem commands,
which is an inserted delay before every modem modem command.   This
can now be set to 0, and the tilde be used to individually control
any delays.   This generally allows the delays to be reduced to
speed up recylcing.

WARNING:  modems are very sensitive to timing.  Experiment carefully
with only change at a time if you want to optimize your modem processing.

o   Prevent modem problems.

Some modems, especially US Robotics modems, including the Courier and
HST, will get into a confused state where they refuse to respond to
further modem commands, when a ring occurs right in the middle of
a modem command.   Ever so often you will find them never answering
with the wrong lights on, and you have to turn the power off and back
on to get the modem working right again.  This problem can be eliminated
by adding an extra carriage return on the end of every modem string.

WARNING:  other modems, such as some Everex modems, will not answer
the phone properly if modem strings are followed by an extra carriage
return.