RBBS SYSOPS, DO YOU REALLY KNOW HOW MUCH USAGE YOUR SYSTEM
                       GETS?  THE PROFESSIONAL ANALYZER KNOW!
                                          
                            Version 12.5B now available
                             Version 13.1A Coming Soon
                                          
                     See the last page for ordering information
                                          
            Be watching for a demo version of The Professional Analyzer
                   in November on better BBS systems everywhere.
            
            
                 The PROFESSIONAL ANALYZER system is an extension to the
            RBBS-PC software.  It provides additional facilities for the
            analysis and  maintenance of  RBBS system and control files.
            Specifically,  the   Professional  Analyzer   provides   the
            following facilities:
            
             1.  Analysis of the RBBS CALLERS file to provide the
                 following:
                 a.  CALLERS file statistics
                 b.  A graph of call distribution by hour of the day
                 c.  A graph of number of calls by baud rate and parity
                     setting
                 d.  A graph comparing upload activity to download
                     activity
                 e.  A graph showing upload activity
                 f.  A graph showing download activity
            
             2.  Analysis of the RBBS MESSAGES file to provide the
                 following:
                 a.  Bytes allocated to messages, bytes used and bytes
                     available
                 b.  Total number of active, killed and blank messages
                 c.  Total number of public, receiver only (private),
                     kill protected and password protected messages
                 d.  Maximum number of messages slots
                 e.  Average size of messages in both records and bytes
                 f.  Percentage of MESSAGES file currently available
            
             3.  Analysis of the USERS file by State in which each user
                 resides
            
             4.  A full function field editor for editing any field in a
                 users profile record found in the USERS file
            
             5.  Facilities for producing statistical reports for use as
                 RBBS bulletins or printed reports
            
            
            
            
            
            












            
            
            
            
            
            
            
            
            
            
            CHAPTER 2  INSTALLATION
            
            
                 Installation  of  the  Professional  Analyzer  is  very
            simple.   The software  is  distributed  on  a  DS/DD  360KB
            diskette.   This diskette should be placed in diskette drive
            A.   The DOS  prompt should  be sitting  on the A drive, the
            +disk to which the system will be installed should be either
            another diskette  or a hard disk.  It is simplest to install
            the Professional Analyzer on the same drive and subdirectory
            as the  RBBS system  files that  will be analyzed.  Once the
            above setup  has been  achieved, enter  the following to the
            DOS prompt:
            
            A:\>INSTALL C:\RBBS
            
            (where C: is the disk drive and \RBBS is the sub-directory
            to which you wish to install the software)
            
                 
                 The system  will then begin installing.  Wait until you
            see the  message, "PROANA  install  completed".    Once  you
            receive this  message the system is now installed.  Put away
            the original diskette for safe keeping and backup purposes.
                 
                 The  Professional   Analyzer  is   not  copy  protected
            although it  does carry  with it  an  identification  module
            named PROANA.UID.   The  integrity  of  this  file  must  be
            preserved.   If this  file is  not present or is in some way
            damaged or  tampered with,  the programs will not run.  This
            file contains the users name and serial number,
                 
                 NOTE:   All    Professional    Analyzer    distribution
            modules/files are assumed to reside on the default drive and
            the current  sub-directory during  execution. Therefore care
            should be  taken to  insure that these files remain together
            in your  system and  that Professional  Analyzer is executed
            only from this sub-directory.
                 
                 You are now ready to begin enjoying your new software!
            
            
            
            












            
            
            
            
            
            
            
            
            
            
            CHAPTER 3  USING THE PROFESSIONAL ANALYZER
            
            
            GETTING STARTED:
            
            At the DOS prompt enter PROANA
            
                   C:\>PROANA
            
                 If this  is  the  first  time  you  have  executed  the
            Professional  Analyzer   since  installing   it,  you   will
            automatically be taken to the configuration menu screen.  If
            you have  already  run  the  program  before  and  are  just
            reviewing this  documentation  you  may  skip  to  the  next
            section following  CONFIGURING THE  SYSTEM entitled THE MAIN
            MENU.   If not,  the system  will respond  with the  message
            "PROANA Configuration  file not found, one will be created".
            You will  then be  presented with a new screen.  This screen
            should be  used to  customize the  system to  your  specific
            installation.
            
            
            CONFIGURING THE SYSTEM:
            
                 The  configuration  screen  will  present  you  with  9
            options which  you may  or may  not need  to  change.    The
            program has  a set  of default  parameters already specified
            You may  used these  defaults or you may change them to your
            needs.   A discussion  of each option follows.  You may skip
            from field  to field  by using  the up  and down cursor keys
            found on the numeric key pad.
            
            o COLOR or MONOCHROME monitor (M or C)
            
                 This field  simply asks  if you  are using  a color  or
            monochrome monitor.  You should enter an M for monochrome or
            a C  for color.  Monochrome is the default and might also be
            advisable for those users who are using a color board with a
            composite signal  monochrome monitor.    If  available,  the
            Professional Analyzer  will  make  full  use  of  the  color
            capability of the PC.
            
            o  RBBS callers file name
            o  RBBS messages file name












            o  RBBS users file name
            o  RBBS DEF file name
            
                 These fields  specify the  name  of  your  RBBS  system
            files.   The standard names for these files are defaults. If
            yours have   not  been renamed  in  the  RBBS  Configuration
            program, then  you may   need  to change  these fields  from
            their default  value.   If your  system doesn't  match these
            defaults then  your specific configuration must be specified
            in these 4 fields.
                 These fields  can contain  up to  21 characters.    Any
            valid DOS  file specification which is 21 characters or less
            is acceptable.  The Professional Analyzer provide DOS device
            and path  specification support.  The following would all be
            valid entries:
                 
                 C:\RBBS\CALLERS
                 A:\USERS
                 A:USERS
                 C:\RBBS\SUB1\MESSAGES
                 MESSAGES
                 \BBS\USERS
                 
            
            o  Statistics output file specification
            
                 This field  specifies the  DOS file  specification  for
            routing Professional  Analyzer hard  copy statistics  out of
            the system.  The default is PROCALL.RPT. This can be renamed
            to any  valid DOS  file specification.  If you wish to route
            the report to a hard copy printer you would specify its file
            spec, such as LPT1: or LPT2:.
                  Many  SYSOPs prefer to create RBBS bulletins from this
            report.   This allows  the RBBS system users to also see the
            statistics of  the systems  utilization.   In this  case you
            might want  to specify this field as BULLETx, where x is the
            bulletin number you wish to uses on the RBBS system for this
            purpose.
            
            o  Beginning date range  (MMDDYY)
            o  Ending date range  (MMDDYY)
            
            
                 The Professional  Analyzer allow  the user to limit the
            analysis of a callers file to certain date ranges within the
            callers file.  If you wish to analyze only a certain date or
            a certain  group of  dates this parameter can be changed for
            the beginning  and ending  dates for which you wish to limit
            your analysis.
            
            
            o  Logo delay time (in seconds)
            













                Once  the  Professional  Analyzer  has  been  completely
            installed and  configured, each subsequent run of the system
            will begin with a graphics display logo.  The amount of time
            the system  keeps this  logo on your screen can be regulated
            here.   Initially, it  has been  set to  9 seconds.  You can
            decrease or  increase this  time period from  1 to 9 seconds
            for all future executions of the system.
            
                 You are  now  finished  with  the  configuration  menu.
            Remember this  menu, as  you may  need to return here in the
            future to  change  some  parameters.    You  will  never  be
            automatically returned  here again  unless  your  PROANA.CNF
            file gets deleted.
            
                 To save  the configuration  hit the ESC key. The system
            will ask if you wish to save the configuration file.  If you
            are happy  with it  now, then reply Y.  If you reply N, then
            you will  have  to  return  back  to  this  menu  again  and
            reconfigure the  system.   The Professional  Analyzer cannot
            properly execute  without the  creation of  a  configuration
            file.
            
            
            
            
            
            
            THE MAIN MENU:
            
                 Once the  configuration process  has been completed and
            saved, you  will be  returned to the logo screen and then to
            the Main Menu screen.
                 
                 The Main Menu is the screen from which all Professional
            Analyzer  functions  are  selected.    These  functions  are
            selected by entering the proper function key associated with
            each function.   F1  selects the  configuration program,  F2
            selects the callers analysis program, F3 selects the message
            file analysis  program ,  F4 selects  the user file analysis
            program and F5 selects the user file editor.
                 
                 No attempt  will be  made  to  explain  in  detail  the
            function of  these programs.   However,  a brief description
            follows along  with a  few notes  to help  make your  use of
            these functions  more  efficient.    The  function  of  each
            program should  be self  evident.  Note the function key and
            control key definitions at the bottom of each screen.  These
            keys will help you use the program.
            
            F1- Configuration Menu
            
                 This is the screen that is automatically generated when
            the system  is first  executed after it is installed.  After
            the first  time, you  will only  return here by request.  If












            your RBBS  system should change its file names or you should
            change your  monitor or  desire to change the date limits of
            the callers  file analysis, you may select the configuration
            program to change these parameters.
            
            F2 - Analyze callers file
            
                 This set  of programs is the most complex to understand
            in the system.  However, since their forunners, known as the
            CALL ANALYZER  have been  well  circulated  and  used,  this
            function should  be familiar  to most  users.  For those who
            are not  familiar with it, you need simply to use it and you
            will become familiar with it.
            
                 Many new  statistics and  graphs have  been added.  The
            function and  control keys  work totally  differently.  Note
            their definitions along the bottom of the displays.
            
            Quick Skip-Ahead
            
            One feature  that is not evident, but is quite handy is what
            we call quick skip-ahead.  You can skip forward or backwards
            several screens at a time by hitting the paging keys (+ or -
            ) several  times.   For instance,  if you are on the callers
            statistics screen  but desire  to  quickly  page  forward  4
            screens to  the baud rate graph, just hit the + (plus) key 4
            time in  quick succession.   The  system will  quickly  jump
            forward 4 screens without you having to wait for the other 3
            screens to  fully display.   To jump back 2 screens quickly,
            just hit the - (minus) key 2 times in rapid succession. This
            feature makes  movement thru  the  displays  very  easy  and
            quick.   All other  functions should  be  obvious  from  the
            function menu along the bottom of each screen.
            
            Site Selected Statistics
            
            Many RBBS  SYSOPS have  modified the  RBBS system  to  write
            additional information  into the  CALLERS file  which is not
            standard to  the CPC  versions of RBBS.  One such well known
            merge file  for RBBS  of this  genre, is the one produced by
            Mark Seiden  in New  York.   In order  to accommodate  these
            users we  have provided  a table  of up  to 19 site selected
            statistics that can be generated by the individual SYSOP who
            so desires.  For a complete discussion of this table and how
            to generate  or modify it, see Appendix A at the end of this
            manual.
            
            F3 - Analyze messages file
            
                 This program provides many summary statistics about the
            current state  and status  of the  RBBS message file.  These
            statistics should be self explanatory.
            
            F4 - Analyze user file












            
                 This program  will read  thru the  RBBS users  file and
            attempt to  analyze, count  and summarize the state in which
            each user  resides.   This is  no small feat since each user
            may have  his own  way of abbreviating his state, or may not
            enter his  city and  state in  a form  which can  easily  be
            recognized.   In those  cases  where  a  state  can  not  be
            recognized as  an integral  part of  the city state field in
            the RBBS  users record,  the  system  will  print  an  error
            message to  the system  printer.  Typically only about 1% of
            users  records   can  not   be  properly   handled  by   the
            Professional Analyzer.
                 
                 This exceptions  error report  can be  used by the RBBS
            SYSOP to  edit users  records to  make the  city state field
            conform to  a standard  which the  user analysis program can
            recognize.     In  addition,   a  state   table,  known   as
            PROSTATE.TBL has  been provided  to allow  SYSOPS to code in
            commonly found  strings which can be recognized as belonging
            to one  state or  another.   This table can be edited by the
            SYSOP with  any text editor.  On many systems, local callers
            might enter  only a large city name such as San Francisco or
            Detroit without providing any state.  The sysop can use this
            table to equate these cities or any similar character string
            to a  specific state.   See Appendix B for details and table
            format information.
                 
                 
            
            
            F5 - Edit users file
            
                 This program  provides full  editing capability for any
            user record  in the RBBS user file.  Often a SYSOP needs the
            ability to change some field or parameter in a users record.
            RBBS provides  some crude editing capability.  However, if a
            SYSOP needs to edit the CITY, STATE field or needs to change
            some user  profile parameters  such as  line feeds on/off or
            graphics on/off, RBBS provides no facilities to do this.
                 
                 This  program   works  exactly  like  the  Professional
            Analyzer configuration  program.   It  is  a  full  function
            editor. The  user can  skip from field to field by using the
            up or  down cursor  keys found  on the numeric key pad.  Any
            field can be edited except the name field, which is the file
            key and the last date and time on the system.
                 
                 To edit  any user  record, enter the users full name at
            the prompt.   Professional  Analyzer will  then  locate  the
            record and  display the data contained in it.  If the record
            does not  exist, you  will receive an error message followed
            by a  prompt for  another users name.   A carriage return to
            the prompt will terminate the editing session.
                 












                 To change the value in any field move the field pointer
            to that  field and  enter the changed data you desire.  When
            you  are   happy  with   your  changes,  hit  the  ESC  key.
            Professional Analyzer  will then  ask if  you wish to update
            this record.   If you do, then reply Y.  An N will result in
            no update.
            
            
            
            
            CHAPTER 4  UPGRADES TO PURCHASERS
            
                 This software is fully supported by Alphasoft and Micro
            South Systems.  It is our intent to keep this software up to
            date with the current level of RBBS.  At the time of release
            of this  version of  the Professional  Analyzer, the current
            version of RBBS was CPC12.5B.  We will provide a new release
            of this  software with  each  MAJOR  new  version  of  RBBS.
            However, it  should not  be necessary  to upgrade  to a  new
            release of  the Professional  Analyzer with each new release
            of RBBS.   The purchaser is encouraged to stay in touch with
            us periodically  to keep abreast of new features which might
            have been added to the system.
                 A licensed  purchaser of  the Professional Analyzer can
            upgrade to  any new release of the system for a $ 20 upgrade
            fee.   Our RBBS system at (404) 761-3635 will always contain
            a bulletin  describing the  current release.  All purchasers
            of Professional  Analyzer are given free access to our RBBS.
            Just call  the system  and leave  your name  and the  serial
            number of  your Professional  Analyzer.  We will provide you
            with full access.
                 We   will   also   provide   upgrade   modules   and/or
            circumventions on  a person by person basis to fix any MAJOR
            bugs which  might be  discovered and  reported to us.  MINOR
            bugs will be corrected in subsequent releases. The preferred
            method for  doing this is thru our RBBS system.  We maintain
            a 24  hour answering  service for leaving messages to report
            errors. The  phone  number  is  (404)  761-8137.    You  can
            generally speak to a real human being by calling this number
            during the weekdays after about 6 PM.  This is the best time
            to call us if you have questions.
                 For software  that sells at such a low price, it is not
            possible for us to return long distance calls to you.
                 If you  wish to upgrade your release of RBBS, send your
            name and  address and  the serial  number  of  your  current
            version along with $20 to:
            
                                 AlphaSoft Systems
                                 2508 Constance Street
                                 Atlanta, Georgia  30344
            
            Allow 3 weeks for delivery.
            
                                 License Agreement












                       Alphasoft Systems/Micro South Systems
                                          
                                          
            AlphaSoft Systems  and Micro  South systems  provides  these
            programs and  licenses their use.  You assume responsibility
            for the  selection of  the programs to achieve your intended
            results, and  for the installation, use and results obtained
            from these  programs.   AlphaSoft Systems  and  Micro  South
            Systems maintain full ownership of these programs.
            
            
            
            
            LICENSE:
            
            You may:
            
            a.   Use these programs on a single machine.
            
            b.    Copy  these programs  for purposes  of  backup  or  in
                 support of  your use  of the  programs  on  the  single
                 machine.     (The  programs,   however,   may   include
                 mechanisms to limit or inhibit copying.)
            
            YOU MAY NOT USE, COPY, MODIFY, OR TRANSFER THESE PROGRAMS OR
            ANY COPY,  OR ANY  PART OF  THIS SOFTWARE  SYSTEM EXCEPT  AS
            EXPRESSLY PROVIDED FOR IN THIS LICENSE.  VIOLATION OF ANY OF
            THE TERMS  OF THIS  LICENSE  AUTOMATICALLY  TERMINATES  YOUR
            LICENSE.
            
            TERM:
            
            This license  is effective until terminated.  You agree upon
            termination of  this license  to destroy  all copies  of the
            program.
            
            
            
            LIMITED WARRANTY:
            
            These programs are provided "as is", without any warranty of
            any kind,  either expressed  or implied,  including, but not
            limited to  the implied  warranties of  merchantability  and
            fitness for a particular purpose.  The entire risk as to the
            quality and  performance of  these  programs  is  with  you.
            Alphasoft Systems  and Micro  South Systems  do not  warrant
            that the  functions contained  in these  programs will  meet
            your needs  or that  the operation of these programs will be
            uninterrupted or  error free.   Alphasoft  Systems and Micro
            South Systems  do warrant the diskette on which the programs
            are furnished  to be  free from  defects  of  materials  and
            workmanship for  a  period  of  ninety  days  from  date  of
            delivery to you as evidenced by a copy of your receipt.
            












            GENERAL:
            
            You agree  that upon  use of these programs you are bound by
            the terms and conditions of this license.
            
            
            
            
            
            
            APPENDIX A   SITE SPECIFIED STATISTICS TABLE DEFINITION
            
                 The Professional  Analyzer allows  a user to specify up
            to 19  site specific  statistics  to  be  reported.    These
            statistics are  based on  searching the  CALLERS file  for a
            specific  character   sting  and   accumulating  the   total
            occurences of each character string in the  CALLERS file.
                 This will  allow a user of the Professional Analyzer to
            modify the  RBBS system  to  report  additional  utilization
            information in  the CALLERS  file.   One popular  RBBS merge
            file  which  provides  some  additional  statistics  is  one
            produced my  Mark  Seiden.    This  merge  to  RBBS  reports
            information about  bulletins read,  comments  left  for  the
            SYSOP and entering and leaving of conferences.
                 The Professional  Analyzer  can  gather  statistics  on
            these CALLERS  file entries.   In  order to  do so, the user
            must specify  the string which is to be searched for and the
            title of  that statistic  as it  should be  displayed by the
            Professional Analyzer.   This file is called PROCALL.CTL and
            can be  created or  edited with  any good  text editor.  The
            file can have up to 19 entries.  The format follows
                 
                 "search string","title of this statistic"
                 "search string","title of this statistic"
                 .
                 .
                 .
                 .
                 .
                 .
                 .
                 .
                 "search string","title of this statistic"
                 
            As an  example lets say that you have modified RBBS to write
            the following  message into  the  CALLERS  file  whenever  a
            caller reads bulletin 6.
            
                 Bulletin #6 read at 23:11:55 by Joe Smith
            
            To add  a statistic  to the  Professional Analyzer  for this
            record  you   would  code   the  following  entry  into  the
            PROCALL.CTL table file.
            












            "Bulletin #6 read at","Times bulletin 6 was read"
            
            The search  string must  be no more than 20 characters long.
            The displayed  string can  be  up  to  25  characters  long.
            Strings which  are longer than this will be truncated on the
            right.   All entires  after the  19th in  the file  will  be
            ignored.
            
            
            
            APPENDIX B  THE USER STATE SYNONYM DEFINITION TABLE
            
            
            The state  synonym table allows the user of the Professional
            Analyzer to equate certain character strings with a specific
            state.   For instance,  many users  call an  RBBS system and
            enter only  a city  in the  RBBS city  and state field.  The
            Professional Analyzer  extract program  cannot differentiate
            between a  state and  city except by the presence of a comma
            (,) or by selecting the last "word" in the city state field.
            In this instances, what the Professional Analyzer assumes to
            be a  state is  incorrect.   It is a city.  In order to make
            the program  equate certain cities (or any character string)
            to certain  states, we have provided a synonym table that is
            editable by  the Professional  Analyzer user.      Any  text
            editor can  be used  for the  purpose of editing this table.
            The format follows:
            
            XX/AAAAAAAAAAAAAAA/BBBBBBBBBBBBBBBBBBB/CCCCCCCCCC/DDDD/EEEE
            
            where XX = A state abbreviation.
                      
                      NOTE:   THIS 2  BYTE PORTION  OF THE  FIELD IS THE
                      STRING TO WHICH ALL OTHERS ARE BEING EQUATED.  FOR
                      THIS REASON,  THE FIRST  2 BYTE FIELD SHOULD NEVER
                      BE EDITED.
            
            AAAAAAAAAAAAAAA = any string
            BBBBBBBBBBBBBBBBBB = any string
            CCCCCCCCCCCCC = any string
            DDDD = any string
            EEEE = any string
            
            As an example:
            
            MA/MASSACHUSETTS/BOSTON/CAMBRIDGE/SALEM/
            
            Up to  5 strings  may follow  the 2  character abbreviation.
            The table  that is  provided with the system already equates
            the  correct   full  spelling   of  each   state  with   its
            abbreviation.  It is the users responsibility to add up to 4
            additional equates as needed.
            













            This feature  should be  used sparingly  as it is limited by
            the additional  4 fields.   It  is best  to edit single RBBS
            USERS records  to conform to the standard city followed by a
            comma followed by a 2 character abbreviation than to try and
            accommodate a few odd USERS records.  This feature should be
            used only when the SYSOP recognizes a common trend that many
            users repeatedly enter such as a city only entry.
            
            
            
            























































            Ordering Information:
            
               To order send $ 49.00 + 3.00 handling and shipping to:
            
                                     AlphaSoft Systems
                                     2508 Constance Street
                                     Atlanta, Georiga  30344
                                     
            Allow 10 days for delivery.  15 day money back gaurantee if
            unsatified.