Copyright 1988 by New-Ware

                        FORMATTING 360K DISKS TO 800K

      FormatMaster includes the unique capability to format 360K low
  low capacity diskettes to 800K in a 1.2M high capacity 5 1/4" drive.
  This is achieved by using the dual head stepping capability built into
  the 1.2M drive to format the 360K disk with 80 vice 40 tracks and by
  adding a 10th sector to each track.

      When formatting a 1.2M disk in a high capacity 1.2M drive, the
  BIOS sets the head stepping to the single-step mode, sets the data
  transfer rate to 500Kb/sec, and formats at 15 sectors per track.  High
  capacity disks have a special media surface capable of handling the
  higher data rate.  When formatting a normal 360K disk in a 1.2 drive,
  the BIOS sets the head stepping rate to the double-step mode, sets the
  data transfer rate to 300Kb/sec, and formats at 9 sectors per track.

      To format a low capacity 360K disk to 800K, FormatMaster forces
  BIOS to set the stepping rate to the single-step mode, the data
  transfer rate to 300Kb/sec, and formats at 10 sectors per track.  Most
  modern AT/PS2 compatible BIOS' have no problem adjusting to the
  non-standard format of the 800K disk but there are some BIOS variants
  that insist upon resetting the stepping rate to the double-step mode
  when accessing any but a 1.2M disk and there are variants of both DOS
  and the BIOS that refuse to recognize the 10th sector on a low
  capacity disk.

      New-Ware now provides a work-around solution to BIOS/DOS variants
  that have trouble recognizing and adjusting to the 800K formatted
  diskette.  The best test to make in order to determine if your system
  needs the extra help provided is to take a normal, low capacity 360K
  floppy, place it in a 1.2M drive, and format it to 800K with
  FormatMaster.  After formatting the disk, terminate FormatMaster and
  use DOS to copy several files to the disk.  If the files appeared to
  copy normally, use the DOS COMP utility to compare the files on the
  target 800K disk and the source files.  If the file compare succeeds,
  you do not need the extra help.

      If you encounter problems during the test above, the next step is
  to use the FormatMaster DOS shell feature.  Go to the Main Menu after
  formatting a disk to 800K and select "Enter DOS".  A special Interrupt
  Service Routine (ISR) is installed that is designed to force DOS
  and/or the BIOS to properly access the 800K disk.  Copy some files to
  the disk and do a file-by-file compare.  If you still have problems,
  then the extra help feature has failed.

      Included in the FormatMaster 2.16 package is a file named
  FM80.COM.  This is a small (688 byte) Terminate and Stay Resident
  (TSR) utility that does essentially the same thing as the FormatMaster
  ISR that is active while shelled out from FormatMaster to DOS.  FM80
  is installed by simply typing the program name and pressing <RETURN>.
  Once this TSR is installed, you should be able to read/write normally
  to FormatMaster 800K disks.  In fact, you will be able to access 800K
  and 1.2M disks, but NOT normal 9 sector 360K disks with the TSR
  installed.  FM80 can be removed from RAM by typing the program name
  followed by a space and then an upper or lower case "R", i.e.,
  entering the command FM80 r from the DOS level or a batch file will
  remove the utility from memory.  Do not attempt to remove FM80 if it
  is not the LAST TSR loaded in RAM.

     There is one other method available to read/write to 800K disks in
  balky systems.  The New-Ware file/disk copy utility CopyMaster has a
  selectable option that will accomplish the same task as FM80 or the
  FormatMaster DOS shell.  When toggled on, this feature will permit
  copying files to/from an 800K disk.

     As a last resort, FormatMaster and FM80 offer a special 720K format
  mode wherein a 360K disk is formatted at 80 tracks and 9 sectors per
  track.  To utilize this mode, enter the string FMSEC=9 into your DOS
  environment with the DOS SET command by either entering the command
  set FMSEC=9 from the DOS level or by placing the same command in your
  AUTOEXE.BAT file and rebooting.  The FormatMaster Main Menu will now
  show a 720K format option instead of an 800K option.  If the
  FormatMaster shell ISR then works okay, you can employ FM80 by adding
  the digit "9" to the command line when loading it, as in FM80 9.
  CopyMaster is also configured to search the DOS environment for the
  string FMSEC=9 for adjustment to a 9 sector, 80 track 720K disk.