Dear Programmer,

thanks for using my Multi-Tasking Subsystem for Turbo Pascal 4.0.
This product was designed to enable everyone to study programming in a
multi-tasking environment, without having to spend a lot of money to
purchase an operating system like OS/2 or XENIX (and of course the
extension memory necessary to run it).

The Turbo Pascal Multi-Tasking Subsystem is a very inexpensive and
yet powerful tool that adds multi-tasking capabilities to your
Turbo Pascal 4.0 programs.
You will be able to study the programming of parallel processes and
problems of interprocess communication using the programming
environment you are accustomed to.

Although the Multi-Tasking Subsystem initially was designed as a means
of experimenting, it became very soon a powerful and easy to use
product, which I hope you will like as much as I do.

At first, I would like to outline the capabilities of the basic system:

- up to 50 (increased on demand) independently executing
  tasks in a single program
- 3 priority levels
- code sharing
- preemptive scheduler, using a dynamic scheduling algorithm
- you may use DOS-functions in your tasks safely. A task is never
  interrupted within a DOS-function or a critical interrupt
- size of timeslice and range of dynamic CPU-allocation programmable
- message passing
- semaphores
- programmable timers
- primitive event processing (up to 10 simultaneously active event
  requests; increased on demand)
- executes on any PC, XT, AT, PS/2 and full compatible running DOS 2.x
  or 3.x
- source code available to registered users


Registered users will get an additional UNIT for FREE(!!) which is
based upon the Multi-Tasking Subsystem and provides you with:

- extended keycodes (Chacter, Scan-Code, Shift-Statusword)
- manipulation of the keyboard buffer (clear, add keycodes at the
  end or in front of the actual buffer contents)
- keyboard lock and unlock
- execute a DOS-program as subtask
- all you need to have tasks wait for a special hot-key that awakes
  them
- all you need to have tasks pop up over the DOS-program and suspend
  the DOS-task while they are executing (another way of writing memory
  resident programs)


Well, no product is perfect!  If you would like to have a function the
Multi-Tasking Subsystem does not include at present, contact me and
perhaps you will find it in the next version. IF I decide to
realize YOUR idea in a later version of the subsystem, you will
receive a FREE-upgrade!  I hope you will understand that I reserve
the right to decide which functions will be added.

In this connection, I would like to thank L. David Baldwin and
TurboPower Software for their fabulous source-level debugger TDebug
PLUS 4.01, that helped me very much during the development of my
Multi-Tasking Subsystem. By the way, most programs written with the
Multi-Tasking Subsystem may be debugged with TDebug PLUS.


Let me stop here!  Please take the time to read carefully through the
documentation before you "dive" into the world of multi-tasking.


Best regards,

   Christian Philipps








                   Turbo  4.0  Multi-Tasking Subsystem


                              User's Manual






                           (c) Copyright 1988 by
                         Christian Philipps, Moers
                            all rights reserved

                       Version 1.10  / September 1988














                     Author:   Christian Philipps
                               H�lsdonker Str. 139a
                               4130 Moers 1
                               West-Germany

                               Fido-Net: PD-Shuttle Bayreuth
                                         Tel.: 0921/67170
                                         Node: 2:509/2
                                         User: Christian Philipps





Trademarks Mentioned

TurboPower Software is trademark of TurboPower Software, Scotts Valley

Turbo Professional is trademark of Sunny Hill Software, used under
license to TurboPower Software

Turbo Pascal is registered trademark of Borland International

MS-DOS, OS/2 and MASM are trademarks of Microsoft Corporation

A86 is trademark of Eric Isaacson Software, Bloomington

UNIX is trademark of AT & T

IBM PC, XT, AT, PS/2 and PC-DOS are trademarks of International
Business Machines Corporation




License Agreement

The Turbo Pascal Multi-Tasking Subsystem is marketed through the
ShareWare marketing concept.

Therefore I grant you the right to reproduce, distribute and use
copies of this ShareWare version of our Multi-Tasking Subsystem
(including the on disk documentation), on the express condition that
you do not receive any payment, commercial benefit, other
consideration for such reproduction or distribution, or change this
license agreement or the copyright notice.

The Multi-Tasking Subsystem, the additional unit MTPOPUP and the
documentation of both are copyright (c) 1988 by Christian Philipps,
H�lsdonker Str. 139a, 4130 Moers 1, West-Germany.

You have the right to evaluate this ShareWare version for a period of
30 days to find out whether it suits your needs. If you decide to
continue using this software, I expect that you become a registered
user by sending DM 50 or $35 (object code license) / DM 100 or $70
(object code + source code license) to

              Christian Philipps
              H�lsdonker Str. 139a

              4130 Moers 1
              West-Germany

As soon as I receive your registration, I will send you your
personal copy of the subsystem plus a FREE unit based upon the basic
subsystem (see introductory letter).
Furthermore you will get technical support through mail, e-mail or
phone during 1 year from the day of receipt.

Users purchasing an oject code license only may receive the source
code of the latest version later at any point of time by sending
another DM 50 or $35 to the adress above.



Disclaimer

I make no warranty of any kind, either express or implied, including
but not limited to implied warranties of merchantability an fitness
for a particular purpose, with respect to this software and the
accompanying documentation.

In no event shall I be liable for any damages (including damages for
loss of business profits, business interruption, loss of business
information, or other pecuniary loss) arising out of the use of or
inability to use this software, even if I have been advised of the
possibility of such damages.





Getting Started

Throughout this documentation I assume that you are familiar with
Turbo Pascal 4.0 in general and with the UNIT concept.
I also assume that you know how to use the advanced features of Turbo
Pascal 4.0, for example type-casting of pointers. If necessary,
please refer to your Turbo Pascal documentation for more information
on any of the compiler's internal functions or the functions contained
in the units Crt, Dos,...


The Multi-Tasking Subsystem mainly consists of three units:

a) TP4MULTI.TPU

   This is the basic Multi-Tasking Subsystem. All further units are
   based upon this piece of software.

b) MTPOPUP.TPU (registered users only)

   MtPopUp is a unit, based upon the basic subsystem and providing
   full control over the system keyboard and supports one DOS-program
   to be run as a separate task. Tasks may be kept waiting for a
   certain key-combination to be pressed and somewhat resident
   programs can be written by executing another COMMAND.COM in the
   foreground. Please note that this unit is available only to
   registered users, who will receive it in return for their
   registration.

c) QUEUE.TPU (Public-Domaine)

   This unit contains several functions, which help you to create,
   delete and manage forward-chained list-structures. The structure
   of a single list element is defined by your application and may be
   any data structure. Passing data between separate tasks, you will
   shortly find out that list structures, as provided by this unit,
   are convenient for implementing pipe-like data structures.
   Studying the routines contained in the accompanying source code for
   QUEUE, you will learn how to assure the consistency of shared data
   at any time during execution.


Let's take a look at the way to USE the Multi-Tasking Subsystem: The
usage of this software is quite straightforward, provided you enable
your compiler to find the necessary units (please refer to your
compiler manual).
You will incorporate the Multi-Tasking library in your programs by
simply including TP4MULTI in the USES-statement. TP4MULTI must be the
first unit of the subsystem preceded, however, by the basic units Crt
(or alternatives) and Dos.

Example: USES Crt, Dos, Tp4Multi, MtPopUp, Queue;

The units TP4MULTI and MTPOPUP use Turbo's CRT-unit, so problems may
arise, when using an alternative CRT-unit (such as the TurboProfes-
sional unit TPCRT) in your program.
For the special case that you own the fantastic TurboProfessional
package of TurboPower Software, your diskette contains files with
the extension .PRO, which I compiled using the TPCRT-unit. You only
need to rename those files to the extension .TPU.

If you wish to use another alternative Crt-unit that conflicts with
the standard CRT-unit, you will have to order the source code and
recompile the subsystem.

After having set up your USES-statement properly, you will have to
include the compiler switch S-, which prevents the compiler
from generating object code that checks the stack boundaries. This
is VERY important, because each task has its own private stack
that is automatically reserved on the heap at the time of creation.
Without the S- directive, you would get a stack overflow abort
shortly after creating the first subtask.

Whenever a task-switch is performed, the Multi-Tasking Subsystem
checks the private stack of a subtask A task which uses up its
stackspace (minus a certain safety margin) is aborted. The subsystem
issues an error message and marks the task as "Crashed". The memory
occupied by its private stack is not freed and may be examined using a
debugger.

Now let's have a look at the system startup. When your program comes
to execution the initialisition code in TP4MULTI captures some
interrupt vectors and sets up the task-table. It creates a
null-process with lowest priority (a simple loop) that consumes
CPU-time whenever no other process is currently computable. Finally
the main program is started as task no. 2.

The shutdown again is fully automatic. When your program terminates
or a runtime error brings you to a halt, TP4MULTI's exit procedure
gains control, disables multi-tasking and restores the interrupt
vectors previously captured.
Only in rare occasions, your system will completely crash. This
could happen, when one of your tasks runs mad and overwrites
valuable system data.

You might start experimenting right now, BUT I recommend studying
the rest of this documentation before. The following sections will
give you a deeper understanding of the concept and the interior of the
Multi-Tasking Subsystem.
Multitasking is too complicated however, to go down to the last.
Those of you, who would like do get a deeper insight into the design
of multi-tasking operating systems should read the book "Operating
Systems, Design and Implementation" by Andrew S. Tanenbaum, Prentice
Hall or scan through the bookshelves of Prentice Hall or Adison
Wesley. The book mentioned above helped me very much in designing the
Multi-Tasking Subsystem and describes a UNIX-like operating system for
personal computers in detail (MINIX + source code available from
Prentice Hall).


The Basic System (TP4MULTI)

1. Introduction

At the moment, more and more programmers become interested in multi-
tasking environments for personal computers. I suppose, anyone who
intends to stay up to date, will have to deal with systems like OS/2
or UNIX / XENIX /...
Unfortunately, those systems are quite expensive and require lots of
extension memory. Only few wealthy private programmers (have you
ever seen one?) will be able to buy such an operating system already
today.

At the time I started developing the Multi-Tasking Subsystem, my
situation had been as described above. Now I'm in the position to
provide you with an inexpensive means to study the design and
synchronisation of parallel processes. In addition to that, the
Multi-Tasking Subsystem will help you to write programs more complex
and much more sophisticated, especially in areas like data
communication, where quite a lot of actions are to be taken nearly
simultaneously.


Concept

Like UNIX or OS/2, the Multi-Tasking Subsystem was designed as a
time-sharing system. It was not designed for real-time applications.
A time-sharing system tries to divide the available computing power
among all computable processes evenly. Therefore, a process that has
used up its timeslice, is temporarily suspended and another
computable process gains control (preemptive scheduling). This is
accomplished by having a timer-interrupt-service-routine monitor the
system activities about 18 times a second. This routine initiates a
task-switch whenever the running task has used up its quantum.
Although I could have used the AT-RTC (Real-Time Clock), which in fact
would decrease the minimum possible timeslice, I have decided not to
do so for several reasons:

a) The task-switch is the most time consuming action, the kernel has
   to perform. A smaller timeslice, increases the number of possible
   task-switches, but increases the kernel overhead as well.

b) The Multi-Tasking Subsystem could not run on PC or XT-computers,
   because those do not have a real-time clock.

With a timer-interrupt occuring 18 times a second, the smallest
possible timeslice is about 55,5 milliseconds. During the
initialisation sequence the timslice is set to 110 milliseconds.
If you choose a 55,5 millisecond timeslice the amount of computing
power consumed by the mere task-switching process will be about 1,4
percent (12 MHz AT-compatible).


Dynamic Scheduling

Normally each task is temporarily suspended whenever it has used up
its timeslice. If this happes inside a DOS-function, however, the
kernel may not safely interrupt the currently executing task. It has
to wait, until it returns from the DOS-call.
Provided this task has to read thousands of records from a data file
and write them to another file, the kernel will be inside DOS
again, when the kernel tries to suspend it at the following
timer-tick. Again, a task switch is impossible! This procedure might
happen again and again until the task has finished.
As you see, under certain circumstances, a task may exceed its
quantum at an amount that cannot be foreseen by the system-kernel.

On the other hand, there might be a task that periodically, lets say
one time a second, look at a particular value taken from a port to
see, whether actions are to be taken. In this case, it will act upon
the condition encountered, otherwise it will go to sleep and give up
its timeslice. Such a task will use up its timeslice very seldom.
If, hovewer, actions are to be taken, it might be suspended in the
middle of its activities because it has used up its quantum. - Indeed
that's not fair!

What can we do to achieve some kind of compensation? OS/2 brought me
to the idea to implement a somewhat dynamic scheduling that proceeds
as follows: Whenever a task gives up its timeslice, the time not used
is placed to this task's credit. If it has to execute longer at a
later point of time, it will not be preempted until it has used up its
current quantum plus its credit. On the other hand, a task that
exceeds its quantum, is not rescheduled until its debit is "used up".

This sounds quite good, but there is a catch to it though. If we
would credit every single tick not used, the task mentioned above
could possibly run for hours if it has to take some action after
all.
For this reason, the amount of ticks beeing placed to a tasks
credit/debit, is limited. You may choose this limit freely and it
defaults to +/- 10 timer-ticks that is slightly above half of a
second.


Priority

The Multi-Tasking Subsystem supports three levels of priority:
"Pri_Nice" which is the lowest, "Pri_User" which is standard and
"Pri_Kernel" which is highest possible priority. Your Pascal
main-program is started at the level "Pri_User" during initialization.

Let's examine, how the different layers of priority are acted upon:
Inside each layer, the tasks are scheduled in straight round-robin
fashion. Whenever there are computable tasks at a higher level none
of the tasks in a level below that will gain control. That means, the
"idle loop" at level "Pri_Nice" will only be activated, if the
layers "Pri_User" and "Pri_Kernel" are empty.

The programmer has to take this concept into account when designing
his application system. The overall system performance depends very
much on the assignment of priorities.

By the way: Throughout this documentation I use the terms "task" and
"process" interchangably, although some experts will be picking up
stones to throw at me at this very moment...  I don't feel guilty
doing so, because those experts seem not to have reached an agreement
yet, about how to define these terms.

Tasks that spend most of their lives waiting for events (waiting for
incoming characters,...), should be given highest priority.
Tasks that spend their lives busily working all the time, should be
given standard pritority.
By doing so, the busy ones will be interrupted whenever an event, a
higher priorized task was waiting for occurs and will be able to work
the rest of the time (which will be most of the time) undisturbed.
The lowest priority level will mostly be occupied only by the idle
loop.


Another Catch To It

DOS does not know about interrupt controlled disk I/O in the
fashion of multi-tasking operating systems! There is a loop inside
your ROM that waits for the disk-controller to issue a completion
interrupt, but that is of no use for us, because a disk I/O
operation must never be interrupted by a task-switch.
Multi-tasking operating systems normally switch to another task,
while the currently running process has to wait for a disk operation
to complete. I didn't know how to achieve this without rewriting
the low-level disk I/O-routines. So for now, we'll wait...

As a consequence, a process that performs lots of disk I/O-operations
and which is running at high priority, will possibly block the whole
system.
In a real multi-tasking operating system however, it is very useful
running I/O-intensive processes at a high priority level for the
reasons stated earlier in the context of mostly waiting tasks.


Inter Process Communication (IPC)

The Multi-Tasking Subsystem contains functions for handling
semaphores and message-passing.
Shared-memory does not require system support, because every task
under DOS has access to any memory location in the whole system.
The programmer will have to use semaphores, however, to avoid race
conditions when accessing commonly used memory areas. The
demonstration program PRO_CON gives examples of how to synchronize
your tasks using semaphores.


Programmable Timers

Programmable timers are a very useful means to take care of timeout-
conditions (for example in communications software).
The Multi-Tasking Subsystem let you define any number (limited by
the available heap) of timers with a resolution of 55,5
milliseconds. If a timer expires, a byte located at the address given
at the time of creation is incremented.
The amount of CPU-time consumed by watching the timers currently
active is negligible and independent of the number of timers defined.


Event Handling

Sometimes it can be useful to have a task waiting for the contents of
a memory location to change. This is what I have chosen to call an
event. Realizing a task that waits for a buffer filled by an
interrupt routine, you can acchieve a very short response time at a
minimum waste of CPU-time by defining an event that reactivates your
task whenever the contents of the buffer's tail-pointer changes.



3. How Is It Done

Most of the subsystem is written in Turbo Pascal 4.0. Only a small
part of the kernel (about 2 KB) is written in assembly language. If
you purchased a source code license, you will find two versions of
the assembly language module on your product diskette. The first one
assembles using Microsofts Macro Assembler V4.0 or higher, the second
one is for programmers using the well known ShareWare assembler A86
V3.19 or higher, written by Eric Isaacson.
Both parts together form a TPU (Turbo Pascal Unit) that contains the
whole subsystem and may be USEd in your programs.


The Task Table

The central element of the Multi-Tasking Subsystem is called "task
table". For reasons of performance, this table was defined
statically in the data segment. It can hold a maximum of 50 tasks at
the moment, but can easily be expanded (if you own the source code).

Every task in the system occupies one entry in the task table. This
entry holds all pieces of information that describe the task's actual
state of execution.

At any point of time each task is in one of the following possible
states:

Running..: This task is currently executed.

Ready....: This task is computable, but another task currently is in
           control of the CPU.

Sleeping.: This task has suspended itself for a certain number of
           timer-ticks.

Crashed..: The subsystem has detected a stack overflow for this task.

Waiting..: This task is currently waiting for an event or a
           resource (a semaphore for example).

Sending..: This task is waiting for the receiver of a message to
           do a receive system call.

Receiving: This task is waiting for another task to send it a message.

Suspended: This task was temporarily disabled by another task in the
           system and needs action from another task to be put into
           the ready-state again.

If a slot in the task-table currently is not occupied by any task its
state-marker will contain the value "Available".

The following state diagram summarizes all possible task-states and
the state-transitions possible among these states. A state-transition
may only take place in the direction indicated by the arrow symbols.







                       ÚÄÄÄÄÄÄÄÄÄÄÄ¿            13 ÚÄÄÄÄÄÄÄÄÄÄÄ¿
               ÚÄÄÄÄÄÄ>³  Running  ÃÄÄÄÄÄÄÄÂÄÄÄÄÄÄ>³  Crashed  ³
               ³       ÀÄÄÄÄÄÂÄÄÄÄÄÙ       ³       ÀÄÄÄÄÄÄÄÄÄÄÄÙ
               ³             ³             ³
              2³            1³             ³
               ³             ³             ÀÄÄÄÄÄÄÄÄÄÄÄÄ¿
               ³             ³                          ³
         ÚÄÄÄÄÄÁÄÄÄÄÄ¿       ³     4 ÚÄÄÄÄÄÄÄÄÄÄÄ¿      ³
         ³   Ready   ³<ÄÄÄÄÄÄÁÄÄÄÄÄÂÄ´ Waiting   ³<Ä¿3  ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÙ             ³ ÃÄÄÄÄÄÄÄÄÄÄÄ´  ³   ³
                                  6ÃÄ´ Sleeping  ³<Ä´5  ³
                                   ³ ÃÄÄÄÄÄÄÄÄÄÄÄ´  ³7  ³
                                  8ÃÄ´ Sending   ³<ÄÅÄÄÄÙ
                                   ³ ÃÄÄÄÄÄÄÄÄÄÄÄ´  ³
                                 10ÃÄ´ Receiving ³<Ä´9
                                   ³ ÃÄÄÄÄÄÄÄÄÄÄÄ´  ³
                                 12ÀÄ´ Suspended ³<ÄÙ11
                                     ÀÄÄÄÄÄÄÄÄÄÄÄÙ




            State Diagram, Multi-Tasking Subsystem Version 1.10



Task Management

Internally, the tasks are managed using queues. Dependent on its
state of execution, a task may be located in

a) the scheduler queue of its priority-level ("Running" or "Ready"),
b) the sleep-queue ("Sleeping") or
c) the sender-queue of the receiver-task, if the latter one is not
   ready to receive the message and the sender indicates that it
   wants to wait until the receiver gets ready ("Sending").

Tasks at the states "Suspended", "Receiving" or "Crashed" are
not located in any queue.
A task that is "Waiting" on an event or a resource may be chained to
the event-table or be located in a semaphore's task-queue.

Whenever a task is created, a task-table entry is allocated to
this task. The slot number of its task-table entry becomes the
task-id (task-number or process-number), which some system-calls
are to be passed as a parameter.
In addition to that, a private stack for the task is allocated and
set up.

The task creation can be completed sucessfully only if a) there is
an empty slot in the task-table and b) the private stack can be
allocated on the heap.



Code-Sharing

The Turbo Pascal compiler generates object code that is mostly
reentrant. Such code may be executed in code-sharing.

The term "Code-sharing" can have different meanings. On the one
hand there may be a number of subroutines which are used by more
than one task in the system. Thus more than one task may be
executing a certain subroutine at the "same" point of time, i. e.
the instruction pointers of those tasks point to a location inside
this subroutine at the same point of time.
Provided the code is reentrant, this will never lead to any
problems. You will have to take care of situations which lead to
more than one task modify global data at the same point of time, of
course, but the type of code-sharing described above will never lead to
a crash or the modification of local variables.

"Code-sharing" may also describe a situation, in which the same part
of code (here: the object code of a procedure - the task) is activated
more than once as a separate process. Each of these tasks is given
its own set of registers, its private stack and its local variables.
The latter are actually allocated on the private stack. Provided the
code is reentrant and provided that you, the programmer, take care of
race conditions, there may be an "unlimited" number of separate tasks
executing the same object code simultaneously.

I have already tried both kinds of code-sharing and did not encounter
any problems so far.


Programmable Timers

Lets now have a closer look at the timers. A timer, which in fact is
a memory location containing a counter beeing decremented at any
timer-tick, needs to be examined whenever a clock-interrupt occurs.
If the kernel realizes that the timer has expired, some action will
be to be taken.
As you see, a small extra amount of computing power is necessary to
countdown timers, act upon their expiration and finally remove them
from the system. Some types of application, communication programs
for example require extensive use of timers. Therefore one should
think about an inexpensive implementation of timers to avoid loss of
performance.
The implementation of timers in the Multi-Tasking Subsystem makes the
kernel overhead constant and independant from the number of timers
presently active. This is achieved by a special queueing method,
taken from the timer implementation of MINIX, a UNIX-like operating
system for the IBM PC. As stated earlier, MINIX has been developed by
Andrew S. Tanenbaum and is currently distributed by Prentice Hall. I
recommend MINIX for everybody, who would like to go deeper into
operating system design, it's fantastic!

Return to the timers: The timer-queue consists of a forward-chained
list of timer-structures. Only the first element of this list is
examined at every timer-tick. If the first timer expires, it will be
removed from the queue after having taken the appropriate action to
signal its expiration to the application. The second element now
becomes the head of the queue, and so on.
When a new timer is inserted into the timer-queue, its counter will be
adjusted to reflect the number of ticks remaining after all previous
elements of the timer-queue have expired.

Example:
                ÚÄÄÄÄÄÂÄ¿    ÚÄÄÄÄÄÂÄ¿    ÚÄÄÄÄÄÂÄ¿
Timer-Queue ÄÄÄ>³  3  ³ÄÅÄÄÄ>³  5  ³ÄÅÄÄÄ>³  1  ³ÄÅÄ´
                ÀÄÄÄÄÄÁÄÙ    ÀÄÄÄÄÄÁÄÙ    ÀÄÄÄÄÄÁÄÙ
Time to wait:      3 Ticks      8 Ticks      9 Ticks


Event Handling

You might think of lots of events that could be handled by an
application.
Currently only the change of contents with respect to a single
memory location is supported. Practically speaking, your application
may wait (without consuming CPU) until the contents of a particular
memory location changes. This memory location is checked whenever a
task-switch occurs.

What to do with it?  Well, I came up with this type of event as I
designed a special application. I had to realize a task that emptied
a ring-buffer which was filled by an interrupt routine. Why not use a
semaphore, you might ask!  - Too slow!  There was just enough time to
insert the characters received into the ring-buffer. On the other
hand the ring-buffer had to be emptied as quickly as possible, again
for the reasons of speed.
A high-priorized subtask permanently looping, keeping an eagle eye on
the ring-buffer is far from beeing a solution - it simply blocks the
whole system. OK, lets try to have the subtask sleep for a while,
take a look at the buffer and sleep again if no characters have
arrived. Well, in the meantime a buffer-overflow has occured...

I suppose, you now understand why the event has been born. Defining
an event that monitored the buffer's tail-pointer, I kept my
high-priority subtask waiting for the buffer to be filled without
blocking the whole system. Awakend very shortly after a change of the
tail-pointer signalizes incoming characters, it busily processed the
buffer contents and went to sleep again. - Works fine!


Inter Process Communication (IPC)

As mentioned earlier, the Multi-Tasking Subsystem provides for
various methods to exchange data between separate tasks and to
synchronize processes executing simultaneously.
I do not intend to go into detail about the underlying concepts,
because there are lots of books available in the market, which discuss
these topics much better than I could do here in this document. Again
I recommend the study of "Operating Systems Design and Implementation"
written by Andrew S. Tanenbaum.


A. Message Passing

The system-calls supporting message passing are quite
straightforward.
A task that wants to send a message to another task in the system
primarily has to know the task-id of the process it would like to
send to. Then it passes its message-buffer and the receiver-id to
the appropriate system-call. An additional parameter tells the
kernel, whether the sender wants to wait if the receiver is not
ready to receive the message or whether the send-request should be
rejected.

A task is ready to receive, whenever it executes a receive-system-
call. It may specify the task-id of the process it wants to receive
from or pass a don't-care code to the system-call, which causes the
kernel to pass through any message sent to this task.
Again, the task may wait until a message arrives or have the system
reject a receive system-call whenever no message is available.


B. Semaphores

There has been written a lot about this topic in the past. Let's have
a look at the internal represetation only at this point.

A semaphore as defined by the Multi-Tasking Subsystem, consists of a
two-byte signal count, which is set to 1 at the time of creation,
and a task-queue to which the processes waiting for this semaphore
are appended.
The busy-state is indicated by a signal-count of zero; any non-zero
value indicates a free-state. Whenever a wait system-call is executed
and the corresponding semaphore is currently busy, the requesting
task is suspended until another process releases this semaphore
through execution of a signal system-call.
Whenever a signal system-call is executed and the task-queue of the
corresponding semaphore is not empty, the first task of this queue
is made computable, otherwise the signal-count is incremented.

Despite the internal structure, tasks refer to semaphores through
untyped pointers. The task creating a semaphore receives this
pointer on return from the system-call and uses it as a handle
furtheron. The actual number of semaphores in the system is
delimited by the amount of free heap space only.


Critical Sections

You may use the standard functions/procedures supplied with your
compiler freely inside your tasks. BUT - procedures like WriteLn are
not designed to work in multi-tasking environments, that means, they do
not protect their critical sections from beeing entered more than once
at a time.
An example will help to understand what I try to explain: Lets think
of two equaly priorized tasks which spend their lives WriteLn-ing
strings to the terminal screen. The process of bringing a bunch of
characters to the screen is much more complicated than the simple
WriteLn-statement makes believe. Therefore it is likely that
sometimes both tasks will be preempted while in the middle of
performing the screen-write. As a consequence the screen output
becomes clobbered.
Imagine the effects of non-synchronized execution of GetMem and
FreeMem...

Another situation in which you have to block a certain section of code
is a routine, that modifies global data or performs some closely
connected actions that form an undivisible unity (atomic action).
Let me give you an example: Provided you got two tasks executing
simultaneously, which at some point of execution output a character to
the screen at a certain position. This is done by executing a GotoXY,
followed by a Write. If the first task was interrupted after having
executed the GotoXY but before having output the character, the second
task might move the cursor to another location on the screen, which
indeed wouldn't lead to the results desired.

There are two basically different approaches to solve this problem.
First you could force exclusive CPU-access during the execution of
your critical section. This solution is only applicable for very
small portions of code, a GotoXY/Write-sequence for example, because
a CPU-bind blocks any scheduler function including the sleep-queue
and timer management.
In most cases a protection scheme using semaphores is preferable.
You can find an example for this kind of process synchronisation in
the example program PRO_CON.PAS, routines RBuffGet and RBuffPut. A
section of code protected by a semaphore, may only be entered by one
task at a time. Any task trying to enter the critcal section whilst
another process is currently inside is suspended until the latter one
has left the protected area.



Global Type- and Data-Definitions


Global Type-Definitions

Priority = (Pri_Nice, Pri_User, Pri_Kernel);

  This type-definition is used to describe the priority-level at
  which a task is to be executed.


WaitFlagType = (Wait, NoWait);

  Passed as a parameter to the system-calls concerned with
  message-passing, this type indicates whether a process intends to
  wait for a) a message to be received or b) a message available to
  be received.


TaskReturn = (Task_Crashed, Task_NotFound, Task_NoMsg,
              Task_NotReady, Task_OK, Task_Invalid);

  The system-calls concerned with message-passing return one of these
  codes to the calling process.

  Task_Crashed...: A task was addressed, which has been disabled
                   following a stack-overflow condition
  Task_NotFound..: The task-table entry indexed by the task-id
                   passed to the executed system-function is
                   out of range or currently empty
  Task_NoMsg.....: There is no message available (Receive with NoWait)
  Task_NotReady..: The receiver is not waiting for a message (Send
                   with NoWait)
  Task_OK........: Fine, that's it
  Task_Invalid...: An invalid task-id was passed to the
                   system-function


TaskStatus = (Running, Ready, Sleeping, Available, Crashed,
              Waiting, Sending, Receiving, Suspended);

  Return value returned by GetTaskState.


SemReturn = (Sem_NoSpace, Sem_NotFree, Sem_OK, Sem_Invalid);

  Some system-calls concerned with semaphore-handling return a value
  of type SemReturn.

  Sem_NoSpace..: There is no heap space available
  Sem_NotFree..: You have tried to delete a semaphore whose task-queue
                 is not empty
  Sem_OK.......: Everything's allright
  Sem_Invalid..: You passed an invalid semaphore-handle (NIL)


TaskNoType = Integer;

  Higher level representation of the task-id. I decided to redefine
  the type integer to be able to change this definition in a later
  version without having to think about the program code.


BPtr = ^Boolean;

  Definition required by GetTimBusy.



Global Constants

Task_NoSpace

  If task creation fails, because there is not enough free dynamic
  memory available to allocate a private stack, CreateTask will return
  this value instead of the task-id.


Task_NoSlot

  If task creation fails, because the maximum number of simultaneously
  active tasks is reached, CreateTask will return this value instead
  of the task-id.


StateText

  StateText is an array indexed by a value of type TaskStatus, which
  contains a textual representation of every possible task state.


AnyTask

  Don't-care-value, passed to the receive system-function whenever a
  process doesn't care from whom it is going to receive a message.


Global Variables

InInt28 (Boolean)

  Whenever COMMAND.COM is waiting for input, it permanently issues
  an INT 28H (DOS multi-tasking interrupt). MtPopUp for example
  catches this interrupt and sets InInt28 to TRUE whilst inside the
  interrupt-handler. This informs the kernel know that a task-switch
  may safely performed although the DOS critical-flag is set.




Reference Section (alphabetically sorted)

                                                             BindCpu


Declaration

   PROCEDURE BindCPU;

Purpose

   BindCPU is used to bind the CPU to the currently running process
   temporarily. No task-switch will be performed an no other
   scheduler activities take place until the CPU is released by a
   ReleaseCPU call.


Example

      ...
   BindCPU;                                    {gain CPU exclusivly}
   GotoXY(1,10);                               {atomic action}
   Write('*');
   ReleaseCPU;
      ...

Remarks

   BindCPU blocks the whole kernel! While the CPU is bound, no
   event-checks, no timer-countdown and no sleep-queue handling are
   performed.
   You should only use BindCPU to protect VERY small portions of
   code. In most cases, the use of semaphores is recommended

See Also

   ReleaseCPU




                                               CancelTimer / CreateSem


Declaration

   FUNCTION CancelTimer(MemPtr:Pointer):BOOLEAN;

Purpose

   If there exists a timer that will cause the memory location at the
   address "MemPtr" to become incremented, it will be removed from the
   system. CancelTimer returns TRUE, if a timer could be found,
   otherwise FALSE is returned.

Example

   VAR Timeout : Boolean;
       Ok      : Boolean;
         ...
   Timeout := False;                           {initialize}
   IF QueueTimer(@Timeout,Seconds(1))          {create Timer}
      THEN  BEGIN
               REPEAT                          {wait}
               ...                             {some action}
               UNTIL Timeout OR Ok;
               IF CancelTimer(@Timeout) THEN;  {Kill Timer}
               ...                             {some more action}
            END;

See Also

   QueueTimer


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


Declaration

   FUNCTION CreateSem(VAR SemPtr:Pointer):SemReturn;

Purpose

   CreateSem allocates a semaphore on the heap and returns a pointer
   that functions as a handle in further system-calls referring to
   this semaphore. The handle is placed into the variable SemPtr.
   The return value of this system-function indicates whether the
   action could be completed successfully.

Example

   VAR  Semaphore : Pointer;       {Handle}
         ...
   IF CreateSem(Semaphore) <> Sem_Ok
      THEN Error;

See Also

   Typedefinition SemReturn, RemoveSem

                                                          CreateTask


Declaration

   FUNCTION CreateTask(TaskPointer:Pointer;Level:Priority;
            BytesStack:Word):TaskNoType;

Purpose

   This function is used to create a subtask.
   The address of the procedure to be activated as an independently
   running task is to be passed in "TaskPointer".
   "Level" describes the desired priority level.
   Finally, the parameter "BytesStack" contains the desired size of
   the task's private stack in bytes.

   CreateTask returns the task-id or a negative value indicating an
   error-condition.

Example

   PROCEDURE SubTask;
   {
     I am a task that beeps every second
   }
   BEGIN {SubTask}
      REPEAT                                   {  Body    Ä¿ }
         Sleep(Seconds(1));                    {           ³ }
         Sound(1000);                          { ACTION!!  ³ }
         Delay(20);                            {    :      ³ }
         NoSound;                              {           ³ }
      UNTIL False;                             {  Body    ÄÙ }
   END;  {SubTask}
         ...
         ...
   BEGIN {Main}
   IF CreateTask(@SubTask,Pri_User,300) < 0
      THEN Error;
         ...
   END. {Main}

Remarks

   With respects to programming, a task is realized as a Pascal
   procedure without parameters, whose body has to be an infinite
   loop. You must NEVER leave the body of a task except by executing
   a Terminate system-call.
   A task is allowed to have local variable definitions, you will
   have to take care however, that the private stack is properly
   dimensioned to be able to hold the local data. You will have to
   add the amount of memory needed to hold the local variables to
   the bytes stackspace the task needs at runtime.
   YOU are responsible for passing a valid stack size!!!! This
   parameter is not checked!!

See Also

   Typedefinitions TaskNoType and Priority, Global Constants,
   Terminate



                                                             DoShutDown



Declaration

   PROCEDURE DoShutDown;

Purpose

   Shutdown the Multi-Tasking Subsystem. All interrupt vectors
   captured are restored to their original state.

Remarks

   This procedure is called internally through the exit-procedure of
   the subsystem-unit.


                                                       DumpTaskTable


Declaration

   PROCEDURE DumpTaskTable;

Purpose

   Display the actual state of all active tasks in the system.

Example

   Nr. Status      Priorit„t  Slice  Delay  Stack free  CPU
     1     Ready      Pri_Nice     2      0         205  18
     2   Waiting      Pri_User     3      0          -1  1
     3   Running    Pri_Kernel    -1      0         221  1
     4   Waiting      Pri_User     2      0         321  5

Remarks

   The current content of your display are overwritten. In case you
   wish to realize a status-window, you should replace DumpTaskTable
   with a routine of your own.

See Also

   Global Constants StateText, GetTaskState

                                                  EventWait / GetPID


Declaration

   FUNCTION EventWait(MemPtr:Pointer):Boolean;

Purpose

   EventWait causes your task to be suspended until the contents of
   the memory-location pointed at by "MemPtr" changes.
   If no empty event-table entry can be found, EventWait returns
   FALSE.

Example

   VAR HeadPointer : Word;                     {Bufferpointer   }
       TailPointer : Word;                     {        "       }
            ...
   IF NOT EventWait(@TailPointer)              {wait for a change}
      THEN Error                               {of the pointer}
      ELSE DoJob;
            ...


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


Declaration

   FUNCTION GetPID:TaskNoType;

Purpose

   By calling GetPID, a task can find out its task-id.

See Also

   Typedefinition TaskNoType

                                           GetTaskState / GetTimBusy


Declaration

   FUNCTION GetTaskState(Task:TaskNoType):TaskStatus;

Purpose

   GetTaskState returns the current status of the task whose task-id
   was passed to the function.

Example

   This task displays its own state on the screen:

   Writeln(StateText[GetTaskState(GetPID)]);

See Also

   Typedefinitions TaskStatus and TaskNoType, Constant StateText


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


Declaration

   FUNCTION GetTimBusy:BPtr;

Purpose

   GetTimBusy returns the address of the timer-busy flag which
   contains a non-zero value whenever the interrupt-handling
   procedure for the INT 8 is active.
   Sometimes an external interrupt-handler needs to know, whether
   the scheduler is currently busy.
   No system-call must be executed whilst the busy-flag is set.

See Also

   Typedefinition BPtr


                                            QueueTimer / ReadySuspended


Declaration

   FUNCTION QueueTimer(MemPtr:Pointer; Counter:Word):BOOLEAN;

Purpose

   Creates a timer that expires after "Counter" ticks and increments
   the contents of the memory-location pointed at by "MemPtr".
   If there is not enough heap space available to allocate a timer,
   QueueTimer will return FALSE, otherwise TRUE is returned.

Example

   VAR Timeout : Boolean;                      {Timeout marker}
            ...
   Timeout := False;                           {initialize    }
   IF NOT QueueTimer(@Timeout,Seconds(1))      {Timeout after 1 sec}
      THEN Error;
            ...
   IF CancelTimer(@Timeout)                    {Remove Timer     }
      THEN ;                                   {if still existent}
            ...

 See Also

   CancelTimer


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


Declaration

   FUNCTION ReadySuspended(Task:TaskNoType):BOOLEAN;

Purpose

   ReadySuspended is used to re-enqueue a task into its
   scheduler-queue wich has been suspended using the Suspend
   system-function.
   If the action could be completed successfully, the value TRUE is
   returned. A return value of FALSE indicates that the task addressed
   was not currently suspended.

See Also

   Suspend

                                                                Receive


Declaration

   FUNCTION Receive(FromTask:TaskNoType; MsgBuff:Pointer;
                    WaitFlag:WaitFlagType):TaskReturn;

Purpose

   By executing a Receive system-call, a task can receive a message
   from another task in the system.
   The first parameter, "FromTask", indicates from which task the
   caller would like to receive. If "FromTask" contains "AnyTask",
   any message is passed through, otherwise only messages sent by
   the process whose id matches "FromTask" are received.
   "MsgBuff" points to the start of a message buffer into which the
   received message is copied. The kernel does not check whether the
   message received fits into the message buffer - it simply
   copies!
   If the caller passes a "WaitFlag" of value "Wait", it will be
   suspended until a message arrives. Otherwise the kernel
   immediately returns control to the caller if no message is
   currently available.

Example

   VAR Puffer : String;                        {Message buffer}
               ...
   IF Receive(AnyTask,@Puffer,Wait) <> Task_Ok
      THEN Error
      ELSE Writeln(Puffer);
               ...

Remarks

   Using the don't care task-id "AnyTask", you could realize a task
   that spends its life waiting for messages from its environment.
   If you had to monitor some sensors, for example, you could have a
   separate task for every sensor to be monitored. Whenever some
   action has to be taken, the corresponding monitor-task sends a
   message to a central workhorse that performs the necessary
   adjustments.

See Also

   Constant AnyTask, Typedefinition TaskReturn, Send, ReceivedFrom

                                           ReceivedFrom / ReleaseCPU


Declaration

   FUNCTION ReceivedFrom:TaskNoType;

Purpose

   By calling ReceivedFrom, a task can find out, who was the sender
   of the last message received.

See Also

   Typedefinition TaskNoType, Constant AnyTask, Receive


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


Declaration

   PROCEDURE ReleaseCPU;

Purpose

   Provided you have bound the CPU by executing a BindCPU, you will
   have to reenable scheduling through execution of a ReleaseCPU.

Example

      ...
   BindCPU;                                    {disable scheduler}
   GotoXY(1,10);                               {atomic action}
   Write('*');
   ReleaseCPU;                                 {...set them free...}
      ...

See Also

   BindCPU;

                                                   RemoveSem / Sched


Declaration

   FUNCTION RemoveSem(VAR SemPtr:Pointer):SemReturn;

Purpose

   RemoveSem physically removes a semaphore. The formerly occupied
   heap space is returned to the memory pool.
   "SemPtr" must be a valid semaphore-handle as returned by the
   CreateSem system-call.
   RemoveSem returns a value of type SemReturn that indicates
   success or failure.

Example

   VAR  Semaphore : Pointer;                   {Handle}
               ...
   IF CreateSem(Semaphore) <> Sem_Ok
      THEN Error;
            ...
   IF RemoveSem(Semaphore) <> Sem_Ok
      THEN Error;
            ...

Remarks

   The system mostly is not able to prove whether a valid handle is
   supplied. It is your job to take care of this.
   You cannot remove a semaphore, whose task-queue currently is not
   empty.

See Also

   Typedefinition SemReturn, CreateSem


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


Declaration

   PROCEDURE Sched;

Purpose

   Initiate a task-switch, give up the current timeslice.
   "Sched" is used internally by many system-functions. If you want
   to have your task give up its timeslice, you should better use
   Sleep(1).


                                                  Seconds / SemClear


Declaration

   FUNCTION Seconds(Sec:Word):LongInt;

Purpose

   "Seconds" returns the number of timer-ticks that make up a second.
   It is recommended that you use this function whenever you need to
   specify a special amount of time. Use of Seconds makes your
   application independent of changes to the task-switch rate.

Example

   IF QueueTimer(@Timeout,Seconds(1) SHR 1)    { timout after   }
      THEN;                                    { half a second  }

See Also

   QueueTimer, CancelTimer


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



Declaration

   PROCEDURE SemClear(SemPtr:Pointer);

Purpose

   Reset a semaphore's signal-count to zero.

Example

   VAR  Semaphore : Pointer;                   {Handle}
               ...
   IF CreateSem(Semaphore) <> Sem_Ok
      THEN Error
      ELSE SemClear(Semaphore);

Remarks

   Internally SemClear is translated into SemSet(Semaphore,0).

See Also

   SemSignal, SemWait, SemClearWait, SemSet

                                                        SemClearWait


Declaration

   PROCEDURE SemClearWait(SemPtr:Pointer);

Purpose

   Reset a semaphore's signal-count to zero and wait until another
   task initiates a SemSignal system-call for this semaphore.
   In contrast to SemWait, SemClearWait ALWAYS leads to the calling
   task beeing suspended.

Example

   VAR Ready : Pointer;                        {Semaphore      }
         ...
   PROCEDURE SubTask;
   {
      I am a task that needs to save the values of some global
      variables during initialisation. The main program, however,
      changes these variables during the process of its execution.
      Therefore, the main program has to wait until I indicate that I
      have transferred the values I need to my local data area.
   }
   BEGIN {SubTask}
         ...                                   {initialize     }
      SemSignal(Ready);                        {O.K. I'm ready }
      REPEAT
         ...                                   {Body           }
      UNTIL False;
   END;  {SubTask}
         ...
         ...
   BEGIN {Main}
         ...
   IF CreateSem(Ready) <> Sem_Ok               {Create a semaphore}
      THEN Error;
   IF CreateTask(@SubTask,Pri_User,300) < 0    {Create a task     }
      THEN Error
      ELSE SemClearWait(Ready);                {wait for O.K.    }
         ...
   END. {Main}

See Also

   SemClear, SemSet, SemSignal, SemWait


                                              SemCut / SemGetSignals


Declaration

   FUNCTION SemCut(SemPtr:Pointer;Task:TaskNoType):BOOLEAN;

Purpose

   If the task whose id is passed as "Task" currently is waiting in
   "SemPtr"'s task-queue, it is removed from this queue.
   SemCut returns TRUE, if the action could be completed successfully.

Remarks

   SemCut is a somewhat brutal function! It forces an innatural
   action and was added for a special application purpose in MtPopUp.
   PLEASE do use it with care!! - Better keep away from it.

See Also

   SemPaste


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


Declaration

   FUNCTION SemGetSignals(SemPtr:Pointer):Word;

Purpose

   Returns the signal-count of the semaphore "SemPtr".

Example

   FUNCTION SemBusy(S:Pointer):BOOLEAN;
   {
      This function checks whether a semaphore is currently busy.
   }
   BEGIN {SemBusy}
      SemBusy := (SemGetSignals(S) = 0);       {Signal-Count = 0}
   END;  {SemBusy}

See Also

   SemSignal, SemWait, SemClear, SemClearWait, SemSet

                                                   SemPaste / SemSet


Declaration

   PROCEDURE SemPaste(SemPtr:Pointer; Task:TaskNoType);

Purpose

   SemPaste unconditionally appends "Task" to the task-queue of the
   semaphore referred to by "SemPtr". No validity checks are performed!

Remarks


   SemCut is a somewhat brutal function! It forces an innatural
   action and was added for a special application purpose in MtPopUp.
   PLEASE do use it with care!! - Better keep away from it.


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


Declaration

   PROCEDURE SemSet(SemPtr:Pointer; Count:Word);

Purpose

   SemSet sets the signal-count of a semaphore to a definite value.
   This action does not have any influence on tasks that might be
   waiting in the task-queue belonging to this semaphore.

Example

   CONST Elements = 100;
   VAR   Buffer   : ARRAY[1..Elements] OF Byte; {Buffer}
         Full     : Pointer;                   {No. of used slots}
         Empty    : Pointer;                   {No. of empty slots}
         ...
   BEGIN {Main}
         ...
      IF CreateSem(Full) = Sem_Ok
         THEN SemClear(Full);                  {no slot used}
      IF CreateSem(Empty) = Sem_Ok
         THEN SemSet(Empty,Elements);          {all slots free}
         ...
   END. {Main}

See Also

   SemSignal, SemWait, SemClear, SemClearWait

                                            SemSignal / SemSoWaiting


Declaration

   PROCEDURE SemSignal(SemPtr:Pointer);

Purpose

   If the task-queue of the semaphore referred to by "SemPtr" is
   currently empty, the signal-count will be incremented. Otherwise
   the first task waiting is re-scheduled and the signal-count remains
   unchanged.

Example

   VAR Critical: Pointer;
         ...
   IF SemCreate(Critical) <> Sem_Ok
   THEN Error;
         ...
   SemWait(Critical);
         ...
   {critical section}
         ...
   SemSignal(Critical);
         ...

See Also

   SemWait, SemClearWait, SemClear, SemSet


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


Declaration

   FUNCTION SemSoWaiting(SemPtr:Pointer):BOOLEAN;

Purpose

   SemSoWaiting returns TRUE, if there are tasks waiting for
   "SemPtr" to become available.

See Also

   SemWait, SemSignal, SemClear, SemClearWait, SemSet, SemGetSignals

                                                      SemWait / Send


Declaration

   PROCEDURE SemWait(SemPtr:Pointer);

Purpose

   If a semaphore's signal count currently is greater than zero, it
   will be decremented. Otherwise the caller is suspended and
   appended to the task-queue of this semaphore.
   It remains suspended until another task issues a SemSignal for
   the semaphore it is waiting for.

Example

   VAR Critical: Pointer;
         ...
   IF SemCreate(Critical) <> Sem_Ok
   THEN Error;
         ...
   SemWait(Critical);
         ...
   {critical section}
         ...
   SemSignal(Critical);
         ...

See Also

   SemSignal, SemClearWait, SemClear, SemSet


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


Declaration

   FUNCTION Send(ToTask:TaskNoType; Msg:Pointer; MsgSize:WORD;
                 WaitFlag:WaitFlagType):TaskReturn;

Purpose

   The system-function "Send" lets a task send a message to another
   process in the system.
   The parameter "ToTask" contains the task-id of the receiver. This
   must be the task-id of a currently active task. You must not use
   the constant "AnyTask" in this context.
   "Msg" points to the start of the message-buffer whose size is
   passed in "MsgSize".
   Finally a wait-flag has to be supplied, that indicates whether
   the sender wishes to wait until the receiver is willing to
   receive the message. If you set "WaitFlag" to "NoWait", the
   kernel will return control to your task immedeately if the
   receiver is not waiting for a message.

                                                        Send / Sleep


Example

   VAR Puffer : String;
         ...
   IF Receive(AnyTask,@Puffer,Wait) <> Task_Ok
      THEN Error
      ELSE Writeln(Puffer);
         ...

Remarks

   The message is physically copied to the message buffer of the
   receiving process. This is not the best solution from the point
   of view of performance, but is provided for the highest possible
   independence of sender and receiver. They could theoretically be
   located on different machines in a networking environment. If
   you better like a pointer to a message to be passed, make your
   pointer the message.

See Also

   Typedefinition TaskReturn, Receive


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


Declaration

   PROCEDURE Sleep(Ticks:LongInt);

Purpose

   "Sleep" lets your task suspend itself for a certain number of
   timer-ticks.

Example

   Writeln('I''m going to sleep for 3 seconds!');
   Sleep(Seconds(3));
   Writeln('Hi, here I am again!');

See Also

   Seconds

                                                Suspend / Terminate


Declaration

   FUNCTION Suspend(Task:TaskNoType):BOOLEAN;

Purpose

   Brutally suspend a task which is currently computable.
   "Task" contains the id of the task to be suspended.
   A task that has been suspended by a Suspend system-call can ONLY
   be reactivated by a ReadySuspended system-call.
   If the task addressed was not computable, Suspend would return
   FALSE to the caller. Otherwise TRUE is returned.

See Also

   Typedefinition TaskNoType, ReadySuspended


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


Declaration

   PROCEDURE Terminate;

Purpose

   A task may terminate itself by executing a "Terminate"-system-call.
   The task-descriptor is marked available and the private stack is
   returned to the memory pool.

See Also

   CreateTask


                                                           TimeSlice


Declaration

   PROCEDURE TimeSlice(Slice, DynQ:Byte);

Purpose

   The width of a timeslice and the +/- maximum number of ticks to
   credit/debit during dynamic scheduling, may be changed by issuing
   a "TimeSlice"-system-call.
   "Slice" describes the size of a timeslice in timer-ticks;
   "DynQ" contains the number of ticks to credit/debit during
   dynamic scheduling.
   "Slice" defaults to 2; "DynQ" defaults to 10.