R E F O R M   Version 5.02

          

                                ASCII FILE REFORMATTER

          

                               (C)COPYRIGHT 1984, 1985

          

                                 ALL RIGHTS RESERVED

          


















                                        - 1 -
          










          

                                INTRODUCTION TO REFORM

          










            REFORM  is a unique software tool designed to allow the user to
          format ASCII data files in a manner which will  allow these files
          to  load  into  spreadsheet programs such as LOTUS  1-2-3  (LOTUS
          1-2-3  is  COPYRIGHT  by   LOTUS  DEVELOPMENT  CORPORATION).  All
          references  to  spreadsheets and all sample sessions will  assume
          that the user is using the 1-2-3  software  using the File Import
          Numbers option (/FINfilename~).

            To appreciate the  importance  of  this  program, the user must
          realize the limitations that are  normal  with  the  File  Import
          option  within  the spreadsheet.  As designed, the user is  faced
          with two options for importing an ASCII file.  Once the cursor is
          located within the spreadsheet, the user may elect to import data
          as TEXT or as NUMBERS. If the TEXT option is selected, then alpha
          and numeric  data  for each record is placed into the same column
          and incremented in increasing rows.  This situation brings in all
          the data, but does not allow access to individual data "elements"
          as separate columns. 

            If the  NUMBERS  option is selected, all alpha data is ignored;
          alpha data is stripped  from  the  alpha-numeric  data fields and
          only  the numeric data is allowed to enter.  The benefit of  this
          option is that the  numeric data is loaded into separate columns,
          but the loss of the alpha information makes the data less usable,
          if not totally unsuitable, for subsequent processing. 

          












                                        - 2 -
          










            What is required  is  for  the  data  to  be  imported into the
          spreadsheet in such a manner that the original format of the data
          is maintained;  that is, alpha and/or alphanumeric data reside in
          separate columns from numeric data.  This provides the ability to
          use the imported data as a data-base or to make references to the
          data through formulas or other operations. 

            Providing the above requirement is the function of REFORM.  The
          program will analyze the data making determinations as to whether
          alpha   or   numeric   formats   are  appropriate.    Once   this
          determination is made, the  program  will  write  this  data to a
          separate file  for loading into the spreadsheet.  The data may be
          imported into a blank worksheet  or  into an existing worksheet. 
          Formulas and cell references  are  not  changed  when  using File
          Import.

            REFORM  is  a  very  versatile  program  and  will allow  great
          flexibility in incorporating  ASCII  print-image  data files into
          worksheets.   Soon  you will be building spreadsheets which  make
          use  of  this  power  by  loading  on-line terminal sessions  and
          download files from main frame computers. 

          































                                        - 3 -
          





























          

                                      SECTION 1

          

                                    P A R S I N G

          


























                                        - 4 -
          










                               Parsing mode - overview





          Using REFORM is straight forward  and  will  become second nature
          once  you understand the underlying logic of the  software.   So,
          PLEASE, study this section in detail and then continue to Section
          2 - OVERRIDE MODE. It is necessary that you gain an understanding
          of the two modes of operation; they are vastly different. 

            REFORM'S  PARSING MODE works by  scanning  each  line  of  your
          specified  input  text   file.    The   program  will  accumulate
          individual characters into a grouping of characters (field) until
          it encounters consecutive spaces  (white  space)  which  equal or
          exceed the PARSING VALUE.  The  default  PARSING VALUE set during
          program initialization is 2. Assuming that the  default  value is
          not  changed, the program will read each line of input  from  the
          specified file and will  gather  characters  until  2 consecutive
          spaces are encountered.  The data field is then  stored  and  the
          process continues until the end of  record (EOR) is read.  An EOR
          is defined as a carriage return / line feed sequence.  A total of
          127 fields can be stored in memory for each record. 

            When the EOR is detected, the program will begin the process of
          writing the  data  to  the  output  file  or  the  screen.   Each
          collected field is analyzed to determine whether it  is  alpha or
          numeric.   Alpha fields are  written  surrounded  by  quotes  and
          numeric  fields are written as a string of digits.  The  separate
          fields  are  comma delimited.  The user may  change  the  default
          program  options  to force  the  output  to  be  formatted  in  a
          different manner. 

            This process of collecting characters into fields,  determining
          type, and writing to the output file or device continues  line by
          line (a line is considered a single record) until the end of file
          (EOF)  is encountered.  The EOF is defined as an ASCII  Character
          with a code value of 26.















                                        - 5 -
          










            Additionally, the program will  compress  white space (equal to
          or exceeding the parsing  value)  preceeding  the first non-space
          character within a record into a single space.   Multiple  spaces
          which occur after the  first non-space character are ignored.  At
          this time, an example is in order. 

          

                                      EXAMPLE 1


          1234567890123456789012345678901234567890123456789012345678901234567890

             ITEM #     QUANTITY    PRICE EA.     TOTAL PRICE
             ------     --------    ---------     -----------
             012AQP           04        1.25            5.00
             0219AR           01       10.45           10.45
             0221AQ           02        4.50            9.00
             0145SD           10        0.50            5.00

            Assume that you logged  onto  your  company's in-house computer
          system  with a PC communication program and saved the  preceeding
          data into a disk file (session file).  You are now ready to begin
          the task of formatting the data for use within  a spreadsheet.  A
          visual look at the data suggests that 4 columns would be required
          within  the  spreadsheet  to  load  the data.  Further  analysis,
          however, indicates  that  the  left data column does not begin in
          position  number 1 of the record - note the 3 spaces to the  left
          of each field.  Using REFORM with  it  default PARSING VALUE of 2
          will cause an empty  column  to be created (so also would a value
          of 3). Selecting a PARSING VALUE of  4 would cause the preceeding
          spaces  to be incorporated into the first data column since 4  or
          more  consecutive  spaces  would  be required to "break" the data
          into  separate fields.  At this time, 4 is decided upon as  being
          the proper  value  to  use  since all columns are separated by at
          least  4  spaces  of white space.  In general, the PARSING  VALUE
          selected should be the lowest value which  will allow the user to
          "fuse" characters into the  desired  format  while still allowing
          the program to "break-out"  individual  fields.   The  output  of
          REFORM using a PARSING VALUE of 4 is indicated below. 

          

          "   ITEM #","QUANTITY","PRICE EA.","TOTAL PRICE"
          "   ------","--------","---------","-----------"
          "   012AQP",04,1.25,5.00
          "   0219AR",01,10.45,10.45
          "   0221AQ",02,4.50,9.00
          "   0145SD",10,0.50,5.00





                                        - 6 -
          










            As can be seen from the example, REFORM  broke  the  input data
          into  its  various  data  types.   Loading  this  data  into  the
          spreadsheet using the File Import Numbers option would provide us
          with 4 distinct columns.  Once the spreadsheet column widths were
          set, the format would appear very  similar  to the online session
          from which the data was captured.   Note  that REFORM ignored the
          spaces between columns 1-2, 2-3, and 3-4.

            REFORM makes data type decisions based upon the following:


               1)   Any non-numeric character (characters other that 0-9
                    and "+", "-", "." and optionally "$" ) in a data field
                    constitutes an alpha data type.  Digits separated by
                    spaces less than the PARSING VALUE also indicate an
                    alpha data type.

               2)   Commas in a field are overlooked for type determination
                    and are not written to the output file if type numeric.
                    Unless defeated,  the dollar sign is also overlooked.

               3)   Decimal points are considered numeric unless they
                    appear in multiple within an otherwise numeric field.

               4)   Signs ("+" and "-") are considered numeric if not
                    separated from the digit string by any spaces and
                    if they only appear once within the field.


               Based upon the above rules,  the following types would assigned:

                    DATA           TYPE                RULE(S)
               -------------     ---------        --------------------------------

               999,999.00          numeric        Rule 2 and 3
                  -123.56          numeric        Rule 3 and 4
               -12345678-          alpha          Rule 4
               + 12345.00          alpha          Parsing value > 1,  Rule 4
                    "              numeric        Parsing value = 1,  Rule 1
               +12345.00.          alpha          Rule 3
                    A1234          alpha          Rule 1
                    1234A          alpha          Rule 1
               $12,345.00          numeric        Default program option
                    "              alpha          User override

            The dollar  sign  may  be  alpha  or  numeric  (default) and is
          controlled by selecting option #5  from  the  main-menu  and then
          choosing "DOLLAR SIGN ALPHA/NUMERIC" from the subordinate menu. 






                                        - 7 -
          





























          

                                      SECTION 2

          

                                       OVERRIDE

          


























                                        - 8 -
          










                               Override mode - overview





          While using REFORM in the default  PARSING  MODE will most likely
          serve most of your needs, there  exists another mode of operation
          - OVERRIDE - in  which  you can specify to the program the manner
          in which you would like to have the  input  data formatted.  This
          need results when you must select a PARSING VALUE large enough to
          "fuse" certain data while a smaller value is required to  "break"
          other data fields. 

            OVERRIDE  is  selected  from  the main menu as option #3.  Upon
          selecting this option for the first time, you will be viewing the
          specification  input screen.  A  brief  review  of  how  OVERRIDE
          specifications must be  presented  to the program is available by
          pressing f(8).  The help screen is repeated below:

          

                              REFORM 5.0                     (C) 1984,5 MRB
          ----------------------------------------------------------------
          YOU HAVE ENTERED THE MANUAL O V E R R I D E  SPECIFICATION ROUTINE.
          YOU MAY INPUT UP TO 32 FIELD SPECIFICATIONS WHICH WILL BE USED TO
          ANALYZE EACH LINE OF INPUT DATA.  THE FORMAT FOR EACH IS AS FOLLOWS:

               (1)       FIELD #1 = STARTING CHARACTER POSITION
               (2)       FIELD #2 = NUMBER OF CHARACTERS IN FIELD
               (3)       FIELD #3 = 0,1,2, OR 3 [SEE BELOW]

          FIELD #3 SELECTED BASED UPON THE FOLLOWING CRITERION :

               SELECTION = 0 = SOFTWARE SELECT FOR FIELD TYPE
                    ''   = 1 = NUMERIC FIELD TYPE
                    ''   = 2 = ALPHA FIELD TYPE
                    ''   = 3 = FIELD NOT WRITTEN TO OUTPUT

          EXAMPLE :
                    1,8,0     ... START CHARACTER = 1, WIDTH = 8, SOFTWARE SELECT
                    9,8,2     ... START CHARACTER = 9, WIDTH = 8, ALPHA TYPE

          Note:     In REFORM version 5,  any delimiter may be used to
                    separate the field specifications.  For the input
                    routine a delimiter is any non-numeric character.








                                        - 9 -
          









          When using the OVERRIDE MODE, it is suggested that the user first
          print the input data file or at least a representative portion of
          the  file.   Then  using   a  straight-edge,  line  the  printout
          vertically creating columns which will represent the way the data
          will appear within the  spreadsheet.   Using a programmers' rule,
          locate  the  starting character position of each column  and  the
          column width.  Continue for  all  columns.   Be  certain that you
          select  the  proper  location  for print position 1 as all  other
          extractions are  relative  to the left margin.  If in doubt about
          the  proper  starting position,  you  may  use  REFORM  with  the
          VERBATIM  MODE  "on" to  direct  the  input  file  to  the  video
          display.  Then using the scale presented on the screen, count the
          character positions. 

          

          NOTE:

            The VERBATIM MODE is selected by first selecting option #5 from
          the  main  menu.   When the option sub-menu appears, position the
          arrow indicator using the 'ESC' key to the line "Verbatim Display
          Mode"  and  press 'ENTER' key.  Respond to the request with a "1"
          and  press  'ENTER'  twice.  The option menu will update and  the
          indicator  will  reposition to "********** E X I  T  **********".
          Press 'ENTER'.

            Should  you  find  a need to edit the  OVERRIDE  parameters,  a
          subsequent  selection of main menu option #3 will  bring  up  the
          current  parameters  and  allow  you to "edit". Scan through  the
          parameters with the 'SPACE'  key  until  the  display  shows  the
          parameter you wish changed.  Press the  'ESC'  key and supply the
          program with the parameter number (the left-most number under the
          the heading "FIELD#"). After pressing 'ENTER' you then supply the
          new starting position, field  width,  and  type  identifier.   Be
          certain to separate the three fields with commas and to terminate
          the entry with 'ENTER'.  Return  to  the  main  menu is automatic
          after scanning through all stored parameters. 

            If  additional  field specifications are required, simply  scan
          through the stored parameters until the last  page  is  displayed
          and press 'ESC'. Then supply the program with the next sequential
          number; ie, if fields 1  through  5  were  displayed  and  it was
          desired  to  add a sixth field, respond with 6 and 'ENTER'  after
          the  request for the field number.  Then supply the program  with
          the  remaining  three  parameters  - separated with commas -  and
          terminate the input with 'ENTER'.









                                        - 10 -
          









          Field  specifications  cannot  be   deleted,   but  they  can  be
          deactivated from producing any  output.  This situation is common
          when it is desired to produce  all  fields  during  a spreadsheet
          development phase, but it is desired to reduce the volume of data
          during the production phase.  Simply edit the field and provide a
          type identifier of  "3".  The  field will no longer be written to
          the output device or file. 

            Care  should be exercised when using the OVERRIDE  Mode  as  no
          checks are  made of the input data under type "1" and "2". If the
          user assigns a field as numeric and the field contains commas and
          dollar signs, they will NOT be removed.  If any doubt exists, the
          field should be assigned "0".

            Whenever applicable, the user  should specify the PARSING MODE.
          However, the power of the  OVERRIDE  MODE  is  available whenever
          required.  If using the OVERRIDE MODE, any changes in the  format
          of  the  input  data  file  will  require  changes  in the  field
          specifications. 

          


































                                        - 11 -
          





























          

                                      SECTION 3

          

                                   PROGRAM OPTIONS

          


























                                        - 12 -
          










                                   Program options

            From the main menu, the option menu may be selected by pressing
          the "5" key.  Upon so selecting, a subordinate  menu is presented
          in  the  center  of  the  screen.   Along  the  right  side is an
          indication of the current status of the program options and along
          the  left  side  is  an indicator which may be  moved  to  select
          different options.  The indicator is positioned with the  "SPACE"
          key for a top to  bottom  motion  and  with  the  "ESC" key for a
          bottom to top motion. 

            Once the  arrow is positioned to indicate the desired choice, a
          depression of the "ENTER"  key  will  log  the request.  A prompt
          will  be  provided  to  the user in the lower part of the  screen
          along  with  the  available  choices  or  parameters.   A   brief
          description of each option is provided on the following pages. 






































                                        - 13 -
          










          



          Field Delimiter This parameter indicates  how  the  output record
                          will   have  individual  fields  separated.   The
                          default  value  is  44  which  indicates a  comma
                          character. 

          Literal (String) Prefix
                          Whenever  REFORM  writes an alpha string  to  the
                          output  device  or   file,  The  alpha  field  is
                          prefixed with  a  special  character  to indicate
                          that it is  alpha.  The default value is 34 which
                          is a double quote character. 

          Literal (String) Suffix
                          Same  as  above  except   is  the  closing  alpha
                          indicator.   Default  value  of  34 to indicate a
                          double quote. 

          End of Line Characters (3)
                          The  end  of  line is also known as  the  end  of
                          record  (EOR).   The   default   value  for  this
                          parameter is 0,13,10 which translates into a null
                          character,  a carriage return  character,  and  a
                          line-feed character. 

          Dollar Sign Alpha/Numeric
                          The dollar sign is  normally  overlooked  when  a
                          field is being classified as  alpha  or numeric. 
                          Turning  this  switch  off  will  result  in  all
                          numeric  fields  containing  a dollar sign to  be
                          considered as alpha.  The default value  for this
                          switch is "ON".



















                                        - 14 -
          












          Null Line Written Output
                          This  switch  controls how REFORM handles a  null
                          line encountered in the input file.   The default
                          value is "OFF" - null lines not  written  to  the
                          output file or device. 

          Key String Thru Filter
                          Many applications require that  data be extracted
                          from within a file based upon the fact  that  the
                          data elements, by record, all have a specific key
                          or  identify.   For  example,  if  a report on  a
                          time-share  application  provided data by  state,
                          and if each record (line) had  the  state name or
                          abbreviation as part of  the data, then this mode
                          of  operation could "filter" all the input  lines
                          and  only  write  records  to  the  output  which
                          contained   the  state  name  or   abbreviation. 
                          Additional parameters  allow  the user to specify
                          where the key must  be  located  to  consider the
                          record as valid or optionally  the  entire record
                          may be searched. 

          Verbatim Display Mode
                          This switch  controls  whether  the input file is
                          displayed on the screen during processing.   When
                          selected "ON" the "SCREEN  MODE  LINE  COUNT"  is
                          changed to 5, but may be subsequently changed  to
                          any value.  This mode  if  normally "OFF" - input
                          file not displayed. 

          





















                                        - 15 -
          












          Maximum Lines to New File
                          Many programs have a limit on the number of lines
                          of data which may be imported at a single  time. 
                          Lotus 1-2-3 has a limit of 2048  lines  of data. 
                          By changing this value, REFORM's  output  may  be
                          directed  to multiple files automatically - up to
                          a  limit  of  99  files.   REFORM  will handle  a
                          maximum of 32767 lines of input and/or output. 

          Strip all Control Codes
                          When this mode is active, all incoming characters
                          are  analyzed,   and   only   pure  alpha-numeric
                          characters (ASCII codes  between  32 and 126) are
                          passed.   This  mode  of  operation  will  remove
                          "happy-faces" and other strange characters from a
                          Lotus   1-2-3   import    file.     Most   modern
                          communications   programs   will   provide   this
                          function for you. 

          Read / Save Parameter File
                          This option allows the user to "Read" or  "Write"
                          the current  REFORM  filenames,  parsing value or
                          override values, and all options  from/to  a disk
                          file.  User must supply Drive I.D., Filename, and
                          Extension  (ie,  A:TESTFILE.ABC)  as   required. 
                          Sub-directories are not supported.  Read file may
                          cause automatic program start-up.  See Appendix.

          ******** E X I T ********
                          This  is  the  "home"  position  for  the  option
                          selection indicator.   Pressing 'ENTER' with this
                          option selected will cause the program  to return
                          to the main menu. 

          

















                                        - 16 -
          










                         Appendix A - Hardware requirements 

            Please note that due  to  the  increased code size of REFORM 5,
          users with only 128K of memory may find that the utility will not
          function properly - therefore, REFORM 5.0 is only recommended and
          supported for machines  with 192K or more of RAM. Users with 256K
          of memory should be  certain  that no RAM-disks or Print-spoolers
          are  installed  which  reduce  the  effective  program  and  data
          segments below 64K each. 

                (Use DOS's CHKDSK to verify 128K minimum of free RAM.)

            Reform is written to  work  on  most PC-DOS / MS-DOS machines. 
          However, the program is only guaranteed  for  the  IBM-PC  and XT
          models and 100% compatibles.  To date,  the  program has been run
          successfully on IBM, COMPAQ,  ATT,  and  SANYO computers.  If you
          experience  problems with REFORM and are running a  "compatible",
          please try processing your software on one of the above mentioned
          machines.  You should also check your DOS version to make certain
          that your are running PC-DOS 2.1 or MS-DOS 2.11 or later. 

            REFORM should process under a  network  environment, but due to
          the varied systems currently available the user is  strictly  "on
          your own" with this arrangement. 

          




























                                        - 17 -
          










                          Appendix B - Making a working copy

            Never use your MASTER REFORM disk for day-to-day work.  Make  a
          duplicate  copy  of  the  program diskette  using  DOS  and  then
          transfer the DOS SYSTEM to the work disk.   Two  methods  may  be
          used as detailed below:



          Using "DISKCOPY"


               (1)  Insert the DOS MASTER Disk in A: and a blank disk in B:
               (2)  Type "DISKCOPY A: B:" (type only what is between quotes)
               (3)  Press "ENTER"
               (4)  Remove DOS disk and insert REFORM MASTER disk
               (5)  Press any key to start copy. Wait until complete and
                    respond with "N" when asked if you wish another copy
               (6)  Remove REFORM MASTER and again insert DOS disk
               (7)  Type:  "SYS B:"     and press "ENTER"
               (8)  Type:  "COPY COMMAND.COM B:"   and press "ENTER"
               (9)  Remove all disks and label new copy.  Store Master.


          Using FORMAT and COPY


               (1)  Insert DOS MASTER in A: and blank disk in B:
               (2)  Type:  "FORMAT B:/S"  and press "ENTER"
               (3)  Remove DOS disk from A: and insert REFORM MASTER
               (4)  Type "COPY *.* B:"   and press "ENTER"
               (5)  Remove all disks and label new copy.  Store Master.






















                                        - 18 -
          










                    Appendix C - Autoexecution of parameter files

            Any completely specified parameter  file  may "take control" of
          REFORM  and  process  data  independent  of  operator control  by
          appending the string "AUTOEXEC"  to  the  end  of  the first line
          within the parameter file.   When  recalled  through  the  OPTION
          'READ Parameter file' mode, the file  will  set all options, open
          the necessary input and output files, and process  until  the EOF
          is read on the input file.  The recommended manner used to modify
          the parameter file is detailed below. 

            Use  DOS  EDLIN to edit the existing parameter file.  The  file
          should be complete;  ie,  all  filenames  and  options  should be
          correct.  The following example assumes  that  our file is called
          "AUTOTEST.DAT" on drive B:, the DOS Supplement diskette (IBM)  is
          in A:, and the "A>" prompt is being displayed. 

          

          Type the following:



                         B:                       (press ENTER)
                         A:EDLIN AUTOTEST.DAT     (press ENTER)
                         1                        (press ENTER)
                         F3                       (Function key)
                         AUTOEXEC                 (Observe case. Press ENTER)
                         E                        (press ENTER)

            When the edited "AUTOTEST.DAT" file  is  read  by  REFORM,  all
          options are reset and execution will begin.  Any errors contained
          in  the  parameter  file  will  cause  execution  to halt and  an
          appropriate  error message will be displayed.  Caution should  be
          exercised to insure that proper  instructions are provided to the
          operator when this mode of operation is used. 

            While no system is  "crash-proof",  using  REFORM with autoexec
          parameter files will provide a measure  of  confidence to routine
          production jobs.  Additionally, the user  may wish to protect the
          parameter file from being overwritten by  using a file utility to
          set   the   file  attribute  byte  to  read-only  (Peter   Norton
          Utilities).











                                        - 19 -
          



      'READ Parameter file' mode, the file  will  set all options, open
          the necessary input and output files, and