TED.COM

The Tiny EDitor, TED.COM, from PC Magazine, Nov. 15, 1988, pp 281-322, has
an error which causes the program to crash and possibly lock up your computer
on disk write errors such as writing to a full disk or one with a full
directory.

This patch, which is done using DEBUG, changes only one POP to a PUSH and
moves a PUSH CS, POP DS pair up three lines.

Here are the necessary changes to fix the disk write error handling with
references to TED.ASM, the offset into TED2.COM in DEBUG, the old code and
the new code.

TED.ASM                       Offset   Old Code          New Code

EXIT PROC NEAR, after DONT_ADD_EOF:

                               08D1    POP DS            PUSH DS
Exit on a write error                  JC WRITE_ERROR    PUSH CS
Was entire file written                CMP AX,CX         POP DS
If not, exit                           JNE WRITE_ERROR   JC WRITE_ERROR
                                       PUSH CS           CMP AX,CX
Get the code segment           08D9    POP DS            JNE WRITE_ERROR

The label WRITE_ERROR is a offset 08B3.
 
The original ASM file can be modified and reassembled, or DEBUG can be used
to make the reqired changes in TED2.COM.  TED-FIX.SCR contains the necessary
instructions for DEBUG.  Place DEBUG.COM, a copy of TED.COM, and TED-FIX.SCR
on a disk.  Issue the following command:

                       DEBUG  TED.COM < TED-FIX.SCR

DEBUG will load TED.COM, make the necessary changes, and write it back out
with the name TED2.COM.

If you unassemble either the original TED.COM or the patched TED2.COM, you
will find that DEBUG interprets the JC commands as JB and the JNE as JNZ.
This makes no difference, the file is correct and will run properly.

The new TED2.COM is identical to the original, except it will not crash or
lock up your computer on a disk write error.
                                                           John M. King
                                                              1/4/89