TED.COM

The Tiny EDitor, TED.COM, from PC Magazine, Nov. 15, 1988, pp 281-322, does
not set its own colors.  As a result, it will come up in DOS white on black
or the colors left by a previous program.  In the latter case, the colors for
the message line at the bottom of the screen may be objectionable.

This patch sets the colors used by TED to brown on black and black on brown
for the inverse portion of the message line and for marked text.  You can
easily select other color combinations by editing the file TEDCOLOR.SCR.

First, use TED-FIX.SCR to patch the bug in TED.COM which can cause crashes
on disk write errors, such as attempting to write to a full disk.

Here are the necessary changes to set colors with references to TED.ASM,
the offset into TED2.COM in DEBUG, the old code and the new code.

TED.ASM                     Offset     Old Code             New Code

COLOR:

Save the normal attributes   0297    MOV NORMAL,AH      MOV BYTE PTR [01E3],06
Flip the color bits                  XOR AH,1110111B    MOV BYTE PTR [01E4],60
                                     MOV INVERSE,AH     NOP

The NORMAL byte is at offset 01E3, followed by INVERSE at 01E4.

The original ASM file can be modified and reassembled, or DEBUG can be used
to make the reqired changes in TED2.COM.  TEDCOLOR.SCR contains the necessary
instructions for DEBUG.  Place DEBUG.COM, a copy of TED2.COM, and TEDCOLOR.SCR
on a disk.  Issue the following command:

                       DEBUG  TED2.COM < TEDCOLOR.SCR

DEBUG will load TED2.COM, make the necessary changes, and write it back out
with the same name.  Note that this overwrites the file that was loaded..

Other colors are 02,20 for green on black;  1F,F1 for bright white on blue;
and 0E,A0 for yellow on black with bright green on black for the inverse color.
You can use anything you find pleasing.

The new TED2.COM is identical to the original, except it will come up in color
on a color monitor.

                                                           John M. King
                                                              1/4/89