RBBS-PC 17.1D change WM042201
                         -----------------------------

                                      by
                                 Warren Muldrow
                             The Software Designer
                                Albany, Georgia
                                  912-432-2440

    The new U. S. Robotics modems have the ability to fix the DTE baud
rate (the rate at which the computer and modem communicate) for high speed
connections, while following the caller's baud rate at connections at or
below 2400 baud.  The fixed rate for high speed connections can be either
19200 or 38400, which allows maximum throughput for file transfers.  RBBS-PC
will support baud rates up to 19200 baud.

    While it is also possible to fix the DTE rate for all callers and leave
RBBS-PC's baud rate permanently at 19200 baud, this can cause problems with
door programs which do not correctly handle the Clear-To-Send (CTS) signal
from the modem.  By taking advantage of the capability of the new modems,
these problems can be eliminated while still providing file transfers at
1600 characters per second or faster when connected to callers using the
high speed modems.

    The changes in the accompanying archive will add a third possible value
for the configuration variable KEEP.INIT.BAUD which is option number 237 on
page 12 of the configuration screens ("Leave modem at initial baud").  The
possible values are:

        NO   -- Always match the DTE baud rate to the caller's baud rate
        YES  -- Always leave the DTE baud rate at its initial rate
        HIGH -- Set the DTE rate to match the caller's baud rate for
                connections at 2400 baud or slower.  Otherwise, keep the
                DTE baud at the initial rate.

    The changes to achieve this are very simple and effect only a few lines
of four programs: CONFIG.BAS, CNFG-SUB.BAS, RBBS-PC.BAS, and RBBSSUB2.BAS.
Also included in this archive is change WM021700 which extends the timeout
value for sending characters to the modem, which allows proper operation at
fixed DTE rates when the caller is using a slow baud rate.  It effects only
one line in RBBSSUB1.BAS.

    The files included are suitable for BLED merging against unmodified
versions of RBBS-PC 17.1D.  If you have made other changes to these programs
I recommend that you apply them by hand to avoid possible incompatibility
problems.


       Set Up Information for U. S. Robotics High Speed Modems
       -------------------------------------------------------

    Displayed below is the response given by my HST as set up for RBBS-PC
operation.  The display was obtained using the "ATI4" command.  Each
parameter which differs from the normal setup will be discussed.

        USRobotics Courier 9600 HST Dual Standard Settings...

           B0  C1  E0  F1  M0  Q0  V1  X1
           BAUD=19200  PARITY=N  WORDLEN=8
           DIAL=HUNT   ON HOOK   TIMER

           &A2  &B0  &C1  &D2  &G0  &H1  &I0  &J0  &K0
           &L0  &M4  &N0  &P0  &R2  &S0  &X0  &Y1

           S00=000   S01=000   S02=043   S03=013
           S04=010   S05=008   S06=002   S07=060
           S08=002   S09=006   S10=007   S11=070
           S12=050   S13=004   S14=000   S15=000
           S16=000   S17=000   S18=000   S19=000
           S20=000   S21=010   S22=017   S23=019
           S24=025   S25=000   S26=000   S27=129
           S28=008   S38=000

    B0  -- For the Dual Standard modem, allows proper connection to incoming
           calls from V.32 compatible modems and will switch to HST mode for
           calls from HST modems.  For other than Dual Standard modems, use
           B1.

    &A2 -- For Dual Standard modems only.  Adds /HST or /V32 to the normal
           extended result code.

    &B0 -- DTE rate follows connection rate.  On the newest modems, switch
           register S27 determines the fixed high speed rate.  On some, &B2
           fixes ARQ calls and follows non-ARQ calls.  Use &B0 when config
           parameter 237 is NO; &B1 when 237 is YES; and &B0 or &B2 when
           237 is HIGH depending on which version of ROM your modem uses.

    &C1 -- For Hayes modems this means the carrier detect signal should be
           true only when a carrier is actually detected.  It is not in the
           USR documentation.

    &D2 -- For Hayes modems this means to disable auto-answer when carrier
           is dropped.  It is not described in USR documentation.

    &H1 -- Causes the modem to lower the Clear-To-Send signal when its
           buffer is full.  Enables hardware handshaking.

    &K0 -- Data compression disabled.  This will result in an increase in
           throughput of around 5 percent when transfering compressed files.

    &R2 -- Will allow the computer to delay data transmission from the modem
           using the Ready-To-Send (RTS) hardware handshaking.

    S13 -- Set to 5 to eliminate the 250 millisecond pause before the modem
           sends result codes to the computer and to cause the modem to return
           itself to its default settings when DTR goes low.  Default value of
           zero may be used.

    S27 -- Set to 1 when config parameter 237 is YES or NO.  Set to 129 when
           237 is HIGH.  The one causes the modem to use V.21 answer sequence
           for 300 baud calls which allows it to successfully connect to both
           V.21 and Bell 103 compatible modems.

    Switch settings should be: U U D D D U U D D U.  This differs from the
RBBS-PC documentation only in the setting of switch 3.  Setting switch 3 down
causes the modem to default to "Quiet Mode OFF," which means that result codes
will be set to the computer.  The only time that RBBS-PC does not look for
result codes is when going off hook for local mode or to exit to DOS.

    Please refer any questions or comments concerning this modification to me
at The Software Designer BBS.  I will accept voice calls on your dime at
(912) 432-7154 during the evenings or on weekends.