ZIP.DOC
                                   -------
                           Instructions for ZIP.COM
                   IBM PC Fast Serial File Transfer Utility
                             Version 1.30 (4/89)

                               (c)1989 E. Meyer


        Requires:  two IBM PC compatible computers; DOS 2.x or above;
                   serial (null modem) cable.



     ZIP is a tiny, fast utility to transfer files between two IBM compatible 
computers over an ordinary serial cable connection.  This can simply be more 
convenient than constantly swapping disks; and of course, it is necessary when 
the computers don't share a common disk format, as in the case of a desktop PC 
with 5" drives and a laptop (or PS/2) with only 3" drives.

     Why use ZIP?  Most computer manufacturers offer additional disk drives or 
other hardware accessories to provide access to data on both 3" and 5" disks; 
but these can cost hundreds of dollars, and make a laptop computer far less 
portable.  There are also several commercial programs for fast serial 
transfer, but they often cost over $100.  (To be fair, some of these probably 
do have extra conveniences that ZIP lacks.)
     You can transfer files over a serial cable using any good communications 
program, but ZIP is easier, and up to 6 times faster for this purpose, than 
any telcom software:
            Telcom programs: modem       2400 bps            0.3 K/sec
            Telcom programs: cable      19200 bps            2.3 K/sec
      --->  ZIP: cable                 115200 bps     up to 14.1 K/sec
ZIP will come about as close to this amazing throughput as your computer speed 
allows -- it can be over twice as fast as some other programs that transmit at 
"115200 bps".  (On my 8MHz XT clone, it reaches about 10K/sec.)  Of course, 
disk access will also take time; with any program, large amounts of data can 
be sent more quickly when transferred to and from a hard or RAM disk, rather 
than a (slow) floppy disk drive.

     (Note: ZIP does not compress files, and is not related to the new PKZIP 
series of file compression utilities by Phil Katz.  This should be obvious but 
I'll say it anyway.)


                           XMODEM TRANSFER BY CABLE

     As you might now suspect, although they are much slower than ZIP, you can 
use most telecommunications programs to transfer files between computers by 
cable, without a modem.  In fact, you may need to do this in order to get a 
copy of ZIP.COM on both computers in order to use it!  The file transfer will 
work the same way as with a remote system, except that there is no modem and 
no dialing involved.  Connect the cable; enter the telcom program on both 
computers; set the parameters (try 19200 bps, 8 bits, no parity); enter 
terminal mode, unless (as in ProComm for example) you're there already; then 
try typing, and see if the characters appear on the other end.  If not, you 
have a problem with the parameters, the port selection, or the cable.  If so, 
go ahead and run the upload function on the machine that has ZIP, and download 
on the other, with your usual protocol (XMODEM, KERMIT, whatever).


                                  BASIC USE

     Once you have a copy of ZIP on both computers, transferring a file is as 
easy as copying it from one disk to another.  To transfer files, once the 
cable is properly connected to the serial ports of the two computers, from the 
DOS prompt:

           1.  MENU-DRIVEN OPERATION.  Simply type "ZIP" on both 
      machines; the program will step you through all the necessary 
      choices, including transferring or receiving files.
           You will also have the option to view file directories.

           2.  Command line operation, for experienced users.
      On the sending machine, type:       On the receiving machine:
             C>zip FILENAME                      C>zip /r
                                             or  C>zip DIRECTORY /r
               Or, for operation using server mode,
      On the active machine, type:        On the server machine:
             C>zip FILENAME                      C>zip /s
         or  C>zip FILENAME /f               or  C>zip DIRECTORY /s

               The "FILENAME" you give can be a single file, or a 
      GROUP specified by wildcards and/or commas (see examples below).  
      Each name may include a directory; files will appear with the 
      same name on the receiving end.
               The "/R" option means RECEIVE.  The "DIRECTORY" to 
      receive files may optionally be specified; otherwise, the 
      current directory is used.
               On the "/S" and "/F" options see SERVER MODE.

     As each file is transferred you should see a blinking asterisk.  When you 
see the message "Verified", you know that the received copy exactly matches 
the original.  When ZIP is running, it can be aborted by pressing any key:
              (1) on either end, during initial handshaking
              (2) on sending end, during file transfer
                    (will abort once current file is finished)
as well as by pressing ^C (or Ctrl-Break) at any prompt.


                          SELECTING THE SERIAL PORT

     By default ZIP uses the COM1 port.  IBM-compatible computers have 
anywhere from one to four serial (RS232) ports.  The first two, COM1 and COM2, 
are implemented at standard addresses (03F8, 02F8); COM3 and COM4, if present, 
can vary from one computer to another.  To use them, or to change the default 
to COM2, you will have to install the appropriate address in ZIP.COM.

     You can select either COM1 or COM2 during operation of ZIP:  in menu 
mode, just select the choice to modify "P"arameters.  In command line mode, 
specify one of the following options:
              /1  = Use the COM1 port.  (This is normally the default.)
              /2  = Use the COM2 port.

     You will see a note in the ZIP signon message, "Port=____", giving the 
port address in use.


                           SELECTING FILES TO SEND

     If you want to transfer only certain files in a group (such as *.BAK) 
with ZIP, you can request that you be prompted to confirm each file 
individually: you will be asked to hit a key (Y/N) to determine whether the 
file is to be sent.  (In menu mode, you can select "O"ptions for a help 
message describing the selective copy operations.)  After the names of files 
to be transferred, in menu or command line mode, specify this option:
              /P  = PROMPT to confirm files individually

     This option (which can be combined with others) can be specified on 
either end -- but the option on the SENDING (or active) end governs each 
transfer.  You will see a note in the ZIP signon message, "Option /P", if this 
option is in effect.


                              OVERWRITING FILES

     It is possible that a file already exists on the receiving end with the 
same name as the one being sent.  By default, ZIP doesn't care: it will 
transfer all files specified, whether or not they overwrite existing ones.  
Several options are provided to modify this behavior.  (In menu mode, you can 
select "O"ptions for a help message describing the selective copy operations.)  
After the names of files to be transferred, in menu or command line mode, 
specify one (or two) of these options:
              /N  = copy NONexisting files only
                       (cannot be used with /E or /T)
              /E  = copy EXISTING files only
              /T  = TIMESTAMP determines overwrite

     The /N option will prevent all files from being overwritten.  The /T 
option will allow overwrites only when the new copy has a more recent time 
stamp.  The /ET combination is especially useful for backup purposes: it 
transfers only more recent copies of files that already exist.

     These options can be specified independently on either computer -- but 
the options on the SENDING (or active) end govern each transfer.  You will see 
a note in the ZIP signon message, "Option /_", if an option is in effect.


                                 SERVER MODE

     You might like to have ZIP stay "on line" on one end, ready to send or 
receive files, or answer directory requests, from the other automatically.  
(It can be convenient to do all your typing on one keyboard, especially if the 
receiving computer is in another room.)  To start server mode: in menu mode, 
just select the choice for "S"erver.  In command line mode, specify the option:
              /S  = Server mode.

     ZIP will then remain ready to communicate until such time as you press a 
key to exit server mode.  You can, at any time, transfer files TO the server 
from the active end; you will be prompted for a destination directory to 
override the default on the server end.

     You can also fetch files FROM the server.  In menu mode, just select the 
choice to "F"etch files.  In command line mode, specify the option:
              /F  = Fetch files from server.

     You must specify the full path with the filenames, if they are not in the 
default or specified directory on the server end.  You will be prompted for a 
destination directory.  The fetch request will fail if server mode is not 
detected on the other end.


                           VIEWING FILE DIRECTORIES

     When ZIP is in menu-driven mode, you will see a choice for "D"ir: this 
offers an alphabetized file listing for your reference.  You will be prompted 
for the files to list, including an optional directory, for example:
              Directory: \WORK\*.BAK

     If you just hit return, ZIP gives the full default directory, *.*.

     If the other computer has ZIP running in server mode, you can also 
request a directory from it.  Simply type a ";" before the filespec for the 
server.  This can be done alone, or together with a request on the active end:
              Directory: ;B:\BACKUP                 server alone
              Directory: \WORK\*.BAK;B:\BACKUP      combined

     This directory request will fail if server mode is not detected on the 
other end.


                      USAGE EXAMPLES (Command line mode)

     C>zip \work\my         sends file C:\WORK\MY

     C>zip gort,klaatu /d2  sends C:GORT, C:KLAATU with delay 2

     C>zip my.* /2 /p       sends all files C:MY.* over COM2, with prompts
                              to confirm each file individually

     C>zip *.* /n           sends all files which don't already exist on
                              receiving directory

     C>zip a:chapter.* /et  sends all files A:CHAPTER.* of which an older
                              version exists on the receiving end

     C>zip b:\baks\my.* /f  fetches all files MY.* from directory B:\BAKS
                              on the other end (which must be in server mode)

     C>zip /r               receives files into current directory

     C>zip \work /r2        receives into directory C:\WORK\ over COM2

     C>zip d:\ /s           waits as server to send or receive files, with
                              default directory D:\ on server end


                              TECHNICAL DETAILS

     Like many communications programs, ZIP does full CRC (Cyclic Redundancy 
Checksum) verification on the received file to ensure accurate transfer.  But 
the ZIP transfer protocol is not compatible with other software, including 
ordinary telcom programs.  Do not disturb the cable when ZIP is running, as 
this may cause the program to stall, requiring a reboot of your computer(s).  
Be sure to use the SAME version of ZIP on both ends: the transfer protocol may 
have changed.

     Your SERIAL CABLE should be a "null modem" cable: if you're building a 
cable, the transmit and receive data lines (pins 2 and 3 on a DB25 -- pins 
differ on a DB9) should be crossed, the frame and signal ground (1 and 7 on a 
DB25) straight through.  No further connections should be needed; ZIP uses no 
hardware handshaking.  Any cable that doesn't work by itself should with a 
null modem adapter.  Use a properly shielded cable; ZIP may be especially 
susceptible to RF interference.  I am not an expert on RS232 hardware: find a 
good book if you need further assistance.


                             Adjusting the Delay

     Most users will not need to worry about the "delay factor".  ZIP 
transfers data as fast as possible -- as close as your computer can come to 
the 115200 bps throughput that the serial port is capable of.  If you are 
sending data from a very fast 80286 or 80386-based AT to a slow PC, the 
receiver might simply not be able to keep up.  Therefore, ZIP has a delay 
factor, ranging from 0-9, to slow down the send rate (0 is the default).  But 
when the initial connection is established, ZIP will if necessary increase the 
delay value until data can be transferred successfully.
     If you do find that ZIP has to use a delay factor, you can speed the 
process up in the future by specifying this value yourself.  For example, if 
you find that ZIP has to reach a delay of 3 before it will send files to a 
slower computer, you can set a delay of 3 yourself -- either as an option, 
each time, or by modifying the default value in ZIP.COM itself (see below).

     To set a delay other than the default: in menu mode, just select the 
choice to modify "P"arameters.  In command line mode, specify this option:
              /D#  = Set the initial delay factor to "#" (0-9).

     This option can be specified independently on either computer -- but it 
is the setting on the SENDING end that governs each transfer.  You will see a 
note in the ZIP signon message, "Delay=_", giving the current default.  ZIP 
reports any change in delay factor when the link is established and tested.


                            Modifying the Defaults

     If you don't instruct it otherwise, ZIP will use its built-in "defaults" 
for the serial port address and delay.  These values appear in simple ASCII 
text form at the start of ZIP.COM, and can be modified to customize your copy 
of ZIP.  To get a quick look at the current settings, just enter:

                      C>type zip.com
                      [ZIP 1.30 Port=03F8 Delay=0]

     For the Port, you can use "03F8" (COM1), "02F8" (COM2), or whatever (see 
your computer manual for COM3 or COM4 port addresses).  The possible values 
for Delay are "0"-"9".  Changes can be made with any patching utility, such as 
DEBUG.  These defaults are at the very beginning of ZIP.COM (starting at 
address CS:0103).  Just change the data to whatever you require.  After 
modifying the defaults, you can still use the menu or command-line options to 
override them.
     Here is how the DEBUG session might look; we Display the default data, 
Enter 0"2"F8 in place of the 03F8 to change to a default of COM2, Display 
again to see the new value, Write the change to the file, and then Quit:

C:\WORK>debug zip.com
-d100,11f
xxxx:0100  EB 20 0D 5B 5A 49 50 20-31 2E 33 30 20 50 6F 72   . .[ZIP 1.30 Por
xxxx:0110  74 3D 30 33 46 38 20 44-65 6C 61 79 3D 30 5D 0D   t=03F8 Delay=0].
-e113 32            ^^                                          ^
-d100,11f
xxxx:0100  EB 20 0D 5B 5A 49 50 20-31 2E 33 30 20 50 6F 72   . .[ZIP 1.30 Por
xxxx:0110  74 3D 30 32 46 38 20 44-65 6C 61 79 3D 30 5D 0D   t=02F8 Delay=0].
-w                  ^^                                          ^
Writing xxxx bytes
-q

     For further information on DEBUG see your MSDOS manual.  Please DO NOT 
distribute modified copies of ZIP.COM; this could confuse other users.  They 
are for your personal use only.


                              ZIP ERROR MESSAGES

   <Argument error>  invalid command line argument(s).
    <Out of memory>  less than 64K free RAM available.
         <Too many>  global filespec (eg *.*) includes over 512 files.
       <Disk error>  trouble reading or writing file.  (No file? Disk full?)
            <Error>  communication error, or error on other end.
          <Aborted>  you pressed a key.


                              PROBLEMS USING ZIP

     ZIP works well on the vast majority of systems; but apparently, certain 
hardware/software combinations can still give ZIP trouble.  There appears, for 
example, to be a problem using ZIP when running DesqView.  I would appreciate 
reports from users if:
     * you experience transmission errors regularly
     * you find a "delay factor" necessary (this may now be superfluous!)


                                   HISTORY

ZIP 1.0  (4/88) - trial release.
    1.1  (4/88) - improved protocol; batch transfers; receive directory 
                 option; original file time/date preserved.
    1.2  (5/88) - improved error handling; patchable default port also 
                 allows use of COM3,4; small bug fixes.
   1.21  (5/88) - slower speed options; fixed bug in initializing ports.
   1.22  (8/88) - improved protocol; fixed bug in deleting temp file.
   1.23  (1/89) - menu-driven operation; detects disk-full errors.
   1.30  (4/89) - selective copy options /P,N,E,T; server mode, fetch; 
                 file directory; internal improvements.


     ZIP and its documentation are (c)1989 E. Meyer, all rights reserved.  
They may be freely distributed, but not modified or sold for profit without 
my written consent.  (Voluntary contributions are welcome.)  The user takes 
full responsibility for any damages resulting from the use of this program.

                 Eric Meyer
            401 12th Ave SE, #139            CompuServe [74415,1305]
              Norman, OK  73071