ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
	  º                                                        º
	  º          ±ÛÛÛ       ±ÛÛÛÛÛÛÛÛ           ±ÛÛÛÛÛÛÛÛ      º
	  º         ±ÛÛ±ÛÛ         ±ÛÛ       ÜÜÜ       ±ÛÛ         º
	  º        ±ÛÛ  ±ÛÛ        ±ÛÛ     ±Û  ±Û      ±ÛÛ         º
	  º        ±ÛÛÛÛÛÛÛ        ±ÛÛ      ÜÛßÛÜ Ü    ±ÛÛ         º
	  º       ±ÛÛÛ  ±ÛÛÛ       ±ÛÛ     ±Û  ±ÛÛ     ±ÛÛ         º
	  º      ±ÛÛÛ    ±ÛÛÛ      ±ÛÛ       ßßß ßß    ±ÛÛ         º
	  º                                                        º
	  º       (AT&T Servicing Utility for Microcomputers)      º
	  º                    ** ATTSUM.EXE **                    º
	  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼




                                 USER'S MANUAL
				       &
		           HARD DRIVE REFERENCE GUIDE


                         By L.J.Risner     January,1988
		   Copyright (c) L.J.Risner 1987, 1988, 1989
			      All rights reserved.

			       [Revised 01/26/89]
                           (For ATTSUM.EXE Ver 3.40)




 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
 ³			         *** CAUTION ***			      ³
 ³									      ³
 ³    AS WITH ANY UTILITY THAT CAN BE DESTRUCTIVE TO DATA, BE SURE THAT YOU   ³
 ³    HAVE BACKED UP YOUR DATA ON THE HARD DRIVE BEFORE YOU ENTER INTO ANY    ³
 ³    OF THE FUNCTIONS THAT CAN FORMAT THE DRIVE(S) - ACCIDENTS CAN HAPPEN!   ³
 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ







       		       - SEE UPDATE LISTING ON PAGE H-1 -



                                    [Page 1]			(Rev 01/26/89)



			   *** TABLE OF CONTENTS ***




	      Title 				            Page
              -----				 	    ----


	     TABLE OF CONTENTS ------------------------------ 2

	     INTRODUCTION ----------------------------------- 3

	     FEATURES --------------------------------------- 4

	     SYSTEM REQUIREMENTS ---------------------------- 5

	     USING THE PROGRAM ------------------------------ 6





	     APPENDICES -
		     Hard Drive Theory ---------------------- A
		     Interleave Theory ---------------------- B
		     Bad Track Formatting ------------------- C
		     Caring For Your Hard Drive ------------- D
		     Answers To Frequently Asked Questions -- E
		     Error Messages ------------------------- F
		     Program Flow Chart --------------------- G
		     Upgrade & Revision Listings ------------ H



	     Figures
	     -------

	     A-1 (Diagram of Typical Drive) --------------- A-1

	     A-2 (Typical Track Sector) ------------------- A-3

	     B-1 (Various Interleave Factors) ------------- B-1

	     B-2 (Timing Chart) --------------------------- B-2

	     G-1 ( Program Flow Diagram) ------------------ G-1








			            [Page 2]			(Rev 10/27/88)


                             *** INTRODUCTION ***
 

	This program was developed primarily out of a need to provide AT&T field
servicing personnel a single professional quality tool for servicing hard drives
in all AT&T microcomputers.  However, while in the process of writing this
program I soon discovered that AT&T microcomputer dealers as well as VARS are
using a variety of utilities to service AT&T CPU's.  I then decided that it
might be best to structure the program for all of those who install/maintain
AT&T CPUs and include features for dealers and users that are not found in other
utilities but are extremely useful. 

	I highly recommend that all user's read this document to get an idea of
what's happening "under-the-hood" and "why" (You will also find that the program
is doing quite a lot to free you from many decisions that other servicing
utilities require). 



GENERAL INFORMATION:

	- Written in Assembler.

	- Assembler = Microsoft Macro Assembler 5.1

	- Editors = MicroEmacs 3.7 and Microsoft MASM "M" editor.

	- All video I/O is achieved through video interrupts allowing for
	  complete video peripheral flexibility.

	- This program has been tested on all AT&T microprocessors.

				   ----------


	      [ATTSUM.COM & ATTSUM.DOC are FREE to any/all users.]


	Inquiries, suggestions or questions in regard to this program or its use
should be directed to:

			       L.J.(Larry)Risner 

		Work:			     Home:
		      1000 Broadway Rm607          2350 Bella Vista Ave.
		      Oakland, CA 94607	   	   Martinez, CA 94553
		      (415)464-4687        	   (415)372-6599

			        attmail!lrisner







                                    [Page 3]			(Rev 11/10/88)

                                  
			       *** FEATURES ***




	- A single small program for ALL AT&T PC's.

	- Totally menu driven.

	- Program is "full" size - does not expand in RAM.

	- Displays DIP switch tables for "PC class" CPU's.

	- Displays hard drive tables for all AT&T PC's.

	- Displays hard drive type switch settings on "PC class" controllers.

	- Program automatically configures to the CPU model.

	- User views only pertinate information for class PC class used.

	- Automatically conforms to ST-506 or ESDI controller/drive.

	- Displays hard drive(s) statistics.

	- Can determine optimum interleave factor.

	- Complete low level formatting features built-in.

	- Real time search/display bad track(s) function.

	- On-screen activity graphic displays.

	- Easy-to-use "bad track" processing feature. 

	- Complete error sensing w/both probable cause and cure messages.

	- Format/test results can be saved to diskette, printer or both.

	- Serial number/ID and date/time stamp on saved record.

	- "SHIPPING" feature for safe drive transporting.

	- Shipping feature "parks" all equipped HDU's when invoked.

	- Displays of "AT&T standard" HDU controller boards w/settings.

	- Monitors drive type switch setting changes with power applied.

	- Operates over networks.






				    [Page 4]			(Rev 12/20/88)


                          *** SYSTEM REQUIREMENTS ***





	To fully use this program the AT&T microcomputer must meet the following
minimum requirements (See note 1):

			- Be an AT&T PC6300, PC6300PLUS, 6300 WGS, PC6310, 
			  6312 WGS, 6286 WGS or 6386/E WGS CPU using AT&T
			  standard ROMBIOS (See note 2).

			- MS-DOS 2.0 or higher.

			- Have at least 128k of RAM.

			- Have one floppy drive ("A" drive).

			- Have at least one hard drive.

			- Use an AT&T supported HDU controller or equiv.

			- Be equipped with a monitor.

			- Parallel printer (See note 3).


(The DIP switch screens, drive type tables and HDU controller boards can be
displayed on any DOS PC.)


   
I recommend a printer and a color monitor for full utilization of this program.




Note 1 - The Dip switch and drive tables may be viewed on any DOS PC.

Note 2 - Future CPU's will be incorporated into this program as needed. 

Note 3 - A printer is optional because the disk record is in ASCII format and is
	 in the same format as a printed record so that it can be printed at a
	 later date if desired.  The printer should be on LPT1. 











                                    [Page 5]                                  

                           *** USING THE PROGRAM ***

STARTING THE PROGRAM:

		- Boot the CPU with DOS 2.0 or higher.
		- Place the diskette containing this program in the "A" drive.
		- At the A> prompt type ATTSUM.

	You should now be presented with an AT&T banner presenting the program
with a "Press any key" prompt at the bottom of the screen. 

THE FIRST MENU:
		   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
             	   ³ [1] - Display PC6300 1.21 DIPSW table. ³
             	   ³ [2] - Display PC6300 1.43 DIPSW table. ³
             	   ³ [3] - Display PC6300 PLUS DIPSW table. ³
             	   ³ [4] - Display PC6300 WGS  DIPSW table. ³
             	   ³ [5] - VIEW THE CURRENT SYSTEM CONFIG.  ³
             	   ³ [6] - HARD DRIVE UTILITIES.            ³
             	   ³ [7] - Display "Information" screen.    ³
             	   ³ [Q]- Quit program and return to DOS.   ³
            	   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

	        SELECTION                        ACTION

		  [1]           Displays PC6300 option dip switches with    
                          	descriptions for 1.21 ROMBIOS.

		  [2]           Same as #1 except 1.43 ROMBIOS.

		  [3]           Same as #1 except for PLUS model.

		  [4]           Same as #1 except for 6300 WGS model.

		  [5]           Program determines if CPU is a valid AT&T   
                          	model and returns the user to DOS if it     
                          	fails tests. If the tests pass it then      
                          	determines the model type, displays one of  
                          	the above tables if appropriate, retrieves  
                          	the current dip switch settings and places  
                          	them on the screen indicating whether they  
                          	are open or closed.
                          	If the CPU is CMOS "based", the program     
                          	gathers the configuration info from the     
                          	various locations and displays a screen     
                          	showing the user the current system config-
				uration. 

		  [6]           Advances the user to the "HARD DRIVE" menu.
 
		  [7]           Displays a brief overview of the program.

		  [Q]           Terminates the program and returns the user
                          	to DOS.

(Note that choice #5 is fully automated.)  

                                    [Page 6]			(Rev 09/25/88)



HARD DRIVE MENU:
		   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
		   ³  [1] - Display HDU "TYPE" tables.      ³ 
       	     	   ³  [2] - Display Drive Controller Boards.³
       	     	   ³  [3] - HARD DRIVE DIAGNOSTICS & FORMAT.³
		   ³  [R] - Return to previous menu.        ³
             	   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


	        SELECTION                        ACTION

		  [1]           Displays the menu for the drive tables.

		  [2]		Displays the menu for HDU controller boards.

		  [3]           Program determines if CPU is a valid AT&T 
                          	model and returns the user to DOS if it 
                          	fails the tests. If the tests pass it then 
                         	Advances to the hard drive statistics screen
                          	and displays the hard drive main menu. The  
                          	program now retrieves and displays all      
                          	information that pertains to the  CPU and   
                          	hard drive in the unit. This might include  
                          	dip switch settings that set the drive type 
                          	option(s).  It also displays the hard drive 
                          	type(s)  with the statistical data for the  
                          	drive.  This screen varies according to the
                          	CPU and hard drive controller models.   
  
		  [R]           Return to first screen.



DRIVE TABLE MENU:
		   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
            	   ³ [1] - Display table for PC6300 w/1.21  ³
             	   ³ [2] - Display table for PC6300 w/1.43  ³
             	   ³ [3] - Display table for PC6300 PLUS    ³
             	   ³ [4] - Display table for PC6300 WGS     ³
             	   ³ [5] - Display table for PC6310/PC6312  ³
             	   ³ [6] - Display table for AT&T6286 WGS   ³
             	   ³ [7] - Display table for AT&T6386/E WGS ³
             	   ³ [R] - Return to previous menu.         ³
              	   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 


	        SELECTION                        ACTION

       	     [1,2,3,4,5,6,7]   	Displays the selected drive "type" table.   
  
		  [R]           Returns the user to the first screen.

(NOTE: The ROMBIOS may differ from display table. If a conflict exists use the
ROMBIOS parameter - not the screen table listing.)

                                    [Page 7]			(Rev 11/13/88)



DISPLAY DRIVE CONTROLLER BOARD MENU:
		   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
		   ³ [1] - Display DTC 5150BX    (PC6300)   ³
		   ³ [2] - Display WD WX1        (PC6300/+) ³ 
		   ³ [3] - Display WD WX2        (PC6300/+) ³ 
		   ³ [4] - Display WD 1002-WA2   (COMBO)    ³
		   ³ [5] - Display WD 1003-WAH   (ST-506)   ³
		   ³ [6] - Display WD 1005-WAH   (ESDI)     ³
		   ³ [7] - Display WD 1007-WA[x] (ESDI)     ³
		   ³ [R] - Return to previous menu.         ³
		   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 


		SELECTION			 ACTION

	     [1,2,3,4,5,6,7]	Displays the selected board with the stand-
				ard "AT&T" options listed.

		  [R]		Returns user to previous menu.


HARD DRIVE MAIN MENU:
		   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
		   ³ [1] - Re-display current drive "TYPE". ³
		   ³ [2] - Find/display bad tracks.         ³ 
		   ³ [3] - LOW LEVEL FORMAT FUNCTIONS.      ³
		   ³ [4] - Prepare drive(s) for "SHIPPING". ³
		   ³ [R] - Return to previous menu.         ³
		   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 


  	        SELECTION                        ACTION

		  [1]           Re-reads the dip switches, if applicable,   
                          	and displays the current settings. (THIS  
                          	CAN BE USED TO WATCH DIP SWITCH SETTING      
                          	CHANGES AS THEY ARE MADE ON AN UP-AND-      
                          	RUNNING CPU - PC CLASS ONLY.)

		  [2]           Clears screen, prompts for drive selection, 
                          	prompts  for interleave factor then advances
                          	to the "display bad tracks" screen.

		  [3]           Clears screen, presents warning message,    
                          	prompts for drive selection, prompts for    
                          	interleave factor then displays the format  
                          	type menu.

		  [4]		Parks the heads on the "equipped" hard drives
				for transporting.

		  [R]           Returns user to main menu.



                                    [Page 8]			(Rev 10/27/88)




FORMAT TYPE MENU:
		   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
		   ³ [1] - ADD/DELETE bad tracks to drive.  ³
		   ³ [2] - FORMAT THE ENTIRE DRIVE.         ³
		   ³ [R] - Return to previous menu.         ³
		   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


	       SELECTION                        ACTION

		  [1]           Use this selection to ADD or DELETE bad
                          	tracks to drive.

		  [2]           Use to format the entire drive surface.     
                             	(Advances to "Preserve Bad Tracks"  menu
                                in "AT" class CPU's only as preservation is  
                                automatic in the "PC"  CPU's.)

		  [R]           Returns user to main menu.

Note: Upon completion of menu selection 2 the program advances the user to
      "BAD TRACK PROCESSING".



PRESERVE BAD TRACK MENU:
("AT" CLASS ONLY)
		   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
		   ³ [1] - FORMAT ALL TRACKS ON DRIVE.      ³
		   ³ [2] - PRESERVE EXISTING BAD TRACKS.    ³ 
		   ³ [R] - Return to previous menu.         ³ 
		   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


	       SELECTION                        ACTION

		  [1]           Formats ALL tracks on drive with "good"
	                        track pattern.

		  [2]           Formats all tracks on drive that are NOT
        	                marked as bad with "good" pattern.
                	        (Doesn't format over existing bad tracks.
                        	Always formats cylinder "0" as good.)

		  [R]           Returns user to main menu.









                                    [Page 9]			(Rev 09/25/88)


SAVE MENU:
		   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
		   ³ [1] - Print out of test results.       ³
		   ³ [2] - Save results to [A:\HDRECORD.DAT]³
		   ³ [R] - Return to previous menu.         ³
		   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


	       SELECTION                        ACTION

		  [1]           Prints copy(s) of results to printer. If
                          	a printer is not attached a message is
                          	displayed with instructions.

		  [2]           A file "HDRECORD.DAT" is either created or
                          	appended to with the test results.

		  [R]           Returns user to main menu.






































                                    [Page 10]			(Rev 09/25/88)


			    ***	HARD DRIVE THEORY ***


	Hard drives are probably the most mystical component in computers. In
this section I hope to both remove the mystery and provide enough detail as to
make working with the drive a lot easier.

	Basically, a hard drive is a rotating surface which has a thin magnetic
coating to store data bits in the form of magnetic spots and a sensor/driver
(head) to read or write the spots.

 	As with any storage type device a strategy must be established that sets
an order to the way data is stored. The method used for drives is to divide the
the surfaces into "magnetic" concentric rings (tracks). Each ring is then split
into areas called sectors (17 for ST506, 34 for ESDI). Each sector must then be
"addressed" in some way for fast random access. Data is stored in the sectors.


A look at a typical drive:

	Hard drives have more than one platter. The surfaces of the platters are
coated with a magnetic material. There is a read/write head for each of the
surfaces. There can be many platters fixed together or "stacked" with a space
between each for the heads to move as shown in (figure A-1).




    Platter				    ÖÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  Head 5
       2   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ	     ³
 			    ³        ³	    ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´  Heads 3&4
       1   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍØÍÍÍÍÍÍÍÍØÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ	     ³
			    ³        ³	    ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´  Heads 1&2
       0   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍØÍÍÍÍÍÍÍÍØÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ	     ³
			    ³        ³	    ÓÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´  Head 0
		    ÚÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄ¿		     ³
	            ³      Drive Motor       ³ 	     ÚÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄ¿
		    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ	     ³  Head Stepping ³
						     ³     Motor      ³
						     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

			Diagram of a typical drive.
			       (Figure A-1)



	Not only are the platters fixed together but the heads are also fixed so
that they move together as a unit.  The stepping motor moves the heads across
the surface of the platter.  The heads are very small and light and are designed
to float on the air currents generated by the spinning platters.  The floating
action positions the heads a few thousands of an inch from the media surface
without ever touching it.  Note that at high altitudes, because the air is much
thinner, hard drives will not work properly (generally above 9,000 feet) - the
air is not dense enough for the cushion effect to work. 


				   [Page A-1]                                 


	The stepping motor (on some drives a voice coil arrangement) is used to
move the heads to predetermined positions, these are called cylinders.  Cylinder
is the name for all of the tracks under the heads at any one time.  For example,
if the heads are at the most outer position they are all on cylinder "0".  Head
number "0" is on cylinder "0", head "1" is on cylinder "0" and so forth.  If the
stepper is actuated once, the heads all move to cylinder "1".  An other way to
think of cylinders is to consider the stepping motor positions.  Position "0" is
cylinder "0", position "1" is cylinder "1" and so on. 

	Now we know there are cylinders and heads and also how they are arrang-
ed.  Tracks are the next item in the numbering scheme of things.  Track numbers
start at cylinder "0" head "0" (track "0"), incrementing to track "1" for
cylinder "0" head "1", track "2" is cylinder "0" head "2", and so on.  With a
little math we can calculate the number of tracks on the drive.  Multiplying the
number of heads by the cylinder count gives the total track count. 

	[Example - (4 heads x 612 cylinders) = 2,448 tracks.]



      - Each of the 2,448 tracks are divided into 17 sectors (ST506). The total
number of sectors is found by multiplying tracks by sectors.

	[Example - (2,448 tracks x 17 sectors) = 41,616 sectors.]


      - There is room for 512 bytes of data in each of the sectors.  To find the
total drive capacity in bytes multiply the sector count by 512. 

	[Example - (41,616 sectors x 512) = 21,307,392 bytes total.]



In summary -

To calculate a drive's capacity in bytes:
	(# of cylinders) x (# of heads) x (# of sectors/track) x 512 = Total
				   ----------
	Because the heads are fixed together note that an entire cylinder can
be read/written before moving the heads to another cylinder. Later you will find
how restoring the files from a backup periodically can help take advantage of
this idea.
				   ----------
	Tracks are numbered consecutively from the first to the last on the
drive. The controller uses the cylinder and head numbers to keep "track" of the
head locations on the drive at all times.
				   ----------
	For low level, or physical, formatting purposes the only factors used
for addressing locations on the drive surface are; Cylinder, head and sector
numbers. More refinements of the addressing plan are incorporated by the user's
operating system; DOS, UNIX,etc..
				   ----------
IMPORTANT ->  ST-506 and ESDI drives/controllers are NOT interchangeable.
(They will not operate and permanent damage will result if you mix these units.)


				   [Page A-2]                   (Rev 10/27/88)


	The sectors are the "containers" for the data. Each sector has a format
very similar to that of a data packet. A typical drive sector is shown in
(Figure A-2).


    ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ Repeated for each sector ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
    ÂÄÄÄÄÄÂÄÄÂÄÄÂÄÄÂÄÄÂÄÄÂÄÄÂÄÄÂÄÄÄÄÂÄÄÄÄÄÂÄÄÂÄÄÂÄÄÄÄÄÄÄÄÄÄÄÂÄÄÂÄÄÂÄÄÄÄÂÄÄÂ
    ³14x4E³A1³ CYL#³H#³S#³ CRC ³3x00³12x00³A1³F8³ 512 BYTES ³ CRC ³3x00³4E³
    ³     ³  ³ID L ³  ³  ³ 1³2 ³    ³     ³  ³  ³   (DATA)  ³ 1³2 ³    ³  ³
    ÁÄÄÄÄÄÁÄÄÁÄÄÁÄÄÁÄÄÁÄÄÁÄÄÁÄÄÁÄÄÄÄÁÄÄÄÄÄÁÄÄÁÄÄÁÄÄÄÄÄÄÄÄÄÄÄÁÄÄÁÄÄÁÄÄÄÄÁÄÄÁ
 					  ÃÄÄÄÄÄÄ Data Field ÄÄÄÄÄ´

	14x4E = (14) "4Eh" bytes		 3x00 = (3) "00h" bytes
	   A1 = "A1h"				12x00 = (12) "00h" bytes
	   ID = Cyl range			   A1 = "A1h"
	    L = Cyl count within range		   F8 = "F8h"
	   H# = Number of heads			 DATA = User data
	   S# = Sector number			 3x00 = (3) "00h" bytes
	  CRC = Checksum bytes 1&2		   4E = "4Eh"

		       (Total sector length is 557 bytes)
(There is also a number of "4Eh" gap fillers between the sectors for spacing).

Note: Refer to a Controller Technical Reference Manual for more information.

			     A typical track sector.
				  (Figure A-2)


	As (Figure A-2) demonstrates there is a fixed structure to all of the
data on the drive. It is important to keep in mind that low level formatting is
a means of "preparing" the drive surface for the operating system format. It
achieves the following:

		- Establishes the cylinder tracks on the surface.

		- Divides each track into sectors.

		- Numbers the sectors according to the interleave factor.
			  ( See "Interleave Theory - Page C-1)

		- Fills each sector's 512 byte data area with the "01101100" bit
		  pattern.
				   ----------

	Also, low level formatting will occur on the number of cylinders as is
found in the drive type table in ROMBIOS for the drive type selected. No secrets
here, if the table reports that there are 5 heads and 638 cylinders on the drive
then the low level format will blindly attempt to use these figures. The rub
comes when the drive does not have at least the number of heads and/or cylinders
that the table says it has. What happens is that the controller simply attempts
to select or move beyond the range of the drive and gets an error returned for
it's efforts. This is why it is important to set the drive type to the exact 
specifications or less for the drive used.


				   [Page A-3]			(Rev 09/07/88)


	All hard drives shipped from a manufacturer must meet the following
criteria:

	- Have zero defects for all heads in cylinder "0".
	- Have a record attached showing inspection test results.
	- Have a record attached showing locations of media errors if any.
	- Be low level formatted.

				   ----------
A FEW HINTS -

      - If a drive's track "0" (cyl "0"/head "0") is not formatted as "good"
	you will receive an error message during powerup diagnostics indicating
	a defective drive.

(TO FIX - Run the low level format function of this program on the drive.)*

      -	If any other track in cylinder "0" is not formatted as "good" you will
	not know it until the DOS format has finished and displayed a "Defect-
	ive Drive" message. 

(TO FIX - Run the low level format function of this program on the drive.)*

      - There is a long delay during powerup diagnostics while testing for the
	drive(s). This applies to "PC class" CPU's only.

(TO FIX - This is caused by having both the internal and external ROMBIOS active
for the hard drive. Disable one or the other with option settings. I suggest
using the motherboard ROMBIOS only if possible.)

      - It is a very good idea to occasionally backup the entire drive(s). Do
	a low level format, partition, and format with the operating system.
	Then restore the the file system from the backup.

(This performs two important operations:
	
	A) The cylinders on the surface are re-aligned to the heads. (With use
	   the head positions can shift slightly because of mechanical wear to
	   the stepper device. This will re-center the data to the head posit-
	   ions.)

	B) The files are written back to the drive on contiguous sectors. (Any
	   files that have been "scattered about" on the drive will be put back
	   together. This will make reading and writing to files faster and may
	   even save a lot of head movement and also reclaim some available 
	   space on the drive.)

Note: I recommend that heavy users perform this operation about every 3 months,
light or occasional users about every 6 months.  If this is overly done some
shortening of the drive life may occur due to the heavy use this places on the
drive. 


* This program avoids this by automatically formatting all of cylinder "0" as
"good" and not allowing the user to select cylinder "0" for bad track process-
ing.
				   [Page A-4]		 	 (Rev 9/06/88)


			    *** INTERLEAVE THEORY ***

	Because of time considerations data cannot always be read or written in
a continuous stream to/from the drive.

The factors that most effect this are:

      - Data must be buffered on the controller. This consists of a 1Kbyte RAM
	that is used to "cache" data to and from the drive.

      - The DMA/CPU must co-ordinate and control all transfers of data 	between
	the controller buffer and system RAM.

      - The clock rate (speed) that the DMA/CPU can handle the actual data.

	As discussed in the Physical Format Description appendix the spacing
between adjacent sectors is very small and because the drive is spinning at 3600
rpm not a lot of time goes by between reading the last sector and starting the
next.  In fact, unless the CPU and the controller are very fast and responsive
they will not be ready for the next sector immediately.  To allow for this a
means was developed by which the sectors can be "interleaved" on the drive to
best match the performance of the CPU/DMA/controller combination. 

Note: New drive technology and new interface specifications (ESDI) have now made
      1:1 possible on the high performance CPU's.  This means that the sectors 
      are arranged in sequence around the tracks and are accessed in sequence
      also. 

	Interleave is totally system dependant.  If a particular system can be
ready to access a next sector in the amount of time it takes for the drive to
pass over a single sector then a 2:1 interleave is appropriate.  Then to read a
full track on the drive two complete revolutions will be required because it is
reading every other sector as they pass under the head.  Some example inter-
leaves are illustrated below in (Figure B-1). 

				 1:1 INTERLEAVE
            || <=== 0.0 msec between sector accesses.
Start --> 01  02  03  04  05  06  07  08  09  10  11  12  13  14  15  16  17
			(1 revolution to read - minimum)


				 2:1 INTERLEAVE
            |----| <=== 1.0 msec between sector accesses.
Start --> 01  10  02  11  03  12  04  13  05  14  06  15  07  16  08  17  09
			(2 revolutions to read - minimum)

				
				 3:1 INTERLEAVE
            |--------| <=== 2.0 msec between sector accesses.
Start --> 01  07  13  02  08  14  03  09  15  04  10  16  05  11  17  06  12
			(3 revolutions to read - minimum)

			   Various Interleave Factors.
				  (Figure B-1)


				   [Page B-1]			(Rev 09/07/88)



Note: The problem here is that if any interleave factor is used other than the
one that is optimal for the system it will take 17 revolutions to read a entire
track.  (Example - reads sector (01), misses (02) then waits for (02) to come
around again for the read.  One revolution wasted.)

	The main reason the world is going 1:1 is evident in (Figure B-2).
Notice that each revolution of the drive takes 16.6 milliseconds. This may seem
like no "big deal" for an everyday user. However, if you are planning to use 
the CPU for a network server this can very quickly become a response "bottle-
neck". By the way, most PC user's with 85-95 msec drives will hardly notice if
the drive is taking 17 revolutions to read a track (the drive is so slow in
other ways that an incorrect interleave factor isn't all that obvious).




	   Number of Revolutions		Elapsed Time (msec)
	   ---------------------                ------------
		     1				    16.6
		     2				    33.3
		     3			 	    50.0
		     4			   	    66.6
		     5				    83.3
		     |			     	     |
	            17   			   283.3


	    Average Access Time (msec)	    For (10) Head Moves (msec)
            -------------------             -------------------
	 	    85				    850
		    35				    350
                    25				    250

				Timing Chart
				(Figure B-2)



PROGRAM INTERLEAVE NOTES -

The interleave screens vary in two ways:

A) Testing only.

	This screen allows the user to enter an interleave factor of 1:1 to 8:1,
"escape" back to the drive menu, or press return for "autoselect".  The user
is presented a suggested factor that is based on the CPU model; 6:1 for PC6300,
3:1 for all others.  Selecting auto causes the program to try reading a track
using all factors and using the fastest.  Because this is only used to read the
drive, it is not critical (worst case will cause a slow down of the testing). If
1:1 is sensed the test will repeat up to three times unless something other than
1:1 is determined before the end of the third cycle.  If a record is made of the
test and no formatting was performed, a notice is added to the record stating
that the interleave shown may not be the actual value used on the drive. 

				   [Page B-2]			(Rev 09/07/88)


	If however, formatting was performed, the preceding action is bypassed
and the formatting interleave factor is reused.  The notice in the save record
is bypassed also. 


B) Formatting.

	The user is given the same choices as above however, auto-select will
actually reformat track 0 using interleave factors 8:1 to 1:1 selecting the
fastest as the best choice.  This method was chosen because it is fairly
reliable but, unfortunately, it destroys the data on this track.  The reason
this track is used is because it is the only track that does not contain
directory, file allocation or customer data and even with the destruction of
this track the drive can still be backed up saving all files. 










































				   [Page B-3]                                 


			  *** BAD TRACK FORMATTING ***

	Each track on the drive is, in essence, a unique entity.  That is,
before the drive is partitioned it consists of a number of unrelated tracks that
have been divided into sectors for data storage purposes.  The only addressing
present at this time is the sector numbering within the individual tracks. 
During the formatting procedure "01101100" (06Ch) is written into the data areas
and an "ID" byte indicating good sectors is written into each of the sector "ID"
bytes.  Using this information, when the operating system formats the partition
area to which it has been assigned by "FDISK", these tracks are accepted as
usable and are then addressed, assigned to blocks/clusters and cataloged as
available in a table. 
	This is fine for good tracks but defective tracks must also be consid-
ered in some way.  Defective tracks are called "bad" tracks.  A track is
defective if there is a flaw that can cause even a single bit error on it. 
Unfortunately, it is not always possible to find the flaws as accurately or
completely as the manufacturer of the drive can.  If the flaw appears in an area
of a sector other than the data area it may not be detectable by utilities
written for the purpose of locating faults.  The best rule to follow is - ALWAYS
FORMAT AS BAD TRACKS THE TRACKS LISTED ON THE STICKER ATTACHED TO THE DRIVE. 
	If the drive does not have a sticker you will not know for sure if it
has bad tracks or not - REPLACE THE DRIVE if you want full data integrity.

	A single track (ST506) has a capacity of 8704 bytes of data (17 sectors
times 512 bytes). Considering the total capacity of the drive what's the loss
of a few tracks if it gives the user a comfortable position??? Not enough to
worry about. Using tracks for a basis, if there are 2,448 tracks what is the
tragedy of losing 5 or even 10 tracks as compared to 20 megabytes of lost data
as the result of a drive "crash"?

	When a track is formatted as bad a data pattern of "11111111" (0FFh) is
written to all data areas on the track and a bad sector "ID" is placed in all of
the sector "ID" bytes in the track.  When the operating system comes across a
track marked as such it will place entries in its tables that will indicate to
the system that they are unusable for data storage. 

BAD TRACK PROGRAM NOTES -

The bad track formatting screen is as simple as it appears.  

		- Entries that are over range are automatically cancelled   
		- The user must enter both head and cylinder numbers.
		- Upon selection depressing "A" will cause the selection to 
		  be formatted as a bad track.
		- Upon selection depressing "D" will format the track as 
		  "good".
		- All formatting is immediate.
		- If a mistake is made the track can be reformatted as 
		  desired.
		- If <ESC> is pressed before any formatting is performed,
		  the program returns the user to the drive menu.
		- If <ESC> is pressed after formatting has occurred, the 
		  user is advanced into the "display bad tracks" operation 
		  to verify with the user the finished hard drive 
		  conditions.

				   [Page C-1]                                 


		       *** CARING FOR YOUR HARD DRIVE ***


	Hard drives will provide many years of trouble free operation if they
are given a little attention. Listed below are key items that, if followed,
should help "maximize" the useful life of your hard drive.

-> Keep the drive running continuously as much as possible.

	It's better to keep your drive running than frequently turning it off
	and on. If you are using the CPU more than once during the day - let
	it run all day. If you using the CPU every day during the week turn it
	off over the weekend only.


-> Do not move the drive while it is running.

	Moving the drive can cause the heads to strike or touch the rotating
	media and damage it beyond use. Place the CPU in a vibration free
	location. Don't slam your desk drawers if the PC is on your desk.


-> Do not position the drive to run upside down.

	The drive can be operated in any position except upside down.


-> Never attempt to open, adjust or service a hard drive unit other than placing
   a bit of lubricant on the static grounding spring.

	If a drive emits a whining or screaming noise a very small amount of a
	heavy silcone grease, approved by the drive manufacturer, can be placed
	on the bearing under the grounding spring (follow the instructions that
	are included with the lubrication kit). If the noise persists the drive
	requires factory servicing. 
		Some users have found that removing the spring stops the
	noise and the drive still works okay. Check with the drive manufacturer
	or an approved service agency (AT&T) before altering the drive because
	it just may void any warranty and/or service contract. If it's your
	drive and you don't have to consider factory or service warranty, do
	what you wish. Just be sure that you know what the risks are before you
	do it.














				   [Page D-1]			(Rev 09/25/88)


		  *** ANSWERS TO FREQUENTLY ASKED QUESTIONS ***

	Q - I have limited space on my desk. Will it hurt the hard drive if I
	    stand the CPU on it's end and/or on the floor?

	A - The hard drive can be operated in any position except upside down.
	    Other considerations are that ventilation slots be open to air flow
	    and the floppy drives should be positioned as high as possible off
	    of the floor to limit the amount of lint and dust being drawn into
	    the drive(s). 


	Q - Should I run a hard drive "head parking" program before moving the
	    hard drive?

	A - Some hard drives are designed to park the heads automatically when
	    the drive in powered off. Unless you know for sure that your drive
	    has this feature you should always park the heads before moving
	    the drive. It doesn't hurt to take this extra precaution - it is
	    quick, quite painless and may save your drive.


	Q - Should I purchase one of the programs that repack files, re-format
	    the tracks and find media errors on the drive without having to
	    backup the drive and do it the long way?

	A - This is a decision that you should make based on your own needs.
	    If however you are occasionally backing up the drive, as you
	    should be, you are already doing most of the work. I personally
	    recommend that users "occasionally" perform a complete backup,
	    lowlevel format, partion, reformat then restore the files from the
	    backup. This operation will do everything that has to be done and
	    all it costs is a little time. By the way, you already have the
	    backups - don't you?
 

	Q - How can I find or locate defects on the media?

	A - You can't unless they are very obnoxious. Most defects are very
	    small and can be located in areas that the user does not have
	    access to (See sector description on page A-3). The only fully
	    reliable method of locating errors is to send the drive to the
	    manufacturer for quality testing. If you cannot use the drive after
	    formatting the defective tracks as listed on the hard drive - give
	    it up and replace the drive. The drive may have problems other than
	    media errors.


	Q - Where is the "BAD TRACK TABLE" located?

	A - On the screen and in RAM. No kidding, there is no such thing as a
	    bad track table on the drive. The table is a display device for the
	    user only. Bad tracks must be individually formatted as bad other-
	    wise they are accepted as good.


				   [Page E-1]			(Rev 09/25/88)


	Q - Can I use a drive that doesn't match up to the "type" tables in the
	    ROMBIOS?

	A - Maybe. Try using a selection that has at least the number of heads
	    and cylinders as your drive. For instance, if your drive has 4 heads
	    and 612 cylinders pick a type that has 4 or less heads and 612 or
	    less cylinders. This may get the drive working but consider that
	    there are many other factors in the table that may cause problems.
	    An obvious one would be that the landing zone (head parking pos-
	    ition) in the table will not be correct for your drive and parking
	    the heads at the wrong cylinder will not protect the drive.


	Q - Even though my system is running fine is there anything I could do
	    to prevent unexpected problems?

	A - Yes, provide surge protection for your computer. ALL computers
	    should be equipped with power surge protection at the 110vac
	    outlet. This may be either in the form of an outlet extender or
	    extension cord type. Typically, these can purchased for under
	    $10.00 and can save you from "mysterious happenings". 


	Q - During the powerup diagnostics a line appears stating "Additional
	    ROM at C800:000 ...". What does this mean?

	A - You are using a HDU controller with it's ROMBIOS enabled. It is
	    standard practice that the ROMBIOS area of upper memory be tested
	    for the presence of additional peripherals such as video adaptors,
	    HDU controller, game adaptor, etc.. This message is telling you
	    that it found something at "C800:0000" which is the reserved
	    location for "external" HDU ROMBIOS. If your CPU is optioned for
	    external HDU ROMBIOS this message is normal (see next question).
	    

	Q - Why is it taking a long time (approx 30 seconds) for the powerup
	    diagnostics to checkout the hard drive?

	A - An extended delay means that the diagnostics has located both the
	    external and internal HDU ROMBIOS and is trying to select a winner.
	    For the CPU to operate properly with the HDU you must disable
	    either the motherboard or controller board ROMBIOS. If you have a
	    choice I recommend using the motherboard HDU ROMBIOS because it is
	    running at the same speed as the rest of the CPU's memory other
	    than off of the BUS. The important note here is that you disable
	    the one not used. When this has been done the delay will go away.


	Q - Can I have more than 2 hard drives?

	A - No, by design DOS allows for only 2 hard drives.





				   [Page E-2]			(Rev 09/25/88)


                            *** ERROR MESSAGES ***

	All error conditions are displayed on the screen with the error and both
probable cause and probable cure statements. Listed below are the error messages
as they might appear including the associated cause/cure statements and a brief
description of the meaning. 

********************************* IMPORTANT ************************************
*      BE AWARE THAT BECAUSE OF THE INTIMATE RELATIONSHIPS BETWEEN THE FEW     *
*  COMPONENTS IN A PC IT MAY BE NECESSARY TO SUBSTITUTE OTHER COMPONENTS THAN  *
*                    THOSE LISTED TO REPAIR THE UNIT.                          *
********************************************************************************

	      *** CMOS CHECKSUM ERROR - RUN "SETUP" TO CORRECT! ***


   A checksum error has been detected in the CMOS RAM. A system configuration
      program must be run to determine the cause and/or correct the error.

Meaning: A test of the CMOS checksum byte has indicated an error condition. To
determine the cause of the error and remedy it the system configuration 
program for the CPU must be run. This error applies to AT class CPU's only.

-------------------------------------------------------------------------------
		          *** NO INDEX MARK FOUND. ***

	The factory placed "index" mark on hard drive cannot be found!
 Verify that the drive "type" is correct for drive used and verify all options.

Meaning: The index marker placed on the hard drive by the manufacturer can not
be located. The drive must be replaced.

-------------------------------------------------------------------------------
			  *** SEEK ERROR ON DRIVE. ***

	     The track selected cannot be found on hard drive!
 Verify that the drive "type" is correct for drive used and verify all options.

Meaning: The track selected by the controller cannot be located on the drive.
If the options and drive type are correct the drive is most probable cause, the
controller is second choice.

-------------------------------------------------------------------------------
		         *** CANNOT WRITE TO DRIVE. ***

	     Errors were detected while writing to the hard drive.
 Verify that the drive "type" is correct for drive used and verify all options.
  Format track "head[hh] cyl[cccc]"as bad track, if still fails replace drive!

Meaning: Data errors were detected while writing to the drive. If the options 
are correct try formatting the indicated track as a bad track then try again.
If it still fails the drive must be replaced.




				   [Page F-1]			(Rev 09/07/88)



			  *** DRIVE IS NOT READY. ***

 The hard drive is not ready. Try restarting program (a timeout has occurred)!
 Verify that the drive "type" is correct for drive used and verify all options.

Meaning: A reset test of the hard drive has failed. If the options are correct
the drive must be replaced. 

-------------------------------------------------------------------------------	
	       *** NO HARD DRIVES FOUND - CHECK OPTION SETTINGS ***

			  No hard drives are present.

Meaning: Upon booting the operating system did not identify the presence of a
hard drive. Be sure to check all connections and options. If they are good then
replace the controller.

-------------------------------------------------------------------------------
   *** SYSTEM CONFIGURATION ERROR: (DRIVE TYPE, # OF HEADS or #CYLINDERS) ***
	  (The out of range category is displayed in the parenthesis.)

    This program is not compatible with your HDU controller and/or options.
   The most likely cause of this is the use of non-AT&T supported peripherals.

Meaning: If you wish to use a controller that has its own HDU ROMBIOS this
program many not recognize the BIOS drive table entries. The program will sense
conditions that are not "AT&T standard" and halt progress to avoid any further
complications. You must use the formatting utilities supplied with the non-
standard unit. If the unit is "AT&T standard" recheck the drive type options.

-------------------------------------------------------------------------------
		    *** THE DRIVE TYPE HAS BEEN ALTERED ***

	IMPORTANT: The drive "TYPE" has been altered since the program 
     was started. You must re-boot if you want the change to be effective.


Meaning: The drive type option has been changed since the CPU was booted. The
CPU must be re-booted with the new setting for the operating to recognize it.

-------------------------------------------------------------------------------
	         *** CANNOT DETERMINE CURRENT INTERLEAVE! ***

			 Fatal error - program exit.

Meaning: The program cannot determine the present interleave factor. This can
be caused by an inoperative clock in the PC. Use the suggested interleave factor
as a default to continue.

-------------------------------------------------------------------------------
	 	       *** FORMAT ERROR ON DRIVE. ***

 Format track "head[xx] cyl[xxxx]" as bad track, if still fails replace drive.

Meaning: The indicated track is returning errors during formatting. Try for-
matting the track as a bad track then run format again. If the trouble persists
replace the drive.
				   [Page F-2]			(Rev 09/07/88)


		         *** TRACK "0" NOT FOUND. ***

	   Track "0" cannot be found. Try restarting program.
 Verify that the drive "type" is correct for drive used and verify all options.

Meaning: The drive cannot locate track "0". If this persists the drive then
must be replaced if the options are correct.

-------------------------------------------------------------------------------
		         *** CONTROLLER TIMEOUT. ***

The hard drive controller has timed out. If optioned correctly try replacing it.

Meaning: The controller is not responding to system calls properly. Replace the
controller if the options are correct.

-------------------------------------------------------------------------------
		         *** HD CONTROLLER ERROR ***

	  The hard drive controller has experienced a FATAL error!
     The most probable cause is the HD controller - try a replacement!

Meaning: The controller has experienced a "crash" condition. Replace the cont-
roller if the options are correct.

-------------------------------------------------------------------------------
		         *** INVALID DRIVE TYPE. ***

	       The drive type is not valid for the CPU.

Meaning: The drive type selected on the controller is not valid for the CPU
model. Reset to a correct setting.

-------------------------------------------------------------------------------
		        *** CAN NOT SAVE TO FILE. ***

	      DRIVE A: NOT READY - Check the diskette and drive!

Meaning: The test data cannot be saved to the floppy disk because either the
drive is open, the diskette is not in place, a write protect tab is on the disk
or there is a problem with the floppy drive. Test data can be saved to file 
"HDRECORD.DAT" on "A" drive only!

------------------------------------------------------------------------------
		         *** TOO MANY BAD TRACKS ***

	The drive has an unacceptable number of bad tracks.
-------------------------------------------------------------------------------
		  *** UNRECOVERABLE TRACK ERROR DETECTED. ***

 Verify that the drive "type" is correct for drive used and verify all options.

Meaning: A "FATAL" error has occurred while accessing the selected track. If
all options are correct replace the drive.


                                   [Page F-3]


	    *** PRINTER NOT READY -check the printer for "ready"! ***

	A printed copy cannot be made until printer is ready for service.

Meaning: The test for presence of a printer on the LPT1 port has failed. Be
sure that the printer is connected properly and is ready.

-------------------------------------------------------------------------------
	     *** PRINTER PAPER ALARM - check for paper in printer! ***

				 Out of paper.

Meaning: A paper out alarm has been sensed for the printer. Check that the
printer has paper and that it is properly inserted.

-------------------------------------------------------------------------------
THE CPU TIMER IS NOT FUNCTIONING - YOU MUST SELECT AN INTERLEAVE FACTOR TO USE!

Meaning: A test of the calender/clock chip on the motherboard has indicated
that it is not functioning properly for the interleave "AUTOSELECT" feature. 
It may be a minor malfunction or the chip/circuit may be defective. One easy
fix is purchase a "NO-SLOT CLOCK" chip that installs under the "LOW" ROMBIOS
chip - no soldering is required. This device has it's own battery as well.
This error is not "fatal" to the operation and therefore you are allowed to 
enter your own interleave choice.




























                                   [Page F-4]			(Rev 11/10/88)


			     *** PROGRAM FLOW ***



		   ÚÄÄÄÄÄÄÄÄÄÄÄÄ¿
		   ³Intro Screen³
		   ÀÄÄÄÄÄÄÂÄÄÄÄÄÙ
			  ³    	 ÚÄÄÄÄÄÄÄÄÄ¿
		 	  ÀÄÄÄÄÄÄ´Main Menu³
			         ÀÄÄÄÄÂÄÄÄÄÙ
				      ³
				      ÃÄÄÄÄÄ Display Dip Switch Tables
				      ³
				      ÃÄÄÄÄÄ View Current System Configuration
				      ³
				      ÃÄÄÄÄÄ Display Information Screen
				      ³
			   ÚÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄ¿
			   ³Hard Drive Utilities³
			   ÀÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÙ
				      ³
				      ÃÄÄÄÄÄ Display Type Tables
				      ³
				      ÃÄÄÄÄÄ Display HDU Controller Boards
				      ³
		     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
		     ³Hard Drive Diagnostics and Format³
		     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
				      ³
				      ÃÄÄÄÄÄ Re-display Current Drive "Type"
 				      ³
				      ÃÄÄÄÄÄ Prepare drive(s) for shipping
				      ³
				      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
				      ³					 ³
			     ÚÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄ¿				 ³
			     ³Low Level Format³				 ³
			     ÀÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÙ				 ³
				      ³					 ³
				      ÃÄÄÄÄÄÄÄÄ Format the Entire Drive  ³
 				      ³			   ³	         ³
		        ADD/DELETE Bad Tracks to Drive ÄÄÄÄÙ		 ³
				      ³				         ³
			  	      ³				         ³
		    	   Find/display Bad Tracks ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
				      ³
			   	      ³
	     Print out and/or save test results to [A:HDRECORD.DOC]



			      Program Flow Diagram
		      (Note: Boxed items represent menus.)
			          (Figure G-1)


				   [Page G-1]			(Rev 11/10/88)


			     *** UPDATE LISTINGS ***

ATTSUM.EXE -

	Version	    Date		             Description
	-------	    ----		             -----------

         1.00     Jun 1988		- Initial release.
	 1.11     Jun 1988		- Upgraded drive tables.
					- Added drive table menu "loop".
					- Centered title of pc+ config screen.
	 1.12     Jul 1988		- Changed telephone number(info screen).
					- Changed incompatibility message to
					  include "UNIX" message.
	 				- Added "not avail" message in 6286
					  drive table screen.
	 1.20	  Aug 1988		- Added 6286 WGS drive table.
					- Added month to initial screen.
	 2.00	  Sep 1988		- Changed all menu "()'s" to "[]'s".
					- Re-worded quit & return lines.
					- Added HDU controller board displays.
					- Changed 6300WGS DIPSW B-1 from "3¬"
					  to "(3«")".
					- Added "shipping" feature.
					- Rplcd' 6300 WGS configuration screen
					  w/instruction message.
					- Fixed "AT" port display for starlan.
					- Menus return to previous menus.
	 3.10	  Oct 1988		- Revised all drive tables to indicate
					  AT&T supported drives.
					- Fixed minor display problem with
					  "ship" screen.
					- Fixed unexpected track "0" format
					  on "AT class" CPU's.
					- Added support for PC6300 PLUS 3.0
					  ROMBIOS.
					- Corrected WA1005 to "ESDI".
					- Moved "ship" to hard drive menu past
					  CPU model tests and it now works for 
					  both PC/XT and PC/AT class CPU's.
					- Added warning note on bottom page A-2.
					- Second drive now accessable in PC/AT
					  class CPU's.
ATTSUM.COM -
	 3.20	   Nov 1988		- Fixed PC6300+ drive selection problem.
					- Changed .EXE to .COM file type.
					- Added CPU timer test for AUTOSELECT.
					- Added 2:1 prompt for PC/AT class CPU.
ATTSUM.EXE -
	 3.30	   Nov 1988		- Fixed floppy save(back to .EXE).
					- Edited PC+ 3.0 table to match BIOS.
	 3.40	   Dec 1988		- Added PC/AT RLL capability.
		   Jan 1989		- Fixed XT format sensitivity problem.
		   Jan 1989		- Fixed PC+ HDU DSW display.

				   [Page H-1]			(Rev 01/26/89)


			    *** REVISION LISTINGS ***


ATTSUM.DOC -

	Revision Date		      		Revised Page Numbers
	-------------			        --------------------

          09/06/88				A-4

	  09/07/88				1,6,7,A-3,A-4,B-1,B-2,D-1,D-2

	  09/10/88				3,E-1,F-1

	  09/25/88				1,2,4,6,7,8,9,G-1,H-1
						Added pages D-1,D-2,E-1

	  10/27/88				1,2,7,8,A-2,H-1,H-2

	  10/29/88                              1,H-1,H-2

	  11/10/88				1,3,F-4,G-1,H-1,H-2

	  11/13/88				7,H-2

	  11/17/88				1,H-1,H-2

	  11/21/88				6,A-1,A-4,H-2

	  12/20/88				1,4,H-1,H-2

	  01/26/89			   	1,H-1,H-2
























				   [Page H-2]			(Rev 01/26/89)