EGA2VGA Copr. (c) 1988 Lawrence Gozum & Marvin Gozum
           ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                                User Manual

    DISCLAIMER

    This  product  is distributed AS IS.  The authors specifically disclaim
    all  warranties  ,expressed  or implied, including ,but not limited to,
    implied  warranties  of  merchantability  and  fitness for a particular
    purpose  with respect to defects in the diskette and documentation, and
    program  license  granted  herein,  in particular, and without limiting
    operation  of  the  program  license  with  respect  to  any particular
    application  use  or  purpose.  In no event shall the authors be liable
    for  any  loss  of  profit or any other commercial damage including but
    not limited to special,incidental, consequential or other damages.  


    LICENSING AGREEMENT

    You  may  use  this program on a TRIAL BASIS only;  this means that you
    may  freely  evaluate  the  usefulness of this program for a reasonable
    period.    Should  you  find  this program useful, you must register it
    (see  last  section  of  this manual).   You will then be provided with
    the  latest release of VGACAD (VGA Computer Assisted Design) and latest
    updates of all released utilities.

    You  may  freely  distribute  copies  of this program in its UNMODIFIED
    state  provided  you do not include it in other software packages, with
    the  exception  of distributing it as part of a bundle of Public Domain
    or  shareware  programs  on a single diskette.  In addition you may not
    charge  more that $3.50 for copying and/or distributing this program in
    the absence of any recognized Users Group guidelines.


    WHAT IS EGA2VGA ?

    EGA2VGA  is  a  conversion  program  that will convert ANY viewable EGA
    640x350x16  color  and  640x480x16  (EGA/VGA)  picture  into a real VGA
    320x200x256  color  picture.  EGA2VGA actually generates 256 new colors
    from  the  original 16 color EGA palette and interprets color mixtures.
    EGA2VGA  also  accurately  calculates  the  correct  aspect  ratio  for
    translation.   Finally, EGA2VGA saves your converted screen and palette
    in  a 'bloadable' format for immediate use in VGACAD (for fine editing)
    or  any  BASIC  application or convert your output to GIF with BLD2GIF.
    Not  only  do you SAVE THOUSANDS of bytes (per picture) in disk storage
    by  conversion,  but you can now apply extensive image processing since
    you  have  256  colors  to  play  with.  VGACAD is designed to edit and
    image process such pictures.

    EGA2VGA  comes with TWO (2) TSR (Terminate and Stay Resident) utilities
    called  EGADMP  (EGA DuMP) and VGADMP (VGA DuMP) which will capture the
    raw  screen  data  of any EGA 640x350x16 or VGA 640x480x16 picture in a
    sequential  order and the 16 color palette out of 64 possible colors in
    files  EGA350SC.nnn  and  EGAPAL16.nnn,  respectively,  for  EGADMP and
    VGA480SC.nnn and VGAPAL16.nnn, respectively, for VGADMP.










    REQUIREMENTS

    You  MUST have a VGA or MCGA adaptor (at least BIOS compatible) present
    and  an  analog  monitor to use VGADMP, EGADMP and EGA2VGA.  EGADMP and
    VGADMP  use  3K of your RAM;  EGADMP need 224,016 of diskspace for each
    captured  picture,  while VGADMP needs 307,984 of diskspce per picture.
    A  HardDisk  is  highly recommended.  EGA2VGA needs about 256KB of your
    available memory and 64K of diskspace for each processed picture.

    Note:    When  in  DOS or using a picture viewer (e.g., EGAGIF, OPTIKS,
    CSHOW)  or  application  which  requires  a keypress to continue, it is
    necessary  to hit any key or a specified key (e.g., spacebar or return)
    after hitting the 'HOTKEY' before EGADMP saves the screen and palette.


    HOW TO USE EGADMP

    Simply  run  EGADMP  before  entering  your  painting/CAD  or digitized
    picture  viewer.    After loading,  press <ALT-F10>, while viewing your
    picture  in  any  drawing/paint/CAD  or  viewing  program. Your current
    screen  and  palette  will be saved in your default drive and directory
    in the standard Bsave format for all BASIC programs.

    The  first  time  you  run  the  program  it  will save your screen and
    palette  to EGA350SC.000 and EGAPAL16.000 respectively.  If there is an
    existing  EGA350SC.nnn  or  EGAPAL16.nnn, then it will increment to the
    next  higher  number.    This  can  be  confusing if you keep unmatched
    screens  and  palettes.    You can use your favorite memory managers to
    remove this TSR or reboot to release it from memory.

    Dual  Floppy  users  (5.25  inch  types) have a problem.  Since the raw
    pixel  dumps  per  file are quite large, you have save the "dump" files
    in another drive.

         For example:

         With  EGADMP  resident  in  memory,  TESTPIC.GIF  in  Drive A: and
         viewing  program  (e.g.,  EGAGIF)  in Drive A: you must switch the
         default drive and view the picture from the other drive.

         1) Type "B:"<ret> to switch to Drive B: as default.
         2) From Drive B: type "A:EGAGIF A:testpic.gif" <ret>.
         3) Now when you hit <ALT-F10> the pixels and palette will be
            "dumped" in Drive B:.


    HOW TO USE EGA2VGA

    EGA2VGA follows a 4 step process.

    STEP 1:  Specify Input and Output files.

         a.   Specify [E]GA 640x350x16 or [V]GA 640x480x16 conversion.

         b.   Specify  the  PATH  (where  the  "dumped"  files are located;
              Hard  Disk  users  can  use  the same directory (assuming you
              have  enough  free  disk space).  Pathnames MUST end with the
              backslash character (i.e.,"\") or it will be rejected.

              Examples:   "A:\" or "B:\" or "C:\GIF\EGA"






         c.   Specify  the  NUMBER  (000-999)  of  the  captured screen and
              palette  dumped  with EGADMP or VGADMP.  If the file does not
              exist  then  an error beep will follow and your input will be
              rejected. 

         d.   Specify  the  FILENAME  that  will  be given to the converted
              picture.    If  there  is  an  existing  file  with  the same
              filename(s)  then  an  error  beep will follow and your input
              will be rejected.  

              The  picture  will be saved in two files: .BLD and .PLT file.
              For   example,   if  you  specify  MYPIC  as  your  converted
              filename,  the  program  will  save your converted picture as
              MYPIC.BLD  and MYPIC.PLT.  These files can be viewed with the
              included  viewer  VGABLD  (source  code included) or in  your
              own BASIC program (discussed in a later section).

              Converted  files  will  be  saved  to  your DEFAULT drive and
              directory  NOT  the  specified PATH;  this is an accomodation
              for DUAL FLOPPY 5.25 inch users.


    STEP 2: Modify the 16 color palette.

         EGA  provides  only  16  colors  from  only  64 hardware-generated
         colors;  these  are  fixed  and  cannot  be modified.  VGA in MCGA
         (320x200x256)  mode allows 256 color from 262,144 possible colors;
         in  VGA  640x480x16 color mode, you are allowed 16 colors from the
         262,144 color selection.

         Your  captured  picture will be displayed in 640x480x16 color mode
         and  will look exactly like your original EGA picture but slightly
         flattened  since  only  350  lines  are used out of 480;  With VGA
         640x480x16  pictures,    it  will be accurate but the picture will
         be  "cropped"  at  line  350  since menu options will appear below
         that  line.   You can then modify the RGB values of each of the 16
         colors assigned to the picture.

         Why  modify  the  16  color palette ?  EGA's 64 color selection is
         quite  limited;  as  a  result you will notice that skin tones are
         forced  to  shades  of  orange,  pink, yellow and red.  With VGA's
         640x480x16  mode  you  can  adjust  each  of the 16 colors to more
         closely  resemble  photographic  quality.    Some  pictures in VGA
         640x480x16 format use the same 64 color selection of EGA as well.

         After  about  4  minutes,  your picture will be in full view and a
         color  line  will  appear asterisks ("*****") representing each of
         the  assigned 16 colors.   You can stop the display at any time by
         pressing  <Esc>.    You  can adjust each of the 16 colors by using
         the following keyboard commands.:

         a.   [SpaceBar]  -  will  cycle  through each of the 16 colors and
              highlight   the   current  selected  color  with  a  "ÛÛÛÛÛÛ"
              highlight block.

         b.   [R],  [G]  or  [B]  - will select the color component of your
              current  color  to  be modified;  an arrow will appear beside
              the RGB (Red Green Blue) value of your current color.








         c.   [+]  will increase the value of your selected color component
              (R,  G or B) within the range of 0 to 63).  As you modify any
              component  you will see the change in your picture and in the
              highlight block.

         d.   [-]  will decrease the value of your selected color component
              within the range 0 to 63.

         e.   [U]ndo  will  restore  the RGB values of the current selected
              color  as  long  as you do not move on to another color to be
              modified.

         f.   [Esc]  will  exit  palette modification and set your 16 color
              palette.


    STEP 3: Crop your picture.

         By  creating  a  "Viewing  WINDOW"  you  can  process only a small
         section  of  the  picture  to  experiment  with  different palette
         settings.

         You  will  first  be  asked  if  you  want to change the "CLIPPING
         WINDOW"  which  are the "cropping" settings you made if you looped
         back  to  the  palette  modification  module (STEP 2).  If you hit
         [N]o then your old settings will be retained.

         Generating  new  colors  is a LONG process, the program must first
         mix  the EGA colors that will be resized into your smaller picture
         (VGA  in  MCGA  mode  uses  on 64000 pixels in comparison to EGA's
         hires  224,000  pixels  or  VGA's  hires 307,200 pixels).  Then it
         will  "look-up"  existing color values and find the closest match.
         If  a  match  is not found then a new color is generated and added
         to your 256 color palette.

         The  whole process can take from 30 minutes to TWO HOURS !!! It is
         best  to  experiment  with  small windows before converting entire
         pictures. Cropping your picture has important functions/results:

              *  It  provides a test area for palette modification, thereby
                 reducing  the  time  required to test new palette settings
                 in  the  conversion  "loop".   See Conversion FlowChart in
                 latter section.

              *  It will reduce processing time for your final picture.

              *  More  new  colors can be generated for your picture, since
                 your  have only 256 colors in your palette.  If you have a
                 large  picture  with  many color combinations at the upper
                 half  of  your  picture,  then  it will use up all the 256
                 colors  before  it  reaches the middle or end part of your
                 picture  (i.e.,  the  bottom  half)  which results in less
                 accurate conversion of the color palette.













         To crop your picture use the following commands:

         a.   [UP]  cursor  key to crop your picture from the bottom border
              moving  up  with  each  successive key press.  You will see a
              black  and  white pattern that will cover the areas that will
              be "cropped-out" of the image.

         b.   [DN] will crop your picture from the top border moving down.

         c.   [LEFT]  will  crop  your picture from the RIGHT border moving
              to the LEFT

         d.   [RIGHT] will crop from the LEFT border to the right.

         e.   [R] will redo your screen so that you can start all over.

         f.   [ESC] will accept your settings and exit this step.


    STEP 4: SELECT use of SKIN.PLT or GENERATE ALL NEW COLORS. 

         Before  finally  converting  your picture you will be asked if you
         want  to  use  the SKIN TONE palette to reserved 64 skin shades or
         not.    The  advantage  of  using the SKIN TONE palette is that it
         will  reserve  64 color for skin tones just in case you run out of
         colors  to generate.  When 256 colors have been generated no other
         color  will  be  created; instead the program will simply find the
         closest  match.   Reject this option if you have a predominance of
         BLUE  and  GREEN  colors  in  your  picture  since  SKIN TONES are
         primarily red/yellow hues.

    NOW  LEAVE  THE  COMPUTER ALONE AND LET IT DO ALL THE WORK.  IF YOU ARE
    CONVERTING  A  WHOLE  PICTURE THE WAITING TIME CAN LAST TWO HOURS.  YOU
    CAN  ACTUALLY  GO  OUT  AND  WATCH A MOVIE OR A TAPE. YOU CAN LEAVE THE
    PROGRAM UNATTENDED; IT WILL SAVE YOUR PICTURE AFTER PROCESSING IT.

             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
             ³   STEP 1: Input/Output Files  ³
             ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                            ÃÄDisplay Picture <ÄÄÄÄÄÄÄÄÄ¿
             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿         ³
             ³   STEP 2: Palette Modification ³         ³
             ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ         ³
                            ³ <Esc>                     ³
             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿         ³
             ³   STEP 3: Cropping             ³         ³
             ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ         ³
                            ³ <Esc>                     ³
             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿         ³
             ³   STEP 4: Conversion           ÃÄÄÄÄÄÄÄÄÄÙ
             ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ   <Esc>
                            ³

                       Save & Exit












    BLOADING CONVERTED PICTURES IN BASIC

    The  following  lines  will  load  one  of  the  captured  screens from
    QuickBASIC  4.0;    if you are using QuickBASIC 1.0, 2.0 or 3.0, I have
    included  VGAMODE.obj which you can include in your UserLib.exe through
    BUILDLIB.exe.

    VGAMODE  is  a BIOS compatible assembly routine which can call the more
    exotic  graphic  modes  of  your  compatible  VGA card (e.g. 800x560x16
    color  mode  of  ATI's  VGA VIP and EGA Wonder); check your user manual
    for the correct hex codes.


         USAGE:  Call VGAMODE(&H13) :    'MCGA 256 color mode
         or      Call VGAMODE(mode%):    'where mode is an integer that
                                         'corresponds to the videomode
                                         'after translating it from HEX

         The following lines will perform just as well.

         Call VGAMODE(&H13):             'init MCGA 256 color mode
         DEF SEG=&HA000:                 'point data segment to
                                         'screen buffer A0000H 
         Bload "MYPIC.BLD",0:            'load the screen

    If  you  are  using  QuickBASIC  (any  version from 1.0 to 4.0), I have
    included  WRITEPAL.obj,  which  is, also a VGA BIOS routines written in
    assembly,   that   you   can   include   in  your  UserLib.exe  through
    BUILDLIB.exe (v3.0 and lower) or LINK (v4.0).

    WRITEPAL  is also a BIOS compatible assembly routine that writes to 256
    palette  registers.    Although  its  main purpose is to facilitate the
    overriding  of  the  VGA  or  MCGA  standard  palette,  since  it is an
    all-purpose  BIOS  routine  it will facilitate changing the palettes of
    more  exotic  screen  modes  such  as  the 640x480x256 color screens of
    IBM's  8514/A  adaptor.  This function is similar to "PALETTE USING" in
    QuickBASIC  with  the  major advantage of following the BIOS convention
    which VGACAP captures and bsaves.

         USAGE:  Call WritePal (Dseg%,Offset%)

         WHERE:  Dseg%  =result of VARSEG for array storage
                  Offset%=result of VARPTR for array storage

         The following lines illustrate its use.

         DIM UserPal%(769)               :' 256 colors x 3 registers=768
                                         :' registers= red grn blu
         Dseg%=VARSEG(UserPal(1))        :' get data segment
         Offset%=VARPTR(UserPal(1))      :' get offset
         DEF SEG=Dseg%                   :' override data segment
         BLOAD "MYPIC.PLT",Offset%       :' bload in correct offset
         Call WritePal (Dseg%,Offset%)

    Palettes  converted with EGA2VGA follow the BIOS calling for contiguous
    RGB  (red  green  blue)  values  for all 256 colors.  One BIOS call can
    update an entire palette with RGB values stored in this manner.









    USING VGABLD

    The  "bloadable"  format  has several advantages.  You will notice that
    the  pictures  load  INSTANTANEOUSLY  !   Bloading a screen is simply a
    memory dump into your display area - crucial for presentations.

    In  addition, keeping the screen and palette separate allows you to use
    one  palette  for  several  pictures or for creating special effects or
    animation.    For  example,  you  can  make a picture shift from a "day
    scene" to a "night scene" by simply changing the palette.

    You  need not go through the tedium of writing your own program just to
    view  your  captured pictures.  VGABLD will load a picture for viewing.
    Captured  screen  and  palette  MUST  have the .BLD and .PLT extensions
    respectively  for  the same picture.  The BASIC source code is included
    and is ready for compilation.

    If  you  want  to  convert  you  screen and palette to CompuServe's GIF
    (Graphics  Interchange  Format);  download  a copy of BLD2GIF from your
    local  BBS  (if  it  has  managed  to  reach your city) or register and
    receive  it  as  part  of your registered package and use it to convert
    the two files into GIF format.


    REGISTRATION

    To  register  your  copy,  send  in the registration form and check for
    $14.95 or $19.95 payable to

                             Dr. Marvin Gozum
                      2 Independence Place Apt. 303-2
                            6th & Locust Street
                          Philadelphia, PA 19106

    For  $14.95  you  will  be  entitled to a registered update (latest) of
    VGACAD  without the shareware notice AND the latest updates of released
    utilities

    a.*  VGACAP  (captures  and  converts  ANY  viewable  320x200x256 color
         picture into 'bloadable' files for use in VGACAD or BASIC)

    b.   CGA2VGA (converts 4-color CGA pictures to VGA 256 color format).

    c.   VGAPRN  (converts  320x200x256  color  pics into 7 user-assignable
         dithered  patterns  and  prints your picture with corrected aspect
         ratios on Epson and IBM compatible printers.

    d.   BLD2GIF   (coverts   ANY   viewable   320x200x256   color  pic  to
         CompuServe's GIF format)

    d.   EGA2VGA which you have.

    For  $19.95  you  will  be  entitled to the next TWO (2) updates of the
    latest  of everything; this means that from the date of receipt of your
    registration  we will send you the latest version of VGACAD and all the
    related  utilities  developed  and  a  premier  copy of any new utility
    developed  as  well  as the next releases of all the aforementioned and
    any new fonts (with the font editor) and Clipart files when available.








    At  this  writing, VGACAD v1.40 supports extensive color 256 management
    and  image  editing/processing  functions: 9600 ways of COLOR SMOOTHING
    in  selected areas or Zoom editing; false colorization of 16, 32 and 64
    gray  shade  pictures;  variable  threshold  gray anti-aliasing, median
    filter  noise  removal,  histogram-based  contrast stretching, variable
    sizing   and   flipping,   cut  &  paste,  graphic  text,  29  brushes,
    Stenciling, more ...

    You  can  expect  spectacular  enhancements in VGACAD's updates. Future
    updates  will  include  3D  and  2D transformations, gradient fills and
    patterns,  and  more; many of these routines are in "C" or assembly and
    work very fast.

    In  the  pipeline  is  QBVGA an extensive library of QuickBASIC VGA 256
    color  graphics  routines,  VGASHW  (a graphics presentation program to
    showoff  your  captured  pictures  or  your  own  paintings  and screen
    design,   VGA3DM  (3D  object/model  editor  for  including  models  in
    VGACAD),  AMG2VGA  (converts  320x400x256  color  Amiga GIF pictures to
    320x200x256  color  format)  and VGA2VGA (coverts 640x480x16 color pics
    and 640x480x256 color pics to 320x200x256 color pics).

    If  you  continue to support maverick authors like us, we will continue
    to  develop  these  products  like  nothing  ever  seen  in  commercial
    packages  -  otherwise  it  will,  as  many  (sigh!)  good  "shareware"
    packages  have  to  go  commercial  or simply die from lack of support.
    Support us and we'll keep developing.


    ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
    Graphics Interchange Format and GIF are trademarks (tm)
    of CompuServe Inc. an H&R Block Company.