EEMRAM 2.00


        Purpose
        -------
        EEMRAM is a small utility that can expand your DOS memory from
        640K to a maximum of 736K using Enhanced or LIM 4.0 expanded
        memory.  To use EEMRAM, you must have a memory board that
        provides EEM or LIM4 memory.  A companion program (DERAM) can be
        used to restore the "normal" 640K if necessary.  EEMRAM will NOT
        work with Intel EMS products if you have an EGA or VGA video
        system.


        Before you run EEMRAM
        ---------------------
        In order for EEMRAM to work, several conditions must be met.
        There's more about this elsewhere in this document, but for now
        run these two checks.

            1. Run MS (just type "MS") and verify that the total free
            memory is 655,360 bytes (640K).  If it is anything else,
            EEMRAM cannot be used.

            2. Run EMSINFO (just type "EMSINFO") and note the results.
            If they scroll beyond one screenful, you can print the
            results by typing:

                EMSINFO > PRN

            EMSINFO must indicate that the EMM type is either "EEMS" or
            "LIM 4.x".  Also, the list of memory segments to which EMS
            memory can be mapped must include the segment "A000".

        If EMSINFO does not indicate that segment A000 is available, you
        probably have an EGA or VGA installed in your system.  See the
        section titled "If you have an EGA or VGA".

        If EMSINFO indicates that EEMRAM cannot be used, and you aren't
        clear on exactly why, just run EEMRAM.  No harm will be done,
        and EEMRAM will display an error message indicating why it won't
        work.  Then look in "EEMRAM error messages" below for possible
        causes and solutions.


        Running EEMRAM
        --------------
        Here is EEMRAM's syntax:

            eemram [/#] [/S]

        When run, EEMRAM will increase DOS-usable memory DOS from 640K
        to a maximum of 736K.  The exact amount depends on your hardware
        configuration, particularly on what type of display adapter you
        have installed.  You may want to run EEMRAM via your AUTOEXEC
        startup batch, ideally as the first external program run by the
        batch:

            echo off
            cd c:\util
            eemram
            ...

        The optional /S parameter is required if you have EEMS memory
        and want to be able to use DERAM (about which, more later).  It
        is not necessary if you have LIM 4.0-compatible memory or don't
        need DERAM.

        The optional /# parameter limits EEMRAM's use of EEMS memory to
        some amount less than the maximum possible.  See the next
        section.

        To see the effects of EEMRAM, just run MS (Memory Size) before
        and after running EEMRAM.


        Limiting Memory Size: /# parameter
        ----------------------------------
        The optional EEMRAM /# parameter can be used to explicitly
        reduce the number of 16K pages of EEMS memory it assigns to DOS
        (see "Memory Allocation Information" for more information about
        memory use).  "#" is a decimal digit from 1 to 6 that specifies
        how many pages you want assigned.

        EEMRAM will normally assign all contiguous pages available from
        A000 to B400 (6 pages maximum, or 96K).  However, there may be
        cases in which you don't want all of this used, and that's what
        /# does.  An example of /# use:

            C> eemram /2

        The /2 means "use only two 16K pages of EEMS memory."

        If you specify more pages than are available, EEMRAM will only
        use the number available, in effect ignoring your parameter.

        Here is a map showing the effects of all possible /#:

            Page       /1  /2  /3  /4  /5  /6
            ----       --  --  --  --  --  --
            A000       XX  XX  XX  XX  XX  XX
            A400           XX  XX  XX  XX  XX
            A800               XX  XX  XX  XX
            AC00                   XX  XX  XX
            B000                       XX  XX <---MDA memory begins
            B400                           XX
            B800                              <---CGA memory begins
                       --  --  --  --  --  --
            KB added   16  32  48  64  80  96
            Total KB  656 672 688 704 720 736



        DERAM
        -----
        EEMRAM works by mapping EEMS memory to DOS addresses beginning
        at memory segment A000; EGA/VGA systems also use this area of
        memory, so you will have a conflict using EGA/VGA hi-res
        graphics modes in an EEMRAM environment.  You may also find that
        you have only a few programs that can really use the extra
        EEMRAM memory and that you prefer to leave the EMS memory free
        most of the time.

        The DERAM program reverses the effects of EEMRAM:  it restores
        the original 640K of DOS memory and releases the EMS memory
        EEMRAM was using back to the free memory pool.  This may allow
        you to use EGA/VGA hi-res modes.

        To restore the original 640K system, just run DERAM:

            C> deram

                [NOTE:  to use DERAM with EEMS memory, you must
                have run EEMRAM with the /S option:

                    C> eemram /s

                This saves certain information the DERAM needs.
                The /S switch is not necessary if you have LIM
                4.0-compatible memory.  When you use /S, EEMRAM
                places in memory a small amount (four bytes) of
                information that DERAM needs.  The information
                is stored in the little used Interapplications
                Communication Area (IACA).  If EEMRAM cannot
                find four consecutive unused bytes in this area,
                it cannot store the information and DERAM won't
                work.]

        As an example of using EEMRAM and DERAM, suppose that you only
        want to have the extra memory available for one program, your
        word processor BESTWP.  The following command sequence will do
        the trick:

            C> eemram /s            [/S needed only for EEMS]
            C> bestwp
            C> deram

        You can enter these commands manually or make a small batch file
        or PCED synonym.

        The opposite situation holds where you want to run with extra
        memory most of the time, but release it before running the EGA
        graphics program GREATGFX.  The following commands may help:

            C> deram
            C> greatgfx
            C> eemram /s            [/S needed only for EEMS]

        IMPORTANT NOTE: it is not possible to guarantee that the system
        will operate correctly after DERAM.  Some programs, especially
        system software, TSRs, and device drivers, assume that the
        amount of memory in your system is fixed--that it will not
        change during a session.  However, that is exactly the effect of
        DERAM.  If you find that something doesn't run after DERAM,
        you'll just have to reboot without EEMRAM.


        Memory Allocation Information
        -----------------------------
        When a typical EEMS or LIM 4.0 memory board is installed, it
        "backfills" DOS memory to 640K; that is, some of the memory on
        the EEMS board is permanently assigned to DOS in such a way that
        the system will appear to DOS to have 640K of main memory.  This
        640K occupies RAM addresses 00000 to 9FFFFF, or, in the more
        traditional segment notation, memory segments 0000 to 9FFF.

        Segments beginning at A000 (the next segment above 9FFF) are not
        assigned to DOS by the EMS manager.

        However, 64K to 96K of addresses beginning at A000 are often
        unused on PC's.  On a machine equipped with a monochrome display
        adapter (MDA), display memory begins at segment B000, leaving
        64K open from A000-AFFF; on a machine equipped with a color
        graphics adapter (CGA), display memory begins at segment B800,
        leaving 96K open from A000-B7FF.

        It is possible to force the EMS manager to assign memory for
        these addresses and to convince DOS that the EMS memory so
        assigned is usable by the system, resulting in as much as 736K
        of DOS-usable memory.  That is what EEMRAM does.

        [Contrary to popular opinion, DOS is not limited to 640K; it can
        use whatever memory is available, up to a limit of 1 megabyte.
        The limiting factor is your hardware.  In particular, some
        hardware such as video display adapters and fixed disk
        controllers may use some areas of memory above the 640K mark.
        Also, the DIP switches on many machines are limited to a maximum
        of 640K switch-settable; to go beyond this, it's necessary for
        software such as EEMRAM to override the switch settings.]


        If you have an EGA or VGA
        -------------------------
        As described above, EEMRAM works by assigning pages of EMS
        memory to DOS addresses beginning at A000h (just above 640K).
        EGA and VGA systems use the same area of memory, so there is a
        potential for conflicts.  However, most EGA/VGA systems use the
        64K of memory between A000 and B000 only in high resolution
        graphics modes, and briefly during mode changes; if you do not
        use high resolution graphics modes frequently, you may still be
        able to use EEMRAM.

        You will have to do some work with your system configuration
        file, CONFIG.SYS.  We STRONGLY recommend that you check the
        following steps on a bootable diskette, not with your hard disk
        CONFIG.SYS.  If you are successful, you can then make the
        apprpriate changes in your hard disk CONFIG.SYS.

        First, check the statement in CONFIG.SYS file that loads your
        EMS driver software.  If you have a parameter that excludes the
        range of memory beginning at A000, you must remove the
        exclusion.  For example, AST's REMM.SYS might be loaded like
        this:

            DEVICE=C:\SYS\REMM.SYS /X=A000-AFFF

        The /X parameter tells REMM.SYS not to permit mapping of EMS
        memory to segment A000, and it must be removed.

        Next, add the statement:

            DEVICE=[d:path]EEMEGA.SYS

        to the file IMMEDIATELY BEFORE the DEVICE statement that loads
        your EMS software.  For example:

            DEVICE=C:\SYS\EEMEGA.SYS
            DEVICE=C:\SYS\REMM.SYS

        Now reboot your system.  It should appear to run normally.  Run
        EMSINFO again and check to be sure that the A000 segment now
        appears in the list of mappable segments.  If it does not, you
        will have to check with your dealer or hardware manufacture to
        see if it's possible to correct the situation.

        If you have EEMS memory, EEMEGA uses 16K of EMS.  It does not
        use any EMS memory if you have a LIM 4.0 EMS driver.

        When EEMRAM is active, EEMEGA.SYS will not allow any EGA/VGA
        BIOS calls to be used.  Thus, your system will not be permitted
        to go into high-resolution graphics modes.  If you have software
        that must be "installed" for a specific video system, you might
        want to install it for CGA or MDA rather than EGA or VGA.


        EEMRAM error messages and solutions
        -----------------------------------
        EEMRAM will not be able to do its job under a number of possible
        conditions.  If EEMRAM reports that it has failed, it will
        display one of the following messages:

        EMS MANAGER IS NEITHER LIM 4.0 NOR EEMS

            In order to use EEMRAM, your Expanded Memory Manager (EMM)
            must conform to either the EEMS 3.2 or LIM 4.0
            specifications.  Check with your dealer to see if a newer
            EMM is available for your EMS board.

        EXPECTED 640K OF DOS MEMORY

            Run MS; in order to use EEMRAM, MS must report exactly
            655,360 bytes of total memory (640K).  If MS reports less
            and you know that you do have a 640K system, it's likely
            that some other TSR or device has taken some memory from
            just below 640K.  Try to locate which TSR or device is doing
            this and check with your dealer to see if there's any way to
            eliminate it.  If MS reports more that 640K, perhaps you've
            already run EEMRAM.

        UNABLE TO RESIZE MEMORY

            EEMRAM must be the owner of the last block of DOS memory
            when it's run.  Always run EEMRAM directly from the DOS
            prompt or from AUTOEXEC.BAT.

        UNABLE TO LOCATE EMS MANAGER

            EEMRAM wasn't able to find the Expanded Memory Manager
            (EMM).  Either you don't have expanded memory, you haven't
            loaded the EMM, or another program is interfering.

        NO PAGES AVAILABLE AT A000

            In order for EEMRAM to work, it must be able to assigne
            chunks of EMS memory to DOS addresses beginning at
            segment A000.  If EEMRAM reports that it can't do this, it's
            usually for one of these reasons:

            1. Your EMS hardware is not capabable of mapping EMS memory
            to arbitrary memory addresses.  This is true of many older
            EMS boards such as the Intel AboveBoard.  There's no
            solution for this other than to purchase new hardware.

            2. Your Expanded Memory Manager (EMM) doesn't support this
            function.  Your EMM must conform to either the EEMS 3.2
            or the LIM 4.0 specification.  Run EMSINFO; it will tell you
            which type of EMM you have.  Check with your dealer to see
            if you can obtain an EEMS or LIM 4.0 EMM for your hardware.

            3. Your EMM has detected that you have an EGA or VGA and has
            in effect "prohibited" mapping memory to A000, even though
            both your EMS board and the EMM are capable of such mapping.
            See the EGA/VGA section for a possible solution.

        NO EMS MEMORY AVAILABLE

            Your EMM has reported that there is no free EMS memory.
            You'll have to reduce the amount of memory used by other
            software.  EEMRAM must have at least 16K free EMS memory and
            can use up to 96K on some systems.

        PROGRAM HAS ALREADY BEEN RUN

            This message will appear only under LIM 4.0 and indicates
            that EEMRAM has already been run since the last reboot.

        ERROR xx ACCESSING EMS MANAGER (AX=yyyy)

            Generic message indicating that there's a problem with the
            EMM or the hardware:  the EMM is corrupted, there's a
            hardware failure, your EMM doesn't support a needed
            function, etc.  The number (xx) indicates the specific error
            code returned that the EMM returned to EEMRAM.  The message
            also indicates the EMS function that failed (register AX
            contents were yyyy at time of EMM function call).

        WARNING: UNABLE TO SAVE /S INFORMATION FOR DERAM

            There is insufficient memory unused in the area that
            EEMRAM/DERAM use to pass needed information back and forth.
            This is a warning message: EEMRAM itself has run successfully,
            but DERAM won't work.


        DERAM error messages
        --------------------

        SYSTEM ALREADY SET TO 640K

            DERAM has found that the system already shows 640K of DOS
            memory, so it hasn't done anything.


        EEMRAM NOT RUN WITH /S OPTION, UNABLE TO RESIZE MEMORY

            In order to use DERAM with EEMS memory, you must run EEMRAM
            with the /S switch.  If you did run EEMRAM with /S and you
            see this message, some other program is using the same area
            of memory that EEMRAM/DERAM use to pass information back and
            forth.  You will not be able to use DERAM in this case
            (fortunately, it's unlikely).

        ERROR xx ACCESSING EMS MANAGER (AX=yyyy)

            Generic message indicating that there's a problem with the
            EMM or the hardware:  the EMM is corrupted, there's a
            hardware failure, your EMM doesn't support a needed
            function, etc.  The number (xx) indicates the specific error
            code returned that the EMM returned to EEMRAM.  The message
            also indicates the EMS function that failed (register AX
            contents were yyyy at time of EMM function call).

        UNABLE TO RESIZE MEMORY

            DERAM can't modify DOS's memory allocation blocks, so
            nothing has been done.  Always run DERAM directly at the
            DOS prompt or via AUTOEXEC; don't run it as a "child" of
            some other program.


        Notes
        -----
        1. We can't promise that EEMRAM will work with any specific
        hardware configuration.  If your hardware conflicts with what
        EEMRAM does (EEMRAM won't run properly, system locks up, etc.),
        there's nothing we can do about it.

        2. EEMRAM is not a TSR (i.e., it is not resident).  It runs and
        terminates, restoring the full amount of memory to the system.
        Because EEMRAM is not a TSR, don't try to use MARK/RELEASE,
        REFEREE, POPDROP, or similar TSR managers to "remove" EEMRAM.
        EEMRAM cannot be removed by these managers.  EEMEGA.SYS is a
        device driver and also cannot be removed; however, it uses very
        little memory.

        3. EEMRAM and DERAM both return an errorlevel of 255 if they
        encounter any errors.

        4. If EEMRAM needs more EMS memory than is available, it will
        use all that is available.  If no EMS memory at all is
        available, it is an error.


        Versions
        --------
        2.00 03/30/89
            Added support for LIM 4.0 memory.
            Added EEMEGA.SYS

       1.01 08/20/87
            Changed test for enhanced memory, may be a little more
            tolerant of older versions of REMM.SYS et al.


        Copyright/License/Warranty
        --------------------------

        This document and the program files EEMRAM.COM, DERAM.COM
        EEMEGA.SYS, MS.COM, and EMSINFO.EXE ("the software") are
        copyrighted by the author.  The copyright owner hereby licenses
        you to: use the software; make as many copies of the program
        and documentation as you wish; give such copies to anyone; and
        distribute the software and documentation via electronic means.
        There is no charge for any of the above.

        You are specifically prohibited from charging, or requesting
        donations, for any such copies, however made; and from
        distributing the software and/or documentation with commercial
        products without prior permission.  An exception is granted to
        recognized user's groups, which are authorized to charge a
        small fee (not to exceed $7) for materials, handling, postage,
        and general overhead.  NO FOR-PROFIT ORGANIZATION IS AUTHORIZED
        TO CHARGE ANY AMOUNT FOR DISTRIBUTION OF COPIES OF THE SOFTWARE
        OR DOCUMENTATION, OR TO INCLUDE COPIES OF THE SOFTWARE OR
        DOCUMENTATION WITH SALES OF THEIR OWN PRODUCTS.

        THIS INCLUDES A SPECIFIC PROHIBITION AGAINST FOR-PROFIT
        ORGANIZATIONS DISTRIBUTING THE SOFTWARE, EITHER ALONE OR WITH
        OTHER SOFTWARE, AND CHARGING A "HANDLING" OR "MATERIALS" FEE OR
        ANY OTHER SUCH FEE FOR THE DISTRIBUTION.  NO FOR-PROFIT
        ORGANIZATION IS AUTHORIZED TO INCLUDE THE SOFTWARE ON ANY MEDIA
        FOR WHICH MONEY IS CHARGED WITHOUT PRIOR PERMISSION FROM THE
        COPTRIGHT OWNER.

        No copy of the software may be distributed or given away without
        this document; and this notice must not be removed.

        There is no warranty of any kind, and the copyright owner is not
        liable for damages of any kind.  By using this free software,
        you agree to this.

        The software and documentation are:

                           Copyright (C) 1987,1989 by
                             Christopher J. Dunford
                            The Cove Software Group
                              Post Office Box 1072
                            Columbia, Maryland 21044

                                (301) 992-9371
                        CompuServe 76703,2002 [IBMNET]