This document gives the switch settings for a Mitsubishi
MR535 ST506/412 interface hard drive.  RLL formatted 
capacity is 65 Mbytes, MFM formatted capacity is 42 Mbytes.
The drive is designed to accommodate BOTH format methods.

SW1

This is the terminating resistor select.  Whereas other
drives have a removable resistor pack, the MR535 has the 
resistor pack permanently soldered in place.  The resistor
pack is switched in or out with the DIP switches in SW1.

TO TERMINATE, or use the drive as the LAST drive, ALL
switches in SW1 should be moved to the ON position.

If the MR535 is not the last drive, ALL switches in SW1
should be moved to the OFF position.

Setting the switches in any other configuration (i.e. some
ON and some OFF) will result in erratic and unreliable
operation.

SW2

Switches 1, 2, 3, and 4 on SW2 correspond to the drive
select lines.  They correspond to Select 0, Select 1,
Select 2, and Select 3, respectively.  The selected
SELECT X is active when in the ON position.  Only one
of these four switches should be in the ON position.
Otherwise, the drive will not read or write.

Switches 5, 6, 7, and 8 are not used when the drive is
operated normally.  They set up test modes used at the
factory.  They should remain in the factory set positions,
which are as follows:

	SW2-5  ON
	SW2-6  OFF
	SW2-7  OFF
	SW2-8  OFF


FORMATTING INFORMATION

The drive has 977 cylinders and 5 R/W heads.
No Write Precompensation is needed.



Information on these drives can be obtained from
Mitsubishi.

Main US Headquarters   213-515-3993  (Los Angelos)
Mt. Prospect, IL       312-298-9223  (Sales Office)
Piscataway, NJ	       201-981-1001  (Sales Office)
Norcross, GA	       414-368-4845  (Sales Office)

Information and Literature:

Mitsubishi Electronics America, Inc.
Computer Peripherals Division
991 Knox Street
Torrance, CA 90502

REVIEW OF THE DRIVE

The MR535 is a unique drive in that it has the capability to
format in both RLL and MFM formats.  This is unique, especially
in that the drive is fast (28mS) and yet falls into the under
$600 range.  So far, I have heard of NO errors or failures
with this drive.  Currently, dealer cost of this drive is about
$350 (qty 10 units).  As of May 1989, word has it that this
drive is allocated by Mitsubishi, however it seems that some
are available to the consumer market in the under $400 range.
This is about the same as a Seagate ST277R (65Mb, 40mS).  This
makes the MR535 a strong runner, since the speed consideration
often makes the largest difference in hard drive cost.