HERCBIOS.ASM                   PAGE 1                                
      THIS SYSTEM IS SHAREWARE, THEREFORE,
	IF YOU LIKE THIS PROGRAM, FIND IT USEFUL, AND DECIDE TO USE IT, 
	    THEN YOU MUST SEND A $5.00 LICENCE FEE  U.S. TO:
                                                Douglas McDaniels
                                                2627 Arlington Dr #101
                                                Alexandria VA 22306 U.S.A.
             
         Hercbios is Copywrite 1988 by Douglas McDaniels.
         HOWEVER, HERCBIOS HAS BEEN RELEASED AS SHAREWARE, SO YOU MAY MAKE
	  ALL THE COPIES THAT YOU WANT, GIVE THEM TO YOUR FREINDS, AND YOU MAY
	  PLACE THIS SYSTEM ON BULLETIN BOARDS.(HBIOSARC.EXE is the recomended
	  format)
             
             First, what is HERCBIOS.COM ?
             All the major video graphics boards for the IBM P.C. series  and
        compatibles,  with  the  single  exception  of the Hercules Monocrome
        Graphics Adapter, have a built in ROM BIOS (accessed though INT  10H)
        that provides the video primitive functions such as the capability to
        put a character on the screen. DOS uses these functions to  impliment
        its  teletype style interface, and these video ROM BIOS functions are
        also accessed by many applications programs. There is no  reason  why
        video  ROM  BIOS  functions  should  not be provided for the Hercules
        Monocrome Graphics Adapter as well, and  that  is  what  HERCBIOS.COM
        does. Using HERCBIOS.COM you can now have a 43 line by 90 column text                                                    43 line by 90 column text
        mode  for  your  M.G.A  (Hercules  compatable)   board,   and   those        mode  for  your  M.G.A  (Hercules  compatable)   board               
        application  programs  that  use  only  BIOS  calls for compatibility
        should run under this mode.
             
              You may be wondering what mode number I have decided to use for
        the  Hercules board. All the IBM video modes have a number associated
        with them, for example monocrome text mode is mode  number  7,  while
        C.G.A text mode is mode number 3. The decision is quite easy. IBM has
        started at 0, and has worked its  way  up  to  mode  20  or  so.  The
        negative  numbers  have not been touched by anyone yet, so now is the
        time to do so. I have  chosen  mode  -2  (or  254)  as  the  Hercules
        monocrome graphics mode, reserving mode -1 for special use. Note that
        this leaves room for a whole series of negative mode numbers for  use
        by  other  non-IBM  board  manufacturers, and also for negative modes                                                  and also for negative modes
        that provide extensions to the INT 10H functions of already  existing        that provide extensions to the INT 10H functions of already  existing
        modes.  This program also implements a mode mapping feature, allowing        modes                                                                
        the user to redirect program requests for an IBM mode to a request to
        change  to one of the negative, non-IBM modes (the special mode -1 is
        involved in this feature, see the documentation  for  video  function
        00h and the assembly listing for program MODEMAP )
        __________________________________________________                   

        HERCBIOS.ASM                   PAGE 2                                


                                     Here  are  general user instructions
								and general comments on the use of HERCBIOS.COM:
              To install the program you simply run it, by entering  HERCBIOS
        43, HERCBIOS 29, or HERCBIOS followed by some other number at the Dos
        prompt.(The meaning of the command line argument is explained  later.
        See  also the description of INT 10H function 08h) But to make use of
        it you must also load the pixel maps. I have provided an accompanying
        mini-program  ASCITABL.COM  which  loads the ASCII pixel bit maps for
        IBM computers and true compatibles, and the Dos program  GRAFTABL.COM
        loads  the  graphics  pixel  maps  for  those  with Dos 3.x. Just run
        HERCBIOS.COM, ASCITABL.COM and GRAFTABL.COM in any order.  For  those
        who  are  still  using  Dos  2.x,  I  have  provided a program called
        GRAFCHAR.COM which duplicates the function of GRAFTABL.COM. Also, for
        machines  which  are not really very IBM compatible, ASCITABL.COM may
        not work. I have therefore provided an alternate program ASCICHAR.COM
        which should work even on those machines, its disadvantage being that
        it takes up more RAM than ASCITABL.COM since it must explicitly  load
        the  pixel  maps, while ASCITABL.COM makes use of the pixel maps that
        are supposed to be already present in the ROM BIOS.    A  word  about
        mini-program  ASCITABL.COM,  this  program simply points INT 44H (the
        interrupt reserved by IBM for just this purpose) to point to the  8x8
        ASCII  pixel  maps,  which  on  IBM  and  true compatibles are always
        located at  0F000:0FA6E,  and  I  have  hard  coded  this  vector  in
        ASCITABL.COM.
             
             To  change  into the Hercules mode you could use EGAMODE.COM (as
        provided by the ZIFF DAVIS Publishing company) but you will  probably
        want  to  use the mini-program CHANGE.COM (included) for this purpose
        since it allows the user to decide whether  or  not  to  map  in  the
        second  graphics  page,  leaving  it  out in order to provide for the
        presence of a CGA card. In order  to  change  to  Hercules  monocrome
        graphics  mode,  run  the  mini-program CHANGE.COM . If you provide a
        command line argument of 0 (.i.e. type CHANGE.COM 0 ) then the second
        graphics  page  (page 1) will be suppressed to allow a CGA compatible
        card to reside in your system at  the  same  time  as  your  Hercules
        compatible  card. To return to text only mode, in order, for example,
        to run  programs  that  write  directly  to  the  screen  simply  run
        TEXT.COM,  which  will  return  your  system  to  video  mode  7 (IBM
        monocrome text only mode)
             
	       
             









        __________________________________________________                   

        HERCBIOS.ASM                   PAGE 3                                


             In order to select, at  the  Dos  prompt,  the  number  of  rows
        displayed   on   the   screen,  I  have  provided  the  mini-programs
        ROWS43.COM, ROWS29.COM, and ROWS25.COM.  Those  users  with  ANSI.SYS
        installed  should  run  ROWS25.COM right off, since ANSI.SYS requires
        that there be only 25 rows on the screen. For those who chose not  to
        use  ANSI.SYS  (and  its  utility is very limited) running ROWS43.COM
        will put 43 rows on the screen when in  Hercules  monocrome  graphics
        mode,  and  running ROWS29.COM will return the display to the default
        value of 29 rows on the screen. (Note that you will probably want  to
        clear  the screen right after running these programs since previously
        written rows are not altered)
        
             A caution about CLS: The CLS  command  provided  with  Dos  will
        suppress  the  alternate  graphics  page,  since when ANSI.SYS is not
        installed, CLS clears the screen by issuing a change mode command  to
        the  currently  active  video  mode.  Therefore,  I have provided two
        clearscreen mini-programs  CLS0.COM  and  CLS1.COM  which  clear  the
        screen, the latter permitting the existence of the alternate graphics
        page, the former suppressing it.
        
        
             Returning to the command line argument of HERCBIOS,  we  see  in
        the  description of function 08H that it reserves enough RAM to store
        the character codes for the read character function for the number of
        rows  specified  in  the  argument.  No  space  is  reserved to store
        character attributes (however, an algorithm is used  that  determines
        if  the attribute is inverse video by examining the pixel patterns on
        the screen. This algorithm works for all but a very few of  the  more
        esoteric characters).
             
             Note  that  line  drawing functions are included with these BIOS
        functions.  I  have  included  the  Turbo  C  program  DAZZLE   which
        demonstrates  the  efficiency  of  the line drawing routines. Try it!
        (But be sure to use CHANGE to change into the new  bios  mode  before
        running DAZZLE)
        
	       All names of products used here are trademarks or registered
	       trademarks of their respective owners.
             
             This  brings  us  to the actual INT 10H AH functions themselves.
        Here follows a writeup of all the supported functions, along with the
        features specific to this implementation.
             
             








        __________________________________________________                   

        HERCBIOS.ASM                   PAGE 4                                


           SET VIDEO MODE (Function 00H)
           
    AX:²²²AH²²²²²²AL²²² CALL
    BX:²²²BH²²²°°°BL°°° AH = 00H
    CX:²²²CH²²²²²²CL²²² AL = Video mode to select
    DX:°°°DH°°°°°°DL°°° BH = Number of highest graphics page to be mapped
                             into memory.(Currently for AL = 254 only)
       °°°°°°°SP°°°°°°° CH = IBM mode number to map (AL =  255 only)
       °°°°°°°BP°°°°°°° CL = Translation for future requests for mode in CH
       °°°°°°°SI°°°°°°°      (AL = 255 only)
       °°°°°°°DI°°°°°°°

       °°°°°°°DS°°°°°°° RETURN
       °°°°°°°SS°°°°°°° None
       °°°°°°°ES°°°°°°°
             
             
             Exceptions and Comments:
             
             When  AL  =  255  a special mode mapping feature is invoked. Any
        future requests for the mode contained in CH will be translated  into
        a request for the mode number contained in CL. Also, the current mode
        will be changed to mode 7 (monocrome text only)  as  a  side  effect.
        Furthermore,    if   mode   254   is   placed   in   CL,   then   the
        Get_Current_Display_Mode function  request  when  in  mode  254  will
        return  the mode number in CL from then on, instead of 254. To undo a
        mode mapping, simply use this function to remap the mode  to  itself.
        It  would  probably  be undesirable to put 255 into CH or CL however,
        unless you are quite sure that you know what you are doing.
             ______________________________________________________

           SET CURSOR TYPE (Function 01H)
           
    AX:²²²AH²²²°°°AL°°° CALL
    BX:°°°BH°°°°°°BL°°° AH = 01H
    CX:²²²CH²²²²²²CL²²² CH = Starting line within character cell for cursor
    DX:°°°DH°°°°°°DL°°° CL = Ending line within character cell for cursor
                                                
       °°°°°°°SP°°°°°°°
       °°°°°°°BP°°°°°°°
       °°°°°°°SI°°°°°°°
       °°°°°°°DI°°°°°°°

       °°°°°°°DS°°°°°°° RETURN
       °°°°°°°SS°°°°°°° None
       °°°°°°°ES°°°°°°°




        __________________________________________________                   

        HERCBIOS.ASM                   PAGE 5                                


                                       Exceptions and Comments:
             
             The default setting for mode 254 is CH = 06 and CL  =  07.  This
        will  place  the  cursor at the bottom of the usual ASCII characters,
        and two scan lines tall. For mode 254 the bottom of the  cursor  must
        fit  within  the character cell, which is 12 scan lines if the number
        of rows on the screen in less than 30, otherwise 8  scan  lines.  The
        cursor does not blink.
             ____________________________
             
             
             
                SET CURSOR POSITION (Function 02H)
           
    AX:²²²AH²²²°°°AL°°° CALL
    BX:²²²BH²²²°°°BL°°° AH = 02H
    CX:°°°CH°°°°°°CL°°° BH = Page number
    DX:²²²DH²²²²²²DL²²² DH = Row
                        DL = Column
       °°°°°°°SP°°°°°°°
       °°°°°°°BP°°°°°°°
       °°°°°°°SI°°°°°°°
       °°°°°°°DI°°°°°°°

       °°°°°°°DS°°°°°°° RETURN
       °°°°°°°SS°°°°°°° None
       °°°°°°°ES°°°°°°°
             
             
             Exceptions and Comments:
             
             There  is a separate cursor associated with both page 0 and page
        1. This function sets the cursor for the page contained in BH  (0  or
        1).  For  mode  254, DH contains the row and may run from 0 to 42, or
        from 0 to 28, depending on how many rows to  display  on  the  screen
        have been selected. DL may run from 0 to 89 for mode 254.
        _________________________________________________________
             
             
             
             









        __________________________________________________                   

        HERCBIOS.ASM                   PAGE 6                                


                READ CURSOR POSITION (Function 03H)
           
    AX:²²²AH²²²°°°AL°°° CALL
    BX:²²²BH²²²°°°BL°°° AH = 03H
    CX:²²²CH²²²²²²CL²²² BH = Page number (see function 02H)
    DX:²²²DH²²²²²²DL²²²

       °°°°°°°SP°°°°°°° RETURN
       °°°°°°°BP°°°°°°° CH = Starting line for cursor
       °°°°°°°SI°°°°°°° CL = Ending line for cursor
       °°°°°°°DI°°°°°°° DH = Cursor's row
                        DL = Cursor's column
       °°°°°°°DS°°°°°°°
       °°°°°°°SS°°°°°°°
       °°°°°°°ES°°°°°°°
             
        ______________________________________________
             
             
                SET DISPLAYED PAGE (Function 05H)
           
    AX:²²²AH²²²²²²AL²²² CALL
    BX:°°°BH°°°°°°BL°°° AH = 05H
    CX:°°°CH°°°°°°CL°°° AL = Page number
    DX:°°°DH°°°°°°DL°°°

       °°°°°°°SP°°°°°°°
       °°°°°°°BP°°°°°°°
       °°°°°°°SI°°°°°°°
       °°°°°°°DI°°°°°°°

       °°°°°°°DS°°°°°°° RETURN
       °°°°°°°SS°°°°°°° None
       °°°°°°°ES°°°°°°°
             
          
             Exceptions and Comments:
             
             For mode 254 there are two displayable pages, page 0 and page 1.
        Users of this function should make sure that page 1 has  been  mapped
        into memory before trying to make use of it.
        ____________________________________________
             
             






        __________________________________________________                   

        HERCBIOS.ASM                   PAGE 7                                


                             SCROLL UP (Function 06H)
           
    AX:²²²AH²²²²²²AL²²² CALL
    BX:²²²BH²²²°°°BL°°° AH = 06H
    CX:²²²CH²²²²²²CL²²² BH = Attribute for blanked area
    DX:²²²DH²²²²²²DL²²² CH = Top left row of window
                        CL = Top left column of window
       °°°°°°°SP°°°°°°° DH = Bottom right row of window
       °°°°°°°BP°°°°°°° DL = Bottom right column of window
       °°°°°°°SI°°°°°°° AL = Lines to scroll
       °°°°°°°DI°°°°°°°

       °°°°°°°DS°°°°°°° RETURN
       °°°°°°°SS°°°°°°° None
       °°°°°°°ES°°°°°°°
             
             
             Exceptions and Comments:
             
             If  bits  0  to 2 are blank and either bit 4,5, or 6 is set then
        the attribute is treated as inverse video, and a solid block is  used
        as a fill character. If AL = 0, then the window is blanked.
        ___________________________________________________________
             
        
                SCROLL DOWN (Function 07H)
           
    AX:²²²AH²²²²²²AL²²² CALL
    BX:²²²BH²²²°°°BL°°° AH = 07H
    CX:²²²CH²²²²²²CL²²² BH = Attribute for blanked area
    DX:²²²DH²²²²²²DL²²² CH = Top left row of window
                        CL = Top left column of window
       °°°°°°°SP°°°°°°° DH = Bottom right row of window
       °°°°°°°BP°°°°°°° DL = Bottom right column of window
       °°°°°°°SI°°°°°°° AL = Lines to scroll
       °°°°°°°DI°°°°°°°

       °°°°°°°DS°°°°°°° RETURN
       °°°°°°°SS°°°°°°° None
       °°°°°°°ES°°°°°°°
             
             








        __________________________________________________                   

        HERCBIOS.ASM                   PAGE 8                                


             Exceptions and Comments:
             
             If  bits  0  to 2 are blank and either bit 4,5, or 6 is set then
        the attribute is treated as inverse video, and a solid block is  used
        as a fill character. If AL = 0, then the window is blanked.
        ___________________________________________________________
                  
                READ CHARACTER AND ATTRIBUTE AT CURSOR (Function 08H)
           
    AX:²²²AH²²²²²²AL²²² CALL
    BX:²²²BH²²²°°°BL°°° AH = 08H
    CX:°°°CH°°°°°°CL°°° BH = Page (must be zero in any graphics mode,
    DX:°°°DH°°°°°°DL°°° including mode 254)
             
       °°°°°°°SP°°°°°°° RETURN
       °°°°°°°BP°°°°°°° AH = Attribute (See note below) [***updated**]
       °°°°°°°SI°°°°°°° AL = ASCII character code
       °°°°°°°DI°°°°°°°

       °°°°°°°DS°°°°°°°
       °°°°°°°SS°°°°°°°
       °°°°°°°ES°°°°°°°
             
             
             Exceptions and Comments
             
             When  installing  HERCBIOS, you may follow the program name with
        an optional command line argument consisting of a number  from  0  to
        43.  This  number  reserves  enough  RAM to store the ASCII character
        codes for the number of rows that you specified starting from the top
        down.  If  a  program  issues a get_char (function 08H) request for a
        character in a row higher than you  specified  in  the  command  line
        argument,  then  the  ASCII  value  for a space character is returned
        instead. This function is used only by programs that  read  from  the
        screen. It is usually apparent to the user that he is using a program
        that does this, so if the user knows that he will not  be  using  any
        programs  that  read  from  the screen in mode 254, then the user can
        invoke HERCBIOS without any command line  argument,  which  will  not
        reserve  any  space  for  the get_character buffer. This can save the
        user up to 43*90 = 3870 bytes, which is almost 4Kb.  Also,  for  mode
        254, xor'ed characters do not currently update the get_char buffer.
             The  correct  normal/inverse  attribute will be returned through
        the use of an algorithm that determins whether or not a character  is
        normal  or  inverse  video  directly  from  the  screen  pixels.  The
        algorithm returns the correct attribute for  all  except  characters,
        177,178,219,220,  and  222,  and  in  43  row mode a few of the funny
        characters in the range 0 to 31 are  also  misread.  This  should  be
        sufficient for all but the most unusual screen reading requirements.


        __________________________________________________                   

        HERCBIOS.ASM                   PAGE 9                                


                                                 WRITE CHARACTER (USING ATTRIBUTE) AT CURSOR (Function 09H)
             Note:  For  mode  254,  this  is  the  same function provided by
        Function 0AH.
           
    AX:²²²AH²²²²²²AL²²² CALL
    BX:²²²BH²²²²²²BL²²² AH = 09H/(also AH = 0AH)
    CX:²²²CH²²²²²²CL²²² AL = Character to write
    DX:°°°DH°°°°°°DL°°° BH = Page
                        BL = Attribute
       °°°°°°°SP°°°°°°° CX = Replication factor
       °°°°°°°BP°°°°°°°
       °°°°°°°SI°°°°°°°
       °°°°°°°DI°°°°°°°

       °°°°°°°DS°°°°°°° RETURN
       °°°°°°°SS°°°°°°° None
       °°°°°°°ES°°°°°°°
             
             Exceptions and Comments
             
             For mode 254, if bit 7 of BL  is  set,  the  character  will  be
        xor'ed  into  the  display. If bits 0 to 2 of BL are blank and either
        bit 4,5, or 6 of BL is set then the attribute is treated  as  inverse
        video.  If  bit  3  of  BL  is  set,  and  bit 7 is not set, then the
        character is Or'ed into the display. Xor'ed characters do not  update
        the  get_char  buffer. Also, if more characters are written with a CX
        greater than 1 than will fit on what remains of the  current  column,
        then the result is unpredictable.
        ______________
             
                WRITE PIXEL (Function 0CH)
           
    AX:²²²AH²²²²²²AL²²² CALL
    BX:°°°BH°°°°°°BL°°° AH = 0CH
    CX:²²²CH²²²²²²CL²²² CX = Column (for mode 254: 0 to 719)
    DX:²²²DH²²²²²²DL²²² DX = Row (for mode 254: 0 to 347)
                        AL = Pixel color (see below)
       °°°°°°°SP°°°°°°°
       °°°°°°°BP°°°°°°° RETURN
       °°°°°°°SI°°°°°°° None
       °°°°°°°DI°°°°°°°
             
       °°°°°°°DS°°°°°°°
       °°°°°°°SS°°°°°°°
       °°°°°°°ES°°°°°°°
             




        __________________________________________________                   

        HERCBIOS.ASM                   PAGE 10                               


             Exceptions and Comments
             
             If bit 7 of AL is set, the pixel will be xor'ed into the screen.
        For mode 254, the allowable colors are 0 and 1 for  black  and  green
        (or  amber,  white ect.) If higher colors are used, additional pixels
        will be placed on the  screen  near  the  selected  dot,  but  in  an
        unspecified fashion. The currently displayed video page is used.
        ____________________________________________________
             
             
                     READ PIXEL ON SCREEN (Function 0DH)
           
    AX:²²²AH²²²²²²AL²²² CALL
    BX:°°°BH°°°°°°BL°°° AH = 0CH
    CX:²²²CH²²²²²²CL²²² CX = Column (for mode 254: 0 to 719)
    DX:²²²DH²²²²²²DL²²² DX = Row (for mode 254: 0 to 347)
             
       °°°°°°°SP°°°°°°°
       °°°°°°°BP°°°°°°° RETURN
       °°°°°°°SI°°°°°°° AL = Pixel color (0 or 1 for mode 254)
       °°°°°°°DI°°°°°°°
             
       °°°°°°°DS°°°°°°°
       °°°°°°°SS°°°°°°°
       °°°°°°°ES°°°°°°°
             
             
             
                     WRITE CHARACTER IN TTY MODE (Function 0EH)
           
    AX:²²²AH²²²²²²AL²²² CALL
    BX:²²²BH²²²²²²BL²²² AH = 0EH
    CX:°°°CH°°°°°°CL°°° AL = Character to write
    DX:°°°DH°°°°°°DL°°° BH = Page
                        BL = Attribute
       °°°°°°°SP°°°°°°°
       °°°°°°°BP°°°°°°°
       °°°°°°°SI°°°°°°°
       °°°°°°°DI°°°°°°°

       °°°°°°°DS°°°°°°° RETURN
       °°°°°°°SS°°°°°°° None
       °°°°°°°ES°°°°°°°
             






        __________________________________________________                   

        HERCBIOS.ASM                   PAGE 11                               


             Exceptions and Comments
             
             For  mode  254,  if  bit  7  of BL is set, the character will be
        xor'ed into the display. If bits 0 to 2 of BL are  blank  and  either
        bit  4,5,  or 6 of BL is set then the attribute is treated as inverse
        video. Xor'ed characters do not update  the  get_char  buffer.  Bell,
        backspace,  linefeed  and  carriage return characters are acted upon,
        and the cursor is advanced appropriately. Linewrap is  also  provided
        (90 characters per column)
        _________________________________________
             
                     GET MODE (Function 0FH)
           
    AX:²²²AH²²²²²²AL²²² CALL
    BX:²²²BH²²²°°°BL°°° AH = 0FH
    CX:°°°CH°°°°°°CL°°°
    DX:°°°DH°°°°°°DL°°°
                       
       °°°°°°°SP°°°°°°°
       °°°°°°°BP°°°°°°°
       °°°°°°°SI°°°°°°°
       °°°°°°°DI°°°°°°°

       °°°°°°°DS°°°°°°° RETURN
       °°°°°°°SS°°°°°°° AL = Current video mode
       °°°°°°°ES°°°°°°° BH = Active video page
             
             
             -----------------------------------------
             
             
                     GET ROWS (Function 20H/11H)
           
    AX:²²²AH²²²°°°AL°°° CALL
    BX:°°°BH°°°°°°BL°°° AH = 11H or 20H
    CX:²²²CH²²²²²²CL²²²
    DX:°°°DH°°°²²²DL²²²
                       
       °°°°°°°SP°°°°°°° RETURN
       °°°°°°°BP°°°°°°° DL = Number of rows seen on screen
       °°°°°°°SI°°°°°°° CX = Number of scan lines per character
       °°°°°°°DI°°°°°°°       (Unique to non IBM video modes)

       °°°°°°°DS°°°°°°°
       °°°°°°°SS°°°°°°°
       °°°°°°°ES°°°°°°°




        __________________________________________________                   

        HERCBIOS.ASM                   PAGE 12                               


                          -----------------------------------------
             
                     GET SIZE (Function 21H/19H)
           
    AX:²²²AH²²²°°°AL°°° CALL
    BX:°°°BH°°°°°°BL°°° AH = 19H or 21H
    CX:²²²CH²²²²²²CL²²²
    DX:²²²DH²²²²²²DL²²²
                       
       °°°°°°°SP°°°°°°° RETURN
       °°°°°°°BP°°°°°°° DX = Number of pixel rows on screen
       °°°°°°°SI°°°°°°° CX = Number of pixel columns on screen
       °°°°°°°DI°°°°°°°      (unique to non IBM video modes)

       °°°°°°°DS°°°°°°°
       °°°°°°°SS°°°°°°°
       °°°°°°°ES°°°°°°°
             
             -----------------------------------------------------
             
                        SET NUMBER OF ROWS ON SCREEN (Function 22H/1AH)
          
              
    AX:²²²AH²²²²²²AL²²² CALL
    BX:°°°BH°°°°°°BL°°° AH = 1AH or 22H
    CX:°°°CH°°°°°°CL°°° AL = Number of rows to set on screen (Unique to non
    DX:°°°DH°°°°°°DL°°°      IBM video modes)
                       
       °°°°°°°SP°°°°°°° RETURN
       °°°°°°°BP°°°°°°° None
       °°°°°°°SI°°°°°°°
       °°°°°°°DI°°°°°°°

       °°°°°°°DS°°°°°°°
       °°°°°°°SS°°°°°°°
       °°°°°°°ES°°°°°°°
             
             ----------------------------------------------
             
                    MOVE TO POINT, PREPARE TO DRAW LINE (Function 23H)
             (Unique to non IBM video modes)
           
    AX:²²²AH²²²²²²AL²²² CALL
    BX:°°°BH°°°°°°BL°°° AH = 23H
    CX:²²²CH²²²²²²CL²²² AL = Color and style of line to be drawn, 0 = black
    DX:²²²DH²²²²²²DL²²²     1 = green/white/amber ,129 = XOR line into screen




        __________________________________________________                   

        HERCBIOS.ASM                   PAGE 13                               


                              °°°°°°°SP°°°°°°° CX = X coordinate of start of line (0 to 719 for
       °°°°°°°BP°°°°°°° Hercules and compatibles)
       °°°°°°°SI°°°°°°° DX = Y coordinate of start of line (0 to 347 for
       °°°°°°°DI°°°°°°° Hercules and compatables)

       °°°°°°°DS°°°°°°°
       °°°°°°°SS°°°°°°° RETURN
       °°°°°°°ES°°°°°°° None
             
        
        -------------------------------------------------------
             
                  
                    DRAW LINE (Function 23H)
             (Unique to non IBM video modes)
           
    AX:²²²AH²²²°°°AL°°° CALL
    BX:°°°BH°°°°°°BL°°° AH = 24H
    CX:²²²CH²²²²²²CL²²²
    DX:²²²DH²²²²²²DL²²²
                       
       °°°°°°°SP°°°°°°° CX = X coordinate of end of line (0 to 719 for
       °°°°°°°BP°°°°°°° Hercules and compatibles)
       °°°°°°°SI°°°°°°° DX = Y coordinate of end of line (0 to 347 for
       °°°°°°°DI°°°°°°° Hercules and compatables)

       °°°°°°°DS°°°°°°°
       °°°°°°°SS°°°°°°° RETURN
       °°°°°°°ES°°°°°°° None
             
        
                Exceptions and Comments
             
             The  start of the line is either set by a move command (function
        23H), or else defaults to the  end  of  the  last  line  drawn,  thus
        successive  draw  commands  can be used to draw polygons with no need
        for any move commands for all but the first point of the  polygon  to
        be  drawn. The style of the line (white, black, or XOR) is set by the
        last issued move command until changed by another move command.
             
             









        __________________________________________________                   

        HERCBIOS.ASM                   PAGE 14                               


                          -------------------------------------------
             
             
           
             
                                    Sincerely,
             
             
             
             
                                    Douglas McDaniels
             
             





































        __________________________________________________