RTCLOCK, version 1.31, by Michael Conley
	 Release date: March 17, 1989

UPDATE:
	RTCLOCK version 1.31 adds the option to set the Real Time Clock
	from the DOS Clock.  In addition, automatic detection of color
	display has been added, as well as some minor refinements in the
	WWV display routines.

PURPOSE:
	RTCLOCK is intended for use on an AT class 80286 or 80386 machine.
	It will read the real time clock and set the DOS clock from it, 
	or read the DOS clock and set the real time clock from it, or it
	will allow the user to set BOTH the real time clock and the DOS 
	clock from the keyboard.	

	If you own the Heathkit "World's Most Accurate Clock" with a
	serial interface, RTCLOCK will allow you to set BOTH your
	real time clock and your DOS clock from WWV, the short-wave
	time data service provided by the U.S. government.

OPERATION:
	Five basic commands are supported, which may be entered either
	on the command line or, if no command is specified, from a menu
	within the program.

	<R> reads the real time clock, and sets the DOS clock.

	<D> reads the DOS clock, and sets the real time clock.

	<S> sets BOTH the real time clock and the DOS clock from
	    the keyboard.
	
	<W> sets BOTH the real time clock and the DOS clock from
	    serial data transmitted by the Heathkit "World's Most 
	    Accurate Clock."  Be sure to read SETUP for additional
	    configuration required for this option.

	<V> views the time data from the Heathkit "World's Most
	    Accurate Clock" until a key is pressed.  It does NOT
	    alter either of the system clocks.  Be sure to read
	    SETUP for additional configuration required for this 
	    option.	

SETUP:
	Commands <R>, <D> and <S> require NO configuration.

	Commands <W> and <V> require the installation of an RS232
	serial line from the Heathkit "World's Most Accurate Clock"
	to the computer.  See the clock manual for wiring information.
	Be sure to set the DIP switch inside the clock for the AUTO
	mode, which provides CONTINUOUS output from the clock.  The
	other mode would require manipulating the DTR line to request
	clock data, and is NOT supported by the program.  Also be sure
	to select an appropriate baud rate and program the correct year
	using the DIP switches inside the clock.

	The program must be informed of the baud rate and the COM port
	in either of two ways:

	1)  You may invoke the program and provide the configuration info
	    on the command line as follows:

		RTCLOCK W COM3 2400 [enter]

	    Allowable choices here are  W or V  for the program mode,
	    COM1 thru COM4 for the data port, and 300, 600, 1200, 2400, 
	    4800, or 9600 for the baud rate.  Other choices or missing 
	    info will produce an error message.

	2)  You may create an ASCII text file (an example is included
	    in this distribution) with the port and baud rate on the
	    SAME line.  Name this file RTCLOCK.CNF and place it in the
	    same directory from which the program will be run.  An 
	    example of the file contents would be:

		COM3 2400

	    Note: The parameters must be on the SAME line.

	Please also note that, if you enter the program with NOTHING on
	the command line (i.e., menu mode) you MUST provide RTCLOCK.CNF
	in order to use the W or V options, as these cannot be entered
	from the menu.  A sample RTCLOCK.CNF is included with this
	distribution.

SERIAL SETUP:
	This release supports COM ports 1 thru 4 and functions entirely 
	without interrupts.  This allows you to avoid the common problem 
	of "interrupt sharing," where COM1 and COM3 share IRQ4, while 
	COM2 and COM4 share IRQ3.

	We recommend that you set your serial I/O card for NO interrupts 
	for the port selected for use with RTCLOCK to avoid possible con-
	flicts with other serial devices.  However, the program will run
	properly even in the event that interrupts are present on the port.

CONCLUSION:
	Your comments and suggestions are welcome.  Please contact the
	Charlatan's Cabin BBS (213) 654-7337 and leave a comment to the
	Sysop (that's me.)  

	A brief warning:  TEST the clock hookup using a communications
	program, such as Qmodem, to verify that it's hooked up and sending
	data correctly.  RTCLOCK will simply TIME OUT if there is no output
	from the clock in the W or V mode.  
	If the clock IS connected, but it cannot produce the correct time, 
	the program WILL gracefully exit with a message, so it can safely 
	be used in a batch file, provided the serial line is present.

						  Michael Conley