T U R B O    P O P

             Memory Resident PopUp Routines Version 1.8d
                     for Turbo Pascal Version 5.0

                          Copyright (c)1988
                       Ross Neilson Wentworth

                Custom software at reasonable prices!

                  THIS PACKAGE IS NOT PUBLIC DOMAIN

                          All Rights Reserved


                              DISCLAIMER

                    This software is provided without
                     warranty, expressed or implied.


The Turbo Pascal Units contained in this package will enable you to
quickly and easily create popup programs.  Also included is a very simple
windowing package.

All source code is included so that you may modify it to your hearts
desire.  Do NOT release modified versions of this package under any
circumstances.

Turbo Pascal Version 5.0 is required to use this package.  TASM 1.01
or MASM 5.1 is required to to re-assemble the low-level modules.  Minor
modifications are required for proper assembly with MASM.

If you find this code useful, please send $20 to the address below or
make a $20 donation to the "The Historic Oaks Foundation", located in
Agoura Hills and Novato, California.  Let me know if you make the
donation and you will receive full credit for registration (receipt or
copy of cancelled check required).

If you use this code in any commerical program this payment is required.
Shareware is considered commercial upon receipt of first registration.

                   Ross Neilson Wentworth
                   Serendipity Software
                   1422 Elkgrove Circle, #3
                   Venice, CA  90291
                   (213)399-1244


Features of This Package
========================

  o Easily create memory resident popup programs (SideKick-like).
  o Automatic program detection to prevent multiple loading.
  o Allows TSR's with conflicting hot-keys
  o Simple program removal
  o Uses proven TSR techniques.
  o All DOS functions allowed from within resident program (except
    I/O redirection), you can safely access the disk!
  o No load-order limitations (except those imposed by other TSR's).
  o Low code overhead, slightly over 1k EXE size increase to standard
    application.

One of the problems with writing popup programs is DOS is not reentrant.
That is, if you popup while DOS is busy you are very likely to crash the
system.  This package does all the necessary checking and will only popup
when it is safe.  This allows your program to do virtually anything including
file access.  The one limitation is that it can not allocate additional memory.
You can still use heap memory, just don't use the DOS function to allocate or
modify a current memory block.

To guarantee a safe pop-up program it is necessary to grab hold of several
interrupt vectors.  When the program is first initialized the following
vectors are intercepted:

     08h      timer
     09h      keyboard
     13h      disk i/o
     28h      backprocess
     2Fh      multiplex

When the program is popped up, two additional vectors are also intercepted:

     23h      control-break
     24h      critical error

In addition, a couple of other internal values are changed while the
program is active:

     The Disk-Transfer-Area is saved and the popup's installed
     The BREAK status is saved then turned off

These four items are restored when the TSR relinquishes control.

A sample program is provided that shows how to implement a popup program.

===============================================================================
Contents of POPUP:

  Function Installed(OurID : Byte) : Byte;

    Given a unique program ID number, this function returns zero (0) if
    the program has not already been installed.  A nonzero value indicates
    it has already been installed or an error has occured:

       1 : PRINT.COM detected.  Under DOS 2.x, the TSR must be loaded
           before PRINT.COM.
       2 : The program is already installed.
       3 : Internal error, can't install.

    Error 3 is usually caused by a poorly designed TSR program that has
    already been loaded into memory.  Try loading your program before any
    others.  Experimenting with the order of loading should point out the
    bad TSR.

  Procedure StayResident(OurID : Byte;
                         ProgramAdress : Pointer;
                         HotKeyOne,HotKeyTwo: Word);

    HOTKEYONE and HOTKEYTWO are your key combinations that will activate
    your program.  If you only want one hotkey then use 0 for HotKeyTwo.
    It is of type WORD where the low byte is the scan code and the high
    byte is the shift status (ALT, CTRL, SHIFT, etc.  See below).
    ProgramAddress is a pointer to your popup procedure that you want
    called.  Precede the program name with an '@' to pass a pointer.

    StayResident($69,@NotePad,Alt+LeftShift + $20,0);  {ALT-LeftShift-D }
                                                       {no second hotkey}
    The shift status values are documented below.

    OurID is a unique number for your resident program.  Each different
    TSR that you write should have a different ID number.  For maximum
    compatibility, you should allow the user to change the ID number,
    perhaps by using a 'command-line' option, i.e. /I=155.  MS-DOS reserves
    ID numbers 0 to 80h for internal use.

  Procedure ReleaseBlock(Segment : Word);

    This inline macro releases the block of memory given a segment number.

  Procedure ReleaseEnvironment;

    Releases the block of memory holding the program's environment.  It keeps
    track of whether it has already been called so that multiple calls will
    not be harmful.

===============================================================================
Contents of UNHOOK:

  Function Installed(MultID : Byte) : Boolean;

    Returns TRUE if the resident program is in memory.

  Function OKToUnload(MultID : Byte) : Boolean;

    Returns TRUE if it is safe to unload the resident program from memory.

  Procedure RemoveProgram(MultID : Byte);

    Releases the memory and restores the interrupt vectors used by the
    resident program.

===============================================================================
Contents of WINDOWS:

  Procedure MakeWindow(X1,Y1,X2,Y2,Foreground,Background : Word;Border : BorderType);

   This procedure saves the current screen memory and creates a bordered
   window.  X1, Y1, X2, and Y2 are the same values used by Turbo's WINDOW
   procedure.  Foreground and Background are the color attributes of the
   window.  Border is the type of border desired.  Possible border types
   are:

          NONE          -   no border
          SINGLE        -   single line
          DOUBLE        -   double line
          DOUBLETOP     -   double top lines, single side lines
          DOUBLESIDE    -   double side lines, single top lines
          SOLID         -   solid block (space character)

    Example useage:

            MakeWindow(5,5,30,10,Black,White,Double);

  Procedure DrawBox(X1,Y1,X2,Y2,Forground,Background : Word;Border : BorderType);

    Works just like MakeWindow but doesn't save the underlying screen and
    doesn't use a matching RemoveWindow.

  Procedure RemoveWindow;

    Removes the current top window, does nothing if there isn't any windows
    defined with the MakeWindow procedure.

  Procedure SetCursor(Cursor : Word);

    Sets the cursor shape.  Some software packages turn off the cursor
    so this is provided so you can set your prefered cursor shape.  The
    windowing package saves the cursor shape of the underlying screen so
    there is no need to restore it.

  Var VideoMode : Word;

    A DOS variable that holds the current video mode.  Use this to test
    for and avoid activating in graphics modes.

===============================================================================
SAMPLE PROGRAMS
===============

POPDICE is a fully functional sample pop-up program.  After loading, pressing
ALT-LeftShift-D will pop-up a fancy dice rolling program designed for war
games and roll-playing games.

NODICE will remove POPDICE from memory if it is safe to do safe.  Alternately,
a second program, REMOVE, can be used to unload ANY resident program written
with this package.  REMOVE accepts a single I.D. number on the command line.
This is the same as the program's signature.

===============================================================================

Caveats
=======

You MUST handle all possible errors.  If at any time the program halts
due to a runtime, I/O, or critical error the system will probably crash.
Before the resident program is entered, POPUP.TPU's critical error handle
is restored so that you can query IOResult for errors.

Use the $M directive to reduce memory requirements.  Make a high guess of
memory requirements for your program then double or triple it.  Compile
and run the program to make sure it runs. If it doesn't increase memory.
If it does run decrease it.  Keep decreasing the memory until the program
crashes then increase memory and add a little extra for slop.

You should test the video mode when your routine is first run.  The windows
unit can not properly save graphics screens so you might want to beep and
exit.  You could, of course, write your own windowing package that can save
graphics screens.  This could be a problem with some of the new video modes
that have tremendous memory requirements.

Shift Keys
==========

RightShift  $01
LeftShift   $02
Control     $04
ALT         $08

ScrollLock  $10   { these four are not supported in this version }
NumLock     $20   {  "     "     "     "     "     "     "     " }
CapLock     $40   {  "     "     "     "     "     "     "     " }
Insert      $80   {  "     "     "     "     "     "     "     " }

The shift status values are defined in the interface portion of the PopUp
unit.  The values are already shifted to the left 8 bits to save you the
trouble.  Simple add the different shift keys you want to the scan code
and pass that value to StayResident.  For example, for a program to popup
when both shift keys are pressed as well as the period you would issue
the command:

       StayResident(@MyPopUp,RightShift + LeftShift + $34,0);

The coding of the popup routines makes undefined keys possible, thus
reducing the chance of keyboard confict.  For example the numeric pad
'5' (the center key) is undefined for most combinations.  This allows
you to use combinations such as (Control + LeftShift + $4C) with a
high degree of certainty that it won't conflict with other programs.

Keyboard Scan Codes
===================

0  $0B     6  $07     C  $2E     I  $17     O  $18     U  $16
1  $02     7  $08     D  $20     J  $24     P  $19     V  $2F
2  $03     8  $09     E  $12     K  $25     Q  $10     W  $11
3  $04     9  $0A     F  $21     L  $26     R  $13     X  $2D
4  $05     A  $1E     G  $22     M  $32     S  $1F     Y  $15
5  $06     B  $30     H  $23     N  $31     T  $14     Z  $2C

BS   $0E
ESC  $01
TAB  $0F
RET  $1C

-  $0C     `  $29
=  $0D     \  $2B
[  $1A     ,  $33
]  $1B     .  $34
;  $27     /  $35
'  $28

LeftShift   $2A
RightShift  $36
ALT         $38
CTL         $1D
Space       $39
CapLock     $3A

F1  $3B     F2  $3C     F3  $3D     F4  $3E     F5   $3F
F6  $40     F7  $41     F8  $42     F9  $43     F10  $44

NumLock     $45       ScrollLock  $46       Home        $47
UpArrow     $48       PageUp      $49       grey -      $4A
RightArrow  $4B       Center      $4C       LeftArrow   $4D
grey +      $4E       End         $4F       DownArrow   $50
PageDown    $51       Ins         $52       Del         $53

==============================================================================
Version History

1.8d 11 May 1989

     Added support for a second hotkey and streamlined some of the
     low-level assembler code.  Now requires TASM 1.01 to re-assemble
     POPUP.ASM.

1.8c 22 January 1989

     Minor bug in the window package was corrected that would cause
     window types of NONE not to be set properly.

1.8b 30 December 1988

     Faster box drawing in the WINDOWS unit by using assembler routine.
     When archive was updated several necessary files were inadvertantly
     left out.

1.8  3 November 1988

     Improved detection of unsafe unload conditions.  Minor bug fixed
     on saving and restoring the cursor shape.  Made changes to source
     so that it will assemble using Turbo Assembler.

1.7  16 October 1988

     Removed the READKEY procedure.  Instead, interrupt 16h is grabbed
     to prevent resident program lock-outs.  Changed to using interrupt
     08h instead of 1Ch.  For some reason, using the later with some
     programs would cause the system to lock up.

1.6  1 October 1988

     Added experimental unload procedure.  Minor cosmetic changes.
     Improved support for conflicting hot-keys.  Removed RestoreVectors
     and placed in a separate unit.

1.5  20 September 1988

     Code added to detect programs that have already been loaded, thus
     preventing multiple loading of the same TSR.  Minor bug fix.
     Documentation corrections.

1.4  31 August 1988

     All source code now included in the archive.  Removed the FREE unit
     due to problems.  Use Mark/Release instead.

1.2  21 March 1988

     Minor correction in the low-level popup code - not all of the
     registers were being saved.

1.1  13 March 1988

     Changed popup code so the user procedure is declared as FAR rather
     than as INTERRUPT.

1.0  Ported from Turbo Pascal 3.0, changed name, and restarted version
     number.

Previously:  Used a lot of INLINE code under Turbo Pascal 3.x.

REFERENCES
==========

Advanced MS-DOS, Ray Duncan, Microsoft Press

The MS-DOS Encyclopedia, Microsoft Press

Magazine articles too numerous to list.

Tidbits of knowledge gained from the Fido/Opus Network.

ACKNOWLEDGEMENTS
================

I wish to thank the many programmers who pioneered the development of
Terminate-and-Stay-Resident programs, on whom's shoulders I am standing.

===============================================================================

Legal Stuff
===========

Sidekick, Turbo Assembler, and Turbo Pascal are Trademarks or Registered
Trademarks of Borland International, Inc.