PLOTTER.DOC

Environmental Optics Inc. Mark V Photoplotter Specifications:


Photoplotters represent a superior technique for the preparation of 
phototooling for the fabrication of printed circuits.  Compared to pen 
plotters, photoplotters draw with a beam of light and do not skip or smear.  
Since they produce one to one art-work directly, further photographic reduction 
is not required, eliminating the possibility that lens distortions will produce 
misalignments.  Because this is a flat bed plotter, there is no accumulated 
skew as can occur in pen plotters which move the paper back and forth under a 
pen.  

For several reasons, a photoplotter can keep up in performance with a much 
faster pen plotter.  Since plotting is the final size there is an immediate 
gain over doing art-work 2X or 4X.  Further, this photoplotter contains 
apertures where a whole object, i.e. a component pad, is flashed onto the film 
at once.  

The Mark V is designed as a compromise between pen plotters which have the 
above problems, and traditional photoplotters which are ten to fifty times as 
expensive.  While of lower precision than more expensive photoplotters, we 
believe it offers sufficient precision for multi-layer and surface mount 
boards.  

The Mark V is light tight so that operation is possible with minimal dark room 
facilities.   All that is needed is a broom closet or similar space that can be 
made dark while film is loaded.  

The package includes a complete IBM compatible XT type computer which with the 
addition of a color monitor is suitable for operation of the DROEGE software.  
Included are a disk drive and adapter, 640k memory, serial and parallel ports, 
a clock calender, and a color adapter.   


Effective Plotting Area: ............. 17" x 22" 
                                       (430mm x 560mm) 

Maximum Plotting Speed: .............. 1 ips (25mm/second), axially
Non-Plotting Moves:  ................. 2 ips (50mm/second), axially

Distance Accuracy: ................... 0.05% of distance moved.
                                       (calibrated by software to 0.01%)

Repeatability: ....................... +/- 0.002" (0.05mm)

Step Size: ........................... 0.001" (0.025mm)

Apertures: ........................... 16 Electronicly Selected

Aperture Size: ...................... 0.005" to 0.150" (.127mm to 3.81mm) or 
                                       to customer specification.  Apertures 
                                       may be used as draws or flashes.  
                                       Aperture plate may be changed in the 
                                       field.  

Size: ................................ 32" x 25" x 7" (812mm x 635mm x 178)

Interface: ........................... Direct drive from plot files stored on 
                                       floppy disk.  Files may be generated 
                                       from the DROEGE CAD program or down 
                                       loaded from the RS-232 interface.  Files 
                                       may also be ported by floppy disk.
                            
Film Required: ....................... LPF-7 or equal speed lithographic film.

Bearings: ............................ Hardened and ground precision steel 
                                       shafts with linear ball bearing 
                                       bushings.  

Note: Specifications are preliminary.