WD1002A-WX1

                           Winchester Disk Controller

          WD1002A-WX1, feature F300R - Half-slot size hard disk controller 
          card with an ST506/ST412 interface.  It supports 2 MFM drives 
          with up to 16 heads and 1024 cylinders and is jumper 
          configurable for secondary addressing and default drive tables.  
          Built in ROM BIOS supports non-standard drive types, virtual 
          drive formatting, dual drive operation, bad track formatting and 
          dynamic formatting.  This board features a power connector for 
          filecard applications and it will also operate in AT systems. 
          Please note that this controller card will be unavailable from 
          the manufacturer (Western Digital) after March, 1989. 

          The following is a list of the most common hard disk drives 
          which have been found to be compatible with the WD1002A-WX1.  
          For a more complete list of drives and their parameters, return 
          to the STORAGE PRODUCTS menu.

          Controller:  WD1002A-WX1

          Drive                                      Formatted Capacity

          Western Digital - WD262                         21 Megabyte
                          - WD362                         21 Megabyte

          Tandon          - TM252                         10 Megabyte
                          - TM3085                        71 Megabyte

          Seagate         - ST125                         21 Megabyte
                          - ST225                         21 Megabyte
                          - ST251                         42 Megabyte
                          - ST4096                        80 Megabyte
                          - ST4038                        38 Megabyte

          NEC             - D5126                         20 Megabyte
                          - D5146                         40 Megabyte

          Miniscribe      - 3650                          42 Megabyte
                          - 8425                          21 Megabyte

          Micropolis      - 1304                          40 Megabyte

          Maxtor          - 1085                          71 Megabyte
                          - 1140                         119 Megabyte

          CMI              - 3426                         20 Megabyte
                          - 6640                          33 Megabyte

          CDC              - 94155-36                     36 Megabyte