Western Digital is a registered trademark of Western Digital 
     Corporation; IBM PC, AT and XT are registered trademarks of the 
     International Business Machines Corporation; MS DOS, OS2 and PC DOS 
     are registered trademarks of Microsoft Corporation.

                                   WD1002A-WX1
                                   User Guide

     Getting Started:

     Installation of the WD1002A-WX1 requires four steps:  1) Confirming 
     BIOS ROM type; 2) Checking or setting jumpers;  3) installing into 
     host computer; 4) formatting the disk drives.  To complete 
     installation, you will need the following:

     Two cables (3 if using two drives); MFM type drive; screwdriver; 
     MSDOS Version 2.0 or later; *DEBUG utility; *FDISK utility; *FORMAT 
     Utility.  (*normally included with MSDOS); 

                                     WARNING
                 HANDLE THE CONTROLLER BY THE ENDS OF THE BOARD
                SOME OF THE CHIPS ARE STATIC SENSITIVE AND DAMAGE
                  MAY OCCUR IF THE BOARD IS INCORRECTLY HANDLED

                                 Confirming BIOS

     At location U12, please confirm that your WD1002A-WX1 BIOS ROM is 
     part number 62-000094-followed by any three numbers  (this BIOS ROM 
     is referred to as Western Digital's SUPERBIOS).  If your controller 
     has any other BIOS, contact Technical Support at 1-800-777-4787.

     Prepare Controller

                      ÚÄÄÄDrive 0ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                      ³ Data Cable   34pin Control Cable   ³
                      ³  ÚÄÄJ2ÄÄ¿    ÚÄÄÄÄÄÄJ1ÄÄÄÄÄÄÄ¿     ³
                ÚÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÙ    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ     ³
                ³        ÚÄÄJ3ÄÄ¿                          ³
                ³        ÀÄÄÄÄÄÄÙ                  123     ³
                ³         Drive 1            ÚU2Ä¿ ùùùW8   ³
                ³       Data Cable           ÀÄÄÄÙ ùùùW4   ³
                ³                             ù1           ³
                ³                          W6 ù2    ùù5    ³
                ³         BIOS                ù3    ùù6    ³
                ³       ÚÄÄÄÄÄÄÄÄÄÄ¿                ùù7    ³
                ³       ³          (                ùù8 S1 ³
                ³       ÀÄÄÄÄÄÄU12ÄÙ                ùù4    ³
                ³                                   ùù3    ³
                ÀÄ¿           ÚÄ¿                   ùù2    ³
                  ³           ÀÙ                   ùù1    ³
                  ÀÄÄÄÄÄÄ¿A31  J4                 A1ÚÄÄÄÄÄÄÙ
                         ³        WD1002A-WX1       ³      
                         ÀÁÁÁÁÁÁÁÁÁÁÁÁÁÁÁÁÁÁÁÁÁÁÁÁÁÁÙ      
                                 Jumper Settings

     Verify that the host computer contains a 135 watt power supply.  
     Verify that the jumper settings on the controller board are correct.  
     Modification of factory jumper settings is rarely necessary.  For 
     jumper settings on W4, W6 and W8, refer to Table 1; Jumper settings 
     for S1 are located on Table 2.

     CLOSED:  Jumper (small shorting pens) is installed
     OPEN:    Jumper is not installed.

                                     Table 1

                Pin
     Jumper     Connects   Status

     W3         Closed     BIOS ROM Enabled
                Open       BIOS ROM Disabled

     W4         2-3        Device Address 320H
                2-1        Device Address 324H
     W6         2-3        Reduced Write Curent (8 Heads)
                2-1        Head Sel 3 (16 heads)
     W8         2-3        Standard factory setting.  First or only
                           disk controller in system.
                1-2        Second disk controller in system.  Requires
                           modification of W4.

     The following S1 jumper settings are for standard 10/20 megabyte hard 
     disk drives using default settings in the SUPERBIOS.  If you are 
     using a standard 10/20 megabyte drive, you may refer to the 
     Simplified Formatting Instructions after completing the hardware 
     installation procedures.  If your drive is a non-standard drive (i.e. 
     20 megabyte drives with other than 4 heads/615 cylinders, or hard 
     disk drives with a formatted capacity greater than 20 megabytes) you 
     will need to refer to the Dynamic Formatting instructions after 
     completing the hardware installation procedure.  

     If you do not know your drive parameters, return to the STORAGE 
     CONTROLLERS menu to access a listing of the most common drives and 
     their parameters which we have provided for your convenience.  If 
     your drive is not listed, refer to your drive manual or contact the 
     manufacturer.

                                     Table 2
                               S1 Jumper Settings

                           10Meg Drive     10 Meg Drive       Standard
                           4Hds/306 Cyl    2Hds/615 Cyl       20Meg Drive

     S1-1                  Open            Closed             Open
     S1-2                  Closed          Open               Open
     S1-3                  Open            Closed             Open
     S1-4                  Closed          Open               Open
     S1-5                  Open            Open               Open
     S1-6                  Open            Open               Open
     S1-7                  Open            Open               Open
     S1-8*                 Open            Open               Open
     S1-8**                Closed          Closed             Closed

     *XT Mode
     **AT Mode

     Now that you have verified the jumper settings, you are ready to 
     install the controller and drive into your host computer.

                                     WARNING
                        MAKE SURE COMPUTER IS TURNED OFF
                           AND POWER IS DISCONNECTED 

                  Installation of Controller into Host Computer

     Remove blank expansion slot bracket and save for future use.  The 
     screw will be used to hold the controller board into place.  

     INSTALL CONTROLLER INTO ANY AVAILABLE SLOT EXCEPT SLOT 8  

     Connect the 34-pin (wide control cable) connector to J1 on the 
     controller board.  Make sure that Pin 1 of the cable connector goes 
     to Pin 1 on the controller board.  Pin 1 of the cable connector is 
     typically located on the color coded side of the cable.

     Connect the 20-pin (data cable) to J2 (Drive 0 Data Connector) on the 
     controller board.  Make sure that Pin 1 on the cable is connected to 
     Pin 1 on the controller board.

     If a second drive is being installed, connect the Drive 1 data cable 
     to J3.

     Verify that the disk drive(s) is(are) installed properly.  This 
     includes correct placement of drive select jumpers and drive 
     terminator installation.  Refer to the disk drive installation manual 
     for further information.  DO NOT USE THE RADIAL SELECT OPTION.

     Install the drive(s) per manufacturer's instructions.

                                     CAUTION
                WHEN ROUTING CABLES, BE CAREFUL NOT TO PINCH
                THEM.  CABLES MUST NOT GET CAUGHT BETWEEN THE
                COVER AND THE BOARDS, NOR SHOULD THEY OBSTRUCT
                ANY AIR FLOW PATH FROM FANS OR VENTS.