Western Digital is a registered trademark of Western Digital 
     Corporation; IBM PC, AT and XT are registered trademarks of the 
     International Business Machines Corporation; MS DOS, OS2 and PC DOS 
     are registered trademarks of Microsoft Corporation.

     SIMPLIFIED FORMATTING INSTRUCTIONS (For Use With Standard 20 Megabyte 
     hard disk drives)

     The format instructions that you follow are simple procedures to tell 
     the computer that you have either one or two Winchester disk drives 
     installed.  Formatting is done in three steps:

          1.  Low level format...Using DEBUG utility;
          2.  FDISK (partitioning)...using FDISK utility;
          3.  High level format...using Format utility

          *These utilities are normally supplied for DOS.  Refer
          to your DOS manual for indepth instructions on these
          utilities.

                                     CAUTION
                    THE FOLLOWING LOW-LEVEL FORMAT PROCEDURE
                    WILL DESTROY ALL DATA ON YOUR HARD DRIVE
                      BACK-UP THE DATA ON YOUR DRIVE BEFORE
                    CONTINUING WITH LOW LEVEL FORMAT ROUTINE.

     DEBUG Utility

     1.  At the A>prompt, load and run the DOS DEBUG Utility by typing 
     DEBUG followed by a RETURN.  "CR" denotes a carriage return or ENTER.

     2.  FOR IBM SYSTEMS ONLY:  At the DEBUG prompt, which is a hyphen (-)
     verify that the system BIOS is 10-27-82 or later by typing in the 
     following command line:

                      -d f000:fff5 fffc

     3.   At the debug prompt, start the low level format program by 
     typing the following command line:

                      -g = c800:5 CR (for primary controller)
                      -g = ca00:5 CR (for secondary controller)

     4.   The Super BIOS format program displays the following message:

          Super BIOS Formatter Rev. 2.4 Copyright Western Digital
                                   Corp. 1987
                               Current Drive is C:
                     Select new Drive or RETURN for current

     Enter your choice of drives at this point.  The program continues:

                             Current Interleave is 3
                  Select new Interleave or RETURN for current.

     Enter your choice of interleave at this point.  The recommended 
     interleave is 3.

             Are you dynamically configuring the drive - answer Y/N

     Answer: No

              Are you virtually configuring the drive? - answer Y/N

     Answer: No

                    PROGRAM DISPLAYS INITIATE FORMAT MESSAGE

               Press "Y" to begin formatting drive (C or D) with 
                  interleave of 03 (or value you entered above)

     If any key other than "Y" is typed, the program displays the 
     following message and returns the operator to DOS:

                      Nothing done exit -
                      returning to system ...
                      A>

     If an error occurs while formatting, the program immediately 
     terminates, displays the following error message, and returns the 
     operator to DOS.  Refer to Table 5 (Error Codes).

                      Error---completion code XX

     If "Y" is typed, the Super BIOS program initiates the low level 
     format.  The following message indicates the Super BIOS is formatting 
     the drive:
                      Formatting. . .

     The Super BIOS displays the following message if there are no 
     resulting errors:

                      Do you want to format bad tracks?  Answer Y/N

     Answer:  No

     If no errors occurred, the Super BIOS ends execution of the low level 
     format with the following message:

                      Format Successful
                      System will now restart
                      Insert DOS diskette in drive A:
                      Press any key when ready.

     5.   If you have a second hard drive.  Repeat step 4.

     6.   Load and execute the DOS FDISK utility for both drives (follow 
     instructions in DOS manual).

     7.   Load and execute the DOS FORMAT utility for both drives (follow 
     instructions in DOS manual).

     DYNAMIC LOW LEVEL FORMATTING INSTRUCTIONS

                                     CAUTION
                    THE FOLLOWING LOW LEVEL FORMAT PROCEDURE
                    WILL DESTROY ALL DATA ON YOUR HARD DRIVE
                      BACK-UP THE DATA ON YOUR DRIVE BEFORE
                    CONTINUING WITH LOW LEVEL FORMAT ROUTINE.

     The format instructions that you follow are simple procedures to tell 
     the computer that you have either one or two Winchester disk drives 
     installed.  Formatting is done in three steps:

          1.  Low level format...Using DEBUG utility;
          2.  FDISK (partitioning)...using FDISK utility;
          3.  High level format...using Format utility

          *These utilities are normally supplied for DOS.  Refer
          to your DOS manual for indepth instructions on these
          utilities.

     DEBUG Utility

     1.  At the A>prompt, load and run the DOS DEBUG Utility by typing 
     DEBUG followed by a RETURN.  "CR" denotes a carriage return or ENTER.

     2.  FOR IBM SYSTEMS ONLY:  At the DEBUG prompt, which is a hyphen (-)
     verify that the system BIOS is 10-27-82 or later by typing in the 
     following command line:

                      -d f000:fff5 fffc

     3.   At the debug prompt, start the low level format program by 
     typing the following command line:

                      -g = c800:5 CR (for primary controller)
                      -g = ca00:5 CR (for secondary controller)

     4.   The Super BIOS format program displays the following message:

          Super BIOS Formatter Rev. 2.4 Copyright Western Digital
                                   Corp. 1987
                               Current Drive is C:
                     Select new Drive or RETURN for current

     Enter your choice of drives at this point.  The program continues:

                             Current Interleave is 3
                  Select new Interleave or RETURN for current.

     Enter your choice of interleave at this point.  The recommended 
     interleave is 3.

             Are you dynamically configuring the drive?  Answer Y/N

     Answer: Yes

     In order to continue, you will need to know the parameters of your 
     drive.  For your convenience, we have prepared a list of common hard 
     disk drives and their parameters.   By returning to the Storage 
     Controller menu, you may access the drive list.  If your drive is not 
     listed, you will need to refer to your drive manual or contact your 
     drive manufacturer for this information.  You will need to know the 
     following:  Number of heads, number of cylinders, starting reduced 
     write current cylinder, write precompensation cylinder, maximum 
     correctable error burst length, step rate code.

     The Super BIOS program displays the initiate dynamic configuration 
     message:
                     Key in disk characteristics as follows:
                            ccc h rrr ppp ee o where
                ccc = total number of cylinders (1-4 digits)
                h = number of heads (1-2 digits)
                rrr = starting reduced write current cylinder (1-4 digits)
                ppp = write precomp cylinder (1-4 digits)
                ee = max correctable error burst length (1-2 digits) range 
                     = 5 to 11 bits, default = 11 bits
                o = CBB option byte, step rate select (1 hex digit) range
                    = 0 to 7, default = 5 refer to controller and drive
                    specification for step rates.

     Enter each value separated by a space and follow the complete entry 
     with a RETURN.  Enter physical cylinder values. 

              Example for ST 251:
                      820 6 821 410 11 5 (CR)

     Program Displays:

     Are you virtually configuring the drive - Answer Y/N

     Explanation:  Current versions of DOS allow no more than 32 megabytes 
     per drive.  Therefore, a 40 megabyte drive may be divided into two 
     virtual drives using the virtual option.  Therefore, if you have a 
     hard disk drive larger than 32 megabytes, you will want to answer Yes 
     to the above question in order to fully utilize your drive's 
     capacity.  For example:  If your drive has a 40 megabyte formatted 
     capacity you may chose to virtually split the drive into either two 
     20 megabyte drives or a 30 megabyte drive and a 10 megabyte drive.  

     NOTE: WITH DOS VERSION 3.30 OR LATER, SAY "NO" TO VIRTUAL 
     CONFIGURATION AND DO PARTITION UNDER FDISK UTILITY.

     If you answer Yes to virtual configuration, you may not attach 
     another physical drive to the controller or add another Winchester 
     controller to the system.  Also, do NOT repeat this low level format 
     procedure for logical drive D.

     The program continues with the following display:

                Key in cylinder number for drive split as vvv ...
          where vvv = number of cylinders for drive C: (1-4 digits)

     Enter the ending cylinder number for drive C:.  Drive D: uses the 
     remaining cylinders.  

     The program continues with the following display:

          Press "Y" to begin formatting drive (C or D) with
          interleave of (03 or value entered above).

     If any key other than "Y" is typed, the program displays the 
     following message and returns the operator to DOS:
                Nothing done exit -
                returning to system...

     If an error occurs while formatting, the program immediately 
     terminates, displays error code and returns operator to DOS.  See 
     Table 3 for error codes.

     If "Y" is typed and there are no errors, the following message 
     appears:
                Formatting....

     Super BIOS now displays the following message:
          Do you want to format bad tracks - answer Y/N

     Note:  A list of bad tracks is normally found attached to your 
     drive.  If "Y" is typed, you will be prompted to enter the bad tracks 
     (see example below).  However, because of the logical addressing used 
     by DOS, marking an entire track bad will result in more than one 
     logical address being marked bad.  As DOS can only accept a limited 
     number of defects, a drive with excessive media defects may cause the 
     FORMAT program to terminate with an error.  The displayed error is 
     typically, "TRACK 00 BAD - DRIVE UNUSABLE."

     If you do choose to format bad tracks by pressing "Y", the program 
     will display the following:
          Key in bad track list as follows:
          ccc h...
          where
          ccc = bad track cylinder number (1-4 digits)
          h   = bad track head number (1-2 digits)

     Type in the cyliner and head numers for the bad tracks separated by a 
     space and press RETURN.

     EXAMPLE:  160 1 161 2 304 3 223 4 223 2 CR

     The program continues:
                More? Y/N

     Enter extra bad tracks as above or terminate bad track formatting by 
     typing:    N  CR

     The program continues:
                BAD TRACK MAP
          TRACK ADDR          PROBLEM
          ccc H           USER-SUPPLIED

     If no errors occurred, Super BIOS message reads:
          Format Successful
          System will now restart
          Insert DOS diskette in drive A:
          Press any key when ready.

     5.   Repeat Step 4 if a second physical drive is to be formatted.  Do 
     NOT virtually configure the second physical drive.  Do NOT run the 
     low level format on the second logical drive if drive C: was 
     virtually configured.

     6.   Load and execute FDISK utility for both drives regardless of 
     virtual or physical configuration.  FDISK partition data should 
     indicate proper split of cylinders for both drives.  Follow DOS 
     instructions for using this utility.

     7.   Load and execute DOS FORMAT utility for both drives, regardless 
     of virtual or physical configurations.  Follow DOS instructions for 
     using this utility.

                              Table 3 - Error Codes

          Code        Completion Code Summary

          01          Bad Command
          02          Address Mark Not Found
          04          Sector Not Found
          05          Reset Failed
          07          Set Parameters Failed
          09          Attempt to DMA across 64K boundary
          0B          Bad Track
          10          Correctable Data Error
          11          ECC Error Corrected
          20          Controller Failure
          40          Seek Failure
          80          Time-out
          BB          Undefined Error
          FF          Read Status Failed

                                 AT INSTALLATION

     Super BIOS expands the compatibility of the WD1002A-WX1 to the IBM PC 
     AT.  For AT operation, the system must contain system BIOS ROMs 
     #6181028 and #6181029 (1981-1984) for use with DOS version 2.1 or 
     system BIOS ROMs #6480090 and #6480091 (1985) for use with DOS 3.0, 
     3.1 and 3.2.  

     Drives operating on the WD1002A-WX1 are not programmed into the AT's 
     configuration memory.  Therefore, configure the IBM Advanced 
     Diagnostic program, Setup, for no (zero) drives and set the 
     controller jumpers as the primary controller (W4 2-3; W8:2-3).  

                                 Troubleshooting

     Eliminate obvious fault causing problems, i.e., reversed cables, 
     overloaded system power supply, improper drive selection, etc.

     Problem:  Winchester activity LED is always lit.

     Solution:  Cables may be reversed

     Problem:  Both Winchester activity LEDs come on at same time.

     Solution:  Improper drive select or termination.  Consult your drive 
     or system manual for information.

     Problem: "Nothing done exit" appears when starting the low level 
     format program.

     Solution:  "Y" was not pressed. Start at Step 1 of the format 
     instructions.

     Problem:  Controller formats 10 MB of a 20 MB drive.

     Solution:  Check S1 settings.

     Problem:  System hangs with controller installed.

     Solution:  System BIOS may not handle Winchester disk.  Update system 
     BIOS.

     Problem:  "Error Reading Fixed Disk" when booting system.

     Solution:  DOS partition not active.

     Problem:  Slow and inefficient operation.

     Solution:  Normally due to incorrect interleave factor which may 
     require some experimentation (see Format instructions).  Interleave 
     factors are dependent on drive access time, controller operation, 
     host operating speed and system, as well as application program.

     Problem:  1701 or 01 Error Code

     Solution:  System BIOS does not support Winchester controller and 
     drive.  Overloaded power supply.  Update system BIOS (refer to format 
     instructions to check the BIOS data).  Install 135 W power supply.  
     Finally, ensure that W3 enables controller BIOS.
     Problem:  Error Code 20

     Solution:  Controller component malfunction.  Consult your dealer.  
     Make sure you properly installed the controller in the expansion 
     slot.  Reversed cables.

     Problem:  Error Code 40

     Solution:  Wrong CCB option byte selected.  Refer to format 
     instructions to check CCB option byte.  Not enough host power for 
     drive.  Install 135 W power supply.

     Problem:  Error Code 80

     Solution:  Not enough drive power.  Check cables, drive select 
     jumpers, and drive termination.  Check drive.

     Problem:  Western Digital Technical Support line is always busy.
     Solution:  Consult your dealer first.  Use our technical support line 
     only if you or your dealer's troubleshooting failed.