{--------------------------------------------------------------}      
     {                     BREAK-PM                                 }      
     {                                                              }      
     {        PRINTMASTER,PRINT SHOP,BASICA GRAPHIC CONVERTER       }      
     {                                                              }      
     {    Input: *.SDR or *.NAM  [ Names of Shape ]                 }      
     {           *.SHP or *.DAT  [ Shape file ]                     }      
     {   Output: "shape".BSG     [BASIC file]                       }      
     {--------------------------------------------------------------}      
                                                                           
         This program will convert a PRINTMASTER graphic file into a       
       PRINT SHOP graphic file, or PRINT SHOP to PRINTMASTER. It will      
       also break up either one and convert them to BASICA graphic         
       arrays.                                                             
                                                                           
          Printmaster graphic files consist of 2 seperate files. A         
       'name file' with the extension of .SDR and a 'graphic file'         
       with the extension of .SHP .                                        
                                                                           
          The name file is an ASCII text file containing the names         
       for each graphic in the shape file. A name consists of a            
       record with the length of 16 bytes. If a name is less then 16       
       bytes, the unused positions are filled with nuls ($00).             
                                                                           
          Printmaster graphics are 88 dots wide by 52 dots high. They      
       are stored in a binary file one after anouther. This takes up       
       572 bytes. Added to this are four bytes at the start of each        
       graphic and one byte at the end (or between each graphic) for       
       a total of 576 bytes per graphic. The first 4 bytes consist of      
       $0B (width in bytes of graphic), $34 (54 bits high), $58 (width     
       in bits) and $00 (nul byte). The last byte between graphics is      
       also a $00.                                                         
                                                                           
          Print Shop's 'name file' is exactly the same as Printmaster's    
       but with the extension of .NAM . The Print Shop graphic file has    
       the extension of .DAT and is the same format as a .SHP file with    
       exceptions. The four bytes before each graphic and the last byte    
       between graphics is missing. In order for Print Shop to "see"       
       the files the filename must start with "GR". The program will add   
       "GR" to the front of the file name and chop off the end if greater- 
       than 8 characters. ie: the PRINTMASTER file STANDARD.SHP would      
       convert to a PRINT SHOP file GRSTANDA.DAT.                          
                                                                           
          The BASICA format for the graphic is an array with the first     
       two bytes the width of the graphic in bits ($58,$00). The second    
       two bytes is the highth in bits ($34,$00). The rest of the array    
       is the graphic. This file can be used in BASIC program with the     
       PUT command. To use the graphic in FONTASY use the load block       
       function.                                                           
                                                                           
          To use the program just run PM-PS-BS.COM and the startup menu
       will begin. Select which conversion. The conversion screen will
       then appear. Enter the filename (no .EXT) and the program will
       start. If you wish to stop before all files are converted just hit
       any key and the program will stop after finishing the current 
       graphic. After the conversion is finished you will be returned to
       the start-up menu.  
             
                This software is placed into the public domain by:         
                                                                           
                              John Paul Michalski                          
                          Infinity Engineering Services                    
                              322 W. Palomino Dr.                          
                              Chandler, AZ   85224                         
                                                                           
                              J.MICHALSKI on GEnie