X.00 Low Level Communications Driver

                         X.00 Copyright (c) 1987 by Raymond L. Gwinn
                                 12469 Cavalier Drive
                              Woodbridge, Virginia 22192
                                 All rights reserved

          You  are  granted   a  conditional  license  to  use  X00.SYS  in
          conjunction with  the Opus Computer-Based Conversation  System by
          Wynn Wagner III and other programs distributed with conditions of
          use similar to  that of Opus.  The user of  X00.SYS must meet the
          conditions of both  the legitimate use  of Opus and the  intended
          legitimate  use of Opus.   X00 may  not be distributed  by anyone
          where fees are charged  or where requests for donations  are made
          without  prior written permission of Raymond  L. Gwinn.  Further,
          the  author  reserves the  right  to  revoke  the license  and/or
          prohibit the use of X00.SYS by anyone for any reason at any time.

          The latest version of X00.SYS is available  for down-loading from
          The Renex BBS (FidoNet 109/106), 703-690-7950.

          Unlike most  software developers,  I make  Beta/test versions  of
          X00.SYS readily available.  This has  caused some confusion among
          various users.  That is, they are using beta versions of  X00.SYS
          and think  they are  using a  fully tested  (if there  is such  a
          thing) versions.   Starting  with version  1.02 of  X00.SYS I  am
          going to use the following method  in numbering the versions.  If
          the  version number ends  with an odd  number, then it  is a beta
          version.   If it  ends with an  even number, then  it is a tested
          version  that is  (relatively)  safe  for  general  use.    Then,
          versions 1.01, 2.15  and 1.07 would  be beta versions.   Versions
          1.00, 1.02, 2.00 and  2.14 would not be beta versions.   The beta
          versions will  always have  (and always  have had)  a lower  case
          letter appended to the version number.  For example, 1.01f is one
          way that you  will see beta versions  identified.  If you  find a
          problem in  a beta/test version, let  me know about  it by direct
          mail.

          X00.SYS  and associated  utilities comes  with  no guarantees  or
          warranties.  Use it at your own risk.




















          X00.SYS provides  enhanced/extended support of INT 14H functions.
          Documentation of the enhanced/extended functions  can be found in
          the included file FOSSIL.DOC by Vincent E. Perriello.

          DoubleDOS.  Since  writing X.00  I have learned  more about  DDos
          than I ever wanted  to know.  A few  rules for DDos users that  I
          know are: 1 -  Do not assign the comm ports  in DDCONFIG.SYS, 2 -
          Be sure to  execute CAPTURE after  you execute DOUBLEDO.   To  be
          safe,  execute CAPTURE  in  both partitions.    3 -  If  you have
          problems with your clock, try  the Defer option.  4 -  Be sure to
          replace  ANSI.SYS with  DBLDANSI.SYS.   For  some  reason, I  had
          problems if the  TOP partition  was not  delayed.   That is,  the
          BOTTOM partition must initialize before the TOP partition does.

          The semi-formal  syntax for  the statement  to be  placed in  the
          CONFIG.SYS file is as follows:

          DEVICE=X00.SYS <options>

          <options> ::= <none>  | <eliminate>  <defer> <port specs>  <baud>
          <size> <fifospec>

          <none> ::=

          <eliminate> ::= E{LIMINATE}

          <defer> ::= D{EFER}

          <fifospec> ::= NOFIFO

          <baud>  ::= B,<port number>,<baud rate>

          <size>  ::= R=<receive buffer size> T=<transmit buffer size>

          <receive buffer size> ::= <buffer size>

          <transmit buffer size> ::= <buffer size>

          <nasty> ::=N{ASTY}

          <buffer size> ::= 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 |
          32768

          <baud rate> ::= 300 | 1200 | 2400 | 4800 | 9600 | 19200 | 38400

          <port spec> ::= <number of ports> | <hardware port assignment>

          <number of ports> ::= 0 | 1 | 2 | 3 | 4

          <hardware port assignment> ::= <port number> = <assignment>

          <port number> ::= 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7

          <assignment> ::= <logical> | <absolute>













          <logical> ::= <comn> {, <irqn>}

          <comn> ::= <COM1> | <COM2> | <COM3> | <COM4>

          <irqn> ::= <IRQ0> | <IRQ1> ........ <IRQ15>

          <absolute> ::= <hex port address> , <irqn>

          <hex port address> ::= Any hex number 0 through 0FFFF.  The first
                                 character must be 0 through 9.
























































          The simplest statement for the CONFIG.SYS file is as follows:

               DEVICE=X00.SYS

          This statement will be all that  is required on the vast majority
          of systems.  It  says that you wish to support  one comm port and
          comm port will be specified by the application program.

          I have found  that communications ports  on some systems must  be
          initialized at boot time.  In  the simplest case shown above, X00
          knows that it  will serve  only one communications  port, but  it
          does  not  know which  comm port.    Thus, the  port will  not be
          initialized.  In many cases, the port to be used is COM1.  If the
          above statement is changed to:

               DEVICE=X00.SYS 0=COM1

          X00  then knows that you  intend to use COM1.   In this case, X00
          will initialize COM1 to a know state.  If you have problems, like
          "modem  not  responding"   then  try  specifically  stating   the
          communication port(s) you intend to use.

          DEFER - DO NOT USE THIS OPTION UNLESS YOU  UNDERSTAND ITS PURPOSE
          AND  YOU  NEED TO  USE IT.    IF YOUR  SYSTEM WORKS  WITHOUT THIS
          OPTION, THEN  DO NOT USE  IT.  If  you needed to use  this option
          with past versions of  X00.SYS then try this version  without it.
          Do not  automatically assume that  you still  need it.   At least
          half of the  reported problems  with X00 have  resulted from  the
          casual use of this option.  This option specifies that X00.SYS is
          not to take  any DOS interrupt  vectors during the boot  process.
          If DEFER  is specified  then CAPTURE  must be  executed prior  to
          executing OPUS.   Your  AUTOEXEC.BAT file  is the  best place  to
          execute  CAPTURE.   With  MultiLink,  CAPTURE should  be executed
          before multi-tasking is  started.   However, as with  99% of  all
          systems,  MultiLink systems  should work  correctly  (and better)
          without the  DEFER option.   Unless  you are  using some  strange
          software, you should not need to  use the DEFER option.  If  your
          system does not  boot correctly with  X00.SYS then try the  DEFER
          option followed by  CAPTURE in your  AUTOEXEC.BAT file.   X00.SYS
          only checks for the D in DEFER.

          ELIMINATE will eliminate  the 5  second commercial  at boot  time
          (which is a direct screen memory write).

          NOFIFO will  cause X00 to  NOT enable the  FIFOs of  the National
          16550.  Some Multi-Tasking systems have problems when the 16550's
          FIFOs  are  enabled.   NOFIFO  allows  the user  to  override the
          automatic use of the 16550's FIFOs by X00.

          Number of  ports.   When  you wish  to use  the default  IBM/Opus
          communication port addresses and IRQs,  you should simply specify
          the number of  ports that you wish to support (the default is 1).
          Although X00 V1.00 and up can support up to 8 ports, you can only












          specify 0 through 4 supported ports.  The reason is that there is
          only  4  defined ports  (COM1,  COM2,  COM3, COM4)  that  X00 can
          default to.  If you use the absolute method (described later) you
          can specify up to  8 devices.  X00 assumes that COM1 and COM2 are
          addressed  as originally  defined by  IBM.  The  default hardware
          characteristics of COM3 and COM4 are  03E8H, IRQ4 and 02E8H, IRQ3
          respectively.  This seems  to be a defacto standard,  although no
          real standard exists that I know of.

          With the software  that uses FOSSIL drivers today, 2 ports is all
          that can reasonably be used.  However, X00 allows you to make one
          or both of those ports COM3 and/or COM4 or non-standard hardware.























































          The T  and R options (or help, the sky is falling).  Trying to be
          all  comm drivers to  all protocols on  all computers (especially
          betas) is not easy.  The T and R options allow you to specify the
          size  of the transmit and receive buffers.   The buffer size must
          be a power of 2.  The sum total, in bytes, of all buffers can not
          exceed 48k bytes.  For example, DEVICE=X00.SYS T=32768 R=16384 is
          valid (only one port).  However, DEVICE=X00.SYS 2 T=16384 R=16384
          is not valid (2 ports each with a 16k transmit and receive buffer
          = 32k per port or  64k).  In the second example  the total buffer
          size  exceeds  the  maximum   of  48k.    X00  SHOULD   (but  not
          necessarily) beep the bell  and display an error message  at boot
          time if you attempt  to define too much buffer space.   Also with
          this option, the default buffer size has been increased to 4k (it
          was 1k) for both the transmit and receive buffers.

          The  <baud> option  allows you  to lock  the baud  rate from  the
          computer to the modem.  When this option is specified for a port,
          the baud rate from the computer to the modem will remain constant
          regardless  of  what  the  application  program  (such  as  Opus)
          requests the baud rate to be.  This option is to  accommodate the
          higher speed  modems like  the  Telebit TrailBlazer  and USR  HST
          modems.  When this option is used, RTS/CTS handshaking is implied
          (forced)  even  if  the  application  program has  not  requested
          RTC/CTS handshaking.   Both Telebit  and USR  recommend in  their
          manuals  that the  computer to modem  baud rate be  constant.  My
          personal experience has show that both modem types operate better
          when the  computer to modem baud  rate is faster than  the actual
          phone line baud rate.

          The <nasty> option  makes X00 get  very aggressive about  keeping
          the COMM  interrupts.  Many  multi-tasking systems and  some TSRs
          mess  around with the  COMM IRQs and  thus, slow things  down.  I
          finally figured out how to keep them  at bay.  However, the NASTY
          option may cause  problems on some systems.  If you are running a
          multi-line system, try  the NASTY option.  If  it does not crash,
          you will  probably see  improved throughput.   Running COMM  type
          code in LIM memory may crash with NASTY enabled.  The default for
          NASTY is disabled.

          The required  communications buffers  are allocated  dynamically.
          All code used  for initialization is  overlaid by the buffers  or
          released to DOS by  X00 when it completes initialization  at boot
          time.

          IRQs.  The AT's additional 8 IRQs are supported.  X00 can support
          multiple ports on  a single interrupt.   When multiple ports  are
          assigned to a single interrupt,  X00 will poll each of  the ports
          to find the interrupting device(s).

          If  you   plan  to  reassign   the  port(s)  to   a  non-standard
          configuration or use some  strange hardware, it is best  to think
          in  port numbers  instead  of COMn.    Most application  programs
          documentation refers  to  COM1  and  COM2.    However,  when  the












          application program communicates  with a FOSSIL driver,  it calls
          COM1 device/port 0 and COM2 is device/port 1.

          Some examples of CONFIG.SYS statements are as follows:

          DEVICE = X00.SYS E
          Which means one port, no commercial.

          DEVICE = X00.SYS 2
          Allocate  space  for buffers  (at  the  default size  of  4k) and
          provide support for COM1 and COM2.

          DEVICE = X00.SYS T=1024 R=4096
          One  port supported,  the transmit  buffer  is to  be 1k  and the
          receive buffer is to be 4k.

          DEVICE = X00.SYS 2 B,1,19200
          Same as the above except COM2 will always  operate at 19200 baud.
          COM1  will  operate  at the  baud  rate  set  by the  application
          program.

          DEVICE = X00.SYS 2 B,0,19200
          Same as  the above  except COM1  is fixed  at 19200.   COM2  will
          operate at the baud rate set by the application program.

          DEVICE = X00.SYS 2 B,0,19200 B,1,9600 NOFIFO
          In this example  the baud rate for  COM1 is locked at  19200 baud
          and COM2 is locked at 9600 baud.   Additionally, the FIFOs of the
          National 16550 will not be enabled.

          DEVICE = X00.SYS 0=COM3
          One port  supported but,  use COM3 on  IRQ4 (the default).   Opus
          will think (and  must be told in  the CTL file) that  it is using
          COM1 in this case.

          DEVICE = X00.SYS 0=COM3,IRQ4
          Exactly the same as above.

          DEVICE = X00.SYS 0=COM3,4
          Exactly the same as above.

          DEVICE = X00.SYS 0=COM3,IRQ1
          Same as above except IRQ1 is to be used.

          DEVICE = X00.SYS 0=COM4 1=COM3
          Two ports  supported, Opus thinks  COM4 is COM1 and  that COM3 is
          COM2.  Use the default IRQs for COM4 and COM3.

          DEVICE = X00.SYS 0=COM4 1=COM3 NASTY
          Exactly the same as the previous  example except the NASTY option
          is enabled.  Note that NASTY may cause problems on some systems.

          Now  some absolute assignment examples.   When hex port addresses
          are used, the IRQ must be specified.













          DEVICE = X00.SYS 0=0FE8,IRQ4
          Support one  serial (8250)  device with  a base  port address  of
          0FE8H and use IRQ4

          DEVICE = X00.SYS 0=3F8,IRQ4 1=2F8,IRQ4
          Support 2 serial devices at  the given hex port address and  both
          will interrupt on IRQ4.

          etc, etc, etc.

          If you are not confused by now, I am, so I'm giving up.























































          REVISION HISTORY

          V0.01
          A problem with transmit  interrupts, unique to some systems,  was
          corrected.  The supporting program CAPTURE.EXE was added.


          V0.02
          The  previously  unsupported  carrier detect  watchdog  code  was
          debugged.    A new  supporting  program, WATCHCD.COM,  was added.
          CAPTURE.EXE was changed to a COM program, now CAPTURE.COM


          V0.03
          Added  2  additional  functions  to  maintain compatibility  with
          OPUSCOMM.


          V0.04
          This version was kind of rushed out because I found a  dumb error
          and corrected it.   New FOSSIL  functions, BOOT, TIMER TICK,  and
          WATCHDOG were added.  The new FOSSIL  function were not tested to
          my satisfaction however,  the corrected  problem warranted a  new
          version  now.    If Opus  said  "OPUS!COMM  not responding"  with
          X00.SYS loaded, try again.


          V0.05
          This  revision  corrected some  problems  and represents  a major
          restructuring  of the code.  The 0 comm port, DEFER and ELIMINATE
          options were added.


          V0.06
          Added one  line  of code  to  correct a  problem  in one  of  the
          enhanced  INT  14H functions.    Function 8  incorrectly returned
          prior to the transmit buffer being empty.


          V0.07
          Henk Weavers (500/1)  reported a problem with  FOSSIL function 13
          which this version  corrects.  This is probably the one that gave
          SEAdog problems.   I have not been  able to get a  SEAdog version
          that uses  FOSSIL drivers, so I am not  able to test X00.SYS with
          SEAdog.


          V0.08
          This version  corrects no problems  (that I know  of).  I  did do
          some re-structuring and general cleanup.   I may have unknowingly
          corrected problem(s).  However, I now have SEAdog V4.0 running on
          my  system  (109/639)  under  MultiLink  (V4.0 also)  using  this
          version of X00.SYS.  I have  been running SEAdog in 2  partitions












          for 2 days  and all  (including mail  events) seems to  be as  it
          should  be.    I  have  also  crashed  mail  all over  the  world
          (literally) and entered messages in one partition while the other
          was sending mail.  You will most likely have to use the *x option
          in your BBS statement  in CONFIG.DOG.  Read the SEAdog manual for
          *x information.   I will document  and make available my  control
          files when time permits.




























































          V0.09n
          This version was never released for general use.  All versions of
          0.09n were/are Beta test versions for the generic (absolute  port
          assignments) features.   These features have not been widely used
          and probably still have problems.  If you are the type that likes
          some excitement in your life, try this:
                  DEVICE=X00.SYS 0=COM2
          or if you are running 2 ports
                  DEVICE=X00.SYS 0=COM2 1=COM1
          These statements effectively reverse the normal Opus assignments.
          Don't forget  to consider  the effect  on your  CTTY, IBMAUX  and
          WATCHDOG statements.   If you doubt that  Murphy lives, reversing
          the defaults will change your mind.

          As a side  note, I used  a ConnectCom 4  from Software Link  (the
          same people that sell MultiLink) to  do all of my testing of  the
          generic functions.  The  Software Link is located in  Atlanta Ga.
          their phone number is 404-998-0700


          V1.00
          I think X00.SYS is now solid enough to be called version one.  At
          least on my system, the glitches, crashes, strange conditions and
          problems have been corrected or explained as not an X00 problem.

          The major enhancements in V1.00 is the addition of the ability to
          specify comm ports in hardware as well as conventional terms.

          On  the  minor side,  the code  has  been streamlined  for faster
          execution in anticipation of the faster modems that are  starting
          to appear  in the  net.   Also, some  problems  in the  interrupt
          service routines have been corrected.  These problems would cause
          lock ups under certain conditions.

          NOTICE NOTICE NOTICE NOTICE NOTICE NOTICE NOTICE NOTICE
          The command line  to invoke  WATCHCD V1.00 is  changed with  this
          release of X00.SYS.  Read the WATCHCD docs.






























          V1.02
          Added some wierd things the keep  SEAlink from getting locked up.
          If you have seen "too many errors" or otherwise had problems with
          SEAlink transfers, this version of X00.SYS  may clear it up.  The
          problem really showed up  when using high speed modems  with high
          speed computers.

          Added the locked baud rate option.

          Cleaned up  some problems  in the  parsing of  the options  line.
          Previous versions  did not like  it if you tried  to specify more
          than 2 ports.

          X00 will now leave DTR alone when a program exits.


          V1.04
          This is fix up  version.  No new features have  been added.  This
          version simply corrects problems introduced with "new features"
          of previous versions.

          All additions/changes  to help some SEAlink  implementations have
          been removed  from X00.   They caused  as many  problems as  they
          fixed.    Don't forget  that  you  can turn  X00's  FOSSIL (comm)
          functions on and off by using CAPTURE ON and CAPTURE OFF.

          Corrected a problem in the modem handshaking that occurred when a
          fixed computer-to-modem  baud  rate was  specified.   Due  to  an
          incorrect assumption  on my part the RTS/CTS  handshaking was not
          always forced on (as it should have been).

          Corrected a problem of slow output when a disconnect occurred.

          Increased the transmit buffer size from  512 bytes to 1024 bytes.
          The  increased  buffer size  hides  an  error  in  some  windowed
          protocol implementations.




























          V1.06
          The DEFER option now (again) implies ELIMINATE.

          Added an internal stack for the driver initialization call.  This
          is necessary for DOS V2.0 and V2.1.

          Added support for Opus definitions of 19200 and 38400 baud.

          Added an internal stack for communications interrupt processing.

          Corrected a  problem with  DTR being  turned on  incorrectly when
          Opus is invoked from the keyboard.

          Corrected a problem in command line parsing with DOS V2.xx.

          Added the ability to specify the size of the transmit and receive
          buffers.  See the specs and examples above.

          Default buffer size was changed to 4k bytes.

          X00 now beeps  the bell if it  displays an error message  at boot
          time.

          Added  some defensive  code  to detect  the  loss of  transmitter
          interrupts.   This problem  showed up  a lot  on systems  running
          DDos.


          V1.08
          Corrected a problem with the timer tick processing when the DEFER
          was specified.   Added functions  to meet draft  4 of the  FOSSIL
          specification.

          Added  FOSSIL  as  a driver  name.    Added all  of  the  draft 4
          specification  changes  except the  dispatcher functions  (7E and
          up).   Inserted code to attempt to fix  a watchdog problem on the
          386's.

          Added  code to  work  around a  DDos bug.   NOTICE  - If  you use
          CAPTURE  or WATCHCD, you  must have v1.08  or above  to work with
          this version of X00.

          Corrected problems in Status function (27).  

          Added Quiet mode call to function 4 (init).

          Added bit 3 (enable sending of XON/XOFF) to function 15 (0FH).




















          Corrected  a  problem in  the RTS/CTS  flow  control.   On slower
          computers  RTS  may  not  have  been  turned   off  soon  enough.
          Computers running less that 6  MHz should not lock the  baud rate
          any higher than 9600 baud

          Function 4 now returns information in BX as  specified by Draft 4
          of the FOSSIL spec.  Prior to 1.07j, it did not.  

          Corrected a problem  where X-ON was being sent at random when the
          sending of X-ON and X-OFF is enabled.

          Made changes  to  speed  a  few things  up  a  little.    Changed
          functions 22, 24,  25, and 27.  Parameters that were passed in DS
          are now passed in  ES.  If a second parameter  was passed with DS
          in SI, it now must be  passed in DI.  See FOSSIL.DOC for  the new
          calling sequence for the above listed  functions.  This time, the
          FOSSIL  specification is being changed to reflect the new calling
          sequences.

          Added  code  to  work  around an  apparent  problem  with SEAdog.
          SEAdog should work  faster with  this version.   Worked over  the
          interrupt service routine.

          Corrected a problem  in the hardware  handshaking.  Disabled  the
          sending X-OFF.

          Corrected a problem with 2000h and 4000h bit returned by function
          three.

          X00 will not initialize the baud rate on a function 4 call.  This
          will allow  outside type  functions to use  X00 at the  same baud
          rate as set by the program that loaded it.


          V1.08a
          Function 22 (16h) does not work correctly in V1.08.  This release
          corrects the problem.


          V1.10
          Added the best  anti-locking system conceived  by man.  This,  of
          course means it will lock up every other time that it is called.

          Hopefully  X00   now  completely   meets  the   Draft  5   FOSSIL
          specification.  The  external function dispatcher was added.  Bit
          3 is  always  turned on  in AL  as returned  by  the status  call
          (function 3).   The baud rate is  no longer set in the  init call
          (function 4).  

                       PROGRAMMERS NOTE THE FOLLOWING FOR V1.10
          With this version  (1.09c) and the  introduction of the  external
          function dispatcher,  interrupt enable is  handled differently by
          X00.  Prior to  this version, X00 would always  enable interrupts












          during  the processing of INT  14H (FOSSSIL) functions.  Starting
          with  this version,  interrupts  are enabled  only  if they  were
          enabled when the  INT 14H is  issued.  Otherwise, the  interrupts
          will  remain  masked throughout  the  processing of  the  INT 14H
          (FOSSIL) function.

          When  external  routines  are  entered  via  the  dispatcher  all
          registers and  status bits  (including interrupt  enable) are  as
          they were when the INT 14H is issued.  This means  parameters may
          be passed in  any register(s).   Additionally, parameters may  be
          passed on the stack (if you dare) and the stack appears as though
          the routine were  entered via a FAR  call and thus, a  FAR return
          should be issued.  When the FAR return is issued,   the return is
          to  the  instruction  following  the  original  INT  14H  in  the
          application program  and NOT to X00.   This means  results can be
          returned in any registrer(s).

          Added transmitter disable/enable to transmitter unlocking code.

          Added code to function zero to allow the setting of the number of
          data bits and to enable even and odd parity.


          V1.10a
          This is not  a beta  (note even  number).  Added  code that  will
          enable  installation of  a  Video  FOSSIL.   Due  to my  lack  of
          attention, this new  feature of the FOSSIL  spec got by me.   The
          ability to specify  locked baud rates  of 600, 1800, 2000,  3600,
          7200, and 38400 was also added in this release.


          V1.11a
          Another Beta.   Added full support for the National  16550a.  Use
          of the 16550a is automatic, the user  need not change anything to
          take advantage of the 16550a.

          Corrected a problem  in function 27,  the buffer size and  FOSSIL
          draft level was incorrect in the returned status.

          Added  the  NOFIFO  directive  to  enable  the  user  to override
          automatic use of the 16550's FIFOS.

          NOTICE NOTICE NOTICE NOTICE NOTICE NOTICE NOTICE NOTICE NOTICE

          On my computer, MultiLink will lock up when a 16550a is installed
          and  a CTTY=COMn is executed.   Once the 16550a's FIFOs have been
          enabled the lock  up always  occurs under MultiLink  even if  the
          FIFOs are  disabled (following  an enable).    This  lock up  has
          nothing  to do with X00 except that  X00 will enable the 16550a's
          FIFOs if not instructed otherwise.  
















          V1.11b
          No actual changes were made to  X00.SYS.  This release introduces
          the  utility  POSTPORT  which  may  correct  the  lockup  problem
          associated with the  16550(a) described above.   See POSTPORT.DOC
          for additional information.   Also, the naming convention of  the
          distribution files of X00  now reflect the version number.   This
          version is distributed as X00V111B.ARC.

          V1.11c
          Changed  assemblers,  from  Intel's   to  MASM,  (TASM  generates
          erroneous code).   Fixed problem  with X00 not  locking at  38400
          baud.   That is, it  will now lock  at 38400  baud.  Added  NASTY
          option  which  may help  throughput  on some  systems, especially
          multi-tasking systems.

          V1.11d
          Changed  the  value returned  in  the  BAUD field  of  the status
          structure  returned  by  function  1Bh  (27).    The  BAUD  field
          previously contained  only the  baud rate  shifted to  the low  3
          bits.  Now the BAUD field contains  the byte last passed in AL of
          function 0.  That is, it contains the baud, parity, and number of
          data bits in 8250 format.

          Added code to  preserve the  BAUD field of  the status  structure
          across an init/deinit sequence.

          changed  the  (constant)  screen  size  returned  in  the  status
          structure from 80/24 to 80/25.

          Added code to detect the monitor type so as to  correctly display
          the window  (that most disable)  at boot time.   This change  may
          cause problems  on some  computers (BIOSs).   The  E option  will
          eliminate the monitor detection.

          V1.20
          This release contains new  versions of CAPTURE and WATCHCD.   The
          older versions will  not work with  this (and future) release  of
          X00.

          Notice developers.  BYPASS.OBJ has been added to the distribution
          files.  Read the document SHARE.IRQ.   Anyone attempting to share
          a single IRQ on multiple comm ports should read SHARE.IRQ

          Extensive changes to improve multiasking performance.

          Many  changes  have   been  made  to   allow  shared  IRQs   with
          mulitaskers.  Eight  RBBSs all sharing  IRQ 3 using DESQview  has
          been successfully  tested with this version  of X00.   The 8 port
          RBBS system was set up and tested by Dan Fox at:

               Defence Logistics Services Center
               74 North Washington
               Battle Creek, Mi. 49021













          Through  a  coding error,  when  the transmit  buffer  size being
          specified,  a random  memory location  was being  changed.   This
          error has been corrected.

          Corrected some problems in processing IRQ 8 through 15.

          The NASTY option is now nastier.  Remember, the NASTY option will
          cause some systems to hang (and some to work).

          Status structure returned  by function 1BH  (27) now returns  the
          actual transmit and receive buffer  size.  Previously the default
          buffer size was returned.

          Code was streamlined for faster execution.

          1.20a
          This is not a beta, in  retrospect possibly 1.20 should have been
          a  beta.  V1.20  introduced code that can  cause X00 to interfere
          with  other communication  programs. This  problems shows  itself
          when an application program exits and leaves the FOSSIL active on
          a  given port.   If another program  uses the comm  port that was
          left  active,  X00   will  interfere   with  the  program.   Most
          noticeably,  it will  miss  received characters.    One way  this
          problem could come up is using Binkley with SHARE  in the command
          line.  There appears to be several programs out there that  leave
          the FOSSIL  hot when they  exit.  Application  programmers should
          always disable any ports  they may have activated when  they exit
          or implement the equivalent of the  Binkley SHARE option which is
          the correct way to exit with the FOSSIL still active.

          The default buffer size has been changed from 4k to 1k.  I really
          don't  buffers  as  large as  4k  is  necessary  on most  systems
          however, you can set them back to 4k using the R and T option  in
          the DEVICE = command line.

          This  version  corrects  a problem  that  made  some Trailblazers
          practically unusable.   Additionally, users of other  modems that
          use RTS/CTS handshaking will see improved performance.

          A problem with mapping ports was corrected.

          Added the quick and  dirty C HLLAPI routines to  the distribution
          file.  See CHLLAPI.DOC in the CHLLAPI.ARC archive.

          I did not  add it to  the semi-formal command line  documentation
          above.  However, a new command line  option has been added.  This
          command allows the  user to specify  the transmit FIFO size  that
          X00 is to use when a 16550 is installed.  The command line option
          is F{IFO}=n where n is  1 to 16.  The default  transmit FIFO size
          is  8.   For  reasons  I do  not  understand,  some systems  have
          problems if the FIFO size  is set to the maximum of 16.  However,
          15 seems to work  on all tested systems.  The  F=n statement will
          be  ignored if a 16550  is not installed.   Through a programming
          error, X00 previously  has never used more  than one byte  of the












          16550  transmit FIFO.  Users  with 16550s installed will probably
          see increased transmit speeds with this  version of X00.  Setting
          the transmit  FIFO to a value larger than  the default value of 8
          may yield marginally better transmit speeds.  However, setting it
          to the maximum of  16 may cause some connections  and/or programs
          to miss characters.

          1.20b
          Version 1.20a  lasted only  about 4  hours.   I  apologize.   The
          correction  of  the  port  assignment  problem in  V1.20a  caused
          another problem  when only one comm  port was used and  that port
          was  not  COM1.    That  problem  is  corrected  (with  a  single
          instruction) in this version.  Again, I apologize.

          -------------------------------
          Time  permitting,  I  will  respond  to  messages  pertaining  to
          X00.SYS.  Please do not get upset if I am slow.

          Ray Gwinn