Manually installing the Above Board software 

                            Introduction

This appendix gives you the information you need to manually add the 
necessary Above Board Plus and Plus I/O commands to your CONFIG.SYS file.  

                               N O T E       

This guide  assumes you know the differences between conventional, 
extended, and expanded memory.  If you don't, refer to Chapter 2 in your 
Above Board manual for definitions. 

             Manually Installing the Above Board software 

The Above Board comes with software that lets you: 

     o use expanded memory 

     o use the conventional memory supplied by the Above Board as mappable 
       conventional memory 

     o create RAM disks 

     o create a print buffer  If you boot from floppy diskettes, 
       install the Above Board software on each system diskette from which
       you boot.  If you boot from a hard disk, install the software just 
       once in the root directory. 

Installing the software involves these steps: 

     o copying files

     o setting up expanded memory

     o setting up RAM disks 

     o setting up a print buffer

In general, you don't have to do all this copying and setting up.  The 
SOFTSET program can do it automatically.  This appendix describes the 
do-it-yourself technique.  

                            Copying files 

Before you can use the Above Board software, you must copy files from the 
Intel diskette to your hard disk's root directory or to your system 
diskettes.  Copy only the files you need. If you have more than one Above 
Board software diskette, check the date on the diskettes, and make sure you 
install the most recent version of the software.  The Above Board software 
includes the following files: 

   File Name       Description     
   EMM.SYS         Activates expanded memory on
                   Above Board Plus or Plus I/O.
                   Also allows mappable conventional memory. 
   QUIKMEM2.SYS    Creates a RAM disk in expanded memory. 
   QUIKBUF2.COM    Creates a print buffer in expanded memory. 

Copy the files you need for the features you want to use. 

                                  -1-



 Setting up expanded memory for Above Board Plus and Plus I/O boards only 

This section describes the command line you need to put into your 
CONFIG.SYS file if Above Board Pluses or Plus I/Os provide all the expanded 
memory in your computer.  If you will use both an Above Board Plus or Plus 
I/O and another type of Above Board (Above Board  286, PS/286, AT, PS/AT, 
PC, or PS/PC) to supply expanded memory, skip this section and go to page 
F-19 for the appropriate EMM command line. To use expanded memory on Above 
Board Plus and Plus I/O boards, add this command as the first line in your 
CONFIG.SYS file: 

DEVICE=EMM.SYS  Computer  I/O_Address 1..16 [Memory_Address]    [EXPF=x]    
[EXPL=x]    [MC]    [MCF=x]    [MCL=x]    [RD]    [ND]    [NP]    [NE]    
[VI]    [H=x]   

The parameters without brackets ([]) are required; those in brackets are 
optional.  The order of the parameters doesn't matter.

                                N O T E       

The MC, RD, MCF, and MCL parameters work only with the Above Board Plus and 
Plus I/O.

                                N O T E       

If there is an Inboard PC installed in your system, the EMM.SYS command 
line must be inserted below the INBRDPC.SYS line in the CONFIG.SYS file. 

Required EMM command line parameters 

The Computer parameter defines the 
type of computer in which the Above Board is installed.  Replace the 
Computer parameter with one of the choices listed here: 

     Parameter       Computer Type 

     pc (or PC)        COMPAQ DESKPRO
                       IBM PC
                       IBM XT
                       IBM PC or XT compatibles 

     at (or AT)        COMPAQ DESKPRO 286
                       COMPAQ DESKPRO 386
                       IBM AT
                       IBM XT 286
                       IBM PS/2 Model 30 286
                       IBM AT compatibles

     mod30 (or MOD30)  IBM Personal System/2 Model 30

The I/O_Address parameters specify which base I/O addresses Above Boards 
use.  Assign a unique I/O address to each Above Board.  No boards in your 
computer can share I/O addresses.  Piggyback Memory boards use the I/O 
addresses of the Above Boards to which they are attached. 

Use one I/O_Address parameter value for each Above Board Plus and Plus I/O 
in your system.  Be sure your I/O_Address parameter values match the I/O 
addresses selected when you ran the SETBOARD program.  These are displayed 
on the final summary screen when you run the SETBOARD program, or if you 
choose the VIEW option in SETBOARD. 

                                   -2-


The possible values are:

     I/O address

         208
         218  
         248
         258
         2A8
         2B8
         2E8

Example.  You're installing two Above Board Plus boards in an IBM AT.  One 
board is set for I/O address 208, the other for address 258.  Use this 
command: 

     DEVICE=EMM.SYS AT 208 258 

Optional EMM command line parameters

The EXPF=x (expanded first) and EXPL=x (expanded last) parameters specify 
the range of addresses of the expanded memory page frame. 

If you omit the EXPF and EXPL parameters, EMM automatically searches the 
address range between 768K and 960K (hexadecimal segment address C000 to 
F000 is checked for ROM or RAM), selecting the largest unused contiguous 
area in that range as the page frame.  The EXPF and EXPL parameters 
override this automatic mapping and let you specify the range of the page 
frame search.  This might be necessary to enable the Above Board to work 
with some network and communication boards.

The EXPF parameter specifies the beginning of the first 16K-byte page.  The 
EXPL parameter specifies the beginning of the last 16K-byte page.  The 
values you use must be hexadecimal segment addresses that represent 
16K-byte boundaries between 768K and 944K.  The range that you specify 
should not overlap any RAM or ROM on other add-in boards in your computer.  

The possible values are:

     Value              Address
     C000               768K
     C400               784K
     C800               800K
     CC00               816K
     D000               832K
     D400               848K
     D800               864K
     DC00               880K
     E000               896K
     E400               912K
     E800               928K
     EC00               944K

You can include either or both of the EXPF and EXPL parameters.  If you 
include both, EMM uses both addresses you specify and searches that range 
for the largest unused contiguous area to use as the page frame (the 
minimum size is 64K).  

If you include just the EXPF parameter, EMM starts the page frame search at 
the EXPF address and selects the largest contiguous area between that 
address and 944K.  

                                   -3-


If you include just the EXPL parameter, EMM selects the largest contiguous 
area it finds between 768K and the end of the 16K-byte area specified with 
the EXPL parameter. If you specify addresses less than C000 or greater than 
DC00, if you specify a page frame that is less than 64K, or if you invert 
the values (that is, specify a larger value for EXPF than for EXPL), EMM 
displays a message and does not install.  

The MC (mappable conventional memory) parameter causes EMM to make all 
conventional memory supplied by Above Board Plus or Plus I/O boards 
mappable.  (You can limit the mappable range by using the MCF and MCL 
parameters.)  Mappable conventional memory enables operating environments 
such as Windows 2.0 and DESQview to perform conventional memory mapping.  

Refer to Appendix E for more information about mappable conventional 
memory. If you want to use conventional memory supplied by the Above Board 
Plus or Plus I/O as mappable conventional memory (described in Appendix E), 
be sure you do the following:

     o       Make sure that you add the MC (or the MCF or MCL parameter) 
             to the EMM command line.

     o       The Above Board must supply the conventional memory you want 
             to make mappable.  Many computers have system boards that 
             provide 512K or 640K of conventional memory, leaving either
             128K or no memory that could be assigned as mappable.  If 
             you want more mappable conventional memory, disable some of
             your system board memory.  See your computer's operation 
             guide for information on disabling some of the conventional
             memory in your computer.  Appendix E has an example.
       

                                  N O T E  

Your computer must supply at least 256K bytes of conventional memory.

                                  N O T E       

Do not use the MC parameter if you have an Intel Inboard 386 installed in 
your computer.

The MCF=x (mappable conventional first) and MCL=x (mappable conventional 
last) parameters provide the same function as the MC parameter (making 
conventional memory supplied by Above Board Plus and Plus I/O boards 
mappable), but they also let you restrict the beginning and ending 
addresses of mappable conventional memory.  

These parameters are useful only if you run an operating environment (such 
as Microsoft Windows 2.0) that uses version 4.0 of the Expanded Memory 
Specification to map conventional memory.  If you include either or both of 
the MCF and MCL parameters, you do not need to include the MC parameter.  
If you don't want mappable conventional memory, you don't need to include 
these parameters. 

When you include the MC parameter, EMM determines the range of the 
conventional memory supplied by Above Board Plus or Plus I/O boards (this 
can start no lower than 256K) and this becomes the range of mappable 
conventional memory.  If you use the MCF and MCL parameters instead of MC, 
you can specify the starting and ending addresses for mappable conventional 
memory within the address range supplied by the Above Board Plus or Plus 
I/O board.  

                                    -4-


The MCF parameter specifies the beginning of the first 16K-byte area of 
mappable conventional memory.  The MCL parameter specifies the beginning of 
the last 16K-byte area of mappable conventional memory.  The values you use 
must be hexadecimal segment addresses that represent 16K-byte boundaries 
(starting at 256K) in the 640K-byte conventional memory area.  The possible 
values are:

     Value   Address            Value   Address

     4000       256K            7000    448K
     4400       272K            7400    464K
     4800       288K            7800    480K
     4C00       304K            7C00    496K
     5000       320K            8000    512K
     5400       336K            8400    528K
     5800       352K            8800    544K
     5C00       368K            8C00    560K
     6000       384K            9000    576K
     6400       400K            9400    592K
     6800       416K            9800    608K
     6C00       432K            9C00    624K

If you specify a value that is not a multiple of 16K, EMM rounds up the 
value to the next 16K increment. You can include either or both of the MCF 
and MCL parameters.  If you include both, EMM uses both addresses you 
specify to determine mappable conventional memory range.  

If you include just the MCF parameter, EMM starts mappable conventional 
memory at the MCF address and ends it wherever the conventional memory 
supplied by the Above Board ends.  

If you include just the MCL parameter, EMM starts mappable conventional 
memory wherever the conventional memory supplied by the Above Board starts, 
and ends mappable conventional memory at the end of the 16K-byte area 
specified with the MCL parameter. 

If you specify addresses less than 256K or greater than 640K, or if you 
invert the addresses (that is, specify a larger address for MCF than for 
MCL), EMM displays a message and does not install.  

Example 1.  

You're using an IBM PS/2 Model 30 286 that includes one Above Board Plus, 
set to I/O port 258.  You want to provide mappable conventional memory for 
operating environments such as Microsoft Windows 2.0.  Your Above Board is 
set to provide conventional memory from 256K to 640K.  You want EMM to 
begin mapping at 256K and stop mapping at 624K (a requirement for Windows 
and DESQview).  Use the following command: 

     DEVICE=EMM.SYS AT 258 MCL=9800

It is not necessary here to specify the starting address, since it will 
automatically use 256K.  Notice that the MCL value (9800) is equivalent to 
608K, not 624K.  That is because the MCL value represents the start of the 
last 16K bytes of mappable memory.  Therefore, 608K + 16K = 624K, where 
mappable conventional memory actually ends. 

Because you did not specify EXPF and EXPL, EMM will automatically search 
for and select an expanded memory page frame for you.


                                  -5-

Example 2.  

You're using an IBM XT that includes one Above Board Plus at I/O port 258.  
The following command assigns all of the Above Board memory as expanded 
memory. DEVICE=EMM.SYS PC 258

Because you did not include the EXPF and EXPL parameters, EMM automatically 
uses the largest unused contiguous area between 800K and 960K as the page 
frame.  The area selected depends on your system configuration.  Other 
add-in boards with RAM or ROM in the address range between 800K and 960K 
will limit the page frame size and location.  To load, EMM requires one 
contiguous 64K-byte block in this range.

The following command instructs EMM to find a page frame between 800K and 
896K:

     DEVICE=EMM.SYS PC 258 EXPF=C800 EXPL=DC00 


The RD (relocate driver) parameter causes EMM to be installed in expanded 
memory instead of conventional memory.  This conserves conventional memory.  
One page (16K) of expanded memory is reserved for use by EMM if you use 
this parameter.

If the RD parameter is absent, EMM will be loaded into conventional memory.

The ND (no diagnostics) parameter tells software to run abbreviated memory 
tests after a warm boot (Ctrl-Alt-Del).  The ND parameter is optional.  If 
ND is in the command line, the EMM will run abbreviated memory tests; if ND 
is absent, the EMM will run full tests.  In either case, full tests are run 
during a cold boot (power-on).

The NP (no pause) parameter overrides the EMM pause after an EMM error or 
advisory message.  The NP parameter is optional.  If NP is in the command 
line, the EMM won't pause after errors or messages.  If NP is absent, the 
EMM will pause.

The NE (no extended memory tests) parameter tells EMM not to run extended 
memory tests.  Use this parameter in an IBM AT or compatible computer if no 
extended memory exists on any Above Board or on your system board.  

The NE parameter is optional.  If NE is in the command line, no extended 
memory tests are performed.  If NE is absent, tests are performed.

                             C A U T I O N 

Using the NE parameter can damage the data on your hard disk if you have 
extended memory in your system.  Do not select this option if your Above 
Board is supplying extended memory. 

The VI parameter lets you cause all information on the EMM configuration to 
be displayed.  It is optional.  If it is in the command line, all EMM 
configuration information is displayed.  If VI is absent, only information 
relating to the parameters you select is displayed. 

The H=x (handle count) parameter lets you tell EMM to support as many 
handles as a particular application program needs.  A handle is a value 
that EMM assigns and uses to identify a block of expanded memory requested 
by an application program.  EMM must keep track of all the handles it 
supports; a large handle count increases the size of EMM.  Specifying a 
small EMM handle count (less than 64) can save conventional memory and 
allow EMM to run faster. 

                                 
                                  -6-


The EMM handle count default is 64 handles.  Application programs written 
to use EMM versions below EMM 4.0 use a maximum of 32 handles.  If you're 
using older application programs, you may change the EMM handle count to 
H=32, but using the default of 64 handles will work fine.  The maximum value 
for x is 255 handles. The H=x parameter is optional.  If the H=x parameter is 
in the command line, the EMM will support the number of handles specified by 
x.  The handle count will also appear on the screen when EMM is installed.  
If H=x is absent, the EMM uses 64 handles.  You won't see a handle count on 
the screen when EMM is installed unless you specify a value for the H 
parameter or use the VI parameter in the command line. 

Example.  

You're using one Above Board Plus in an IBM AT.  You want expanded memory to 
be installed at D000.  The board is set for I/O address 258.  You want all 
conventional memory made mappable, and you want EMM installed in expanded 
memory.  You want the handle count default of 64.  Use this command: 

     DEVICE=EMM.SYS AT EXPF=D000 258 MC RD 

Set up when different Above Board types supply expanded memory 

This section describes the command line you need to put into your 
CONFIG.SYS file if you are using both an Above Board Plus or Plus I/O and 
another type of Above Board (Above Board 286, PS/286, AT, PS/AT, PC, PS/PC) 
to provide expanded memory in your computer. To use expanded memory on your 
boards, add this command as the first line in your CONFIG.SYS file: 
DEVICE=EMM.SYS   Computer   Memory_Address   I/O_Address 1...16    [EXPF=x]    
[EXPL=x]    [ND]    [np]    [ne]    [vi]    [H=x] The parameters without 
brackets ([]) are required; those in brackets are optional.  The order of 
the parameters doesn't matter.  For explanations of these parameters, see 
pages F-5 through F-18.  All the previously described parameters work 
except MC, MCF, MCL, and RD -- these parameters work in computers that 
contain the Above Board Plus or Plus I/O only.

                               N O T E       

If there is an Inboard 386/PC installed in your system, the EMM.SYS command 
line must be below the INBRDPC.SYS line in the CONFIG.SYS file.

Setting up RAM disks

You can set up Above Board RAM disks in expanded memory.  This section 
explains how. For each RAM disk you install in expanded memory, put a line 
like this in the CONFIG.SYS file after the EMM.SYS line: 

     DEVICE=QUIKMEM2.SYS x 

The x parameter specifies the size of the RAM disk in K bytes and must be at 
least 16.  Values that aren't multiples of 16 are rounded up to the 
next-higher multiple of 16.  The maximum size of a RAM disk is 8M bytes 
(8192K). 

Example.  

For two 1600K-byte RAM disks in expanded memory, put these two lines in the 
CONFIG.SYS file: DEVICE=QUIKMEM2.SYS 1600
DEVICE=QUIKMEM2.SYS 1600 DOS 
limits you to 26 disk drives, which includes all of the fixed and floppy 
disk drives and RAM disks in the system.  It also assigns a unique drive 
letter to each disk drive.  For a typical computer with a hard disk, the 
first RAM disk is D.  For a twoÄfloppy computer with no hard disk, the 
first RAM disk is C.  Additional RAM disks receive sequential letters.

                                 -7-

Setting up a print buffer

To set up a print buffer in expanded memory each time you turn on or 
restart your computer, you'll need to add a command to your AUTOEXEC.BAT 
file.  Use any ASCII file editor (such as EDLIN) to edit your file.

                               N O T E       

You can have only one print buffer.  If a command in your AUTOEXEC.BAT file 
already sets one up, delete that command before adding the commands 
described in this section.  To set up the print buffer in expanded memory, 
use this command: 

     QUIKBUF2  c  x  d  t

The c parameter tells the QUIKBUF program what type of computer you're 
using.  The choices for the c parameter are:

     Parameter                Computer Type
     at (or AT)               IBM AT
                              IBM AT compatibles
                              IBM AT and XT/286
                              COMPAQ DESKPRO 286
                
     pc (or PC)               IBM PC
                              IBM XT
                              IBM PC and XT compatibles
                              COMPAQ Deskpro 86

     mod30 (or MOD30)         IBM Personal System/2 Model 30

     mod30/286 (or MOD30/286) IBM Personal System/2 Model 30 286

The x parameter specifies the size of the buffer in K bytes and must be 32 
or greater.  Any value that isn't a multiple of 16 is rounded up to the 
nextÄhigher multiple of 16.  16K of the buffer is reserved for the pop-up.

The d parameter tells the QUIKBUF program what display adapter your 
computer uses. Choices for the d parameter are:

     M (or m)                        IBM Monochrome Adapter.
     H (or h)                        Hercules Monochrome Graphics
                   Adapter.
     G (or g)                        IBM, Zenith, AT&T, or Hercules
                 Color Graphics Adapter.  IBM
                   Personal System/2 Model 30 
                    or COMPAQ monochrome or 
                       color adapter. 
     E (or e)                        IBM Enhanced Graphics Adapter.
     V (or v)                        IBM Video Graphics Array.
                      IBM Model 30 286 Adapter.
     O (or o)                        All other adapters, including the
                      Hercules Graphics Plus Adapter.
                        Choosing this option disables the
                      print buffer command menu,
                     described in Chapter 13.  The print 
                   buffer will still work, but you 
                       won't be able to control it from
                       the command menu.

The t parameter indicates the type of port to be buffered.  

Here are the choices: 

     P       Parallel  (LPT1, LPT2, or LPT3)
     S1      Serial  (COM1)
     S2      Serial  (COM2)

If you choose P, the first thing you print or the print buffer commands you 
use will determine whether the buffered port is LPT1, LPT2, or LPT3.  See 
the print buffer chapter in the manual for details.  If you omit the 't' 
parameter, the print buffer defaults to parallel.

If you choose S1 or S2, you may need to add one or two MODE commands to 
your AUTOEXEC.BAT file.  See the DOS manual or Chapter 15 in the Above 
Board manual for details.

                                  -8-


Example.  Suppose you have an IBM AT and an IBM Enhanced Graphics Adapter.  
If you want a 144K-byte print buffer in expanded memory and you want to 
print your data on a serial printer attached to COM1, use this command: 

     QUIKBUF2 AT 160 E S1

This creates a print buffer of 160K bytes, but since 16K is used for the 
pop-up, you are left with the 144K-byte buffer you wanted. Using the 
optional programs

This section describes the optional programs available on the Above Board 
diskette.  These programs don't need to be run; they're included for your 
convenience.

Here's how to start these programs:
   
     1       With your screen displaying the DOS prompt, insert a copy of
             the Intel diskette into drive A.

     2       Type A:[command] and press Enter.  

             Replace the command parameter with the command listed in the 
             following table for the specific program you want to run.

     Command         Program

     CHKMEM          Displays the amount of conventional, extended, (IBM AT
                     and compatible computers only) and expanded memory in
                     your computer.

     TESTAB          Tests and pinpoints bad RAM chips on your Above Board.

     SOFTSET         Sets up expanded memory, mappable conventional memory,
                     RAM disks, and a print buffer.




























                                   -9-