CONTENTS


 1.  DESCRIPTION..........................................................   2

 2.  EXIT STATUS..........................................................   4

 3.  COMMANDS.............................................................   5
     3.1   Interrupt Keys.................................................  10

 4.  NUMERIC PARAMETERS...................................................  11

 5.  ENVIRONMENT VARIABLES................................................  14

 6.  EXAMPLES.............................................................  17

 7.  IN CASE OF DIFFICULTY................................................  18
     7.1   LOCKUPS........................................................  18
           7.1.1  Insufficient Memory  18
           7.1.2  Environment TOO BIG  18
           7.1.3  Bad COMM Port Configuration  19
     7.2   Incorrect Batch Files..........................................  19
     7.3   Commands Entered in Upper Case.................................  19
     7.4   No Carrier Detect..............................................  20
     7.5   PKARC 3.6......................................................  20
     7.6   DOS 3.x........................................................  20
     7.7   Perstor Controllers............................................  20
     7.8   IBM PS/2 Model 50Z.............................................  20
     7.9   Brain Damaged UARTS............................................  21
           7.9.1  Everex Internal Modems  21
     7.10  Weird Iron.....................................................  21
     7.11  Will the real YMODEM please stand up?..........................  22
     7.12  286 and 386 Extended Memory....................................  22

 8.  BACKGROUND OPERATION.................................................  23

 9.  CALLING DSZ FROM COMM PROGRAMS.......................................  25
     9.1   GT POWER 13.00/14.00...........................................  25
     9.2   PROCOMM........................................................  25
     9.3   PROCOMM PLUS...................................................  25
     9.4   Qmodem.........................................................  26
     9.5   BULLETIN BOARDS................................................  27

10.  FLOW CONTROL.........................................................  28

11.  ERROR MESSAGES.......................................................  29
     11.1  Got ZRPOS......................................................  30
     11.2  Serial Input Error: Line Status Register xx ...................  31
     11.3  COMMAND NOT FOUND..............................................  32
     11.4  Out of Environment.............................................  32











12.  SLOW TRANSFERS.......................................................  34

13.  ASSOCIATED DOCUMENTS.................................................  35
     13.1  ZMODEM Developer's Collection..................................  35

14.  FILES................................................................  36

15.  CHANGES..............................................................  37

16.  Other Omen Technology Products.......................................  41

17.  FAIR PLAY............................................................  42
     17.1  Sharing DSZ Files..............................................  42
     17.2  REGISTRATION...................................................  43
     17.3  Files on Registration Disk.....................................  45
     17.4  Bulletin Board Registration....................................  46

18.  ACKNOWLEDGEMENTS.....................................................  47









































        DSZ - a ZMODEM, True YMODEM(TM), XMODEM File Transfer Program


                                Chuck Forsberg

                             Omen Technology Inc


                                   ABSTRACT



                    ZMODEM - Not just another XMODEM hack

DSZ is one of many available programs that implement the ZMODEM file transfer
protocol.

DSZ's ZMODEM provides advanced file management features including two levels
of Intelligent Crash Recovery(TM), and flexible control of selective file
transfers.  Omen Technology's Professional-YAM Communications Tools also
provide security verified command downloading.

The ZMODEM file transfer protocol provides reliable file and command transfers
with complete END-TO-END data integrity between application programs.
ZMODEM's 32 bit CRC protects against errors that sneak by "error free" modems
and even the most advanced networks.

ZMODEM safeguards all data and supervisory information with effective error
detection.  (XMODEM and many recently introduced protocols do not protect
vital supervisory data.)

ZMODEM rapidly transfers files, particularly with buffered (error correcting)
modems, timesharing systems, satellite relays, and wide area packet switched
networks.  ZMODEM's streaming operation eliminates delays caused by
Kermit/XMODEM/YMODEM/JMODEM block acknowledgements.  ZMODEM eliminates the
classic XMODEM/YMODEM/JMODEM PACKET LENGTH compromises between transfer
efficiency and error recovery.  ZMODEM's packet length is the entire file.

User Friendliness is an important ZMODEM feature.  ZMODEM AutoDownloadm
(Automatic file Download initiated without user intervention) greatly
simplifies file transfers compared to traditional protocols.

















        DSZ - a ZMODEM, True YMODEM(TM), XMODEM File Transfer Program

                                Chuck Forsberg

                             Omen Technology Inc


                         Omen Technology Incorporated
                        The High Reliability Software

                     17505-V Northwest Sauvie Island Road
                            Portland Oregon 97231
      TeleGodzilla BBS: 503-621-3746 Speed 1200,2400,19200(Telebit PEP)
                              FAX: 503-621-3735
                       CompuServe:70007,2304  GEnie:CAF
                      UUCP: ...!tektronix!reed!omen!caf

  *************************************************************************
There's something special about DSZ registration.  With most programs,
registration applies only to the current version.  DSZ isn't like that.

DSZ registration bypasses the shareware announcement and unlocks the advanced
features in all past and future versions of DSZ.  You don't have to pay and
pay again for new versions.  Omen's Demand Upgrade(TM) technology allows you
to download future DSZ versions without further registration!
  *************************************************************************



































Chapter 1 Pg 2            DSZ Reference Rev 11-14-89          Typeset 11-14-89



1.  DESCRIPTION

DSZ is a "protocol driver" that uses the ZMODEM, True YMODEM(TM), or XMODEM
protocol to transfer files over a serial port with a variety of programs.

ZMODEM Transfers feature 32 bit CRC, advanced file management, and Crash
Recovery, ZMODEM Crash Recovery can be used to complete interrupted file
transfers started with any protocol.[1]

DSZ has two main commands for ZMODEM transfers: "sz" sends file(s), and "rz"
receives them.

When calling bulletin boards to download files with ZMODEM you can avoid the
bother of starting DSZ for each transfer by calling DSZ first, before asking
the BBS for the download.

        dsz t

The "t" command allows you to keyboard the file request directly to the BBS.
(The "t" stands for "terminal emulation".) Just give the "dsz t" command from
DOS or your comms program's DOS GATEWAY.  DSZ's ZMODEM AutoDownload then
receives the file automatically, using the filename provided by the BBS,
without any wasted keystrokes or delay.  Try it, you'll like it!  (The "t"
command is described below.)

YMODEM downloads are almost as easy.  Use the "t" command as shown above, and
hit the F3 key after telling the board to download a file with YMODEM.

ZMODEM and True YMODEM(TM) transfers preserve exact file length and
modification time.

DSZ supports XMODEM-1k (XMODEM with 1024 byte blocks, sometimes mislabeled as
ymodem) and CRC-16 with the sx -k and rc commands.

DSZ is derived from Omen Technology's "Professional-YAM" high reliability
communications tools (also known as PowerCom(TM)) and Omen Technology's ZCOMM
User Supported Communications Software.  DSZ supports a subset of Pro-YAM's
file transfer related commands.  This documentation makes extensive references
to contemporary editions of the Pro-YAM or ZCOMM manual, and is incomplete
without it.  (Registered copies include an alternate, copyrighted file.)

DSZ is usually called from a communications or bulletin board program.

DSZ uses its own modem I/O.  The original interrupt vector, UART parity, and
interrupt configuration are restored on exit.  The original state of the 8259


__________

 1. Provided the other protocol did not write false data to the file.







Chapter 1 Pg 3            DSZ Reference Rev 11-14-89          Typeset 11-14-89



interrupt mask bit for this vector is also restored on exit.

DSZ uses DOS standard output (stdout) for messages.  It never writes directly
to the screen.  DSZ expects its standard output to point to the console, a
logging file, or NUL, but never the modem port.  If dsz's standard output is
redirected to the modem (as with ProComm's Host mode DOS shell), the
combination will lock up the computer.  When necessary, dsz's standard output
can be redirected back to the console device with the CON command.

Users of pcAnywhere must use dsz's A command to disable pcAnywhere host mode
during file transfers.














































Chapter 2 Pg 4            DSZ Reference Rev 11-14-89          Typeset 11-14-89



2.  EXIT STATUS

DSZ exits with 0 status for successful transfers, or the value of the Q
parameter (default 1) if a file transfer failed, or if no files were
transferred.  Many languages and "door" programs do not return this
information to the calling program.  Some languages and "door" programs freak
out (hang) on certain non-zero exit values.

A batch file that calls DSZ directly may be used to detect the DSZ exit status
with the DOS "errorlevel" construct.  Please refer to the Q numeric parameter
below for more information.

DSZ's log file entries may also be examined to determine the success or
failure of a file transfer.











































Chapter 3 Pg 5            DSZ Reference Rev 11-14-89          Typeset 11-14-89



3.  COMMANDS

DSZ commands are an improper subset of Pro-YAM/PowerCom/ZCOMM commands.  The
file transfer commands are fully described in ZCOMMDOC.ARC, the ZCOMM User's
Manual.  Relevant portions of the ZCOMM User's Manual are provided in
DSZBG.ZOO, a Copyrighted file included with the DSZ registration disk.  You
may refer to one of those documents for details on the following commands.


















































Chapter 3 Pg 6            DSZ Reference Rev 11-14-89          Typeset 11-14-89



         ***********************************************************
                                  NOTE WELL
    Except as noted, all commands and options must be typed in lower case.
                           DO NOT USE UPPER CASE!!
                             Case is significant!
         ***********************************************************

Optional commands or arguments are shown in square brackets [].

dsz [A] [CON] [port N] [speed S] [handshake XX] [D] [d] command

When used (in any combination), the A, CON, port, speed, handshake, estimate,
and d commands must be used in exactly this order.


A     Suspend pcAnywhere operation during file transfers.  This is necessary
      to avoid lockups caused by pcAnywhere host mode.  This command should be
      given to the program running under pcAnywhere host mode.

      EXAMPLE: C>dsz A sz *.foo Sends files from a pcAnywhere hosted machine
      to you.


      Fm: Al de la Torre

      1 sending from host to remote
             type: "dsz A sz filename.ext" ENTER
             shell to dos on remote machine (ctrl-Rshift)
             type: "dsz A rz" ENTER

      2 sending from remote to host
             type: "dsz A rz" ENTER
             shell to dos on remote machine (ctrl-Rshift)
             type: "dsz A sz filename.ext" ENTER


CON   Redirect message output to the DOS "CON"  (console)  device,  overriding
      any previous redirections.  This is necessary to avoid lockups caused by
      ProComm host mode.  Most  programs  do  not  require  this  hack.   This
      command is unique to DSZ.

estimate length  [speed] Use  the  specified  length  and  optional  specified
      effective  transfer speed for the next receive file to be created.  This
      command must come after any port, speed, or handshake commands.   Please
      refer to DSZBG.ZOO or the ZCOMM User's manual for details.

      The following makes DSZ calculate file transfer times on  the  basis  of
      290 character per second aggregate transfer rate:

      EXAMPLE: dsz port 2 speed 9600 estimate 0 2900 rz







Chapter 3 Pg 7            DSZ Reference Rev 11-14-89          Typeset 11-14-89



      EXAMPLE: dsz port 2 speed 9600 estimate 0 2900 sz bimama.zip


handshake XX Enable one of several choices of hardware handshake.  (The
      default is XOFF/XON software handshake).  This command is documented in
      the ZCOMM or Pro-YAM manual, and in DSZBG.DOC.  (The ZCOMM manual is
      available on all bulletin boards registered for DSZ as ZCOMMDOC.ARC.) On
      DSZ the "handshake" command may be abbreviated to "ha".

port N select port N (n = 1,2,3,4,5,6,7,8, 10,11,12,13,14,15,16,17,18) Default
      is port 1 (COM1) or read from the DSZPORT dos environment variable.
      COM11 to COM18 refer to the COM1 to COM8 ports on the PS/2.

         *****************************************************************
                                        NOTE
      Only COM1 and COM2 are standard on all PC compatible computers.
      Multiple standards exist for COM3 and above, so use only COM1 or COM2
      when first installing DSZ.
         *****************************************************************

      DSZ's COM3 uses 3E8 and IRQ4.  DSZ's COM4 uses 2E8 and IRQ3.

      DSZ's COM7 uses 3E8 and IRQ5.  DSZ's COM8 uses 2E8 and IRQ5.

      If you wish to use COM3 or COM4 and your computer is not wired according
      to one of these choices, you MUST use the "portx" command to specify
      base address and interrupt vector.

      EXAMPLE: to use COM2:
      dsz port 2 rz

      In multitasking operation, accessing a port used by another running
      program will hang the machine.


portx base,irq Select arbitrary port address and interrupt vector.  Please
      refer to DSZBG.DOC (provided on the Registration Diskette) or the
      Professional-YAM or ZCOMM (ZCOMMDOC.ARC) manuals for details on this
      command.

      EXAMPLE: portx 3e8,4


speed S Set the specified speed.  This command is rarely needed because DSZ
      reads the port's current speed by default.  Please refer to the FLOW
      CONTROL, MAIN COMMANDS and SOFTWARE COEXISTENCE chapters in DSZBG.ZOO or
      the ZCOMM or Pro-YAM manual for important information about the speed
      command.  DSZ supports a maximum speed of 38400.  Please study all the
      chapters of this document when using speeds above 2400 bps.








Chapter 3 Pg 8            DSZ Reference Rev 11-14-89          Typeset 11-14-89



D     Disables the modem (drops Data Terminal Ready, DTR) if carrier is lost.
      This may be used to prevent spurious events (phone ringing) from
      interfering with the calling bulletin board's recovery from carrier
      loss.

d     Disables carrier dropout monitoring, for modems that do not properly
      drive the "Carrier Detect" input on the PC.  If you see a No Carrier
      Detect message, you need to give the d command.  Before using the d
      command, make sure you have the proper port selected!!!


LARG  Convert ARG to lower case, then parse arg.


o     Turn off Data Terminal Ready (DTR), terminating ("offing") the
      connection if the modem responds to DTR.  Useful with the "t" command to
      disconnect afterwards.

      EXAMPLE: dsz t o


pxN   Set a numeric parameter x to N.  These parameters are mostly a subset of
      the Pro-YAM/ZCOMM numeric parameters, and are listed below.  They assume
      their defaults each time DSZ is called.  Without an argument, p displays
      the numeric parameters and their values.

      EXAMPLE: C>dsz p

      z pxN Set zmodem numeric parameter x to N.  These parameters correspond
      to the Pro-YAM or ZCOMM "zmodem" parameters and rarely need changing.
      These parameters assume their defaults each time DSZ is called.  Without
      an argument, z p displays the zmodem numeric parameters and their
      values.

restrict Restrict pathnames to the current disk and directory tree, and
      disallow overwriting of existing files.  When DSZ is restricted, it will
      refuse to transfer files containing the string autoexec.bat and
      command.com in upper or lower case.  This provides some defense from
      malicious uploaded files.

t     [-T] [-8g] Talk with ZMODEM AutoDownload.

      The optional -T forces DSZ to exit after it has recognized a ZMODEM
      AutoDownload(Tm) request.

      The optional -8g (available on registered copies only) allows "BBS
      (ANSI) graphics".  (A video device driver such as ANSI.SYS must be
      loaded to support some types of graphics.) A small subset of ZCOMM/Pro-
      YAM term function subcommands are recognized.  Keyboard F1 or ALT-X to
      exit.  F3 receives file(s) with True YMODEM(TM), ALT-P toggles parity
      between the 8n default and 8g (enables ANSI "graphics").  ALT-H toggles






Chapter 3 Pg 9            DSZ Reference Rev 11-14-89          Typeset 11-14-89



      two local echo ("Half Duplex") modes; the second displays a newline
      (CR/LF) when Enter is keyboarded.  Keyboarded ASCII characters are sent
      to the modem.  ALT-B sends a break.

      Modem characters print on the screen.  A device driver such as ANSI.SYS
      may be used to recognize escape sequences.

      DSZ's ZMODEM AutoDownload(Tm) detects the start of a ZMODEM file
      download and accepts the file(s) without operator intervention.

rz    [-abenprt+Yy] [dir] [file ...]          (ZMODEM receive) **

rb    [-abt+y] [dir] [file ...]     (YMODEM receive) **

rb -g [-abt+y] [dir] [file ...]     (YMODEM-g receive) **

rc    [-abt+y] file1                (XMODEM/CRC receive)

ro    [-abt+y] file1                (XMODEM OverThruster receive)

rx    [-abt+y] file1                (XMODEM receive)

rx -g [-abt+y] file1                (Qmodem-G receive) **

      ** Download directory specification and -g ignored w/o registration


sz    [-abefnprtFYQS+y] [-w[N]]  [PREFIX=p | ONAME=n] file ...(ZMODEM send)

      The "sz" and "sb" commands exploit DOS's tree structured file system.  A
      directory or disk specifier expands to all files in that directory.

      If you use PREFIX= or ONAME= with the "sb" or "sz" commands, these
      pathnames should be entered in lower case unless the underlying file
      system supports upper AND lower case.


sb    [-ft] [PREFIX=p | ONAME=n] file ...     (YMODEM or YMODEM-g send)

sb -k [-ft] [PREFIX=p | ONAME=n] file ...     (YMODEM-1k or YMODEM-g send)

sx    [-t] file1                    (XMODEM, XMODEM/CRC, Qmodem-G send)

sx -k [-t] file1                    (XMODEM-1k send)


v     Verify the serial number by writing a log entry (see DSZLOG).

      v      1     0 bps    0 cps   0 errors     0  128 s/n 13027

      The letter "v" indicates a verification entry.  The first numeric field






Chapter 3 Pg 10           DSZ Reference Rev 11-14-89          Typeset 11-14-89



      is 1 if YMODEM-g is supported.  The last field is the serial number.
      Unregistered copies show a s/n of 0.

The meanings of optional arguments to the file transfer commands are described
in DSZBG.DOC and the ZCOMM/Pro-YAM manual.

The s (SlugBait) option prevents a receiver from receiving a file without
accounting for it.  Attempts to do so are flagged with a Q status in the log
file.  This option can cause a transfer that legitimately fails near the very
end of the file to be reported as Questionable rather than ERROR.

Send files may be specified indirectly:
                             dsz sz @C:files.lst
sends the files in C:files.lst.  This provides another means of bypassing the
DOS command line limit.  The first letter must be "@" and the third letter
must be ":" to distinguish this from an ordinary pathname.  Pathnames in the
indirection file may be separated by any combination of space(s), tab(s), CR
and/or LF.  No spaces may appear inside a pathname; "FOO     .BAR" won't work.

3.1  Interrupt Keys

Ctrl-Break Terminates the transfer in progress.

ALT-N Abruptly terminates (NUKES) the transfer in progress.

Ctrl-X Typing a dozen Ctrl-X characters to another ZMODEM program terminates
     ZMODEM operations.

ALT-F Skips the current file in ZMODEM transfers.

ALT-B Cancels the current ZMODEM session.


























Chapter 4 Pg 11           DSZ Reference Rev 11-14-89          Typeset 11-14-89



4.  NUMERIC PARAMETERS

DSZ uses the following main numeric parameters, settable with the pxN command.

EXAMPLE: C>dsz pQ0


In addition, DSZ uses the Pro-YAM/ZCOMM zmodem numeric parameters described in
the Pro-YAM/ZCOMM reference manual and in DSZBG.DOC.


B   Set the size of buffer used for disk reads and writes.  The default is
    1024, 4096 maximum.  If your copy of DSZ is running on a floppy disk
    system or a very slow turkey hard disk, a larger value may give better
    results.  Too large a value may exhaust memory, induce receiver timeouts,
    cause disconnects(!), or generate spurious CRC errors.  If performance
    logging doesn't work, this parameter is too big.  This parameter is
    supported on versions compiled with TurboC.

    EXAMPLE: C>dsz pB4096 sz A:floppy.fil

    Setting the buffer size may lock out the performance log, DSZFILES, and/or
    indirect pathname list in the "tiny model" DSZ flavor.

    IF YOU AREN'T BLOODY SURE YOU NEED A BIGGER BUFFER, DON'T USE ONE.

O   This parameter controls XMODEM OverThruster(TM).  It is described in
    dszbg.doc.  This file is part of the software package sent to paid
    registrants.

P   After a "speed" command, giving a p command (display parameters), the P
    parameter value will indicate the type of serial I/O UART chip detected.
    DSZ automatically detects and enables the FIFO buffer on the NS16550A and
    Intel 82510 chips.

    EXAMPLE: dsz port 1 speed 19200 p


    0  Indicates a standard 8250 or 16450 UART with no special features.

    1  Indicates an NS16550A with 16 deep receive buffering.  This is the
       preferred chip.

    2  Indicates an Intel 82510 with 3 deep receive buffering.

    The sequence "port 1 pP1 speed 19200" bypasses DSZ's verification checks
    normally performed on the FIFO configuration and may allow a defective
    FIFO on certain chips to be used.  This incantation is not required for
    the NS16550A.








Chapter 4 Pg 12           DSZ Reference Rev 11-14-89          Typeset 11-14-89



Q   Error code returned to DOS (default 1).  (Success always returns 0.) Some
    programs toss cookies when confronted with certain exit codes.

    EXAMPLE: C>dsz pQ-1 sz foo.bar


    DSZ reports an error if no files have been transferred, even if the
    command used wasn't supposed to transfer any file(s).

S   Timeout in seconds (default 15) waiting for restraint release (XON and/or
    handshake).

W   Wait for Enter key before exiting after an error.  Effective only on
    registered copies.  Useful when calling DSZ from DESQview, allows the
    window to close unless there is an error message that should remain
    visible.

    EXAMPLE: C>dsz pW1 sz foo.bar


a   Calibrates certain protocol timeouts used with XMODEM and YMODEM transfers
    (Cybernetic Data Recovery(TM)).  This parameter does not affect ZMODEM
    transfers.

    The a numeric parameter is automatically set to 2000 for a 4.77 mHz PC or
    XT, 4000 for a PS2/30, 6000 for an 8 mHz 1ws AT, and 12000 for a PS2/80.
    If your computer has a speedup card or otherwise runs unusually fast (or
    slow!) for its type, you may set the a numeric parameter to a value that
    reflects its speed.

    EXAMPLE: dsz port 2 pa4000 rb


    NOTE: Setting this parameter does not suppress the "Unknown Machine Type"
    message which is displayed before the command line is scanned.

d   A non zero value (the default) causes incoming files received with ZMODEM
    and full YMODEM transfers to have their Date set to that sent in the file
    header.  ZMODEM's file management features depend on the transmission of
    each file's modification date.  Files will have the same creation date,
    even if the two machines are in different time zones.  When transferring
    files to/from a Unix system, creation dates are interpreted according to
    GMT or Universal Coordinated Time.  File dating may be disabled with a pd0
    command.
    NOTE: Backdating file creation times may confuse some backup programs.

v   Verbose level (debugging output) Negative values inhibit some routine
    messages.  Setting v to 1 or greater causes serialized copies to ring the
    bell when a transfer is done.








Chapter 4 Pg 13           DSZ Reference Rev 11-14-89          Typeset 11-14-89



z   Timezone in minutes behind GMT, used for ZMODEM and True YMODEM file
    transfers to coordinate the actual date of the file with computers in
    other time zones.  Effective on registered copies.  PDT or MST corresponds
    to 420.  This may be preset with the ZONE DOS environment variable.





















































Chapter 5 Pg 14           DSZ Reference Rev 11-14-89          Typeset 11-14-89



5.  ENVIRONMENT VARIABLES

The following DOS environment variables may be set to modify DSZ operation.
DOS environment variables are set by giving a command to DOS.


EXAMPLE: set DSZPORT=2


These DOS "set" commands may be placed in your AUTOEXEC.BAT file or given just
before you run your communications program.

IMPORTANT! Do not put spaces in these commands!!
set DSZPORT  =  2 WILL NOT WORK!


DIRRX (Registered copies only.) Specifies the directory to receive (download)
    files.  If the sting in DIRRX ends with "/", directory and/or disk
    designators in the incoming pathname are stripped, and only the stem (name
    and extension) is used.  Otherwise, if an incoming file has an absolute
    pathname, the incoming pathname is used.

    EXAMPLE: set DIRRX=C:/rxdir/
    dsz rz -r


    EXAMPLE: set DIRRX=B:/

    The DOS "set" command defining the receive directory may be placed in your
    AUTOEXEC.BAT file.  Make certain there is enough environment space to hold
    this value.  Confirm this by typing "set" to the DOS prompt and verifying
    the DIRRX value is listed correctly.

DSZFILES May contain a list of up to 9999 pathnames to transmit, with entries
    separated by spaces.  If present, DSZFILES is used in place of a normal
    command line list of files to send with the sb and sz commands.

    EXAMPLE: C>set DSZFILES=file1 file2 file3 *.c
    C>dsz port 2 handshake on sz -rr

    In practice, this string would be built up by a calling program and passed
    to DSZ with a "spawnvpe", "execvpe", or similar subroutine call.

    SEE ALSO: Pathname list specification @C:files.lst

DSZLOG log file to receive entries for files sent and received.  (Default
    null).  Sample entries:

Z  46532 38400 bps 3324 cps   0 errors    66 1024 DSZ.COM 1177
Z 124087 19200 bps 1880 cps   0 errors     6 1024 MXY.TMP 1177







Chapter 5 Pg 15           DSZ Reference Rev 11-14-89          Typeset 11-14-89



    Transfer times are based on the DOS time of day clock and have up to two
    seconds' uncertainty.  As with all protocol throughput reports generated
    by Omen Technology programs (and contrary to the false claims of some
    critics), DSZ's throughput figures for ZMODEM, Kermit, and True YMODEM(TM)
    transfers do not take "credit" for pathname and/or protocol overhead
    characters.  DSZ's throughput reports do not include the time required to
    send the pathname.  This understates the true time required to transfer
    files, but the time required to send the pathname often depends on the
    alacrity of the operator, and thus does not always reflect the performance
    of the protocol itself.

    Transfers measuring less than one second are reported as having 9999
    characters per second throughput.

    The unlabeled numeric field after the error (retry) count is the number of
    flow control stoppages encountered sending the file.  This number gives an
    indication of flow control restrictions (overloaded networks, etc.)
    encountered during the transfer.

    The last numeric field before the file name is the YMODEM block size or
    ZMODEM subpacket length used for the last block in the file.

    The last field is the serial number of the other program, or -1 if this
    information is not available.

    The code letter indicates the type of transfer, Z (ZMODEM), S (X/YMODEM),
    R (X/YMODEM), E (error), or L (transfer terminated by loss of data
    carrier).

    WARNING: If DSZ encounters a loss of carrier or other fatal error
    condition before a file COMMENCES transmission, a log entry may not be
    made.


    EXAMPLE: C>set DSZLOG=C:/yam/dszlog






















Chapter 5 Pg 16           DSZ Reference Rev 11-14-89          Typeset 11-14-89



DSZOPT (Registered copies only) String containing default options for DSZ file
    transfers.  Options are optional modifiers to the DSZ sz, rz, sx, rx, sb,
    rb commands.

    A T may be appended to the string to force DSZ to exit after it has
    recognized a ZMODEM AutoDownload(Tm) request.

    An 8g may be appended to the string to make BBS (ANSI) graphics the
    default for DSZ's t command.  The ability to preset these options is
    especially helpful for controlling ZMODEM automatic downloads from DSZ's t
    command.

    EXAMPLE: C>set DSZOPT=r
    Enables DSZ's Intelligent Crash Recovery(TM) as a default.

    Let's say you wish ZMODEM crash recovery, and BBS "graphics" for the DSZ
    term function:
    C>set DSZOPT=r8g


    WARNING: Do NOT include "ena" or any other commands in the DSZOPT string.
    With the exception of the "8g" mode, only **options** may be placed in the
    DSZOPT string!  (Options are the letters that modify the sz, rz, sb, etc.
    commands.  In "rz -r", "r" is an option.)

MAXBYTES Maximum number of bytes allowed for transfer.  If this number is
    exceeded, DSZ skips the offending files (ZMODEM) or aborts remaining files
    in the batch (YMODEM).

DSZPORT Default communications port override, default 1.

    EXAMPLE: C>set DSZPORT=2

    IMPORTANT! NO SPACES!!



ZONE sets the z numeric parameter to the number of minutes the current local
    time lags GMT time.  PDT or MST corresponds to 420.  PST corresponds to
    480.
    EXAMPLE:
    C>set ZONE=420















Chapter 6 Pg 17           DSZ Reference Rev 11-14-89          Typeset 11-14-89



6.  EXAMPLES

dsz sz c:foo.arc              (send 1 file with ZMODEM)

dsz sz f1.c f2.c f3.c         (send 3 files with ZMODEM)

dsz sz c:foo.* b:*.c          (send multiple files with ZMODEM)

dsz sz -Z *.lst               (send text files with compression)

dsz sz -r bigone.arc          (CRASH RECOVERY: resume interrupted transfer)

dsz rz -r                     (CRASH RECOVERY: resume interrupted transfer)

dsz rz -rr                    (CRASH RECOVERY with file comparison)

dsz handshake both sz yzmodem.arc       (Hardware+Software handshake)

dsz sz -n *.*                 (send files that are newer or rx has no copy)

dsz sz -Yn *.*                (Only send files that are newer than receiver's
copy)
                              (Do not send files that do not exist on
receiver's disk)

dsz rz C:/UPLOADS             (receive files to specified directory #)

dsz port 2 speed 38400 handshake both restrict rz
                              (Restrict provides protection for BBS's)

dsz rz  -y prog.arc           (ZMODEM, single file pathname override)

dsz z pr1 rx foo.dat          (XMODEM receive, remove file if error)

dsz pO60 ro foo.dat           (XMODEM/OverThruster receive, GEnie MNP #)

DSZ LRC L-Y NEWPROG.ARC       (generate lower case "rc -y" command)

dsz sz foo >debug.dmp         (Debugging data dump)

dsz sz @C:/bbs/files.lst      (Indirect file list)

# Registered copies only














Chapter 7 Pg 18           DSZ Reference Rev 11-14-89          Typeset 11-14-89



7.  IN CASE OF DIFFICULTY

If you have difficulty getting DSZ to work, start with the following command
to DSZ, given directly from the DOS prompt, without running any TSR or other
COMM program:

                              dsz port 1 speed 2400 d t

Type it exactly as it appears above; do NOT use upper case.

(Change the port number and speed as necessary.  Use only COM1 or COM2 for
testing.)

This connects you to the modem.  Dial a bulletin board by typing AT commands
to the modem ("ATDP621-3746 <enter>") to make it dial the BBS.  Log in as
usual.  Then, request a ZMODEM download of a file you don't already have.  The
file will download automatically, you don't have to do anything.  This
procedure verifies the correct operation of DSZ.


7.1  LOCKUPS

7.1.1  Insufficient Memory
DSZ complains when it detects insufficient memory to operate.  When calling
DSZ from another program, there may be ALMOST enough memory for proper
operation, but DSZ locks up during a transfer or the calling program freezes
after DSZ displays the "DSZ Finished" message.

Sometimes there is a message about insufficient memory, sometimes just a
lockup and no message.  To verify this problem, call CHKDSK from within your
comms program (not from DOS!) by defining it as an external protocol.  If you
use an interface program (Hotkeyz, Prodoor, etc.), you must call CHKDSK from
that program, as those programs also reduce the memory available to DSZ.

CHKDSK should report at least 64k free memory.  If less memory is reported,
reduce the size of the COMMS program's capture buffer, or reboot the system
with fewer/smaller device drivers and TSR programs.  Calling DSZ directly from
the comms program instead of from an interface also saves memory.


7.1.2  Environment TOO BIG
A large environment may cause DSZ.COM to lockup.  The size of the environment
(the amount of text you get when you give the DOS "set" command) is subtracted
from the data space available to 8086 C programs.  This can be a problem with
DSZ.COM, whose 8086 tiny model limits code, data, stack, and environment to 64
kb TOTAL.  If DSZ.COM complains about the environment being too big, you
should correct the problem.  Use DSZ.EXE (compiled with 8086 small model) to
alleviate this problem.









Chapter 7 Pg 19           DSZ Reference Rev 11-14-89          Typeset 11-14-89



7.1.3  Bad COMM Port Configuration
DSZ is fastidious about which interrupt vectors it takes over.  Unlike some
programs, DSZ uses only the correct interrupt vector for its interrupt service
routine.  (This allows multitasking.)

DSZ obtains and releases this vector with standard DOS function calls.  This
allows multi line operation under DESQview and other multitasking systems.

Incorrectly configured serial ports that work with programs that pig out both
IRQ3 and IRQ4 will lock up with DSZ.  If DSZ locks up the machine as soon as
it tries to send or receive data, this is usually the fault.  Make sure the
comm port is strapped correctly; COM1 uses IRQ4, COM2 uses IRQ3.  DSZ will
lock up if the comm port is not properly set up.

In addition, DSZ will not work properly if two devices are connected to the
same IRQ line, even when some other programs (that don't use interrupts as
intensively) do work normally on the same machine.

COM3 and above are not widely standardized.  If you have problems with COM3,
chances are your "COM3" is non standard.


7.2  Incorrect Batch Files

Incorrect batch files are the number one source of problems using DSZ for
uploads and downloads.  Bulletin board programs with convoluted batch file
mechanisms exacerbate the problem.

DSZ's command line echo was added to assist in correcting defective batch
files.  You should see a display like:

Command line = 'rz '
or
Command line = 'port 2 speed 9600 sz foo.baz '

In general, the Command line display should look like one of the examples in
this document or those displayed by DSZ itself.  (The Command line display
does not include the name of the DSZ program itself.)

Try running DSZ by itself, without any batch files or TSR programs, calling it
directly from DOS as described above.


7.3  Commands Entered in Upper Case

Most DSZ commands and options must be entered in lower case (small letters,
not big letters).  Where the documentation or help screen indicates "rz", you
must use "rz" and not "RZ".









Chapter 7 Pg 20           DSZ Reference Rev 11-14-89          Typeset 11-14-89



7.4  No Carrier Detect

If you see a No Carrier Detect message, and you haven't lost the connection,
you need to give the d command:
                              dsz port 1 speed 2400 d t

Better yet, fix your modem cable or modem to allow proper operation of the
Carrier Detect signal (CD)!

Some BBS and/or "door" programs hang when the program (such as DSZ) they call
returns with a non 0 exit status.  Please refer to the "EXIT STATUS" chapter
of the document for more information.

7.5  PKARC 3.6

It has been reported that PK36 grabs some interrupts and doesn't restore them
on exit in an attempt to prevent hacks of the program.  Since eliminating that
particular version and cleaning up memory, high speed xfers even with 8250
UARTS work properly again.

The problem with PK 3.6 appears to be most severe if a BBS operator has
doorware, etc that accesses the PK programs from a shell of some sort.  This
info may be helpful to users who are having otherwise inexplicable file xfer
problems.

Phil Katz has written me that this problem has been corrected in subsequent
versions.


7.6  DOS 3.x

DOS 3.x systems may need to have a "STACKS = 8,256" line in CONFIG.SYS to
prevent antisocial behavior. This is required on the NEC Multispeed, or if
certain TSR's are used.


7.7  Perstor Controllers

Several reports have been received indicating Perstor disk controllers
interfere with data communications.  Perstor is reportedly working on a fix.


7.8  IBM PS/2 Model 50Z

Early samples of this machine have a design error on the motherboard that
causes comms programs to lock up the machine.  Replacing the motherboard with
a correctly functioning unit from current production corrects the problem.
The part number of the replacement PS2/50 Z motherboard is 35F5928.
(Information provided by John M. Choma 73047,3566) U.S. IBM has stonewalled on
this issue, but in December 1988 agreed to replace the defective motherboards
under warranty.






Chapter 7 Pg 21           DSZ Reference Rev 11-14-89          Typeset 11-14-89



7.9  Brain Damaged UARTS

Omen Technology has received reports of problems with buggy 8250 type UART
integrated circuits in Leading Edge modem boards, serial port interfaces, and
computers.  The defective chip logic affects high performance software.
Replacing the buggy chip with a newer chip (16450 or NS16550AN) corrects the
problem.

The UM82450 chip in the Zoom 2400HC also appears to cause problems.

The NS16550AN is a pin compatible plug in replacement for 8250 and 16450
serial chips.  Omen Technology software enables the FIFO buffer in the
NS16550AN to prevents loss of data from poorly written device drivers, TSR
programs, etc.

The NS16550AN has better electrical characteristics than the older UART chips.
386 and fast 286 machines should use the NS16550AN for best results.  Omen
Technology software has been written to allow time for the older UART chips to
operate. However, there is a limit to how much the software can rearrange chip
accesses without resorting to performance robbing wait loops.  Some other
software is not as forgiving of slow chips.

Jameco Electronics at 415-592-8097 sells National NS16550AN chips mail order
(credit card) in small quantities.  Another source is Arrow Electronics at
800-932-7769 (516-467-1000).  Be sure to ask for the NS16550AN.  It's
important to get the "AN" part, other versions won't do.

PC BRAND at 800-722-7263 (in Illinois 312-226-5200) is selling I/O cards in
which both UARTs are socketed, allowing them to be replaced by NS16550AN
devices.  Shipping and handling is included in their $45 price.  (From Roger
E.  Hough)



7.9.1  Everex Internal Modems
Numerous reports have been received concerning difficulties with Everex modem
cards.  Some of these cards contain buggy 8250 chips which are not up to the
demands of full duplex streaming protocols such as ZMODEM.  Replacing the
buggy 8250 chip with a 16450 (or better yet NS16550AN) chip corrects these
problems.


7.10  Weird Iron

A few machines, some with V20 CPUs, don't like DSZ.COM.  We have not been able
to repeat this; TeleGodzilla (using a V20) runs DSZ.COM without a hitch.
Switching to DSZ.EXE has cleared up the problems on other machines.










Chapter 7 Pg 22           DSZ Reference Rev 11-14-89          Typeset 11-14-89



7.11  Will the real YMODEM please stand up?

Some XMODEM programs claiming to support YMODEM do not send or accept the
YMODEM pathname block.  1024 byte XMODEM is XMODEM-1k, not the YMODEM defined
by Ward Christensen in 1985 when he invented the term YMODEM.  1987 and later
versions of YMODEM.DOC remind the reader of the official YMODEM definition,
which has not changed since YMODEM's coinage in 1985.


7.12  286 and 386 Extended Memory

Virtual memory disk caches and ramdisks using 80286 or 80386 extended memory
require a kludge hardware reset of the CPU chip to return to the normal "real
mode" after accessing extended memory.  This interference to the interrupt
response time causes lost characters on comm ports, and may be minimized by
specifying shorter memory transfers.

Switching to a National NS16550AN UART chip helps tremendously, allowing
transfers at 115200 bps instead of 9600 bps with a standard 8250.  Please
refer to the subchapter on "Brain Damaged UARTs".





































Chapter 8 Pg 23           DSZ Reference Rev 11-14-89          Typeset 11-14-89



8.  BACKGROUND OPERATION

Three DESQview description files are provided to demonstrate background
operation with modest (66 kb window) memory requirements.  DSZ uses tight
C/ASM code, table driven CRC generators, and buffered receive and transmit for
good performance in the background without hogging CPU cycles.  On a QIC Labs
8 mHz PC-AT clone, DSZ can download files in the background (3 background
clock ticks, 9 foreground clock ticks) with a throughput better than 9600 bps.

2S   Prompts for file name(s) and sends them with ZMODEM protocol.  File: 2S-
     PIF.DVP

2T   Talks to the modem and allows manual YMODEM (F3) or automatic ZMODEM
     downloads.  File: 2T-PIF.DVP

2A   Like 2T, but using Quarterdeck's dvansi.com memory resident ANSI CRT
     device driver to process ANSI screen codes.  File: 2A-PIF.DVP DS.BAT is
     the batch file used by 2A.

These files are written for a port 2 local connection and \TMP directory, but
may be modified to suit your requirements using the DESQview CP command.  The
W numeric allows DESQview to close the window after DSZ finishes, providing a
pleasant user interface.

Other DVPs, Scripts, and Batch files are available on the DESQView conference
on the Sound of Music as DVDSZ20Z.ARC.

Please consult the DESQview documentation for instructions on installation
procedure for the DVP files.

Operation at high speed (above 9600 bps) may require the DESQview "Optimize
communications" performance Advanced Setup option.

Newer versions of DESQview may require more "common memory" allocation (6-8 k
bytes) to operate with DSZ.  Some versions of DESQview do not operate properly
with DSZ; DESQview 2.0 is known to work, and DESQview 2.25 is reported to have
fixed bugs in intermediate versions.

On 286 and 386 machines, some DESQview operations involve swapping memory
contents with buffers in extended memory.  As with extended memory ramdisks
and disk caches, this causes errors with high speed communications.  The
considerations discussed in the "286 and 386 Extended Memory" subchapter apply
here.  Since this DESQview extended memory swapping is asynchronous with
respect to DSZ's file transfers, "handshake slow" doesn't help.  The solution
is to force DESQview's memory swaps to use smaller blocks (with interrupts
allowed between blocks) and/or use NS16550AN chips for the serial interface.

         ***********************************************************
                                   WARNING
When running DSZ under a multi tasking system such as DESQview, do not allow
two programs to access the same comm port at the same time.  At best, such






Chapter 8 Pg 24           DSZ Reference Rev 11-14-89          Typeset 11-14-89



actions will disrupt communications.  At worst, your computer will attempt to
open a subspace channel to V'ger.

When running a comm program under DESQview or any related multitasking
executive, DSZ must be called directly from the comm program, in the same
window.  DO NOT open a separate window for DSZ unless you were about to power
down the computer anyway.
         ***********************************************************

With some communications programs, you can make the call, log in, and then
exit (closing the window) without disconnecting the modem.  At this time you
can fire up DSZ with the "t" command to allow YMODEM or ZMODEM downloads in a
small window.
Example File: 2A-PIF.DVP

Alternatively, you can start DSZ from the DOS prompt, then type "AT" commands
to the modem to call the bulletin board.  DESQview's "learn" facility may be
helpful here.







































Chapter 9 Pg 25           DSZ Reference Rev 11-14-89          Typeset 11-14-89



9.  CALLING DSZ FROM COMM PROGRAMS

It may be necessary to give a

SET COMSPEC=A:\COMMAND.COM

(change as needed) in your AUTOEXEC.BAT file to allow programs to call DSZ.

Note: NO SPACES in the SET command!

9.1  GT POWER 13.00/14.00

GT Power version 13/14 includes a YMRX.BAT (YMODEM-g receive) file with an
"rz" command.  You guessed it, "rz" is for ZMODEM protocol (the z means
ZMODEM!).  Please change the file to use the correct "rb -g" for YMODEM-g.

The files ZMTX.ARC and GT1300.NOT available on many bulletin boards contain
useful information for GT Power users.

9.2  PROCOMM

DSZ may not operate properly when called from ProComm if ProComm has files
open at the time.

A number of reports have been received of problems running DSZ from ProComm
Plus because of insufficient memory.  Please refer to the subchapter on
LOCKUPS.

When running under ProComm's Host mode, failure to use the DSZ CON command may
cause ProComm to lock up the computer, or at least interfere with file
transfers, etc.

EXAMPLE: DSZ CON sz %1


A number of third party programs have been developed to provide a congenial
interface to DSZ if you have enough memory to spare.  The POE, PCALL, DSZ_ZAP,
and PROZ programs have been popular in interfacing DSZ to ProComm's editor
gateway.  These programs are available on many bulletin boards.

Hint: the DOS PATH environment variable must include ProComm's directory to
allow POE to locate all the POE files,.  The POE files should be stored in the
ProComm directory.  Setting the "PROCOMM" environment variable is
insufficient.

9.3  PROCOMM PLUS

DSZ may not operate properly when called from ProComm if ProComm has files
open at the time.

Here are some handy settings for ProComm Plus.






Chapter 9 Pg 26           DSZ Reference Rev 11-14-89          Typeset 11-14-89



First, set the DOS environment as necessary before running ProComm.  Give
these commands to DOS before running ProComm.

Note: NO SPACES in the SET command!
SET DSZPORT=2                           (Only needed for COM2)
SET DSZLOG=DSZ.LOG            (Only if you wish a log file)

Then set ProComm's external protocol strings to:
A- External protocol 1 upload filename:  ZMODEMU
B- External protocol 1 download filename: ZMODEMD

The following batch files are included in the DSZ archive:
ZMODEMU.BAT contains:         DSZ sz %1 %2 %3 %4 %5 %6 %7 %8 %9
ZMODEMD.BAT contains:   DSZ rz
ZMODEMDR.BAT contains:   DSZ rz -r
ZMODEMAD.BAT contains:        DSZ t

Once you've got the hang of things the "ProComm way", try the "dsz t" command
described above to give you automatic ZMODEM downloads (Look Ma, no
keystrokes!!!)..

9.4  Qmodem

The following is based on a message from Mike Cody, sysop of HomePlate 313-
385-9969 3/12/24/96 HST

Go into Qinstall and go to frame 3 Directories. Then select External protocols
#3 I think. Now you will see a definition area to tell Qmodem the
Letter,batchfile combo to use.

Now put Z in the letter definition, Zup.bat in the u/l batch zdown.bat in the
d/l batch, and Y in the batch protocol. Now save it at the menu with f10 and
S.

Then go to DOS and create the following batch files in your Qmodem
directory...

zdown.bat: DSZ port %2 speed %1 rz -rr

zup.bat: DSZ port %2 speed %1 sz %3

These are the batch files that will be called by Qmodem.  If you did
everything right when you hit PGDN or PGUP you will see an external protocol
called Z) Zmodem in the box. For an easier time do a search for either
External.arc or maybe the string "Qmodem" in the file database as there is a
file with several external protocols and batch files available in the Mahoney
file section (EXEC BBS).

The following batch files for Qmodem are included in the DSZ archive:

ZDOWN.BAT contains:           DSZ port %2 speed %1 rz -rr






Chapter 9 Pg 27           DSZ Reference Rev 11-14-89          Typeset 11-14-89



ZUP.BAT contains:             DSZ port %2 speed %1 sz %3

9.5  BULLETIN BOARDS

When installing DSZ on a bulletin board or host system, be sure to check for
proper operation when the caller hangs up while a file is being sent or
received.

Currently, Only the TurboC version supports file sharing (shared read access
on files sent by  dsz).

Some bulletin board interface routines do not call DSZ to send a file until
they have verified the file's presence by opening the file.  If this checking
is done in DOS's default exclusive open mode, dsz's file sharing will be
defeated.










































Chapter 10 Pg 28          DSZ Reference Rev 11-14-89          Typeset 11-14-89



10.  FLOW CONTROL

If you plan to send files over Telenet (PC-Pursuit), you must refer to the
Pro-YAM or ZCOMM Reference manual (in ZCOMMDOC.ARC) FLOW CONTROL chapter for
vital information on flow control considerations necessary for proper
operation of ZMODEM and other streaming protocols.



















































Chapter 11 Pg 29          DSZ Reference Rev 11-14-89          Typeset 11-14-89



11.  ERROR MESSAGES

Virus check passed.  This message indicates DSZ's virus check has not
discovered a virus infection.

Virus check failed.  This message indicates DSZ's virus check has detected a
possible virus infection, or some hardware or software condition has prevented
the check from completing normally.

COM2 1200 bps Carrier Detect enabled Handshake slow
Command line = (commands)
This is a normal message displayed to help resolve problems with incorrect
batch files.  The port number, speed, carrier detect ("enabled" or "DISABLED")
and "handshake" indicate the selected mode of operation.

DSZ FINISHED! exit code = 0
This is DSZ's normal exit when at least one file has been transferred and no
unrecoverable errors have been detected.  If an error such as a failed file
transfer had been detected, the exit code would be 1, or the value set in the
Q numeric parameter.

As the message implies, DSZ has done all of its processing, and has return the
communications port and vector to its original value before displaying this
message.  If the computer locks up after this message is displayed, there's
something wrong with the program that called DSZ, not with DSZ itself.

Unknown Machine Type XX, 'a' parameter preset to 6000 indicates a ROM BIOS
that does not follow the IBM specification for identifying the machine type.
If your computer causes DSZ to display this message, you may set the a numeric
parameter described elsewhere in this document.  This message is generated
before any commands are read, so do not be alarmed when you "discover" that
setting the a parameter doesn't make this message go away.  The a parameter
does not affect ZMODEM transfers.

Please send us a postcard or letter indicating the reported hex value for
machine Type, name of the computer, and its speed so we can include that
machine type in a future release.

Need more memory to run DSZ or Abnormal program termination is displayed by
the TurboC startup routine if DSZ is run in too small a memory partition.  If
you see this message, use a larger memory partition for DSZ or remove some
memory resident programs.  This message may also appear if the calling program
fails to free memory before calling DSZ.

No Carrier Detect is displayed when DSZ recognizes a lack of carrier detect
signal from the modem.  Most support calls concerning "No Carrier Detect" are
caused by the user failing to tell DSZ to use the correct port.  DSZ does not
magically divine the COM port number; if the default COM1 is incorrect, DSZ
must be told what port to use with the port command or the DPORT environment
variable.







Chapter 11 Pg 30          DSZ Reference Rev 11-14-89          Typeset 11-14-89



No Carrier Detect may also be caused by a line disconnect, defective cable, or
incorrect modem strapping.  It may be disabled with the d command.  Sometimes
this is caused by setting the B parameter to too large a value.

Garbage Count Exceeded Indicates ZMODEM has not detected a valid start of
header in a reasonable number of characters.

If DSZ becomes "stuck" on emitting this messages, it is possible the sending
program may not be able to recognize and act upon transmission requests (ZROPS
headers).  The sending program should be corrected.  In the meantime, setting
a ZMODEM packet length with the "zmodem pl4096" ("l" is the small letter l)
command will force the sender to wait for the receivers' progress reports.

Permission denied comes from the Microsoft C Library.  This is caused by
attempts to modify a read only file or directory, or to create a file in a
nonexistent directory.

A furtive flashing appearance of XOFF or FLOW during ZMODEM or YMODEM-g file
sending signifies DSZ is responding to flow control restraint.  This is normal
operation when buffered modems or packet switched networks are used.  ZMODEM's
robustness and reliability allow creative users to transfer files over unusual
multiple computer lash-ups, causing modem data lights and computer status
displays to dance in unfamiliar rhythms.

Not allowed to overwrite %s By default, DSZ will not overwrite an existing
file.  Use the -y or -n or -r option to overwrite/update existing files.


11.1  Got ZRPOS

Got ZRPOS indicates the receiving program has detected a transmission error
and has requested retransmission.  In other words, ZMODEM is doing its job of
detecting and correcting missing and garbled data.  If this happens more often
than observed line errors would indicate is reasonable, there may be a flow
control problem in one of four areas:

  + Between the sending program and its modem.  If using an interface speed
    higher than the transmission speed, or modem to modem error correction
    (MNP, LAPB, PEP, etc.), check that the modem and the sending program are
    configured for the same flow control methods.  Omen Technology's software
    is faster than most other programs, and may expose flow control problems
    not seen with slower software.

  + Between the sending modem and the network.  Correcting this requires
    "handshake both" to allow the sending program to honor both hardware (CTS)
    flow control from the modem and software flow control (XON/XOFF) from the
    network.

  + Between parts of the network.








Chapter 11 Pg 31          DSZ Reference Rev 11-14-89          Typeset 11-14-89



  + Between the receiving modem and the receiving program.  This can happen at
    high transmission speeds when the receiver has specified a large I/O
    buffer size with the B numeric parameter.

    Excessive interrupt latency from extended memory ramdisks or disk caches,
    and poorly written hard disk drivers also wreak havoc on streaming
    protocols but do not affect start-stop protocols (XMODEM, etc.).  Problems
    with extended memory disk caches may cause errors at regular intervals;
    check the receiver's error messages.

    To work around these problems, give the "handshake slow" command to the
    receiver.

Byte NNNN retry M: <error message> These messages appear when the protocol has
detected an error and is attempting to retransmit the garbled data.  These are
normal messages.


11.2  Serial Input Error: Line Status Register xx

Serial Input Error: Line Status Register HH indicates a slow device driver,
TSR program, or other software is disabling interrupts too long for the
program to accept incoming data, and some characters are lost.  A slow
response to folow control also triggers this message.

The value of the line status register is displayed in HEX.  The following
error conditions when present OR into the Line Status Register.


01   The Interrupt level circular buffer has been overrun.  The remote did not
     respond to 's XOFF or hardware flow control, and continued to send
     characters after being told not to.  This problem is alleviated by
     correct modem flow control configuration.


02   An 02 value for the LSR indicates Data Overrun.  "Data Overrun" means the
     computer was not able to respond to an incoming character from the UART
     (modem) in time to make room for the next incoming character.  Data
     Overruns are caused by poorly designed software (or ROM BIOS "firmware")
     locking out interrupts for excessive periods.  These lockouts prevent the
     communications program from responding to the incoming characters quickly
     enough.

     To correct Data Overruns, correct the offending condition(s) to allow the
     communications program to operate properly.

     Common causes of excessively long interrupt lockouts ("critical code
     regions") are disk drivers (BIOS), window managers, disk caches, TSR
     programs, EGA/VGA board auto-select.

     Some BIOS programs are written without regard to their effect on high






Chapter 11 Pg 32          DSZ Reference Rev 11-14-89          Typeset 11-14-89



     speed communications.  Sometimes better versions of the offending BIOS
     programs are made available if enough users complain about poor
     performance.

     Interrupt latency caused by EGA/VGA board auto-select can be often
     corrected by disabling the board's Auto-Select.

     Other chapters in this document give suggestions for working around
     excessive interrupt latency, primarily the handshake slow command and use
     of the NS16550AN UART chip.  Please refer to the "Brain Damaged UARTS"
     subchapter.

     Please try all the suggestions mentioned here before contacting Omen
     Technology about data overruns.


08   Framing Error generally caused by line noise or an incorrect transmission
     speed ("baud rate") or format (number of bits).  Most protocols require 8
     bits no parity (-8n) for proper operation.  This is set automatically by
     Omen Technology programs, but other programs may not be so smart.


10   Break Interrupt generally caused by line noise or an incorrect
     transmission speed ("baud rate") or format (number of bits).


18   Framing Error and Break Interrupt (see above) in combination.

Please refer to the In Case of Difficulty chapter of this document for
solutions.

Less commonly encountered DSZ error messages are explained in the Pro-YAM
manual.


11.3  COMMAND NOT FOUND

If you see this message, make sure DSZ is in the DOS PATH.  Sometimes this
error is caused by having too many environment variable strings.


11.4  Out of Environment

means there is not enough room in the program environment to accept more data.

DOS prints this message when it cannot allocate more memory to accommodate a
"set" command, such as "set dirrx=c:/downloads/".

Try moving the "set" commands to the batch file that calls your comms program,
or to your AUTOEXEC.BAT file.







Chapter 11 Pg 33          DSZ Reference Rev 11-14-89          Typeset 11-14-89



To increase environment, use the /E switch. The default is 160 bytes.

An example for your CONFIG.SIS file: SHELL= C:COMMAND.COM/E:256

NOTE: Large environments may cause DSZ.COM to lockup.  This is less of a
problem with DSZ.EXE.



















































Chapter 12 Pg 34          DSZ Reference Rev 11-14-89          Typeset 11-14-89



12.  SLOW TRANSFERS

Some users report slower than expected file transfers even when few or no
errors are reported.  Some possible causes are:

If "handshake slow" is used, throughput may suffer.  Try one of the other
solutions to the "Line Status Register = 02" error problem discussed above.
It may be possible to increase the modem's interface speed, say from 9600 to
19200 bps.

Bad phone lines will silently slow MNP modems, sometimes without any error
indications.  Of the modems disconnect fairly often you should suspect
marginal phone line conditions that are begin "covered up" by the MNP.

The other ZMODEM may have a parameter or option is use that acts to slow the
transfer under certain conditions.









































Chapter 13 Pg 35          DSZ Reference Rev 11-14-89          Typeset 11-14-89



13.  ASSOCIATED DOCUMENTS

Consult the Professional-YAM, PowerCom, or ZCOMM manual chapter "OPTIONS FOR
FILE TRANSFERS" for descriptions of the file transfer options.  The "FILE
TRANSFER BASICS" chapter explains the relative merits of XMODEM, YMODEM,
ZMODEM, and other protocols and gives tips on their use.  The "MAIN COMMANDS"
chapter describes the rb, rx, rc, rz, sb, and sz commands.  The "MODEM
INTERFACING" and "FLOW CONTROL" chapters contain important information on the
use of buffered modems with DSZ.

Information on the ZMODEM Inter Application File Transfer Protocol may be
found in ZMODEM.DOC, part of YZMODEM.ARC (available on CompuServe (IBMCOM) and
GEnie (IBM Roundtable)).

C Source code for XMODEM, YMODEM, and ZMODEM transfers is included in
RZSZ.ZOO.  This file includes a Pro-YAM/ZCOMM script to upload a bootstrap
file to a Unix system, force its compilation, and (if the compilation is
successful) upload the rz/sz source files.

The C source code now includes VAX/VMS support.

13.1  ZMODEM Developer's Collection

Omen Technology sells the "ZMODEM Developer's Collection" for $89.00.  This
diskette includes the most recent public domain versions of YMODEM.DOC,
ZMODEM.DOC and the Unix/VMS rz/sz C source code for YMODEM and ZMODEM.  A set
of public domain PC-DOS executable programs are included for convenience.  For
many developers, this collection affords a significant labor savings in
obtaining these materials.




























Chapter 14 Pg 36          DSZ Reference Rev 11-14-89          Typeset 11-14-89



14.  FILES

DSZ.COM, DSZ.DOC, 2A-PIF.DVP, 2S-PIF.DVP, 2T-PIF.DVP, BBS_REG.TXT, DS.BAT,
FIX.BAT, MAILER, ZMODEMAD.BAT, ZMODEMD.BAT, ZMODEMDR.BAT, and ZMODEMU.BAT
constitute Omen Technology's DSZ.ARC.  These same files are in DSZ.ZOO on the
distribution diskette mailed to registered users.[1]

2S-PIF.DVP, 2A-PIF.DVP, DS.BAT, and 2T-PIF.DVP are used with Quarterdeck
Office Systems' DESQview multitasking executive for background operation.
Their use is described in a previous chapter of this document.

ZCOMMDOC.ARC (manual), ZCOMMEXE.ARC (programs), ZCOMMHLP.ARC (help processor
and database), make up the ZCOMM communications tools shareware distribution.
The ZCOMM files are available on finer bulletin boards.

RZSZ.ZOO contains ZMODEM "C" source code for COMPLETE VAX VMS and Unix/Xenix
programs licensed for use transferring files to/from licensed Omen Technology
products.

DSZ.EXE compiled with the Xenix to DOS XC provides moderately higher maximum
throughput (1700 vs 1300 cps downloading to a 4.77 mHz XT).  The speed
difference is a function of the compiler, the source code is the same.  The
Xenix XC version requires more memory, and does not support file sharing or a
large I/O buffer.  This flavor is available in DSZEXE.ZOO.

ZCOMM and Pro-YAM also run at a higher speed than DSZ.COM.

DSZBG.ZOO contains DSZBG.DOC.  Part of the DSZ registration disk (and not for
public distribution), this file provides background information on the
ZCOMM/Pro-YAM commands provided in DSZ.  The same information is available in
ZCOMMDOC.ARC.

The ZOO archive format is a machine independent improvement on the PC-DOS
specific .ARC format. The ZOO format has been precisely defined, and stable
ZOO archivers/dearchivers are available on a wide variety of systems.

LOOZ.EXE unpacks .ZOO archives.  LOOZ.DOC describes LOOZ.EXE.  Be certain to
type the arguments to LOOZ in lower case, UPPER CASE WILL NOT WORK.







__________

 1. DSZ.ZOO is supplied to registrants instead of DSZ.ARC because not all
    registrants have copies of unarchiving programs.  The registration disk
    includes a copy of LOOZ, a simple dearchiver for ZOO files.







Chapter 15 Pg 37          DSZ Reference Rev 11-14-89          Typeset 11-14-89



15.  CHANGES

Be sure to save your serial number/password (SNP) card and the putsnp program
you received from Omen to use with future versions of DSZ you may download!
The current DSZ version is maintained on GEnie (IBM Roundtable), EXEC-BBS,
CompuServe (IBMCOM and CONSULT SIGs) as well as TeleGodzilla.

A problem in the 1/17/89 and 2/2/89 versions corrupts files under unusual
circumstances.  Please delete all instances of the 1/17/89 and 2-02-89
version.

A reminder: the -Z option is effective only when it is given to the sending
program.

If you use PREFIX= or ONAME= with the "sb" or "sz" commands, these pathnames
must be entered in lower case unless the underlying file system supports upper
AND lower case.

11-14-89 The Virus detection routine now identifies "Environment Too Big" as
distinct from detected infection of the program.  Please note that a
sufficiently large envioronent may cause DSZ.COM to fail in unpredictable
ways; use DSZ.EXE if DSZ.COM complains about the environment being too big.

11-11-89  Virus detection was added to DSZ.COM.  Incorrect filename
date/length transmitted in headers was corrected.

10-28-89 A T may be appended to DSZOPT or "dsz t -T" may be used to force DSZ
to exit after it has recognized a ZMODEM AutoDownload(Tm) request.

10-24-89  BBS registered copies (serial numbers 8000-8999 and 20000-23999) are
now fully featured.

The BBS registration form has been modified.  Please read this form carefully
before applying a BBS serial number.  Use of BBS serial numbers (4000, 20000
series) acknowledges acceptance of this contract.

The IMP/KMD compatibility file length information in the YMODEM header
generated by the sb command now uses the correct byte ordering.  Changes to
the XMODEM/YMODEM sz/sb commands were made to accommodate programs that ise CK
or CKL.  (As predicted in 1985, networks sometimes interfere with these
sequences.)

Files passed over because of creation errors at the receiving end are now
counted by the "sz" command as errors.  The receiving program must be a 9/89
or later version for this to be effective.

The specified directory form of the rz and rb commands has been enanced to
accommodate certain forms of erroneous syntax.

6-19-89 A documentation error (concerning DSZPORT) was corrected in the DOC
file.






Chapter 15 Pg 38          DSZ Reference Rev 11-14-89          Typeset 11-14-89



5-25-89  Corrects a protocol negotiation problem encountered when the rz or sz
-e option is used.

Host programs can now specify an alternate CANCEL sequence (not used for DOS
and Unix).

The ZMODEM "Slow Send" mode inserts a brief pause after each subpacket when
invoked with the -F option, or automatically when the "sz" command detects
failing flow control.  The zmodem F numeric parameter (default 1) sets the
pause in tenths of seconds.

4-24-89 The -rr option has been improved.  Long file compares are done in two
stages to save time when the first portions do not match.  Diagnostic code and
undocumented commands have been removed to decrease the program size.

DSZ now defaults to "handshake both" if the speed is greater than 2400 and the
clear to send signal is high when DSZ selects the comm port (was "handshake
on" in 3-19).

The "IN CASE OF DIFFICULTY" chapter has been expanded.

The 4-18 version introduces ZMODEM variable length headers of up to 16 bytes
information field instead of the previous fixed 4.  Selection of variable
length header capability is automatic and downward compatible.  Variable
length headers allow future extensions to ZMODEM's capabilities.

ZMODEM Crash Recovery now understands the -rr option to compare the CRC-32 of
the assumed common file segment before continuing an incomplete file transfer.
The "zmodem R" numeric parameter may be set to limit the number of bytes in
the files that are compared; the default R value of 0 allows all of the file
to be compared, an R value up to 32000 (up to 2 billion on 32 bit flavors)
limits the comparison to the first R bytes of the two files.  The ZMODEM -rr
option is supported by Omen Tech versions April 18 1989 and later.

When ZMODEM Crash Recovery detects incompatible source and destination file
contents, the destination file is now truncated to zero length before
proceeding with the transfer.  Crash Recovery requires the destination file to
be no longer than the source file.

Error reporting on unregistered copies has been enhanced to point the user to
solutions described in the relevant chapters in DSZ.DOC.

3-18-89 In order to work around a bug in the new TCOMM bbs, DSZ now defaults
to "handshake on" if the speed is greater than 2400 and the clear to send
signal is high when DSZ selects the comm port.

The "o" command has been added to disconnect the modem after a terminal
session: "dsz t o" disconnects the modem when the terminal session is
completed.

The "P" (capital P) numeric parameter (q.v.) has been added to display and






Chapter 15 Pg 39          DSZ Reference Rev 11-14-89          Typeset 11-14-89



control the UART fifo on some clone chips.

BBS registrations postmarked after Feb 28 1989 must be accompanied by a paid
DSZ registration.  The free program expired Feb 28 1989.  Outside help has
been hired to process and verify applications received under that program.

2-23-89 The term function now sends BREAK in response to the ALT-B key.
Handling of the Ctrl-Break vector has been changed so an untimely keyboarded
Ctrl-C or Ctrl-Break will not hang DOS.

2-15-89  DIRRX is enabled for BBS registrations (8xxx numbers).  Logic has
been added to simulate transmit interrupts on chips that have problems in this
area.  The "A" command does not require registration.  An interaction between
ONAME= or PREFIX= and the file count display has been removed.  Time/date
conversion routines have been enhanced to deal with files with missing dates.
The "v" command has been added to allow bbs programs to interrogate DSZ's
serial number.

2-06-89 A spurious error message at the completion of YMODEM downloads with a
download directory specified on the command line has been eliminated.

2-05-89 DSZ now returns a non 0 status unless at least one file has been
transferred.  An inappropriate pathname/disk specifier check on specified
download directories has been removed.

Previous versions:

Added the "A" command to prevent pcAnywhere host mode from locking up DSZ.
SlugBait logic has been simplified, reporting any failed file transfer where
any of the last 1K of the file was sent with Q status.

Introduced ZMODEM RLE compression with the -Z option.  (registered DSZ copies
also accept "Z" in the DSZOPT environment variable.) ZMODEM RLE compression
packs runs of the same character in two or three character sequences.
Compression is useful for screen dumps, uncompressed workspaces, compiler
listings, and other files rich with strings of repeated characters, but not
.ARC, .ZOO and other compressed files.  Compression percentages range from -1
per cent for already compressed files to more than 1000 per cent (10x
speedup!) for the Personal Computing text file benchmark(!).  When sending to
programs that do not support ZMODEM compression, the -Z option is ignored.
The -Z option is effective when specified to the sending program only.

Good news for tired frog stompers!  The ZMODEM rz/sz programs are now
available in a VMS C flavor.  The VAX/VMS source files are contained in the
RZSZ.ARC (RZSZ.ZOO) archive file.

"Handshake slow" has been added to disable the RTS signal to the modem while
writing to disk, even if the interrupt buffer is not chock full of bytes.
This should help systems with excessive interrupt latency on disk writes.

Setting the v (verbose) parameter to 1 or greater causes serialized copies to






Chapter 15 Pg 40          DSZ Reference Rev 11-14-89          Typeset 11-14-89



ring the bell when a transfer is done.

DSZ.DOC has been extensively rewritten and reorganized.  DSZ now supports the
advanced buffering of the National NS16550AN and Intel 82510 serial interface
devices.  Please refer to the subchapter on "Brain Damaged UARTs".

Pirated/hacked versions of DSZ have cost users and DSZ's developer thousands
of dollars in lost time and other expenses, in addition to injuring the
reputation of Omen Technology and its products.  Regrettably, Omen Technology
cannot support prior versions of DSZ because of this piracy.

Name             Length                           Date        Time   CRC

dsz.com          51138  Crunched   15%     43790  14 Nov 89   6:53a  2331
dsz.exe          56769  Crunched   19%     46289  11 Nov 89   3:12a  a568
PKZIP -vt 32 bit CRC: 050DAAA5   51138 dsz.com
PKZIP -vt 32 bit CRC: C83EAA0E   56769 dsz.exe

Your copy of DSZ should show this information as provided by

       arc v dsz
or
      pkxarc -v dsz
      lharc v dsz

ARC, and LHARC use a 16 bit CRC.


ZIP uses a 32 bit CRC compatible with the  Professional-YAM  and  ZCOMM  "crc"
command.
      pkzip -vt dsz
The following Pro-YAM/ZCOMM command gives the 32 bit CRC for DSZ.COM:

EXAMPLE: >>>c: crc dsz.com


If your copy shows a different CRC or file length, insist on a legitimate copy
and report the source of the bogus/pirated copy to Omen Technology Inc.  Omen
Technology has received reports of serious problems caused by unauthorized
patches to DSZ, and cannot assume liability for the performance of the
resultant code.
















Chapter 16 Pg 41          DSZ Reference Rev 11-14-89          Typeset 11-14-89



16.  Other Omen Technology Products

Omen Technology makes Professional-YAM, a comprehensive comms program with
unmatched power.  Flavors are available for PC-DOS, Unix, Xenix, and OS/2
Protected mode.

ZCOMM is a full featured shareware version with a $40.00 basic registration.
Registered DSZ users upgrading to ZCOMM get a free binder!

















































Chapter 17 Pg 42          DSZ Reference Rev 11-14-89          Typeset 11-14-89



17.  FAIR PLAY

Unlike snazzy menu interfaces, reliable high speed transfer protocols take
many hours of testing, often over expensive phone connections, to develop.
Two decades of communications experience and protocol testing are distilled in
DSZ.

DSZ is a user supported program developed and supported by Chuck Forsberg,
owner of Omen Technology.  Countless hours of work and expen$ive resources
went to develop and support DSZ for the myriad environments users use it in.
The fact that most of the problems people encounter with DSZ are caused by
other software, hardware problems, failure to read the supplied documentation,
or pirating has not kept users from seeking and getting help, even if it means
calling the author in the middle of his sleep.

Beyond this, the world of communications is constantly evolving, and it
requires a significant ongoing effort to keep DSZ and its documentation up to
date with the current state of the art.  Individuals with little knowledge of
the dynamic nature of telecommunications (or hidden agendas) have
misrepresented the frequency of enhancements to DSZ as a sign that DSZ is
"unstable" and unworthy of "serious consideration".  If you think such sniping
is fair play, you are more than welcome to use one of the many other protocol
programs available, each of which claim to offer speed and reliability
comparable to DSZ.

Non registered users are welcome to use DSZ for a reasonable evaluation
period.  "Reasonable" means "until you've decided whether the program is worth
$20.00".  It does not mean "until some competing program gets around to adding
ZMODEM or True Ymodem(TM)".  Once you've evaluated DSZ, ethical use of DSZ
requires registering the copy.

DSZ is not and never has been Public Domain.  Every version of DSZ has
included a Copyright Notice and a prohibition against sale or modification.
There is no usage counter or other Trojan Horse in DSZ, but if you use this
program, you have a moral and ethical obligation to register it.

Paid registration enables OverThruster(TM), YMODEM-g, and other advanced
features that are present in DSZ.ARC in encrypted form.  The registration
package serializes and decodes all past and future versions of DSZ.COM and
DSZ.EXE.  You can get a fully featured upgrade of DSZ simply by downloading a
newer version from TeleGodzilla, GEnie (IBM Roundtable), CompuServe, and
trusted bulletin boards.

17.1  Sharing DSZ Files

You are welcome to share unmodified copies of DSZ.ARC or DSZ.ZOO with your
friends and associates for their evaluation.  This documentation file and the
MAILER file must be provided with all copies of DSZ except by prior written
permission from Omen Technology Inc.  Because of piracy problems, Omen
Technology must INSIST that DSZ be distributed only as part of the DSZ.ARC
file EXACTLY as provided by Omen Technology Inc, or in an archive which






Chapter 17 Pg 43          DSZ Reference Rev 11-14-89          Typeset 11-14-89



displays a CRC value for DSZ.COM equal to that shown in the CHANGES chapter.
If DSZ.ARC is "zipped" or otherwise repacked, no files may be added to or
removed from the archive.

If you see an improperly packed or otherwise modified DSZ archive or parts
thereof in a bulletin board, please ask the board's operator to replace such
files with DSZ.ARC exactly as provided by Omen Technology Inc.  Flame them
until they behave ethically.

No version of DSZ may be sold without the prior written permission of Omen
Technology Inc.

Distribution or use of programs or procedures that modify, patch, disassemble,
decompile, or otherwise reverse engineer DSZ without the prior written
permission by Omen Technology Inc is a bloody theft of intellectual property
and services and is a violation of Federal Copyright Law.  The same applies to
debug scripts and documentation written for the same purposes.  These perform
the same function as pirate satellite and/or cable descramblers, to obtain
benefit from encrypted communications without proper payment.  Piracy has been
investigated by the FBI and prosecuted under federal statutes.  Applicable law
provides for damages and recovery of attorney's fees.  Omen Technology has
received reports of serious problems caused by unauthorized patches to DSZ,
and cannot assume liability for the performance of the resultant code.  So
far, none of the slime producing such bilge have seen fit to sign their real
name and address to their cretinous attempts at ego gratification.

Distribution of DSZ in any medium without this documentation file is an
unauthorized modification to DSZ that deprives the rightful author of
registration revenues.  That is a theft of intellectual property.  Such
distribution damages the author by forcing the user and author to waste time
and phone bills scrounging for the documentation, and answering questions that
are fully covered in the documentation.

If any version of DSZ is distributed with any other product, software or
hardware, the product documentation must clearly and prominently state that
the customer's continued use of DSZ requires registration directly with Omen
Technology or its duly authorized agent(s).  When unregistered copies of DSZ
are distributed on disk, a contemporary copy of ZCOMMDOC.ARC should be
included on the same disk.

Thank you for your support.

17.2  REGISTRATION

After a short evaluation period, ethical users must register their copy of DSZ
with a check for $20.00 in U.S. funds sent to:

       Omen Technology Inc.
       P.O. Box 4681
       Portland, OR 97208







Chapter 17 Pg 44          DSZ Reference Rev 11-14-89          Typeset 11-14-89



The address on your check is sufficient, no need to fill out forms.

       For VISA/MC Registrations, you can also:
       Call VOICE: 503-621-3406

       Or register online: 503-621-3746  300-1200-2400 bps
       Or FAX the INSTANT MAILER to: 503-621-3735

Don't bother scrounging for an envelope, just print the INSTANT MAILER
included in this archive!

Overseas registrations are sent out International Air Mail.  Users, especially
those overseas, may choose to register their copy of DSZ for $25.00 U.S.  by
providing their VISA or Mastercard card number with expiration date and their
name as it appears on their credit card.

Purchase orders for less than $150 must be prepaid.  Omen Technology Inc
Federal TAX ID #: 930858776 Oregon TAX ID #: 536565

  *************************************************************************
The user registration package includes a printed serial number password (SNP)
card.  The registration "care package" diskette contains the latest versions
of the DSZ programs, additional user documentation, and the installation
program which uses your personal SNP to enable advanced features and bypass
the opening advertisement.

The registration package unlocks the extra value in all past and future
versions of DSZ.COM and DSZ.EXE.
  *************************************************************************

The unique serial number on the registration card is registered to the user,
and is acceptable proof of registration to corporate auditors.

The putsnp program inserts your unique DSZ Serial Number Password (SNP) into
you copy of DSZ with the following command:
       putsnp dsz.com
Putsnp accepts your SNP and asks appropriate questions before inserting the
SNP to enable the extra value in DSZ.

Some TSR programs have been known to interfere with putsnp.  If you have a
lockup running putsnp, run it without any TSR programs.


The only legitimate way to disable the opening advertisement in DSZ is to
insert an authorized SNP obtained from Omen Technology into DSZ with the
putsnp program.  Any other suppression or modification of the opening screen
is an illegal, unethical theft of services.  Omen Technology has received
reports of serious problems caused by unauthorized patches to DSZ, and cannot
assume liability for the performance of the resultant code.

Piracy is stealing.






Chapter 17 Pg 45          DSZ Reference Rev 11-14-89          Typeset 11-14-89



17.3  Files on Registration Disk

The following files are currently included on the Registration Disk sent to
paid registrants.

LOOZ.EXE       Program to unpack .ZOO archives.  Please note that commands to
               LOOZ must be given in lower case.  "looz x dsz" works, "LOOZ X
               DSZ" fails.  LOOZ.DOC describes LOOZ.EXE.


DSZEXE.ZOO     Contains DSZ.EXE.

               To dearchive with looz: looz x dszexe (Note: x must be lower
               case, X won't work!)

               Type "looz" without arguments to see the help message.


DSZ.ZOO        Contains DSZ.COM, this document, DESQview description files,
               and an instant no-effort registration mailer.

               To dearchive with looz: looz x yzmodem (Note: x must be lower
               case, X won't work!)


RZSZ.ZOO       ZMODEM C source code, porting base for several dozen ZMODEM
               implementations

               To dearchive with looz: looz x rzsz (Note: x must be lower
               case, X won't work!)


PUTSNP.EXE     Installs your unique registered serial number to enable the
               extra value in DSZ.


DSZBG.DOC (in DSZBG.ZOO) Background information for DSZ, consisting of
               relevant parts of the ZCOMM User's Manual.  DSZBG.DOC is for
               paid registered users only; registered bulletin boards and
               unregistered users are welcome to read the same information
               contained in the ZCOMM manual (contained in ZCOMMDOC.ARC).

               To dearchive with looz: looz x dszbg (Note: x must be lower
               case, X won't work!)













Chapter 17 Pg 46          DSZ Reference Rev 11-14-89          Typeset 11-14-89



17.4  Bulletin Board Registration

DSZ may be freely used and copied by public bulletin board systems which obey
the conditions stated in the accompanying bbs_reg.txt file including display
of the ZCOMM files.  (For this BBS registration, a multi node bulletin board
operating from a single, common file system counts as one machine.) BBS
registrations postmarked after Feb 28 1989 must be accompanied by a paid DSZ
registration.  The free program expired Feb 28 1989.

Those not abiding to these conditions must obtain a paid registration for each
computer that runs DSZ.

The purpose of bulletin board registrations is to support and promote ZCOMM
and Professional-YAM by popularizing the ZMODEM protocol and featuring the
ZCOMM shareware files available for downloading.  BBS registrations must be
submitted on the bbs_reg form with signature and date, and must accompany a
paid DSZ or ZCOMM registration.








































Chapter 18 Pg 47          DSZ Reference Rev 11-14-89          Typeset 11-14-89



18.  ACKNOWLEDGEMENTS

32 bit CRC code courtesy Gary S. Brown.

The High Reliability Software(TM), Demand Upgrade(TM), TurboLearn Script
Writer(TM), Cybernetic Data Recovery(TM), ZMODEM AutoDownload(TM), Intelligent
Crash Recovery(TM), Error Containment(TM), Full Time Capture(TM), True
YMODEM(TM), OverThruster(TM), Password Guardian(TM), CryptoScript(TM), and
TurboDial(TM) are Omen Technology trademarks.

PowerCom was trademarked in 1985 by POLYTRON Corporation, Hillsboro Oregon.

True YMODEM(TM) is an Omen Technology Trademark signifying YMODEM protocol
support that meets the full YMODEM specification.

DSZ and this documentation are Copyright 1989 by Omen Technology Inc, all
rights reserved.  DSZ is not and never has been Public Domain.  Every version
of DSZ has included a Copyright Notice and a prohibition against sale or
modification.  This prohibition applies to any theft of the intellectual
property and trade secrets contained in DSZ by decompilation, disassembly, or
any other form of reverse engineering including but not limited to profiling,
tracing, data analysis, or monitoring the operation of DSZ.

                         Omen Technology Incorporated
                        The High Reliability Software

                     17505-V Northwest Sauvie Island Road
                            Portland Oregon 97231
                Modem: 503-621-3746 Speed 1200,2400,19200 PEP
                              FAX: 503-621-3735
                       CompuServe:70007,2304  GEnie:CAF