SWAP Version 1.2
     (c) Copyright 1988-1989 Nico Mak and Mansfield Software Group
                          All rights reserved
                             March 5, 1989

SWAP provides an application independent method for one MS-DOS
application to run another, even if both would normally not fit in
memory at the same time.  A typical use is to temporarily swap out a
text editor so that you can run memory hungry compilers, linkers, or
even debuggers without losing your place in an editing session.

SWAP works by copying conventional memory used by the currently running
application to expanded memory, extended memory, or to a disk file,
thereby freeing conventional memory used by the application.  SWAP then
runs the desired program before restoring the original environment.

SWAP is compatible with most MS-DOS programs.  However, before relying
on it, you should test SWAP with your own configuration in case of
conflicts with TSRs and other software.

SWAP operation and internals are detailed in an article in the April,
1989 issue of Dr. Dobb's Journal.  The article includes source code.

SWAP version 1.1 includes these new features:

- It will swap to extended memory if your system supports XMS (the
  Extended Memory Specification).
- SWAP is easier to use from Personal REXX (see the example below).

Version 1.2 includes these new features:

- If the -d and -x options are NOT used and if SWAP can't swap to EMS,
  it will try to use XMS.  If it can't swap to XMS it will automatically
  swap to disk.

- When swapping to disk, the process id of the program that gets swapped
  out is included in the fileid, so that you can swap to disk
  recursively.

                          SWAP command syntax

The SWAP command can be entered at the DOS prompt, or it can be part of
the command string that your application sends to DOS to run another
program.  See below for examples.

SWAP [options] command [command-parameters] [ > fileid]

Brackets indicate optional parameters.  Valid SWAP options are:

-C Copy redirected output to the console.
-D Disk file C:\SWAPxxxx.TMP is used instead of expanded memory
   (where xxxx is the process id of the program that gets swapped out).
-F Forces SWAP to continue even if an interrupt vector points to the
   program that gets swapped out.  Use this option when possible, but
   only if you are sure that the program that gets swapped out does not
   hook interrupt vectors.
-Q Quiet operation.  Informational messages are not displayed.
-R REXX interface - required when used from Personal REXX.
-X XMS (extended) memory is used instead of expanded memory.

"command" is any command that can be issued at the DOS prompt.
"command-parameters"  are parameters or options for the command.
"fileid" is a DOS file or device to which output from command can be
directed.

                                Examples

Assume you have shelled to DOS from within your editor in order to
compile a program.  If the command you normally use to assemble your
program is

    MASM filename;

then the command to run your assembler with SWAP becomes

    SWAP MASM filename;

To run SWAP to swap out dBase and load your favorite editor, you could
enter the dBase command

    RUN SWAP -F KEDIT filename

Alternately, you could at the following line to your CONFIG.DB file:

    TEDIT = SWAP.COM -F KEDIT.EXE

and subsequently enter the following dBASE command to edit a file:

    MODIFY COMMAND filename

To run SWAP in a REXX program to swap out Personal REXX, use the -R
option.  For example,

    'SWAP -R -F dBase'

Note that SWAP cannot swap REXX out if REXX was made resident.

                                -------

This software is provided with the standard disclaimers:  no warranties
or guaranties, either explicit or implied.  No promises that the
software will work or be supported.  Use at your own risk.

                                -------

Questions, comments, and suggestions are welcome.  You can contact me on
CompuServe at user id 70056,241 or on BIX as Nico_Mak.