COPYD --- COPY with Descriptions utility, for 4DOS.

             Version 0.41
             (C) Bit Bucket Software
             David P. Lemire
             4/14/89


        INTRODUCTION

             COPYD is a general purpose file copying utility.  It
        supplements the built-in 4DOS COPY and MOVE command by
        processing both files and descriptions.  It accepts the same
        command line syntax as the 4DOS COPY command, except for
        minor restrictions, and provides seversl options to customize
        the copying process.  COPYD is invoked by typing:

        COPYD [switches] SourceSpec [SourceSpec] [DestinationSpec]
              Allowed switches are /d|b|m|f|u|a|w|k|c|l|n|p|q|v|x|h|?

        Typing only COPYD with no arguments will print a usage
        message (the line above).  Using the /H or /? options will
        produce a help screen explaining the effects of the switches.

             File specifications will be fully qualified, and
        reported to the console using the 4DOS "FileFrom => FileTo"
        notation for ordinary copies, and variations on that notation
        where appropriate (see the section on switches).  If a
        description exists for the file in the source directory, the
        description will be copied to the destination directory,
        overwriting any existing description.  Descriptions are saved
        to the destination directory only after all copies are
        complete.  The file processing report appears before the copy
        or move action is performed.  The user can terminate the copy
        operation after the current file by pressing the ESCAPE key.
        This wil cause COPYD to finish copying or moving the current
        file and its descriptions, save the target directory
        description file and exit to DOS.  (This feature is similar
        to the use of the ESCAPE key in the DOS XCOPY utility.  It
        does prevent the use of type-ahead while COPYD is running.)


        COMMAND LINE SWITCHES AND ENVIRONMENT VARIABLE

             The following lists summarize the available switches and
        their affects.  Certain switches can be places in an environ-
        ment variable named COPYDSW to change the "default" mode of
        operation.  If conflicting switches are used, the last switch
        processed determines the operation of the program; command
        line switches override program defaults and environment
        variable options.  For example, if the command line
        contained:

                                     /DBQ






        COPYD would copy both files and descriptions (the /B), and
        provide no output (the /Q).  COPYD does not distinguish
        between lower and upper case on switches.

        File copy control switches:

        *    /D -- Copy descriptions only, not files.  Reports will
                   be in the form "FileFrom -d-> FileTo," to
                   distinguish them from normal copies.

        +    /B -- Copy both files and descriptions.

             /M -- Move files (instead of copying), and copy
                   descriptions. Reports will be in the form
                   "FileFrom -> FileTo," to distinguish them from
                   normal copies.  This function can also be used to
                   rename files while preserving their descriptions.

             /F -- Freshen, copy files that match the souce spec,
                   exist at both the source and the destination, but
                   have newer versions at the source.

             /U -- Update, copy all files that match the source spec
                   from source to destination, unless source files
                   are not newer than matching files at destination.

        +    /A -- Copy all specified files, default mode of
                   operation.

        *    /W -- Wipe the target description file of a description
                   if the corresponding source file does not have a
                   description.

        +    /K -- Keep the description of a destination file even if
                   the corresponding source file does not have a
                   description.  Opposite of /W.

        *    /C -- Clean-up all description files (source and target)
                   accessed during execution.  Unlike /W, this
                   function purges each description file of any
                   descriptions for which a corresponding file or
                   directory does not exist.

        +    /L -- Leave "dead" descriptions untouched.  Do not clean
                   up description files.  Opposite of /C.

        Program control switches:

             /H or
             /? -- Help, show help screen summarizing the use of the
                   COPYD switches

        *    /P -- Prompt, query user for each file if it should be
                   copied or moved






        +    /N -- No Prompt, process files normally

        *    /Q -- Quiet, no output to console, unless there is an
                   error

        +    /V -- Verbose, report all file/description copy actions
                   to the console.

        *    /X -- Suppress copyright banner.  If no files are
                   copied, due to the use of /Update or /Freshen,
                   this switch also suppresses the "0 file(s) copied"
                   report.

        NOTES:   + indicates default program operating mode.  These
                 switches may appear in the environment variable, but
                 will not change program operation as they repeat the
                 default operating modes.

                 * indicates other switches that may appear in the
                 environment variable.

             The freshen switch allows the use of a *.* source spec
        to copy only altered files, not new or unchanged files to the
        target.  The update switch will copy all files that match the
        source specification, but will save time by not copying
        unchanged files.  These switches only have an effect when
        files are being copied; they are ignored when used with the
        /DescriptionsOnly or /Move options.  The /Prompt option also
        overrides the /Freshen and /Update switches.

             Switches intermingled with files are processed, however,
        all switches are processed before copying starts, so it is
        not possible to "group" switches with files (as you can with
        certain 4DOS commands, particularly DIR).  For example

                  COPYD *.COM /Q *.EXE \TEMPDIR

        would copy all .COM and .EXE files to \tempdir and produce no
        output.

             The user can set an environment variable COPYDSW (COPYD
        SWitch) to alter the default parameters.  The switches D, B,
        P, N, A, W, K, C, L, V, Q and X are legal in the environment
        variable.  COPYD will abort with an error message if any of
        the other switches (M, F, U, H or ?) appear in the
        environment variable.  For example, SET COPYDSW=D will cause
        COPYD to copy only descriptions as its default mode of
        operation.  COPYD can still be made to copy both files and
        descriptions with a /B on the command line.  The command line
        switch overrides both the environment setting.







        NOTES AND RESTRICTIONS

             COPYD only saves the target DESCRIPT.ION file if it has
        been altered.  This speeds execution in some cases, for
        example when backing up files to a floppy that is fairly
        current.  If using the descriptions only option, this can be
        somewhat disconcerting as the program reports the file names
        as each is processed, but then does not write to the target
        disk, after stating "n description(s) copied."

             COPYD checks during move operations, and prevents the
        user from moving multiple files to a single target file.  If
        an operation such as COPYD /M *.C FILENAME.BAK is attempted,
        the first file matching *.C will be moved to FILENAME.BAK and
        the operation aborted with the second file.  The description
        will not be moved, and can be "recovered" by copying or
        moving FILENAME.BAK back to its original *.C name.

             When the /DescriptionsOnly option is specified, COPYD
        will process all files that match the source file
        specification without regard to /F or /U file date and
        existence considerations.  The /CleanUp option, or subsequent
        use of the 4DOS DESCRIBE command or the Multifile Describe
        Utility (MDU) will clear the extra names and descriptions out
        of the target DESCRIPT.ION file.

             The /CleanUp function adds a noticable amount of
        overhead to the execution of the program.   Unlike /Wipe,
        this function purges each description file of any
        descriptions for which a corresponding file or directory does
        not exist.  /Wipe only removes descriptions from the target
        directlry, and only removes descriptions associated with
        files that were copied or moved.  /CleanUp can be made the
        default mode of operation using the environment variable,
        however the built-in default is the faster mode of operation.
        The 4DOS DESCRIBE command always cleans up the descript.ion
        file affected, so the /CleanUp function is not necessary on
        every copy operation.  It is particularly appropriate to use
        with the /DescriptionsOnly option, which is likely to leave
        unnecessary descriptions in the target directory.

             The use of DOS devices (e.g., CON:, LPT1:) is not
        supported by COPYD.  If you need, for example, to create a
        file by copying from the console it will be necessary to use
        the 4DOS COPY command, rather than COPYD.  File concatenation
        (e.g., file1+file2) also is not supported.

             COPYD can handle up to 150 files per source file
        specification.  This limit is due to the way directories are
        handled internally.  If you are copying a directory with more
        than 150 files, it will be necessary to use multiple wild
        cards, rather than a *.* to specify the files.






        SUMMARY OF PROGRAM SWITCHES:

             /DescriptionsOnly:  Copy descriptions only, not files.

             /Both:              Copy both files and descriptions.

             /Move:              Move files and copy descriptions.

             /Freshen:           Copy only newer versions of existing
                                 files.

             /Update:            Copy all specified files unless not
                                 newer.

             /All:               Copy all specified files.

             /Wipe:              Remove target description if none at
                                 source.

             /Keep:              Retain target description,
                                 regardless of source.

             /CleanUp:           Remove "dead" descriptions.

             /Leave:             Retain "dead" descriptions
                                 untouched.

             /Help or /?:        Show help screen.

             /Prompt:            Query user for each file.

             /NoPrompt:          Process files normally.

             /Quiet:             No output to console, unless error
                                 occurs.

             /Verbose:           Report all actions to the console.

             /X:                 Suppress copyright banner, 0 file
                                 notice.