Full Page Format Description			John Bridges	2/09/86
----------------------------			------------	-------

Enhancements by Doug Wolfgram May, 1986
__________________________________________________________________________________

offset 0 is a word,	marker that is always 01234h
offset 2 is a word,	x size of page in pixels 
offset 4 is a word,	y size of page in pixels
offset 6 is a word,	x offset into page where lower left hand corner of viewport
			is located (default of 0 is ok)
offset 8 is a word,	y offset into page where lower left hand corner of viewport
			is located (default of 0 is ok)
offset 10 is a byte,	bits 0-3 is the number of bits per pixel per bit plane
			and bits 4-7 is the number of extra bits planes (so
			4 color cga mode would be 02h and 16 color ega would
			be 31h and plantronics 16 color would be 12h)


offset 11 is a byte,	marker that is always a 0ffh
offset 12 is a byte,	single uppercase letter indicating which video mode
			this picture was created in, can default to 0.
			A=320x200x4 cga
			B=320x200x16 pcjr stbplus
			C=640x200x2 cga
			D=640x200x16 ega
			E=640x350x2 ega
			F=640x350x4 ega
			G=640x350x16 ega
			H=720x348x2 hercules
			I=320x200x16 plantronics
			J=320x200x16 ega

offset 13 is a word,	extra information descriptor defines what is in
			the extra information that follows this header,
			0=nothing
			1=pallet (single byte) border (single byte)
			2=pcjr or non ECD EGA 16 color registers (0-15) one byte each
			3=EGA with ECD 16 color registers (0-63) one byte each

offset 15 is a word,	size of extra information in bytes

offset 17 is a byte array,
			the actual extra data the size which is defined
			by esize (at offset 15).

struct head {
	unsigned int mark=0x1234;	/* marks begining of a page file */
	unsigned int xsize;		/* x size of page */
	unsigned int ysize;		/* y size of page */
	unsigned int xoff;		/* current x offset into picture of viewport */
	unsigned int yoff;		/* current y offset into picture of viewport */
	unsigned char bitsinf;
}

struct extra {
	unsigned char emark=0xff;
	unsigned char evideo;
	unsigned int edesc;
	unsigned int esize;
}

/* number of packed blocks in page file or 0 if not packed */

unsigned int numseg;

/*  if the file is packed then what follows is a multi block packed file,
otherwise (if the file is not packed) the actual data follows */

/* bit planes follow each other in the file and when packed each bit plane
but start in a new packed block. */

/* a simple example would be a 320x200, 4 color, packed page file, of a white
screen. */


	dw	0x1234		;marker
	dw	320		;x size
	dw	200		;y size
	dw	0		;x offset
	dw	0		;y offset
	db	02h		;bits per pixel and 1 bit plane

	db	0xff		;new extra info flag
	db	'A'		;vidmode
	dw	1		;extra area descriptor (pal and bord)
	dw	2		;bytes in extra area
	db	2,0		;pallet and border

	dw	2		;number of packed blocks
;first block
	dw	5+5		;packed block size
	dw	8192		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	8192		;16 bit run count
	db	0xff		;byte to fill run with
;second block
	dw	5+5		;packed block size
	dw	7808		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	7808		;16 bit run count
	db	0xff		;byte to fill run with

/* another example would be a 640x350, 16 color, packed page file, of 
a red screen (color 4). */

	dw	0x1234		;marker
	dw	640		;x size
	dw	350		;y size
	dw	0		;x offset
	dw	0		;y offset
	db	31h		;bits per pixel and 1 bit plane

	db	0xff		;new extra info flag
	db	'G'		;vidmode
	dw	3		;extra area descriptor (pal and bord)
	dw	16		;bytes in extra area
	db	0,1,2,3,4,5,14h,7
	db	38h,39h,3ah,3bh,3ch,3dh,3eh,3fh

	dw	16		;number of packed blocks
;block 1 of first bit planes
	dw	5+5		;packed block size
	dw	8192		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	8192		;16 bit run count
	db	0		;byte to fill run with
;block 2 of first bit planes
	dw	5+5		;packed block size
	dw	8192		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	8192		;16 bit run count
	db	0		;byte to fill run with
;block 3 of first bit planes
	dw	5+5		;packed block size
	dw	8192		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	8192		;16 bit run count
	db	0		;byte to fill run with
;block 4 of first bit planes
	dw	5+5		;packed block size
	dw	3424		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	3424		;16 bit run count
	db	0		;byte to fill run with
;block 1 of second bit planes
	dw	5+5		;packed block size
	dw	8192		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	8192		;16 bit run count
	db	0		;byte to fill run with
;block 2 of second bit planes
	dw	5+5		;packed block size
	dw	8192		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	8192		;16 bit run count
	db	0		;byte to fill run with
;block 3 of second bit planes
	dw	5+5		;packed block size
	dw	8192		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	8192		;16 bit run count
	db	0		;byte to fill run with
;block 4 of second bit planes
	dw	5+5		;packed block size
	dw	3424		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	3424		;16 bit run count
	db	0		;byte to fill run with
;block 1 of third bit planes
	dw	5+5		;packed block size
	dw	8192		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	8192		;16 bit run count
	db	0xff		;byte to fill run with
;block 2 of third bit planes
	dw	5+5		;packed block size
	dw	8192		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	8192		;16 bit run count
	db	0xff		;byte to fill run with
;block 3 of third bit planes
	dw	5+5		;packed block size
	dw	8192		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	8192		;16 bit run count
	db	0xff		;byte to fill run with
;block 4 of third bit planes
	dw	5+5		;packed block size
	dw	3424		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	3424		;16 bit run count
	db	0xff		;byte to fill run with
;block 1 of fourth bit planes
	dw	5+5		;packed block size
	dw	8192		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	8192		;16 bit run count
	db	0		;byte to fill run with
;block 2 of fourth bit planes
	dw	5+5		;packed block size
	dw	8192		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	8192		;16 bit run count
	db	0		;byte to fill run with
;block 3 of fourth bit planes
	dw	5+5		;packed block size
	dw	8192		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	8192		;16 bit run count
	db	0		;byte to fill run with
;block 4 of fourth bit planes
	dw	5+5		;packed block size
	dw	3424		;unpacked block size
	db	0		;marker byte
	db	0		;mark a run
	db	0		;a 16 bit run count follows
	dw	3424		;16 bit run count
	db	0		;byte to fill run with

/* for more detail lets consider a block that isn't all the same. Say the
   data consists of 30 2's, and 8, a 4, and 300 1's. */

; the block would look like this 

	dw	5+10		;packed block size
	dw	100		;30 + 1 + 1 + 300 bytes as above
	db	ff		;what to mark a run with,
                                ; because there are no ff's in our example.

	db	ff		;mark a run 
	db	30		;8 bit run count
	db	2		;byte to fill run with - 2

	db	8		;not a run marker, so must be data

	db	4		;not a run marker, so must be data

	db	ff		;mark a run
	db	0		;means 16 bit run count follows
	dw	300		;run count	
	db	1		;byte to fill run with - 1




The actual unpacked data that resides in memory consists 2 seperate
sections.

1. The control structure: contains x size, y size, x offset, y offset,
   segment of bit mapped data, number of bits per pixel and number of
   additional bit planes. this information is kept in pcpaint's data segment.

2. The actual bit mapped data: contains the actual page image, mapped from
   bottom left (so bottom scan line is first). The data is contiguous within
   each bit plane, so scan line 1 follows scan line 0 directly. the page
   can and does cross segment boundires (a bit plane can be larger than
   64k). each bit plane follows the previous but starts on a paragraph
   boundry, the printer driver will be passed the offset in paragraphs
   between bit planes and the number of additional planes.
   The bit planes start with bit 0, each additional plane is the next bit.
   One note, it is possible in the future that the number of bit planes will
   not be a power of 2 (like 8 color displays) also it is possible that a bit
   plane may have more than 1 bit per pixel.