WRITTEN BY 
SAMUEL I. FINKELMAN
80 AVENUE P
BKLYN, N.Y. 11204

CONTRIBUTIONS EXCEPTED......


   Documentation for SEGMENT.COM  STACK.COM and RAX RBX RCD RDX RBP RSI RDI

    All these programs will tell you what the registers will be in that
machine when a COM program loads with particular parameters (it matters with
AX and BX)

SEGMENT will give you the segment at which a COM file would start or,in other
words,how far up in memory you are loaded.
 STACK tells you where SP is. If there is enough room for all of COMMAND.COM
and 64K it is FFFF.
   RAX etc tell you what those registers are when a COM file starts.AX and BX
are usually 0000 but can be 00FF or FF00 or FFFF if what follows the file name
on the command line looks like a drive [in other words a colon is the second
charcater after a space and the first after a letter or number or some other
characters.]   and the drive is invalid. CX is usually FF. SI and DI are
usually 100 Only BP seems to be always 0000 except that it looks like it is
different in later versions of DOS. I only looked at 2.1 and 3.2 or 3.3.

   These are the registers of a PC or 8088. Though their registers are longer,
 all 286's,386's etc emulate it.Lines indicate what's usually connected.

  __________   __________   __________  __________  __________  __________
  |    |    |  |    |    |  |    |    | |    |    | |         | |         |
  | AH | AL |  | BH | BL |  | CH | CL | | DH | DL | |   BP    | |   SP    |
  |____|____|  |____|____|  |____|____| |____|____| |_________| |_________|
                      :                                  |            |
     AX           BX  :.......  CX          DX  _________|____________|
                      :      :.                /
  __________   _______:__   __:_______  ______/___  __________  __________
  |         |  |         |  |         | |         | |         | |         |
  |   CS    |  |   DS    |  |   ES    | |    SS   | |   SI    | |    DI   |
  |_________|  |_________|  |_________| |_________| |_________|/|_________|
  _____|____        \             |                     /     / __________
  |         |        \____________|____________________/     /  |   The   |
  |    IP   |                     |                         /   |  FLAG   |
  |_________|                     |________________________/    |_Register|

     The way you will usually see this displayed in DEBUG is:

AX=0000  BX=0000  CX=0000  DX=0000  SP=217E  BP=0000  SI=0000  DI=0000
DS=1B84  ES=1B84  SS=1B84  CS=1B84  IP=0100   NV UP EI PL NZ NA PO NC
1B84:0100 3AC4          CMP AL,AH

Debug shows you it differently from the way it when a COM file is
loaded. This is what it would actually look like if DEBUG was right:

AX=0000* BX=0000* CX=00FF  DX=1B84  SP=217E  BP=0000  SI=0100  DI=0100
DS=1B84  ES=1B84  SS=1B84  CS=1B84  IP=0100   NV UP EI PL ZR NA PE NC
1B84:0100 3AC4          CMP AL,AH

* usually - can be used to detect if drives exist.


  Actually CX is usually FF while SI and DI are 100. BP is 0000 but in some
cases a higher number and DX is equal to whatever the sgment registers are.
AX and BX can be different than 0000 if the first or second parameters have a
colon as the second character.

   In addition to that the flags are different.When a COM file starts the Zero
flag is Zero or on,not off;and the Parity flag is even,not odd.You also cannot
see how the command line is actually handled in Debug. PSP:80 always contains
the length of the command line tail which always has ends with a carriage
return [0D or ASCII 13 or Ctrl-M] If there was nothing enetred after the
filename positions 80h and 81h are 00 and 0D. A common way to test for this is
to clear CH and put position 80 in CL and jump if CX is zero [JCXZ ]

  These facts can be used and you can use these prograsms to understand what
actually happens.

   Code might go:


assume cs:cseg,ds:cseg,es:cseg,ss:cseg.  ;only needed in EXE assemblers like
               ;like MASM or ASM - *** use CHASM or A86 or WASM instead.***
100  MOV SI,80
103  LODSB
104  XOR CX,CX
106 MOV CL,AL
108 JCXZ 300
10A [there was a parameter]

    Actually this is somewhat cumbersome.  Better is maybe

100   CS:  ; (unnecessary byte in COM files)DEBUG looks at this way most
101  MOV CX [80]               assemblers act differently.
105  XOR CH,CH
107  JCXZ....

 or

100   CS:
101   MOV SI,80
104   LODSB
105   CMP AL,0
107   JZ....

   Or even better yet,in COM files

100   MOV CL,[SI-80]
103   JCXZ .....      ; Jump CX not zero exists-almost.It is LOOP. Until this
105                         moment I thought it jumped if not zero but it
                              jumps if not 1.It can still be used if this is
This could also be LOOP ...        paired with a zero test. A value of 1 could
                                    also prove useful by itself.

in which case the parsing would be located in some other portion of the
code.That could be used if you returned to the start.An early section off code
could have LOOP.Soon you might XOR CX and start over this time going someplace
else. Thus:

100 LOOP 160   160 might end...

174 XOR CX,CX ;make CX Zero
176 INC CX    ; Add 1
177 PUSH SI   ;Place 100 - start of the code - on the stack
178 RET       ;Even though it was a conditional jump-we return!

       Maybe that should be

174 XOR CX,FE  ;make CX 1 if CX is FF - which it is at the start
176 PUSH SI   ;Place 100 - start of the code - on the stack
177 RET       ;Even though it was a conditional jump-we return!


 Another possible thing to do in the jump ahead is

160 MOV byte ptr [si-1],1 ; interesting point in DEBUG Typing MOVE with an e
                          ; will add 14 to the value of SI DEBUG
                          ; finds a way to interpret the e.

Later on you might restart the code again.Of course jumping back only to 102
is perfectly all right but this LOOP might not be the very first instruction.

   My ORTIONAL.COM gets input from the keyboard of nothing was entered after
the command line.The sequence of code goes - Actually it just as well be JZ

100 BB0002        MOV BX,0200   ;location of translation buffer
103 31D2          XOR DX,DX     ; DX is not zero at the start as you might
                                ; might think.It also must be made 0 in case
                                ; we are here for the second time.

   These two are really preliminary instructions.

105 BE8100        MOV SI,0081   ;This is where 0D would be if nothing was
108 AC            LODSB         ;the command name - get it in AL
109 3C0D          CMP AL,0D     ; is it a carriage return?
10B E115          LOOPZ 0122    ; if yes goto 122  This was intended to not
                                ; if this was on the second go-round and
                                ; exactly 13 characters had been entered
                                ; Then SI would also be 0D.

  This is what you would jump to:

122 B409          MOV AH,09     ; print the following message
124 BAA001        MOV DX,01A0   ; at location 1A0 -it's a request to
127 CD21          INT 21        ; type  INT 21h completes this instruction.
129 BF8000        MOV DI,0080   ; BX SI DI and BP for that matter can be
12C 893D          MOV [DI],DI   ; used to refer to location in memory.This is
                                ; to be an input buffer with INT 21 AH = A.
                                ; The first byte mustbe the number it can take
                                ; Maximum is 80. Here 80 is both the location
                                ; and the number!
12E 89FA          MOV DX,DI     ; Now put that location in DX - I didn't need
130 B40A          MOV AH,0A     ; to clear DX  ---  keyboard input
132 CD21          INT 21        ; up to a who;e line
134 31C9          XOR CX,CX     ; for my LOOP  but this was a mistake
                                ; it should be XOR CX,FE
136 31C0          XOR AX,AX     ; not needed either.
138 EBC6          JMP 0100      ; go back to start.

10D AC            LODSB         ; if not,it must be a space -get next byte.
                                ; on the other hand if this is the second
                                ; while it's not a space it is a count byte
                                ; of the number of bytes just entered and
                                ; there is no leading space.

10E D7            XLAT          ; get the value of that character.
10F 01C2          ADD DX,AX     ; add it to a running total in DX.
111 3C0D          CMP AL,0D     ; 0D has been made equal to 0D in the table.
113 75F8          JNZ 010D      ; that's how we exit. If not 0D go back
                                ; and get the next byte.
115 8EC2          MOV ES,DX     ; EXIT  Stuff DX in some register. You can
117 B409          MOV AH,09     ; use a segment register. - 9 is print string.
119 BA3B01        MOV DX,013B   ; Location must be in DX
11C CD21          INT 21        ; Print it
11E 8CC0          MOV AX,ES     ; Get the value in AL
120 EB58          JMP 017A      ; routine to translate and print out this
                                ; hexidecimal value.