WWIV Modem Documentation




                             By William Daystrom





                    Copyright (c) 1989 White Star Software








































                           WWIV Modem Documentation


   One of the more tedious aspects to configuring your bulletin board is
   modem setup. There are countless brands and variations of modems on the
   market, and despite standards, most have slight differences in the way
   they will work best with WWIV. However, once you have your modem
   functioning correctly with WWIV, you probably will never have to bother
   with modem init functions again until you acquire a different modem.

   If you are intending to be a sysop, it is generally assumed that you
   know enough about your modem to at least have it operating correctly
   with your computer. Therefore, this part of the documentation will not
   detail how to install your modem. It will show you how to configure your
   modem to work with the BBS, as running a bulletin board requires special
   settings.

   A word about modem cables. It is possible for your modem and cable to
   work perfectly well with your terminal program, yet not work with the
   BBS. This is because the BBS requires certain information to be carried
   between the modem and the computer that is ordinarily not required by
   normal use. The vast majority of modem cables manufactured today will be
   fine with WWIV. If you constructed your own cable, however, you must be
   sure that the following pins are connected (on the DB-25): 2, 3, 7, 8,
   and 20.

   Now on to modem settings. Your modem will need to tell the BBS
   information to enable it to answer and terminate calls correctly. The
   first important setting is the carrier detect, or CD. Most modems have
   two possible settings for this parameter, either always on, or carrier
   is monitored. The second setting is required to enable the BBS to detect
   whether or not a caller is on-line. Most modems default to the first
   state, however, so you will usually have to change this setting so that
   carrier is monitored.

   Modems vary in how they may be configured. More modern modems utilitze
   software switching to alter default states. In simple language, this
   means that your modem will alter its configuration based on commands
   given to it from a computer program (such as a terminal program). For
   example, with Hayes compatible modems, the command "ATZ" tells the modem
   to reset to default configuration. Other modems use physical switches to
   alter the default characteristics of the modem. If your modem has such
   switches, your modem manual will describe what each of them controls,
   and how to change them. In either case, the first goal is to alter your
   modem's configuration so that it will monitor carrier. With physical
   switch modems, locate the proper switch and make sure it is in the
   position for CD monitoring. With software-switch modems, your task is
   easier. Using the INIT program, you can alter the default initialization
   command issued to the modem each time you run the BBS. You can do this
   in Section 4 of INIT. Any commands you add to the command line must be
   entered just before the {. Your modem manual will tell you what the
   correct command is to monitor carrier. With many modems of this type,
   &C1 is the command needed to track carrier. Check your modem manual
   anyway to verify.







                                    - 1 -




                           WWIV Modem Documentation


   The second important modem setting is Data Terminal Ready, or DTR. It
   is used by your computer to control carrier. When DTR is turned off,
   the modem will drop carrier and hang up on the caller. As with CD, most
   modems are configured incorrectly for BBS use. There are two common
   settings for DTR: controlled and ignored. When DTR is monitored and
   controlled, your computer is capable of instructing the modem to drop
   carrier. When DTR is ignored, the computer cannot do this. Obviously,
   for bulletin board operation, DTR will need to be controlled. You can
   change this default by using the same procedure you used to alter the CD
   default. With most modems of the software-switch type, &D2, added to the
   modem init string in INIT, is the correct command.


                          Special Modem Requirements

   There are a wide variety of modems available in the marketplace today,
   and many of the newer ones require special configuration to work with
   WWIV. It is beyond the scope of this documentation to detail the steps
   needed to make all modems fully compatible with WWIV. Therefore, try
   to install your modem following the guidelines already presented. If
   you still have difficulty, contact the sysop of a WWIV Support BBS.
   See the text file, SUPPORT.LST, for a listing of support systems.




































                                    - 2 -