IBM ~ Cluster 1350

Facts and Features

July 6, 2004

| Cluster 1350 Building Block Machine type - model / feature Cluster function System packaging | IBM ~® xSeries® 335 8676-L1X, L2X, M1X, M2X, G1X, G2X compute node rack drawer (1U) | IBM ~ xSeries 345 8670-L1X, M1X, G1X management node rack drawer (2U) | IBM ~ xSeries 345 8670-L1X, M1X, G1X compute or storage node rack drawer (2U) |
| --- | --- | --- | --- |
| Number of servers per cluster (min/max) | 2 / 511c | 1 / 1 | 0 / 32 |
| Microprocessor type | Intel® Xeon™ | Intel Xeon | Intel Xeon |
| # of processors/system | 1 or 2 | 2 | 1 or 2 |
| Clock rates available | 2.8, 3.06, 3.2 GHz | 2.8, 3.06, 3.2 GHz | 2.8, 3.06, 3.2 GHz |
| System memory (standard/maximum) | 512MB / 8GB a | 512MB / 8GB a | 512MB / 8GB a |
| Level 2 (L2) cache | 512KB / 1MB b | 512KB / 1MB b | 512KB / 1MB b |
| Reliability, availability, serviceability |  |  |  |
| ECC memory | X | X | X |
| Service processor | X | X | X |
| Light path diagnostics | X | X | X |
| Hot-swappable disks e | X | X | X |
| Redundant hot-plug power | - | O | O |
| Redundant hot-plug cooling | - | O | O |
| Capacity |  |  |  |
| Maximum PCI slots available | 2 PCI-X (64-bit) | 5 PCI-X (1 32-bit, 4 64-bit) | 5 PCI-X (1 32-bit, 4 64-bit) |
| Maximum PCI bus speed (MHz) | 100 | 133 | 133 |
| Disk bays (standard / optional) | 1 / 1 | 1 / 5 | 1 / 5 |
| Minimum / maximum internal SCSI disk storage | 36.4GB / 293.6GB | 36.4GB / 880.8GB | 36.4GB / 880.8GB |
| Minimum / maximum internal IDE disk storage | 40GB / 240GB | - | - |
| Cluster interconnect |  |  |  |
| Gigabit Ethernet | X | X | X |
| Myrinet™-2000 | X | - | X |
| TopSpin® Infinband | X | - | X |
| Communications and connectivity |  |  |  |
| Serial/asynchronous | X | X | X |
| 10/100 Mbps Ethernet | X | X | X |
| Gigabit Ethernet | X | X | X |
| Systems management |  |  |  |
| Remote Supervisor Adapter | X | X | X |
| Storage interfaces |  |  |  |
| IBM Single Channel Ultra320 SCSI | X | X | X |
| ServeRAID-6I Ultra320 SCSI | - | X | X |
| ServeRAID-6M Ultra320 SCSI | X | X | X |
| ServeRAID-5I Controller 7 – Ultra320 or 160 | X | X (PCI slot 2 only) | X (PCI slot 2 only) |
| IBM TotalStorage® FC-20133 | X | X | X |

| Cluster 1350 Building Block Machine type - model / feature Cluster function System packaging | IBM ~ BladeCenter™ HS20 8832- L1X, 31X, G1X compute node rack drawer (7U/14 server blades) | IBM ~ 325 8835-21X, 22X, 31X, 32X, 51X, 52X, 61X, 62X, 71X, 72X compute or management node rack drawer (1U) |
| --- | --- | --- |
| Number of servers per cluster (min/max) | 2 / 511 c | 2 / 512 c |
| Microprocessor type | Intel Xeon | AMD Opteron™ |
| # of processors/system | 1 or 2 | 1 or 2 |
| Clock rates available | 2.8, 3.06, 3.2 GHz | 1.4, 1.6, 2.0, 2.2, 2.4 GHz |
| System memory (standard/maximum) | 512MB / 8GB a | 1GB / 12GB a |
| Level 2 (L2) cache | 512KB\1MB b | 1MB b |
| Reliability, availability, serviceability |  |  |
| ECC memory | X | X |
| Service processor | X | X |
| Light path diagnostics | X | - |
| Hot-swappable disks | O | X |
| Redundant hot-plug power | X | - |
| Redundant hot-plug cooling | X | - |
| Capacity |  |  |
| Maximum PCI slots available | 1 PCI-X (64-bit) | 2 PCI-X (64-bit) |
| PCI bus speed (MHz) | 100 (I/O expansion card connection) | 100 |
| Disk bays (standard / optional) | - | 1 / 1 |
| Minimum / maximum internal SCSI disk storage | 0GB / 146.8GB (with optional storage expansion unit) | 36.4GB / 293.6GB |
| Minimum / maximum internal IDE disk storage | 40GB / 80GB per blade | 80GB / 240GB |
| Cluster interconnect |  |  |
| Gigabit Ethernet | X (standard) | X |
| Myrinet-2000 | X | X |
| TopSpin Infinband | - | X |
| Communications and connectivity |  |  |
| Serial/asynchronous | X | X |
| 10/100 Mbps Ethernet | - | X |
| Gigabit Ethernet | X | X |
| Systems management |  |  |
| Remote Supervisor Adapter | - (Management Module standard in each chassis) | X (Imbedded systems management processor) |
| Storage interfaces |  |  |
| IBM Single Channel Ultra320 SCSI | O | - |
| ServeRAID-6I SCSI Controller | - | X |
| ServeRAID-6M Ultra320 SCSI | - | X |
| ServeRAID-5I Controller 7 | - | - |
| IBM TotalStorage FC-2-133 | O | - |

IBM ~ Cluster 1350 building blocks include:

Server Nodes

8676 - L1X, L2X, M1X, M2X, G1X, G2X			xSeries 335, compute node

8670 - L1X, M1X, G1X					xSeries 345, management node

8670 - L1X, M1X, G1X  					xSeries 345, compute/storage node

8835 - 21X, 22X, 31X, 32X, 51X, 52X, 61X, 62X,		e325, compute node

71X, 72X

8832 - L1X, 31X, G1X	 				BladeCenter HS20, compute node

Interconnect options

Gigabit Ethernet

Myrinet-2000

TopSpin Infiniband

Racks

1410-42X 		          	IBM ~ Cluster 42U Enterprise Rack

1410-25X			IBM ~ Cluster 25U Enterprise Rack

1417-1LX			IBM ~ Cluster 11U Enterprise Rack

External storage options

1722-60U*		          IBM FAStT600 Storage Server

24P8066		          IBM FAStT600 Two EXP700 Attachment

24P8215		          IBM FAStT600 w/Turbo Attachment

24P8149		          IBM FAStT 1st EXP700 Attachment

24P8151		          IBM FAStT 2nd EXP700 Attachment

1742-90U*		          IBM FAStT900 Storage Server Model

1742-1RU*		          IBM FAStT700 Storage Server Model 1RU (Fibre Channel-attached) (4U)

1740-1RU*		          IBM FAStT EXP700 FC Expansion Unit

1733-1RU		          IBM FAStT EXP400 Ultra320 SCSI Expansion Unit

1733-1RU		          IBM EXP Ultra 320 SCSI Expansion Unit

1710-10U		          IBM FASt EXP100 Storage Expansion

*  In Europe / Middle East / Africa:  1722-60X; 1742-90X; 1742-1RX; 1740-1RX

Software

The Cluster 1350 supports the following Linux Distributions:

- RHEL 3.0

  - RHEL 3.0 WS 32 bit (all managed nodes) and WS 64 bit (e325-managed nodes)

  - RHEL 3.0 ES 32 bit (e325 management node)

  - RHEL 3.0 AS 32 bit (x345 management node) and AS 64 bit (e325 management node)

- SLES 8

  - SLES 8 32-bit (all nodes except e325 management node)

  - SLES 8 64-bit (all e325 nodes including management node)

The following software is available for the Cluster 1350:

  - Linux Cluster Install Tool (LCIT) V3.2

  - IBM Cluster Systems Management (CSM) for Linux V1.3.3

  - IBM General Parallel File System (GPFS) for Linux V2.2 (optional)

IBM ~ Cluster 1350 node scalability:

The minimum and maximum number of nodes per Cluster 1350 is shown in the following table.  Larger clusters are available through special order.

| Type of Node | Minimum | Maximum |
| --- | --- | --- |
| Compute Node | 2 | 511 |
| Management Node | 1 | 1 |
| Storage Node | 0 | 32 |
| Total Nodes in Cluster 1350 | 3 | 512 |

Footnotes

X = Supported

- = Not supported

O = Optionally Available

a = Shared memory

b = Per processor (model dependent)

c = Larger clusters available via special order

d = 2 to 512 as cluster node

| IBM services IBM services provide the capabilities and solutions needed to manage virtually every aspect of an open systems environment and at any level chosen. They complement the support already included with IBM ~ Cluster 1350 systems. IBM world-class services and support allow you to better manage resources and focus on what matters most – your business. The Cluster 1350 includes on-site hardware installation and setup. Customers must obtain the required version of the Linux operating system as specified by IBM, and may choose to have IBM install Linux and CSM using optional fee-based Linux cluster installation services, have this service performed by a qualified business partner, or install it themselves. The additional Linux cluster installation services may include customization of the cluster to meet specific customer needs, on-site skills transfer and troubleshooting, project management services for complex cluster installations, and installation of additional software. IBM also offers Support Line for Linux clusters, which extends the maintenance support provided with the Cluster 1350 and includes support for IBM hardware and software, Linux operating system and Open Source, and non-IBM components integrated into the solution. Project support services Operating system porting/conversion Operating system migration assistance Systems integration IBM and non-IBM software customization IBM application development Site planning services Continuing support services Customer Support Center services Electronic/voice IBM and non-IBM hardware and software On-site software maintenance support Capacity planning Maintenance services, including multivendor environment Technical/application specialists Network custom services Education | IBM financing IBM Global Financing provides an additional incentive. An array of attractive and flexible financing programs eases the acquisition of new technology and helps protect from the risk of obsolescence. Financing may be available to credit-qualified customers. Rates are based on credit rating, financing terms, and other options. Other restrictions may apply. More information Contact your IBM marketing representative or IBM Business Partner. Access http://www.ibm.com/eserver/clusters on the Internet to get to the IBM ~ cluster page1. Product announcement letters containing more details on hardware and software offerings are available at http://www.ibm.com/common/ssi. | © Copyright IBM Corporation 2004 IBM Corporation Marketing Communications Systems and Technology Group Route 100 Somers, New York 10589 Produced in the United States of America July 2004 All Rights Reserved This document was developed for products and/or services offered in the United States. IBM may not offer the products, features, or services discussed in this document in other countries. The information may be subject to change without notice. Consult your local IBM business contact for information on the products, features and services available in your area. All statements regarding IBM future directions and intent are subject to change or withdrawal without notice and represent goals and objectives only. IBM, the IBM logo, the e-business logo, ~, BladeCenter, TotalStorage and xSeries are trademarks or registered trademarks of International Business Machines Corporation in the United States or other countries or both. A full list of U.S. trademarks owned by IBM may be found at http://www.ibm.com/legal/copytrade.shtml. Linux is a registered trademark of Linus Torvalds in the United States, other countries or both. Intel and Xeon are trademarks or registered trademarks of Intel Corporation or its subsidiaries in the United States and other countries. AMD Opteron is a trademark of Advanced Micro Devices, Inc. Myrinet is a trademark of Myricom, Inc. Topspin is a registered trademark of Topspin Communications, Inc. Other company, product, and service names may be trademarks or service marks of others. IBM hardware products are manufactured from new parts, or new and used parts. Regardless, our warranty terms apply. Photographs show engineering and design models. Changes may be incorporated in production models. Copying or downloading the images contained in this document is expressly prohibited without the written consent of IBM. This equipment is subject to FCC rules. It will comply with the appropriate FCC rules before final delivery to the buyer. Information concerning non-IBM products was obtained from the suppliers of these products. Questions on the capabilities of the non-IBM products should be addressed with the suppliers. 1 The IBM home page on the Internet can be found at http://www.ibm.com. Cluster 1350 F&F - 07 |
| --- | --- | --- |